## Slide 1
Chapter 7 Computer Arithmetic
Smruti Ranjan Sarangi, IIT Delhi
Computer Organisation and Architecture
PowerPoint Slides
PROPRIETARY MATERIAL. © 2014 The McGraw-Hill Companies, Inc. All rights reserved. No part of this PowerPoint slide may be displayed, reproduced or distributed in any form or by any means, without the prior written permission of the publisher, or used beyond the limited distribution to teachers and educators permitted by McGraw-Hill for their individual course preparation. PowerPoint Slides are being provided only to authorized professors and instructors for use in preparing for classes using the affiliated textbook. No other use or distribution of this PowerPoint slide is permitted. The PowerPoint slide may not be sold and may not be distributed or be used by any student or any other third party. No part of the slide may be reproduced, displayed or distributed in any form or by any means, electronic or otherwise, without the prior written permission of McGraw Hill Education (India) Private Limited.

## Slide 2
Download the pdf of the book
www.basiccomparch.com
videos
Slides, software, solution manual
Print version
(Publisher: WhiteFalcon, 2021)
Available on e-commerce sites.
The pdf version of the book and all the learning resources can be freely downloaded from the website: www.basiccomparch.com
2nd version

## Slide 3: Outline
Addition
Multiplication
Division
Floating Point Addition
Floating Point Multiplication
Floating Point Division

## Slide 4: Adding Two 1 bit Numbers
Let us add two 1 bit numbers – a and b
  0 + 0 = 00
  1 + 0 = 01
  0 + 1 = 01
  1 + 1 = 10
The lsb of the result is known, as the sum, and the msb is known as the carry

## Slide 5: Sum and Carry
a
a
a
b
carry
sum
Truth Table
a
b
s
c
0
0
0
0
0
1
1
0
1
0
1
0
1
1
0
1
c = a.b

## Slide 6: Half Adder
Adds two 1 bit numbers to produce a 2 bit result
a
b
a
b
C
S
Half
adder
a
b
S
C

## Slide 7
Full Adder
Add three 1 bit numbers to produce a 2 bit output
a | b | cin | s | cout
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 8: Equations for the Full Adder
s

## Slide 9: Circuit for the Full Adder
a
b
a
b
Full
adder
a
b
S
a
b
c
in
c
in
c
out
c
in
s
c
in
c
out

## Slide 10: Addition of two n bit numbers
We start from the lsb
Add the corresponding pair of bits and the carry in
Produce a sum bit and a carry out
1 0 1 1
0 1 0 1
1 0 0 0 0
1
1
1
1

## Slide 11: Observations
We keep adding pairs of bits, and proceed from the lsb to the msb
If a carry is generated, we add it to the next pair of bits
At the last step, if a carry is generated, then it becomes the msb of the result
The carry effectively ripples through the bits

## Slide 12: Ripple Carry Adder
Half
adder
A
1
B
1
A
2
B
2
c
A
3
B
3
c
A
n
B
n
c
Full
adder
Result
c
carry

## Slide 13: Operation of the Ripple Carry Adder
Problem : Add A + B
Number the bits : A1 to An and B1 to Bn
  lsb → A1 and B1
  msb → An and Bn
Use a half adder to add A1 and B1
Send the carry(c) to a full adder that adds : A2 + B2 + c
Proceed in a similar manner till the msb

## Slide 14: How long does the Ripple Carry Adder take ?
Time :
  Time of half adder : th
  Time of full adder : tf
  Total Time : th + (n-1)tf

## Slide 15: Asymptotic Time Complexity
Most of the time, we are primarily interested in the order of the function
For example : we are only interested in the n2 term in (2n2 + 3n + 4)
We do not care about the constants, and terms with smaller exponents
  3n and 4
We can thus say that :
  2n2 + 3n + 4 is order of (n2)

## Slide 16: The O notation
Formally :
  We say that: f(n) = O(g(n))
  if, , for all . Here c is a positive constant.
In simple terms:
  Beyond a certain n , g(n) is greater-than-equal to a certain constant times f(n)
    For example, beyond 15, (n2 + 10n + 16) ≤ 2n2

## Slide 17: Example of the big O Notation
f(n) = 3n2 + 2n + 3. Find its asymptotic time complexity.
Answer:
f(n) = 3n2 + 2n + 3
≤ 3n2 + 2n2 + 3n2 (n > 1)
≤ 8(n2)
Hence, f(n) = O(n2).
0
100
200
300
400
500
600
700
800
0
2
4
6
8
10
time
f(n)
8n^2
n
8n2 is a strict upper bound on f(n) as shown in the figure.

## Slide 18: Big O Notation - II
We shall use the asymptotic time complexity metric (big O notation) to characterize the time taken by different adders
Example:
f(n) = 0.00001n100 + 10000n99 + 234344. Find its asymptotic time complexity.
Answer: f(n) = O(n100)

## Slide 19: Ripple Carry Adders and Beyond
Time complexity of a ripple carry adder :
  O(n)
Can we do better than O(n) ?
Yes

## Slide 20: Carry Select Adder O(√n) time
Group bits into blocks of size (k)
If we are adding two 32 bit numbers A and B, and k = 4, then the blocks are :
Produce the result of each block with a small ripple carry adder
A
32
A
1
A
2
A
3
A
4
A
31
A
30
A
29
B
32
B
1
B
2
B
3
B
4
B
31
B
30
B
29
A
5
A
6
A
7
A
8
B
5
B
6
B
7
B
8
Carry propagating
across blocks

## Slide 21: Carry Select Adder - II
In this case, the carry propagates across blocks
Time complexity is O(n)
Idea :
  Add the numbers in each block in parallel
  Stage I : For each block, produce two results
    Assuming an input carry of 0
    Assuming an input carry of 1

## Slide 22: Carry Select Adder – Stage II
For each block we have two results available
Result → (k sum bits), and 1 carry out bit
Stage II
  Start at the least significant block
    The input carry is 0
    Choose the appropriate result from stage I
  We now know the input carry for the second block
    Choose the appropriate result
    Result contains the input carry for the third block

## Slide 23: Carry Select Adder – Stage II
Given the result of the second block
  Compute the carry in for the third block
  Choose the appropriate result
Proceed till the last block
At the last block (most significant positions)
  Choose the correct result
  The carry out value, is equal to the carry out of the entire computation.

## Slide 24: How much time did we take ?
Our block size is k
  Stage I takes k units of time
There are n/k blocks
  Stage II takes (n/k) units of time
Total time : (k + n/k)

## Slide 25: Time Complexity of the Carry Select Adder
T = O(√n + √n) = O(√n)
Thus, we have a √n time adder
Can we do better ?
Yes

## Slide 26: Carry Lookahead Adder (O(log n))
The main problem in addition is the carry
If we have a mechanism to compute the carry quickly, we are done
Let us thus focus on computing the carry without actually performing an addition

## Slide 27: Generate and Propagate Functions
Let us consider two corresponding bits of A and B
  Ai and Bi
Generate function : A new carry is generated (Cout = 1)
Propagate function : Cout = Cin
Generate and Propagate Functions are :

## Slide 28: Using the G and P Functions
If we have the generate and propagate values for a bit pair, we can determine the carry out
Cout = gi + pi.Cin

## Slide 29: Example
Example:
Let Ai = 0, Bi = 1. Let the input carry be Cin. Compute
gi, pi, and Cout.
Answer:

## Slide 30: G and P for Multi-bit Systems
Couti → output carry for ith bit pair
Cini → input carry for ith bit pair
gi → generate value for ith bit pair
pi → propagate value for ith bit pair

## Slide 31: G and P for Multibit Systems - II

## Slide 32: G and P for multibit Systems - III

## Slide 33: Patterns
1 bit
2 bit
3 bit
4 bit
n bit

## Slide 34: Computing G and P Quickly
Let us divide a block of n bits into two parts
Let the carry out and carry in be : Cout and Cin
We want to find the relationship between
  G1,n, P1,n and (Gm+1,n, G1,m, Pm+1,n, P1,m)
n
1,m
m+1,n
C
out
C
in
C
sub

## Slide 35: Computing G and P Quickly - II
G1,n = Gm+1,n + Pm+1,n.G1,m
P1,n = Pm+1,n.P1,m

## Slide 36: Insight into Computing G and P quickly
Insight :
  We can compute G and P for a large block
    By first computing G and P for smaller sub-blocks
    And, then combining the solutions to find the value of G and P for the larger block
  Fast algorithm to compute G and P
    Use divide-and-conquer
    Compute G and P functions in O (log (n)) time

## Slide 37: Carry Lookahead Adder – Stage I
  Compute G and P functions for all the blocks
  Combine the solutions to find G and P functions for sets of 2 blocks
  Combine the solutions fo find G and P functions for sets of 4 blocks
  ….
  ….
  Find the G and P functions for a block of size : 32 bits

## Slide 38: Carry Lookahead Adder – Stage I
32
31
30
3
2
1
29
4
G,P
32-31
G,P
30-29
G,P
2-1
G,P
4-3
G,P
32-29
G,P
4-1
G,P
32-25
G,P
24-17
G,P
16-9
G,P
8-1
G,P
32-17
G,P
16-1
G,P
32-1
Block 1
Block 16
level 4
level 5
level 3
level 2
level 1
level 0
Computation

## Slide 39: CLA Adder – Stage I
Compute G, P for increasing sizes of blocks in a tree like fashion
Time taken :
  Total : log(n) levels
  Time per level : O(1)
  Total Time : O(log(n))

## Slide 40: CLA Adder – Stage II
32
31
3
2
29
4
G,P
32-31
G,P
30-29
G,P
2-1
G,P
4-3
G,P
32-29
G,P
4-1
G,P
32-25
G,P
24-17
G,P
16-9
G,P
8-1
G,P
32-17
G,P
16-1
G,P
32-1
G,P
28-25
c
in
c
in
c
in
c
in
c
in
c
out
G,P
20-17
G,P
18-17
17
18
2-bit RC Adder
2-bit RC Adder
2-bit RC Adder
2-bit RC Adder
2-bit RC Adder
level 4
level 5
level 3
level 2
level 1
level 0
G,P
r1- r2
c
in
c
out
G,P block
1
1
1
1
1
32
Result Bits
Computation
30
1

## Slide 41: Connection of the G,P Blocks
Each G,P block represents a range of bits (r2, r1) (r2 > r1)
  The (r2, r1) G,P block is connected to all the blocks of the form (r3, r2+1)
  The carry out of one block is an input to all the blocks that it is connected with
Each block is connected to another block at the same level, and to blocks at lower levels

## Slide 42: Operation of CLA – Stage II
We start at the leftmost blocks in each level
  We feed an input carry value of Cin1
  Each such block computes the output carry, and sends it to the all the blocks that it is connected to
Each connected block
  Computes the output carry
  Sends it to all the blocks that it is connected to
The carry propagates to all the 2 bit RC adders

## Slide 43: CLA Adder – Stage II
32
31
3
21
29
4
G,P
32-31
G,P
30-29
G,P
2-1
G,P
4-3
G,P
32-29
G,P
4-1
G,P
32-25
G,P
24-17
G,P
16-9
G,P
8-1
G,P
32-17
G,P
16-1
G,P
32-1
G,P
28-25
c
in
c
in
c
in
c
in
c
in
c
out
G,P
20-17
G,P
18-17
17
18
2-bit RC Adder
2-bit RC Adder
2-bit RC Adder
2-bit RC Adder
2-bit RC Adder
level 4
level 5
level 3
level 2
level 1
level 0
G,P
r1- r2
c
in
c
out
G,P block
1
1
1
1
1
32
Result Bits
Computation
30

## Slide 44: Time Complexity
In a similar manner, the carry propagates to all the RC adders at the zeroth level
Each of them compute the correct result
Time taken by Stage II :
  Time taken for a carry to propagate from the (16,1) node to the RC adders
  O(log(n))
Total time : O(log(n) + log(n)) = O(log(n))

## Slide 45
Time complexities of different adders:
Ripple Carry Adder:
Carry Select Adder:
Carry Lookahead Adder:

## Slide 46: Outline
Addition
Multiplication
Division
Floating Point Addition
Floating Point Multiplication
Floating Point Division

## Slide 47: Multiplicands
13 → Multiplicand
9 → Multiplier
117 → Product
1 3
9
1 1 7
1 0 0 1
1 1 0 1
0 0 0 0
0 0 0 0
1 1 0 1
1 1 0 1
1 1 1 0 1 0 1
(a)
(b)
Partial sums

## Slide 48: Basic Multiplication
Consider the lsb of the multiplier
  If it is 1, write the value of the multiplicand
  If it is 0, write 0
For the next bit of the multiplier
  If it is 1, write the value of the multiplicand shifted by 1 position to the left
  If it is 0, write 0
Keep going ….

## Slide 49: Definitions
If the multiplier has m bits, and the multiplicand has n bits
  The product requires (m+n) bits
Partial sum: It is equal to the value of the multiplicand left
shifted by a certain number of bits, or it is equal to 0.
Partial product: It is the sum of a set of partial sums.

## Slide 50: Multiplying 32 bit numbers
Let us design an iterative multiplier that multiplies two 32 bit signed values to produce a 64 bit result
What did we prove before
  Multiplying two signed 32 bit numbers, and saving the result as a 32 bit number is the same as
  Multiplying two unsigned 32 bit numbers (assuming no overflows)
We did not prove any result regarding saving the result as a 64 bit number

## Slide 51: Class Work
Theorem: A signed n bit number . Ai is the ith bit in A’s 2’s
complement based binary representation (the first bit is the LSB). A1...n-1 is a binary
number containing the first n-1 digits of A’s binary 2’s complement representation.

## Slide 52: Iterative Multiplier
Multiplicand (N), Multiplier (M), Product(P) = MN
U is a 33 bit register and V is a 32 bit register
beginning : V contains the multiplier, U = 0
UV is one register for the purpose of shifting
U
V
Multiplicand

## Slide 53: Algorithm
Algorithm 1: Algorithm to multiply two 32 bit numbers and produce a 64 bit result
Data: Multiplier in V , U = 0, Multiplicand in N
Result: The lower 64 bits of UV contains the product
i ← 0
for i < 32 do
i ← i + 1
if LSB of V is 1 then
if i < 32 then
U ← U + N
end
else
U ← U − N
end
end
UV ← UV >> 1 (arithmetic right shift)
end

## Slide 54: Example
1 add 2
1 add 2
0 --
0 --
00010
0011
after shift:
00001
0001
1
00000
0011
beginning:
U
V
Multiplier (M)
0011
Multiplicand (N)
0010
Product(P)
0110
before shift:
00011
0001
after shift:
00001
1000
2
before shift:
00001
1000
after shift:
00000
1100
3
before shift:
00000
1100
after shift:
00000
0110
4
before shift:
2
3
6

## Slide 55: 3 * (-2)
0 --
1 add 3
1 add 3
1 sub 3
00000
1110
after shift:
00000
0111
1
00000
1110
beginning:
U
V
Multiplier (M)
1110
Multiplicand (N)
0011
Product(P)
1010
before shift:
00011
0111
after shift:
00001
1011
2
before shift:
00100
1011
after shift:
00010
0101
3
before shift:
11111
0101
after shift:
11111
1010
4
before shift:
3
-2
-6

## Slide 56: Operation of the Algorithm
Take a look at the lsb of V
  If it is 0 → do nothing
  If it is 1 → Add N (multiplicand) to U
Right shift
  Right shifting the partial product is the same as left shifting the multiplicand, which
  Needs to be done in every step
Last step is different

## Slide 57: The Last Step ...
In the last step
  lsb of V = msb of M (multiplier)
  If it is 0 → do nothing
If it is 1
  Multiplier is negative
  Recall : A = A1 .. n-1 - 2n-1An
  Hence, we need to subtract the multiplicand if the msb of the multiplier is 1

## Slide 58: Time Complexity
There are n loops
  Each loop takes log(n) time
  Total time : O(n log(n))

## Slide 59: Booth Multiplier
We can make our iterative multiplier faster
If there are a continuous sequence of 0s in the multiplier
  do nothing
If there is a continous sequnce of 1s
  do something smart

## Slide 60: For a Sequence of 1s
Sequence of 1s from position i to j
  Perform (j – i + 1) additions
New method
  Subtract the multiplicand when we scan bit i ( ! count starts from 0)
  Keep shifting the partial product
  Add the multiplicand(N), when we scan bit (j+1)
  This process, effectively adds (2j+1 – 2i) * N to the partial product
  Exactly, what we wanted to do …

## Slide 61: Operation of the Algorithm
Consider bit pairs in the multiplier
  (current bit, previous bit)
  Take actions based on the bit pair
  Action table
(current value, previous value)
Action
0,0
-
1,0
subtract multiplicand from U
1,1
-
0,1
add multiplicand to U

## Slide 62: Booth's Algorithm
Algorithm 2: Booth’s Algorithm to multiply two 32 bit numbers to produce a 64 bit result
Data: Multiplier in V , U = 0, Multiplicand in N
Result: The lower 64 bits of UV contain the result
i ← 0
prevBit ← 0
for i < 32 do
i ← i + 1
currBit ← LSB of V
if (currBit,prevBit) = (1,0) then
U ← U − N
end
else if (currBit,prevBit) = (0,1) then
U ← U + N
end
prevBit ← currBit
UV ← UV >> 1 (arithmetic right shift)
end

## Slide 63: Outline of a Proof
Multiplier (M) is positive
  msb = 0
  Divide the multiplier into a sequence of continuous 0s and 1s
    01100110111000 → 0,11, 00, 11, 0, 111, 000
  For sequence of 0s
    Both the algorithms (iterative, Booth) do not add the multiplicand
    For a run of 1s (length k)
      The iterative algorithm performs k additions
      Booth's algorithm does one addition, and one subtraction.
      The result is the same

## Slide 64: Outline of a Proof - II
Negative multipliers
  msb = 1
M = -2n-1 + Σ(i=1 to n-1)Mi2n-1 = -2n-1 + M'
  M' = Σ(i=1 to n-1)Mi2n-1
Consider two cases
  The two msb bits of M are 10
  The two msb bits of M are 11

## Slide 65: Outline of a Proof - III
Case 10
  Till the (n-1)th iteration both the algorithms have no idea if the multiplier is equal to M or M'
  At the end of the (n-1)th iteration, the partial product is:
    Iterative algorithm : M'N
    Booth's algorithm : M'N
      If we were multiplying (M' * N), no action would have been taken in the last iteration. The two msb bits would have been 00. There is no way to differentiate this case from that of computing MN in the first (n-1) iterations.

## Slide 66: Outline of a Proof - IV
Last step
  Iterative algorithm :
    Subtract 2n-1N from U
  Booth's algorithm
    The last two bits are 10 (0 → 1 transition)
    Subtract 2n-1N from U
  Both the algorithms compute :
    MN = M'N – 2n-1N
    in the last iteration

## Slide 67: Outline of a Proof - V
Case 11
Suppose we were multiplying M' with N
  Since (M' > 0), the Booth multiplier will correctly compute the product as M'N
  The two msb bits of M' are (01)
  In the last iteration (currBit, prevBit) is 01
  We would thus add 2n-1N in the Booth's algorithm to the partial product in the last iteration
  The value of the partial product at the end of the (n-1)th iteration is thus :
    M'N - 2n-1N

## Slide 68: Outline of a Proof - VI
When we multiply M with N
  In the (n-1)th iteration, the value of the partial product is : M'N – 2n-1N
  Because, we have no way of knowing if the multiplier is M or M' at the end of the (n-1)th iteration
  In the last iteration the msb bits are 11
    no action is taken
  Final product : M'N – 2n-1N = MN (correct)

## Slide 69
00 --
10 add -3
01 add 3
00 --
00000
0010
after shift:
00000
0001
1
00000
0010
beginning:
U
V
Multiplier (M)
0010
Multiplicand (N)
00011
Product(P)
0110
before shift:
11101
0001
after shift:
11110
1000
2
before shift:
00001
1000
after shift:
00000
1100
3
before shift:
00000
1100
after shift:
00000
0110
4
before shift:
3
2
6

## Slide 70
00 --
10 add -3
11 --
11 --
00000
1110
after shift:
00000
0111
1
00000
1110
beginning:
U
V
Multiplier (M)
1110
Multiplicand (N)
00011
Product(P)
1010
before shift:
11101
0111
after shift:
11110
1011
2
before shift:
11110
1011
after shift:
11111
0101
3
before shift:
11111
0101
after shift:
11111
1010
4
before shift:
3
-2
-6

## Slide 71: Time Complexity
O(n log(n))
Worst case input
  Multiplier = 10101010... 10

## Slide 72: O(log(n)2) Multiplier
Consider an n bit multiplier and multiplicand
Let us create n partial sums
1 0 0 1
1 1 0 1
1 0 0 1
0 0 0 0 0
1 0 0 1 0 0
1 0 0 1 0 0 0
partial sums

## Slide 73: Tree Based Adder for Partial Sums
P
1
P
2
P
3
P
4
P
n-3
P
n-2
P
n-1
P
n
Final product
log(n) levels

## Slide 74: Time Complexity
There are log(n) levels
Each level takes
  Maximum log(2n) time
    Adds two 2n bit numbers
Total time :
  O(log(n) * log(n)) = O(log (n)2)

## Slide 75: Carry Save Adder
A + B + C = D + E
Takes three numbers, and produces two numbers
A
B
C
D
E
Carry
save
adder

## Slide 76: 1 bit CSA Adder
Add three bits – a, b, and c
  such that a + b + c = 2d + e
  d and e are also single bits
We can conveniently set
  e to the sum bit
  d to the carry bit

## Slide 77: n-bit CSA Adder
+

## Slide 78: n-bit CSA Adder - II
How to generate D and E ?
  Add all the corresponding sets of bits (Ai, Bi, and Ci) independently
  set Di to the carry bit produced by adding (Ai, Bi, and Ci)
  set Ei to the sum bit produced by adding (Ai, Bi, and Ci)
Time Complexity :
  All the additions are done in parallel
  This takes O(1) time

## Slide 79: Wallace Tree Multiplier
Basic Idea
  Generate n partial sums
  Partial sum : Pi = 0, if the ith bit in the multiplier is 0
  Pi = N << (i-1), if the the ith bit in the multiplier is 1
  Can be done in parallel : O(1) time
Add all the n partial sums
  Use a tree based adder

## Slide 80: Tree of CSA Adders
Carry Lookahead
Adder
P
1
P
2
P
3
Final product
log (n) levels
CSA
P
4
P
5
P
6
CSA
CSA
P
n-5
P
n-4
P
n-3
CSA
P
n-2
P
n-1
P
n
CSA
CSA
CSA
3/2

## Slide 81: Tree of CSA Adders
Group the partial sums into sets of 3
  Use an array of CSA adders to add 3 numbers (A,B,C) to produce two numbers (D,E)
  Hence, reduce the set of numbers by 2/3 in each level
After log3/2(n) levels, we are left with only two numbers
Use a CLA adder to add them

## Slide 82: Time Complexity
Time to generate all the partials sums → O(1)
Time to reduce n partial sums to sum of two numbers
  Number of levels → O(log(n))
  Time per level → O(1)
  Total time for this stage → O(log(n))
Last step
  Size of the inputs to the CLA adder → (2n-1) bits
  Time taken → O(log(n))
Total Time : O(log(n))

## Slide 83: Outline
Addition
Multiplication
Division
Floating Point Addition
Floating Point Multiplication
Floating Point Division

## Slide 84
THE END