## Slide 1: The Memory System
PROPRIETARY MATERIAL. © 2014 The McGraw-Hill Companies, Inc. All rights reserved. No part of this PowerPoint slide may be displayed, reproduced or distributed in any form or by any means, without the prior written permission of the publisher, or used beyond the limited distribution to teachers and educators permitted by McGraw-Hill for their individual course preparation. PowerPoint Slides are being provided only to authorized professors and instructors for use in preparing for classes using the affiliated textbook. No other use or distribution of this PowerPoint slide is permitted. The PowerPoint slide may not be sold and may not be distributed or be used by any student or any other third party. No part of the slide may be reproduced, displayed or distributed in any form or by any means, electronic or otherwise, without the prior written permission of McGraw Hill Education (India) Private Limited.
1
Processor Design
The Language of Bits
Smruti Ranjan Sarangi, IIT Delhi
Computer Organisation and Architecture
PowerPoint Slides
Chapter 10 The Memory System

## Slide 2
Download the pdf of the book
www.basiccomparch.com
videos
Slides, software, solution manual
Print version
(Publisher: WhiteFalcon, 2021)
Available on e-commerce sites.
The pdf version of the book and all the learning resources can be freely downloaded from the website: www.basiccomparch.com
2nd version

## Slide 3: Outline
Overview of the Memory System
Caches
Details of the Memory System
Virtual Memory

## Slide 4: Need for a Fast Memory System
We have up till now assumed that the memory is one large array of bytes
  Starts a 0, and ends at (232 – 1)
  Takes 1 cycle to access memory (read/write)
All programs share the memory
  We somehow magically avoid overlaps between programs running on the same processor
  All our programs require less than 4 GB of space

## Slide 5
All the programs running on my machine. The CPU of course runs one program at a time. Switches between programs periodically.

## Slide 6: Regarding all the memory being homogeneous  NOT TRUE
Should we make our memory using only flip-flops ?
  10X the area of a memory with SRAM cells
  160X the area of a memory with DRAM cells
  Significantly more power !!!
Cell Type
Area
Typical Latency
Master Slave D flip flop
0.8
Fraction of a cycle
SRAM cell in an array
0.08
1-5 cycles
DRAM cell in an array
0.005
50-200 cycles
Typical Values

## Slide 7: Tradeoffs
Tradeoffs
  Area, Power, and Latency
  Increase Area → Reduce latency, increase power
  Reduce latency → increase area, increase power
  Reduce power → reduce area, increase latency
We cannot have
the best of all worlds

## Slide 8: What do we do ?
We cannot create a memory of just flip flops
  We will hardly be able to store anything
We cannot create a memory of just SRAM cells
  We need more storage, and we will not have a 1 cycle latency
We cannot create a memory of DRAM cells
  We cannot afford 50+ cycles per access

## Slide 9: Memory Access Latency
What does memory access latency depend on ?
  Size of the memory → larger is the size, slower it is
  Number of ports → More are the ports (parallel accesses/cycle), slower is the memory
  Technology used → SRAM, DRAM, flip-flops

## Slide 10: Solution : Leverage Patterns
Look at an example in real life
  Sofia's workplace
desk
shelf
cabinet

## Slide 11: A Protocol with Books
Sofia keeps the
  most frequently accessed books on her desk
  slightly less frequently accessed books on the shelf
  rarely accessed books in the cabinet
Why ?
  She tends to read the same set of books over and over again, in the same window of time → Temporal Locality

## Slide 12: Protocol – II
If Sofia takes a computer architecture course
  She has comp. architecture books on her desk
After the course is over
  The architecture books go back to the shelf
  And, vacation planning books come to the desk
  Idea : Bring all the vacation planning books in one go. If she requires one, in high likelihood she might require similar books in the near future.

## Slide 13: Temporal and Spatial Locality
Spatial Locality
It is a concept that states that if a resource is accessed at some point of
time, then most likely similar resources will be accessed again in the near
future.
Temporal Locality
It is a concept that states that if a resource is accessed at some point of
time, then most likely it will be accessed again in a short period of time.

## Slide 14: Temporal Locality in Programs
Let us verify if programs have temporal locality
Stack distance
  Have a stack to store memory addresses.
  Whenever, we access an address → we bring it to the top of the stack
  Stack distance → Distance from the top of the stack to where the element was found
  Quantifies reuse of addresses

## Slide 15: Stack Distance
top
memory address
stack
distance

## Slide 16: Stack Distance Distribution
Benchmark : Set of perl programs
0
50
100
150
200
250
stack distance
0.00
0.05
0.10
0.15
0.20
0.25
0.30
p
r
o
b
a
b
i
l
i
t
y
Most stack distances are very low  High Temporal Locality

## Slide 17: Address Distance
Maintain a sliding window of the last K memory accesses
Address distance :
  The ith address distance is the difference in the memory addresses of the ith memory access, and the closest address in the set of last K memory accesses.
  Shows the similarity in addresses

## Slide 18: Address Distance Distribution
K=10, benchmark consisting of perl programs
0.00
0.05
0.10
0.15
0.20
0.25
0.30
p
r
o
b
a
b
i
l
i
t
y
–100
–50
0
50
100
address distance
Address distances are typically ± 20  High Spatial Locality

## Slide 19: Exploiting Temporal Locality
Use a hierarchical memory system
L1 (SRAM cells), L2 (SRAM cells), Main Memory (DRAM cells)
L1 cache
L2 cache
Main memory
Cache hierarchy

## Slide 20: The Caches
The L1 cache is a small memory (8-64 KB) composed of SRAM cells
The L2 cache is larger and slower (128 KB – 4 MB) (SRAM cells)
The main memory is even larger (1 – 64 GB) (DRAM cells)
Cache hierarchy
  The main memory contains all the memory locations
  The caches contain a subset of memory locations

## Slide 21: Access Protocol
Inclusive Cache Hierarcy
  addresses(L1) ⊏ addresses(L2) ⊏ addresses(main memory)
Protocol
  First access the L1 cache. If the memory location is present, we have a cache hit.
    Perform the access (read/write)
  Otherwise, we have a cache miss.
    Fetch the value from the lower levels of the memory system, and populate the cache.
    Follow this protocol recursively

## Slide 22: Advantage
Typical Hit Rates, Latencies
  L1 : 95 %, 1 cycle
  L2 : 60 %, 10 cycles
  Main Memory : 100 %, 300 cycles
Result :
  95 % of the memory accesses take a single cycle
  3 % take, 10 cycles
  2 % take, 300 cycles

## Slide 23: Exploiting Spatial Locality
Conclusion from the address locality plot
  Most of the addresses are within +/- 25 bytes
Idea :
  Group memory addresses into sets of n bytes
  Each group is known as a cache line or cache block
  A cache block is typically 32, 64, or 128 bytes
Reason: Once we fetch a block of 32/64 bytes. A lot of accesses in a short time interval will find their data in the block.

## Slide 24: Outline
Overview of the Memory System
Caches
Details of the Memory System
Virtual Memory

## Slide 25: Overview of a Basic Cache
Saves a subset of memory values
  We can either have hit or miss
  The load/store is successful if we have a hit
Memory
address
Store value
Load value
Cache
Hit/Miss

## Slide 26: Basic Cache Operations
lookup → Check if the memory location is present
data read → read data from the cache
data write → write data to the cache
insert → insert a block into a cache
replace → find a candidate for replacement
evict → throw a block out of the cache

## Slide 27: Cache Lookup
Running example : 8 KB Cache, block size of 64 bytes, 32 bit memory system
Let us have two SRAM arrays
  tag array → Saves a part of the block address such that the block can be uniquely identified
  block array → Saves the contents of the block
  Both the arrays have the same number of entries

## Slide 28: Structure of a Cache
Tag array
Address
Data array
Cache controller
Store
value
Load
value
Hit / Miss

## Slide 29: Fully Associative Cache
We have 213 / 26 = 128 entries
A block can be saved in any entry
26 bit tag, and 6 bit offset
Tag array
(CAM cells)
Tag
Encoder
Hit/Miss
Index of the
matching entry
Data array
Tag
Offset
Address format

## Slide 30: Implementation of the FA Cache
We use an array of CAM cells for the tag array
Each entry compares its contents with the tag
Sets the match line to 1
The OR gate computes a hit or miss
The encoder computes the index of the matching entry.
We then read the contents of the matching entry from the block array
Refer to Chapter 6: Digital Logic

## Slide 31: Direct Mapped Cache
Each block can be mapped to only 1 entry
Tag(19)
Index(7)
Offset(6)
Address format
Tag array
Data array
Hit/Miss
Index
Tag
Index

## Slide 32: Direct Mapped Cache
We have 128 entries in our cache.
We compute the index as idx = block address % 128
We access entry, idx, in the tag array and compare the contents of the tag (19 msb bits of the address)
If there is a match → hit
  else → miss
Need a solution that is in the middle of the spectrum

## Slide 33: Set Associative Cache
Let us assume that an address can reside in 4 locations
  Access all 4 locations, and see if there is a hit
Thus, we have 128/4 = 32 indices
Each index points to a set of 4 entries
 We now use a 21 bit tag, 5 bit index
Tag
19
2
5
Index
6
Block

## Slide 34: Set Associative Cache
Tag array
Set index
Tag array index
generator
Tag
Encoder
Hit/Miss
Index of the
matched entry
Data array

## Slide 35: Set Associative Cache
Let the index be i , and the number of elements in a set be k
  We access indices, i*k, i*k+1 ,.., i*k + (k-1)
  Read all the tags in the set
  Compare the tags with the tag obtained from the address
  Use an OR gate to compute a hit/ miss
  Use an encoder to find the index of the matched entry

## Slide 36: Set Associative Cache – II
Read the corresponding entry from the block array
Each entry in a set is known as a way
A cache with k blocks in a set is known as a k-way associative cache

## Slide 37: Data read operation
This is a regular SRAM access.
Note that the data read and lookup can be overlapped for a load access
  We can issue a parallel data read to all the ways in the cache
  Once, we compute the index of the matching tag, we can choose the correct result with a multiplexer.

## Slide 38: Data write operation
Before we write a value
  We need to ensure that the block is present in the cache
Why ?
  Otherwise, we have to maintain the indices of the bytes that were written to
  We treat a block as an atomic unit
  Hence, on a miss, we fetch the entire block first
Once a block is there in the cache
  Go ahead and write to it ....

## Slide 39: Modified bit
Maintain a modified bit in the tag array.
If a block has been written to, after it was fetched, set it to 1.
Tag
Modified
bit

## Slide 40: Write Policies
Write through → Whenever we write to a cache, we also write to its lower level
  Advantage : Can seamlessly evict data from the cache
Write back → We do not write to the lower level. Whenever we write, we set the modified bit.
  At the time of eviction of the line, we check the value of the modified bit

## Slide 41: insert operation
Let us add a valid bit to a tag
  If the line is non-empty, valid bit is 1
  Else it is 0
Structure of a tag
Tag
Modified
bit
Valid bit
If we don’t find a block in a cache. We fetch it from the lower level. Then we insert the block in the cache  insert operation

## Slide 42: insert operation - II
Check if any way in a set has an invalid line
  If there is one, then write the fetched line to that location, set the valid bit to 1.
Otherwise,
  find a candidate for replacement

## Slide 43: The replace operation
A cache replacement scheme or replacement policy is a method to replace an entry in the set by a new entry
Replacement Schemes
  Random replacement scheme
  FIFO replacement scheme
    When we fetch a block, assign it a counter value equal to 0
    Increment the counters of the rest of the ways

## Slide 44: Replacement Schemes
FIFO
  For replacement, choose the way with the highest counter (oldest).
Problems :
  Can violate the principle of temporal locality
  A line fetched early might be accessed very frequently.

## Slide 45: LRU (least recently used)
Replace the block that has been accessed the least in the recent past
  Most likely we will not access it in the near future
  Directly follows from the definition of stack distance
  Sadly, we need to do more work per access
  Proved to be optimal in some restrictive scenarios
True LRU requires saving a hefty timestamp with every way
  Let us implement pseudo-LRU

## Slide 46: Psuedo-LRU
Let us try to mark the most recently used (MRU) elements.
Let us associate a 3 bit counter with every way.
  Whenever we access a line, we increment the counter.
  We stop incrementing beyond 7.
  We periodically decrement all the counters in a set by 1.
  Set the counter to 7 for a newly fetched block
  For replacement, choose the block with the smallest counter.

## Slide 47: evict Operation
If the cache is write-through
  Nothing needs to be done
If the cache is write-back
  AND the modified bit is 1
  Write the line to the lower level

## Slide 48: The read(load) Operation
lookup
data read
lookup
miss
Lower level
cache
hit
replace
insert
evict
read block
insert
Time
Lower level
cache
if write
back cache

## Slide 49: Write operation in a write back cache
lookup
data write
hit
lookup
miss
Lower level
cache
replace
insert
evict
Lower level
cache
insert
write
block
Time

## Slide 50: Write operation in a write through cache
lookup
data write
hit
lookup
miss
Lower level
cache
replace
insert
evict
Lower level
cache
insert
write
block
Time

## Slide 51: Outline
Overview of the Memory System
Caches
Details of the Memory System
Virtual Memory

## Slide 52: Mathematical Model of the Memory System
AMAT → Average Memory Access Time
fmem → Fraction of memory instructions
CPIideal → ideal CPI assuming a perfect 1 cycle memory system

## Slide 53: Equation for AMAT
Irrespective of an hit or a miss, we need to spend some time (hit time)
This is the hit time in the L1 cache (L1hit time)
This time should be discarded while calculating the stall penalty due to L1 misses
stall penalty = AMAT - L1hit time

## Slide 54: n-Level Memory System

## Slide 55: Definition: Local and Global Miss Rates, Working Set
local miss rate
It is equal to the number of misses in a cache at level i divided by the total number of accesses at
level i.
global miss rate
It is equal to the number of misses in a cache at level i divided by the total number of memory
accesses.
working set
The amount of memory, a given program
requires in a time interval.

## Slide 56: Types of Misses
Compulsory Misses
  Misses that happen when we read in a piece of data for the first time.
Conflict Misses
  Misses that occur due to the limited amount of associativity in a set associative or direct mapped cache. Example: Assume that 5 blocks (accessed by the program) map to the same set in a 4-way associative cache. Only 4 out of 5 can be accommodated.
Capacity Misses
  Misses that occur due to the limited size of a cache. Example: Assume the working set of a program is 10 KB, and the cache size is 8 KB.

## Slide 57: Schemes to Mitigate Misses
Compulsory Misses
  Increase the block size. We can bring in more data in one go, and due to spatial locality the number of misses might go down.
  Try to guess the memory locations that will be accessed in the near future. Prefetch (fetch in advance) those locations. We can do this for example in the case of array accesses.

## Slide 58: Schemes to Mitigate Misses - II
Conflict Misses
  Increase the associativity of the cache (at the cost of latency and power)
  We can use a smaller fully associative cache called the victim cache . Any line that gets displaced from the main cache can be put in the victim cache. The processor needs to check both the L1 and victim cache, before proceeding to the L2 cache.
  Write programs in a cache friendly way.

## Slide 59
Victim Cache
Processor
L1 cache
L2 cache
Victim Cache
R
R
R

## Slide 60: Schemes to Mitigate Misses - III
Capacity Misses
  Increase the size of the cache
  Use better prefetching techniques.

## Slide 61: Some Thumb Rules
Associativity Rule → Doubling the associativity is almost the same as doubling the cache size with the original associativity
  64 KB, 4 way ←→ 128 KB, 2 way

## Slide 62
int addAll(int data[], int vals[]) {
int i, sum = 0;
for (i=0; i < N; i++)
sum += data[vals[i]];
return sum;
}
int addAllP(int data[], int vals[]) {
int i, sum = 0;
for (i=0; i < N; i++) {
__builtin_prefetch(& data[vals[i+100]] );
sum += data[vals[i]];
}
return sum;
}
Software Prefetching
Original Code
Modified Code
with
Prefetching

## Slide 63
Hardware Prefetching
Processor
L1 cache
L2 cache
Prefetcher

## Slide 64: Reduction of Hit Time and Miss Penalty
For reducing the hit time, we need to use smaller and simpler caches
For reducing the miss penalty :
  Write misses
    Send the writes to a fully associative write buffer on an L1 miss.
    Once the block comes from the L2 cache, merge the write
    Insight: We need not send separate writes to the L2 for each write request in a block.
Processor
L1 cache
Write
buffer
L2 cache

## Slide 65: Reduction of the Miss Penalty
Read Miss
  Critical Word First : The memory word that cause the read/write miss is fetched first from the lower level. The rest of the block follows.
  Early Restart : Send the critical word to the processor, and make it restart its execution.

## Slide 66
Technique | Application | Disadvantages
large block size | compulsory misses | reduces the number of blocks in the cache
prefetching | compulsory misses, capacity misses | extra complexity and the risk of displacing useful data from the cache
large cache size | capacity misses | high latency, high power, more area
increased associativity | conflict misses | high latency, high power
victim cache | conflict misses | extra complexity
compiler based techniques | all types of misses | not very generic
small and simple cache | hit time | high miss rate
write buffer | miss penalty | extra complexity
critical word first | miss penalty | extra complexity and state
early restart | miss penalty | extra complexity

## Slide 67: Outline
Overview of the Memory System
Caches
Details of the Memory System
Virtual Memory

## Slide 68: Need for Virtual Memory
Up till now we have assumed that a program perceives the entire memory system to be its own
Furthermore, every program on a 32 bit machine assumes that it owns 4 GB of memory space, and it can access any location at will
We now need to take multiple programs into account. The CPU runs program A for some time, then switches to program B, and then to program C. Do they corrupt each other’s data?
Secondly, we need to design memory systems that have less than 4 GB of memory (for a 32 bit memory address)

## Slide 69: Let us thus define two concepts ...
Physical Memory
  Refers to the actual set of physical memory locations contained in the main memory, and the caches.
Virtual Memory
  The memory space assumed by a program.
  Contiguous, without limits.

## Slide 70: Virtual Memory Map of a Process (in Linux)
Header
0
0x08048000
Text
Static variables with initialized values
Data
Static variables not initialized, filled with 0s
Bss
Heap
Memory mapping
segment
Stack
0xC0000000

## Slide 71: Memory Maps Across Operating Systems
User programs
OS kernel
3 GB
1 GB
User programs
OS kernel
2 GB
2 GB
Linux
Windows

## Slide 72: Address Translation
Convert a virtual address to a physical address to satisfy all the aims of the virtual memory system
Address
translation
system
Physical
address
Virtual
address

## Slide 73: Pages and Frames
Divide the virtual address space into chunks of 4 kB → page
Divide the physical address space into chunks of 4 kB → frame
Map pages to frames
  Insight: If a page/frame size is large, most of it may remain unused
  If the page/frame size is very small, the overhead of mapping will be very high

## Slide 74: Map Pages to Frames
Virtual memory of program A
Physical memory
Page
Frame
Virtual memory of program B

## Slide 75: Example of Page Translation
Page
table
Physical
address
Virtual
address
Page number
Offset
Frame number
Offset
20
12
20
12

## Slide 76: Single Level Page Table
Page number
Frame number
20
20
Page table

## Slide 77: Issues with the Single Level Page Table
Size of the single level page table
  Size of an entry (20 bits = 2.5 bytes) *
  Number of entries (220 = 1 million)
  Total → 2.5 MB
For 200 processes (running instances of programs)
  We spend 500 MB in saving page tables (not acceptable)
Insight : Most of the virtual address space is empty
      Most programs do not require that much of memory
      They require maybe 100 MBs or 200 MBs (most of the time)

## Slide 78: Two Level Page Table
Page number
Frame number
20
20
Primary page
table
10
10
Secondary page tables

## Slide 79: Two Level Page Tables - II
We have a two level set of page tables
  Primary and secondary page tables
Not all the entries of the primary page table point to valid secondary page tables
Each secondary page table → 1024 * 2.5 B = 2.5 KB
  Maps 4MB of virtual memory
Insight: Allocate only those many secondary page tables as required.
  We do not need many secondary page tables due to spatial locality in programs
  Example: If a program uses 100 MB of virtual memory and needs 25 secondary page tables, we need a total of 2.5KB * 25 = 62.5 KB of space for saving secondary page tables (minimal).

## Slide 80
Page number
Frame number
20
20
Inverted
page table
Pid
Hashing
engine
Hashtable
Compare the page
num, process id with
each entry
Frame number
Page number
20
20
Inverted
page table
(a)
(b)
Inverted Page Table
Advantage: One page table for the entire system

## Slide 81
Memory Access
Processor
MMU (Memory Mgmt. Unit)
Caches
Every access needs to go through the MMU (memory management unit)
It will access the page tables, which themselves are stored in memory (very slow)
Fast mechanism  Cache N recent mappings. Due to temporal and spatial locality, we should observe a very high hit rate. We need not access the page tables for every access.

## Slide 82
Memory Access with a TLB
Processor
TLB
Caches
Page Tables

## Slide 83: TLB
TLB (Translation Lookaside Buffer)
  A fully associative cache
  Each entry contains a page → frame (mapping)
  Typically contains 64 entries
  Very few accesses go to the page table.
Accesses that go to the page table
  If there is no mapping, we have a page fault
  On a page fault, create a mapping, and allocate an empty frame in memory. Update the list of empty frames.

## Slide 84: Swap Space
Consider a system with 500 MB of main memory.
  Can we run a program that requires 1 GB of main memory ?
  YES
Add an additional entry in the page table.
  bit → Is the frame found in main memory, or somewhere else (???)
  Hard disk (studied later) contains a dedicated area to save frames that do not fit in main memory. This area is known as the swap space.

## Slide 85
System with a Hard Disk
Processor
L1
L2
Main Memory
Hard Disk
Swap space

## Slide 86
TLB hit?
Yes
Memory
access
Send mapping
to processor
Page table
hit?
Yes
No
Populate
TLB
No
Send mapping
to processor
Free frame
available?
No
(1) Evict a frame
to swap space
(2) Update its page
table
Yes
Create/update mapping
in the page table
Populate
TLB
Send mapping
to processor
Read in the new frame
from swap space (if possible),
or create a new empy frame
Flowchart

## Slide 87: Advanced Features
Shared Memory → Sometimes it is necessary for two processes to share data. We can map two pages in each virtual address space to the same physical frame.
Protection → The pages in the text section are marked as read-only. The program thus cannot be modified.

## Slide 88
THE END