## Slide 1
Chapter 11 Multiprocessor Systems
Smruti Ranjan Sarangi, IIT Delhi
Computer Organisation and Architecture
PowerPoint Slides
PROPRIETARY MATERIAL. © 2014 The McGraw-Hill Companies, Inc. All rights reserved. No part of this PowerPoint slide may be displayed, reproduced or distributed in any form or by any means, without the prior written permission of the publisher, or used beyond the limited distribution to teachers and educators permitted by McGraw-Hill for their individual course preparation. PowerPoint Slides are being provided only to authorized professors and instructors for use in preparing for classes using the affiliated textbook. No other use or distribution of this PowerPoint slide is permitted. The PowerPoint slide may not be sold and may not be distributed or be used by any student or any other third party. No part of the slide may be reproduced, displayed or distributed in any form or by any means, electronic or otherwise, without the prior written permission of McGraw Hill Education (India) Private Limited.

## Slide 2
Download the pdf of the book
www.basiccomparch.com
videos
Slides, software, solution manual
Print version
(Publisher: WhiteFalcon, 2021)
Available on e-commerce sites.
The pdf version of the book and all the learning resources can be freely downloaded from the website: www.basiccomparch.com
2nd version

## Slide 3: Outline
Overview
Amdahl's Law and Flynn's Taxonomy
MIMD Multiprocessors
Multithreading
Vector Processors
Interconnects

## Slide 4: Processor Performance Scaling has reached its Limits
Clock frequency has remained constant for the last 10 years
6000
5
000
4000
3000
2000
1000
0
29/10/99
12/03/01
25/07/02
07/12/03
20/04/05
02/09/06
15/01/08
29/05/09
11/10/10
23/02/12
Date
Clock frequency (MHz)

## Slide 5: Processor Performance
Performance is also saturating
40
35
30
25
20
15
10
5
0
Speclnt 2006 Score
29/10/99
12/03/01
25/07/02
07/12/03
20/04/05
02/09/06
15/01/08
29/05/09
11/10/10
23/02/12
Date

## Slide 6: Future of computer architecture
Is computer architecture dead ?
We need to use extra transistors to add more processors per chip rather than add extra features
No

## Slide 7: Multiprocessing
The term multiprocessing refers to multiple processors working in parallel. This is a generic definition, and it can refer to multiple processors in the same chip, or processors across different chips. A multicore processor is a specific type of multiprocessor that contains all of its constituent processors in the same chip. Each such processor is known as a core.

## Slide 8: Symmetric vs Asymmetric MPs
Symmetric Multiprocessing: This paradigm treats all the constituent processors
in a multiprocessor system as the same. Each processor has equal access to the
operating system, and the I/O peripherals. These are also known as SMP systems.
Asymmetric Multiprocessing: This paradigm does not treat all the constituent
processors in a multiprocessor system as the same. There is typically one master
processor that has exclusive control of the operating system and I/O devices.
It assigns work to the rest of the processors.

## Slide 9: Moore's Law
A processor in a cell phone is 1.6 million times faster than IBM 360 (state of the art processor in the sixties)
Transistor in the sixties/seventies
  several millimeters
Today
  several nanometers
The number of transistors per chip doubles roughly every two years → known as Moore's Law

## Slide 10: Moore's Law - II
Feature Size → the size of the smallest structure that can be fabricated on a chip
In 1965, Gordon Moore (co-founder of Intel) conjectured that the number of
transistors on a chip will double roughly every year. Initially, the number of
transistors was doubling every year. Gradualy, the rate slowed down to
18 months, and now it is about two years.
Year | Feature Size
2001 | 130 nm
2003 | 90 nm
2005 | 65 nm
2007 | 45 nm
2009 | 32 nm
2011 | 22 nm
2014 | 14 nm

## Slide 11: Strong vs Loosely Coupled Multiprocessing
Loosely Coupled Multiprocessing: Running multiple unrelated
programs in parallel on a multiprocessor is known as loosely
coupled multiprocessing.
Strongly Coupled Multiprocessing: Running a set of programs in
parallel that share their data, code, file, and network connections
is known as strongly coupled multiprocessing.

## Slide 12: Shared Memory vs Message Passing
Shared Memory
  All the programs share the virtual address space.
  They can communicate with each other by reading and writing values from/to shared memory.
Message Passing
  Programs communicate between each other by sending and receiving messages.
  They do not share memory addresses.

## Slide 13: Let us write a parallel program
Write a program using shared memory to add n numbers in parallel
  Number of parallel sub-programs → NUMTHREADS
  The array numbers contains all the numbers to be added
  It contains NUMSIZE entries
We use the OpenMP extension to C++

## Slide 14
/* variable declaration */
int partialSums[N];
int numbers[SIZE];
int result = 0;
/* initialise arrays */
...
/* parallel section */
#pragma omp parallel {
/* get my processor id */
int myId = omp_get_thread_num();
/* add my portion of numbers */
int startIdx = myId * SIZE/N;
int endIdx = startIdx + SIZE/N;
for(int jdx = startIdx; jdx < endIdx; jdx++)
partialSums[myId] += numbers[jdx];
}
/* sequential section */
for(int idx=0; idx < N; idx++)
result += partialSums[idx];

## Slide 15: The Notion of Threads
We spawn a set of separate threads
Properties of threads
  A thread shares its address space with other threads
  It has its own program counter, set of registers, and stack
  A process contains multiple threads
  Threads communicate with each other by writing values to memory or via synchronisation operations

## Slide 16: Operation of the Program
Parent thread
Time
Spawn child threads
Child
threads
Thread join operation
Sequential
section
Initialisation

## Slide 17: Message Passing
Typically used in loosely coupled systems
Consists of multiple processes.
A process can send (unicast/ multicast) a message to another process
Similarly, it can receive (unicast/ multicast) a message from another process

## Slide 18: Example
We use a dialect similar to the popular parallel programming
framework, MPI (Message Passing Interface)
Example: Write a message passing based program to add a set of numbers in
parallel. Make appropriate assumptions.
Answer: Let us assume that all the number are stored in the array, numbers, and this
array is available with all the N processors. Let the number of elements in the
numbers array be SIZE. For the sake of simplicity, let us assume that SIZE
is divisible by N.

## Slide 19
/* start all the parallel processes */
SpawnAllParallelProcesses();
/* For each process execute the following code */
int myId = getMyProcessId();
/* compute the partial sums */
int startIdx = myId * SIZE/N;
int endIdx = startIdx + SIZE/N;
int partialSum = 0;
for(int jdx = startIdx; jdx < endIdx; jdx++)
partialSum += numbers[jdx];
/* All the non-root nodes send their partial sums to the root */
if(myId != 0) {
/* send the partial sum to the root */
send (0, partialSum);
} else {
/* for the root */
int sum = partialSum;
for (int pid = 1; pid < N; pid++) {
sum += receive(ANYSOURCE);
}
/* shut down all the processes */
shutDownAllProcesses();
/* return the sum */
return sum;
}

## Slide 20: Outline
Overview
Amdahl's Law and Flynn's Taxonomy
MIMD Multiprocessors
Multithreading
Vector Processors
Interconnects

## Slide 21: Amdahl's Law
Let us now summarise our discussion
For P parallel processors, we can expect a speedup of P (in the ideal case)
Let us assume that a program takes Told units of time
  Let us divide it into two parts – sequential and parallel
  Sequential portion : Told * fseq
  Parallel portion : Told * (1 - fseq )

## Slide 22: Amdahl's Law - II
Only, the parallel portion gets sped up P times
The sequential portion is unaffected
Equation for the time taken with parallelisation
The speedup is thus :

## Slide 23: Implications
Consider multiple values of fseq
Speedup vs Number of processors
# Processors

## Slide 24: Conclusions
We are limited by the size of the sequential section
For a very large number of processors, the parallel section is actually very small
Ideally, a parallel workload should have as small a sequential section as possible.

## Slide 25: Flynn's Classification
Instruction stream → Set of instructions that are executed
Data stream → Data values that the instructions process
Four types of multiprocessors : SISD, SIMD, MISD, MIMD

## Slide 26: SISD and SIMD
SISD → Standard uniprocessor
SIMD → One instruction, operates on multiple pieces of data. Vector processors have one instruction that operates on many pieces of data in parallel. For example, one instruction can compute the sin-1 of 4 values in parallel.

## Slide 27: MISD
MISD → Mutiple Instruction Single Data
  Very rare in practice
  Consider an aircraft that has a MIPS, an ARM, and an X86 processor operating on the same data (multiple instruction streams)
  We have different instructions operating on the same data
  The final outcome is decided on the basis of a majority vote.

## Slide 28: MIMD
MIMD → Multiple instruction, multiple data (two types, SPMD, MPMD)
SPMD → Single program, multiple data. Examples: OpenMP example that we showed, or the MPI example that we showed. We typically have multiple processes or threads executing the same program with different inputs.
MPMD → A master program, delegates work to multiple slave programs. The programs are different.

## Slide 29: Outline
Overview
Amdahl's Law and Flynn's Taxonomy
MIMD Multiprocessors
Multithreading
Vector Processors
Interconnects

## Slide 30: Logical Point of View
All the processors see an unified view of shared memory
Proc 1
Shared memory
Proc 2
Proc n

## Slide 31: Implementing Shared Memory
Implementing an unified view of memory, is in reality very difficult
The memory system is very complex
  Consists of many caches (parallel, hierarchical)
  Many temporary buffers (victim cache, write buffers)
  Many messages are in flight at any point of time (not committed). They also pass through a complex on-chip network.
Implications : Reordering of messages

## Slide 32: Coherence
Behaviour of the memory system with respect to access to one memory location (variable)
Examples
  All the global variables are initialised to 0
  All local variables start with 't'

## Slide 33: Example 1
Is t1 guaranteed to be 1 ?
Can it be 0 ?
Answer : It can be 0 or 1. However, if thread 2 is scheduled a long time after thread 1, most likely it is 1.
Thread 1:
x = 1
Thread 2:
t1 = x

## Slide 34: Example 2
Is (t1, t2) = (2,1) a valid outcome ?
NO
  This outcome is not intuitive.
  The order of updates to the same location should be the same for all threads
Thread 1:
x = 1
x = 2
Thread 2:
t1 = x
t2 = x

## Slide 35: Axioms of Coherence
Coherence Axioms
  Messages are never lost
  Write messages to the same memory location are always perceived to be in the same order (by different threads)
  These two axioms guarantee that a coherent memory appears the same way as a single shared cache(across all processors), where there is only one storage area per memory word
Completion: A write must ultimately complete.
Order: All the accesses to the same memory address need
to be seen by all the threads in the same order.

## Slide 36: Memory Consistency – Behaviour across multiple locations
Is (1,0) a valid outcome ?
Is it intuitive?
Thread 1:
x = 1
y = 1
Thread 2:
t1 = y
t2 = x
x = 1
y = 1
t1 = y
t2 = x
x = 1
t1 = y
t2 = x
y = 1
t1 = y
t2 = x
x = 1
y = 1
(0,1)
(0,0)
(1,1)

## Slide 37: Definitions
An order of instructions that is consistent with the semantics of a thread is said to be in program order. For example, a single cycle processor always executes instructions in program order.
The model of a memory system that determines the set of likely (and valid) outcomes for parallel programs, is known as a memory consistency model or memory model.

## Slide 38: Sequential Consistency
How did we generate the set of valid outcomes ?
  We arbitrarily interleaved instructions of both the threads
  Such kind of an interleaving of instructions where the program order is preserved is known as a sequentially consistent interleaving
  A memory model that allows only sequential consistent interleavings is known as sequential consistency (SC)
  The outcome (1,0) is not in SC

## Slide 39: Weak Consistency
Sequential consistency comes at a cost
  The cost is performance
  We need to add a lot of constraints in the memory system to make it sequentially consistent
  Most of the time, we need to wait for the current memory request to complete, before we can issue the subsequent memory request.
  This is very restrictive.
Hence, we define weak consistency that allows arbitrary orderings

## Slide 40: Weak Consistency - II
We have two kinds of memory instructions
  Regular load/store instructions
  Synchronisation instructions
Example of a synchronisation instruction
  fence → Waits till all the memory accesses before the fence instruction (in the same thread) complete. Any subsequent memory instruction in the same thread can start only after the fence instruction completes.

## Slide 41: Add n numbers on an SC Machine
/* variable declaration */
int partialSums[N];
int finished[N];
int numbers[SIZE];
int result = 0;
int doneInit = 0;
/* initialise all the elements in partialSums and finished to 0 */
...
doneInit = 1;
/* parallel section */
parallel {
/* wait till initialisation */
while (!doneInit){};
/* compute the partial sum */
int myId = getThreadId();
int startIdx = myId * SIZE/N;

## Slide 42: SC Example - II
int endIdx = startIdx + SIZE/N;
for(int jdx = startIdx; jdx < endIdx; jdx++)
partialSums[myId] += numbers[jdx];
/* set an entry in the finished array */
finished[myId] = 1;
}
/* wait till all the threads are done */
do {
flag = 1;
for (int i=0; i < N; i++){
if(finished[i] == 0){
flag = 0;
break;
}
}
} while (flag == 0);
/* compute the final result */
for(int idx=0; idx < N; idx++)
result += partialSums[idx];

## Slide 43: Add n numbers on a WC Machine
/* variable declaration */
int partialSums[N];
int finished[N];
int numbers[SIZE];
int result = 0;
/* initialise all the elements in partialSums and finished to 0 */
...
/* fence */
/* ensures that the parallel section can read the initialised arrays */
fence();
Initialisation

## Slide 44
/* All the data is present in all the arrays at this point */
/* parallel section */
parallel {
/* get the current thread id */
int myId = getThreadId();
/* compute the partial sum */
int startIdx = myId * SIZE/N;
int endIdx = startIdx + SIZE/N;
for(int jdx = startIdx; jdx < endIdx; jdx++)
partialSums[myId] += numbers[jdx];
/* ensures that finished[i] is written after
partialSums[i] */
fence();
/* the thread is done */
finished[myId] = 1;
}
Parallel Section

## Slide 45
/* wait till all the threads are done */
do {
flag = 1;
for (int i=0; i < N; i++){
if(finished[i] == 0){
flag = 0;
break;
}
}
}while (flag == 0) ;
/* sequential section */
for(int idx=0; idx < N; idx++)
result += partialSums[idx];
Aggregating the Results

## Slide 46: Physical View of Memory
Shared Cache → One cache shared by all the processors.
Private Cache → Each processor, or set of processors have a private cache.
Proc 1
Shared L1 cache
Proc 2
Proc n
Proc 1
Proc 2
Proc n
L1
L1
L1
Shared L2 cache
Shared L2 cache
Proc 1
Proc 2
Proc n
L1
L1
L1
L2
L2
L2
(a)
(b)
(c)

## Slide 47: Tradeoffs
Typically, the L1 level has private caches.
L2 and beyond have shared caches.
Attribute
Private Cache
Shared Cache
Area
low
high
Speed
fast
slow
Proximity to the processor
near
far
Scalability in size
low
high
Data replication
yes
no
Complexity
High (needs cache coherence)
low

## Slide 48: Shared Caches
Assume a 4MB Cache
  It will have a massive tag and data array
  The lookup operation will become very slow
  Secondly, we might have a lot of contention. It will be necessary to make this a multi-ported structure (more area and more power)
Solution : Divide a cache into banks. Each bank is a subcache.

## Slide 49: Shared Caches - II
4MB = 222 bytes
Let us have 16 banks
Use bits 19-22 to choose the bank address.
  Access the corresponding bank
  The bank can be direct mapped or set associative
  Perform a regular cache lookup

## Slide 50: Coherent Private Caches
A set of caches appears to be just one cache.
Proc 1
Shared L1 cache
Proc 2
Proc n
Proc 1
Proc 2
Proc n
L1
L1
L1
Shared L2 cache
Shared L2 cache
One logical
cache

## Slide 51
What does one cache mean?
A distributed cache needs to be perceived as a single array of bytes by all threads
AIM
When can problems happen?
T1:
x = 1
x = 2
x = 3
T2:
x = 4
x = 5
x = 6
T3:
t1 = x
t2 = x
T4:
t3 = x
t4 = x
(t1,t2) = (2,4)
(t3,t4) = (4,2)

## Slide 52
What does a single cache mean?
How to ensure coherence?
Is there a problem if multiple threads read at the same time? NO
  We only care about the order of writes (for any specific memory address)
  Reading is just fine
  You will always read the same data as long as there are no intervening writes (for the same location) The order of reads does not matter if there are not intervening writes

## Slide 53
What about writes?
Writes need a global ordering.
  Global ordering  All threads see the same order
Acquire access to an exclusive resource
  Exclusive resource  A resource, which can be acquired by any one request at any point of time
IDEA: Let us designate a bus (set of copper wires) as an exclusive resource. The read/write request that has exclusive access to the bus, can use it to transmit a message to caches in a distributed cache, and thus effect a read or write.

## Slide 54
The order of accesses to the bus induces a global ordering
The ordering of reads does not matter
However, the order of writes does matter. The mutual exclusivity of the bus lets us have an order for writes.

## Slide 55: Snoopy Protocol
All the caches are connected to a multi-reader, single-writer bus
The bus can broadcast data. All caches see the same order of messages, and also all the messages.
Proc 1
Proc 2
Proc n
L1
L1
L1
Shared bus

## Slide 56: Write Update Protocol
Tag each cache line with a state
  M (Modified) → written by the current processor
  S (Shared) → not modified
  I (invalid) → not valid
Whenever there is a write, broadcast it to all the caches. All the caches update the data. They thus see the same order of writes.
For a read, broadcast it to all the caches, and ask everybody if they have the block. If any cache has the block, it sends a copy of the block. Otherwise, we read from the lower level.
While evicting a block that has been modified write it to the lower level.
We should be seamlessly able to evict unmodified data from the cache.

## Slide 57: State Diagram
I
S
M
read miss/ Broadcast read miss
Write hit/ Broadcast write
evict/ Write back
read hit/
evict/
Write hit/ broadcast write
read hit/
Write miss/ Broadcast write miss
For any write message received from another cache (via the bus)  update the value
Whenever, you do a write: broadcast the data

## Slide 58: Write Invalidate Protocol
There is no need to broadcast every write
  This is too expensive in terms of messages
  Let us assume that if a block is there in the M state with some cache, then no other cache contains a valid copy of the block
  This will ensure that we can write without broadcasting
The rest of the logic (more or less) remains the same.

## Slide 59: State Transition Diagram for Actions Taken by the Processor
I
S
M
Read miss/ Broadcast miss
Write hit/ Broadcast write
Evict/ Write back
Read hit/
Evict/
Write hit/
read hit/
Write miss/ Broadcast miss

## Slide 60: State Transition Diagram (for events received from the bus)
I
S
M
Write hit/
Read miss/ Send data and
write back
Write miss/ Send data
Read miss/ Send data
Write miss/ Send data

## Slide 61: Directory Protocol (Broad Idea)
Let us avoid expensive broadcasts
Most blocks are cached by a few caches
Have a directory that
  Maintains a list of all the sharers for each block
  Sends messages to only the sharers (for a block)
  Dynamically updates the list of sharers

## Slide 62: Outline
Overview
Amdahl's Law and Flynn's Taxonomy
MIMD Multiprocessors
Multithreading
Vector Processors
Interconnects

## Slide 63: Multithreading
Multithreading → A design paradigm that proposes to run multiple threads on the same pipeline.
Three types
  Coarse grained
  Fine grained
  Simultaneous

## Slide 64: Coarse Grained Multithreading
Assume that we want to run 4 threads on a pipeline
Run thread 1 for n cycles, run thread 2 for n cycles, ….
1
3
2
4

## Slide 65: Implementation
Steps to minimise the context switch overhead
For a 4-way coarse grained MT machine
  4 program counters
  4 register files
  4 flags registers
  A context register that contains a thread id.
  Zero overhead context switching → Change the thread id in the context register

## Slide 66: Advantages
Assume that thread 1 has an L2 miss
  Wait for 200 cycles
  Schedule thread 2
  Now let us say that thread 2 has an L2 miss
  Schedule thread 3
We can have a sophisticated algorithm that switches every n cycles, or when there is a long latency event such as an L2 miss.
  Minimises idle cycles for the entire system

## Slide 67: Fine Grained Multithreading
The switching granularity is very small
  1-2 cycles
Advantage :
  Can take advantage of low latency events such as division, or L1 cache misses
  Minimise idle cycles to an even greater extent
Correctness Issues
  We can have instructions of 2 threads simultaneously in the pipeline.
  We never forward/interlock for instructions across threads

## Slide 68: Simultaneous Multithreading
Most modern processors have multiple issue slots
  Can issue multiple instructions to the functional units
  For example, a 3 issue processor can fetch, decode, and execute 3 instructions per cycle
  If a benchmark has low ILP (instruction level parallelism), then fine and coarse grained multithreading cannot really help.

## Slide 69: Simultaneous Multithreading
Main Idea
  Partition the issue slots across threads
  Scenario : In the same cycle
    Issue 2 instructions for thread 1
    and, issue 1 instruction for thread 2
    and, issue 1 instruction for thread 3
Support required
  Need smart instruction selection logic.
    Balance fairness and throughput

## Slide 70: Summary
T
i
m
e
Coarse grained
multithreading
Fine grained
multithreading
Simultaneous
multithreading
Thread 1
Thread 2
Thread 3
Thread 4
issue
slots

## Slide 71: Outline
Overview
Amdahl's Law and Flynn's Taxonomy
MIMD Multiprocessors
Multithreading
Vector Processors
Interconnects

## Slide 72: Vector Processors
A vector instruction operates on arrays of data
  Example : There are vector instructions to add or multiply two arrays of data, and produce an array as output
  Advantage : Can be used to perform all kinds of array, matrix, and linear algebra operations. These operations form the core of many scientific programs, high intensity graphics, and data anaytics applications.

## Slide 73: Background
Vector processors were traditionally used in supercomputers (read about Cray 1)
Vector instructions gradually found their way into mainstream processors
  MMX, SSE1, SSE2, SSE3, SSE4, and AVX instruction sets for x86 processors
  AMD 3D Now Instruction Set

## Slide 74: Software Interface
Let us define a vector register
  Example : 128 bit registers in the MMX instruction set → XMM0 … XMM15
  Can hold 4 floating point values, or 8 2-byte short integers
  Addition of vector registers is equivalent to pairwise addition of each of the individual elements.
  The result is saved in a vector register of the same size.

## Slide 75: Example of Vector Addition
Let us define 8 128 bit vector registers in SimpleRisc. vr0 ... vr7
vr1
vr2
vr3

## Slide 76: Loading Vector Registers
There are two options :
  Option 1 : We assume that the data elements are stored in contiguous locations
  Let us define the v.ld instruction that uses this assumption.
  Option 2: Assume that the elements are not saved in contiguous locations.
Instruction | Semantics
v.ld vr1, 12[r1] | vr1  ([r1+12], [r1+16],[r1+20], [r1+24])

## Slide 77: Scatter Gather Operation
The data is scattered in memory
  The load operation needs to gather the data and save it in a vector register.
Let us define a scatter gather version of the load instruction → v.sg.ld
  It uses another vector register that contains the addresses of each of the elements.
Instruction | Semantics
v.sg.ld vr1, vr2 | vr1  ([vr2[0]], [vr2[1]], [vr2[2]], [vr2[3]])

## Slide 78: Vector Store Operation
We can similarly define two vector store operations
Instruction | Semantics
v.sg.st vr1, vr2 | [vr2[0]]  vr1[0] [vr2[1]]  vr1[1] [vr2[2]]  vr1[2] [vr2[3]]  vr1[3]
Instruction | Semantics
v.st vr1, 12[r1] | [r1+12]  vr1[0] [r1+16]  vr1[1] [r1+20]  vr1[2] [r1+24]  vr1[3]

## Slide 79: Vector Operations
We can now define custom operations on vector registers
  v.add → Adds two vector registers
  v.mul → Multiplies two vector registers
  We can even have operations that have a vector operand and a scalar operand → Multiply a vector with a scalar.

## Slide 80: Example using SSE Instructions
void sseAdd (const float a[], const float b[], float c[], int N)
{
/* strip mining */
int numIters = N / 4;
/* iteration */
for (int i = 0; i < numIters; i++) {
/* load the values */
__m128 val1 = _mm_load_ps (a);
__m128 val2 = _mm_load_ps (b);
/* perform the vector addition */
__m128 res = _mm_add_ps(val1, val2);
/* store the result */
_mm_store_ps(c, res);
/* increment the pointers */
a += 4 ; b += 4; c+= 4;
}
}
Roughly 2X faster

## Slide 81: Predicated Instructions
Suppose we want to run the following code snippet on each element of a vector register
  if(x < 10) x = x + 10 ;
Let the input vector register be vr1
We first do a vector comparison :
  v.cmp vr1, 10
  It saves the results of the comparison in the v.flags register (vector form of the flags register)

## Slide 82: Predicated Instructions - II
If a condition is true, then the predicated instruction gets evaluated
  Otherwise, it is replaced with a nop.
Consider a scalar predicated instruction (in the ARM ISA)
  addeq r1, r2, r3
  r1 = r2 + r3 (if the previous comparison resulted in an equality)

## Slide 83: Predicated Instructions - III
Let us now define a vector form of the predicated instruction
  For example : v.<p>.add (<p> is the predicate)
  It is a regular add instruction for the elements in which the predicate is true.
  For the rest of the elements, the instruction becomes a nop
Example of predicates :
  lt (less than) , gt (greater than), eq (equality)

## Slide 84: Predicated Instructions - IV
Implementation of our function :
  if (x < 10) x = x + 10
v.cmp vr1, 10
v.lt.add vr1, vr1, 10
Adds 10 to every element of vr1

## Slide 85: Design of a Vector Processor
Salient Points
  We have a vector register file and a scalar register file
  There are scalar and vector functional units
  Unless we are converting a vector to a scalar or vice versa, we in general do not forward values between vector and scalar instructions
  The memory unit needs support for regular operations, vector operations, and possibly scatter-gather operations.

## Slide 86: Graphics Processors – Quick Overview

## Slide 87: Graphics Processors
Modern computer systems have a lot of graphics intensive tasks
  computer games
  computer aided design (engineering, architecture)
  high definition videos
  desktop effects
  windows and other aesthetic software features
  We cannot tie up the processor's resources for processing graphics → Use a graphics processor

## Slide 88: Role of a Graphics Processor
Synthesize graphics
  Process a set of objects in a game to create a sequence of scenes
  Automatically apply shadow and illumination effects
  Convert a 3D scene to a 2D image (add depth information)
  Add colour and texture information.
  Physics → simulation of fluids, and solid bodies
Play videos (mpeg4 encoder)

## Slide 89: Graphics Pipeline
vertex processing → Operations on shapes, and make a set of triangles
rasterisation → conversion into fragments of pixels
fragment processing → colour/ texture
framebuffer proc. → depth information
shapes, objects
rules,
effects
Vertex processing
Rasterisation
Fragment
processing
Framebuffer
processing
triangles
fragments
pixels
framebuffer

## Slide 90
NVidia Tesla GeForce 8800, Copyrights belong to IEEE
Host CPU
Bridge
System Memory
Host interface
Input assembler
Vertex work
distribution
Viewport/clip/setup
/raster/zcull
Pixel work
distribution
Compute work
distribution
TPC
Texture unit
SM
SM
TPC
Texture unit
SM
SM
TPC
Texture unit
SM
SM
ROP
L2
DRAM
interconnection network
ROP
L2
DRAM
ROP
L2
DRAM
(1)
(2)
(8)
(1)
(2)
(6)

## Slide 91: Structure of an SM
Geometry Controller → Converts operations on shapes to multithreaded code
SMC → Schedules instructions on SMs
SP → Streaming processor core
SFU → Special function unit
Texture Unit → Texture processing operations.
TPC
Geometry controller
SMC
SM
I cache
MT issue
C cache
SP
SP
SP
SP
SP
SP
SP
SP
SFU
SFU
Shared
memory
SM
I cache
MT issue
C cache
SP
SP
SP
SP
SP
SP
SP
SP
SFU
SFU
Shared
memory
Tex. L1
Texture unit

## Slide 92: Computation on a GPU
The GPU groups a set of 32 threads into a warp. Each thread has the same set of dynamic instructions.
We use predicated branches.
The GPU maps a warp to an SM
Each instruction in the warp executes atomically
  All the units in the SM first execute the ith instruction of each thread in the warp, before considering the (i+1)th instruction, or an instruction from another warp
  SIMT behaviour → Single instruction, multiple threads

## Slide 93: Computations on a GPU - II
SM multithreaded
instruction scheduler
Warp 8, instruction 11
Warp 1, instruction 42
Warp 3, instruction 95
Warp 8, instruction 12
Warp 1, instruction 43
Warp 3, instruction 96

## Slide 94: Computations on a GPU - III
We execute a new instruction (for every thread in a warp) every 4 cycles
  8 threads run on 8 SP cores once every two cycles
  8 threads run on the two SFUs once every two cycles
Threads in a warp can share data through the SM specific shared memory
A set of warps are grouped into a grid. Different warps in a grid can execute independently.
They communicate through global memory.

## Slide 95: CUDA Programming Language
CUDA (Common Unified Device Architecture)
  Custom extension to C/C++
A kernel
  A piece of code that executes in parallel.
A block, or CTA (co-operative thread array) → (same as a warp)
Blocks are grouped together in a grid.
Part of the code executes on the CPU, and a part executes on the GPU

## Slide 96: CUDA Example
#define N 1024
/* The GPU kernel */
__global__ void vectorAdd (int *gpu_a, int *gpu_b, int *gpu_c) {
/* compute the index */
int idx = threadIdx.x + blockIdx.x * blockDim.x;
/* perform the addition */
gpu_c[idx] = gpu_a[idx] + gpu_b[idx];
}
void main() {
/* Declare three arrays a, b, and c */
int a[N], b[N], c[N];
/* Declare the corresponding arrays in the GPU */
int size = N * sizeof (int);
int *gpu_a, *gpu_b, *gpu_c;

## Slide 97
/* allocate space for the arrays in the GPU */
cudaMalloc ((void **) &gpu_a, size);
cudaMalloc ((void **) &gpu_b, size);
cudaMalloc ((void **) &gpu_c, size);
/* initialize arrays a and b */
.....
/* copy the arrays to the GPU */
cudaMemcpy (gpu_a, a, size, cudaMemcpyHostToDevice);
cudaMemcpy (gpu_b, b, size, cudaMemcpyHostToDevice);
/* invoke the vector add operation in the GPU */
vectorAdd <<< N/32, 32 >>> (gpu_a, gpu_b, gpu_c);
/* Copy from the GPU to the CPU */
cudaMemcpy (c, gpu_c, size, cudaMemcpyDeviceToHost);
/* free space in the GPU */
cudaFree (gpu_a); cudaFree(gpu_b); cudaFree (gpu_c);
}

## Slide 98: Outline
Overview
Amdahl's Law and Flynn's Taxonomy
MIMD Multiprocessors
Multithreading
Vector Processors
Interconnects

## Slide 99: Network On Chip
Layout of a multicore processor
Cache bank
Core
Memory
controller
Router
Tile

## Slide 100: Network on Chip (NoC)
A router sends and receives all the messages for its tile
A router also forwards messages originating at other routers to their destination
Routers are referred to as nodes. Adjacent nodes are connected with links.
The routers and links form the on chip network, or NoC.

## Slide 101: Properties of an NoC
Bisection Bandwidth
  Number of links that need to be snapped to divide an NoC into equal parts (ignore small additive constants)
Diameter
  Maximum optimal distance between any two pair of nodes (again ignore small additive constants)
Aim : Maximise bisection bandwidth, minimise diameter

## Slide 102: Chain and Ring
Chain
Ring

## Slide 103: Fat Tree

## Slide 104: Mesh

## Slide 105: Torus

## Slide 106: Folded Torus

## Slide 107: Hypercube
H
0
H
1
H
2
H
3
H
4
0
0
1
00
01
10
11
000
001
010
011
110
111
101
100
(a)
(b)
(d)
(c)
(e)

## Slide 108: Butterfly
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
00
01
10
11
s
00
01
10
11
00
01
10
11

## Slide 109: Summary
Topology
# Switches
# Links
Diameter
Bisection Bandwidth
Chain
0
N-1
N-1
1
Ring
0
N
N/2
2
Fat Tree
N-1
N(log(N))
2log(N)
N/2
†
Mesh
0
2N –
2√
N
2√
N –
2
√ N
Torus
0
2N
√ N
2√
N
Folded Torus
0
2N
√ N
2√
N
Hypercube
0
N log (N)/2
log(N)
N/2
Butterfly
N log (N)/2
N
+
N log (N)
log(N)+1
N/2
†
Assume that the size of each link is equal to the number of leaves in its subtree
In a fat tree, we assume that the size of each link is equal to the number of nodes in its subtree.

## Slide 110
THE END