## Slide 1
Chapter 9:
Multicore Systems

## Slide 2: Background Required to Understand this Chapter
Caches
On-Chip Network
Graph Algorithms
Chapters 7 and 8

## Slide 3: Contents
1.
Parallel Programming
2.
Theoretical Foundations
3.
4.
5.
AGENDA ITEM 06
Green marketing is a practice whereby companies seek to go above and beyond.
Cache Coherence
Memory Models
Data Races
6.
Transactional Memory

## Slide 4: Era of Sequential Computing is Over
Single core performance from 2001 to 2010
It has clearly saturated after 2008.
40
35
30
25
20
15
10
5
0
Speclnt 2006 Score
29/10/99
12/03/01
25/07/02
07/12/03
20/04/05
02/09/06
15/01/08
29/05/09
11/10/10
23/02/12
Date

## Slide 5: Solution
Have multiple cores that collaboratively solve a task.
Big Problem
Smaller problems
Map each sub-problem
to a core

## Slide 6: Problem
Take an array numbers with SIZE elements.
Compute the sum of all of its elements.
Distribute the work among N threads.
Approach
Divide the array into N parts.
Assign each part to a core.
Compute the partial sum (sum of each part)
Add the partial sums

## Slide 7: Shared Memory based Programming
Each core runs a thread.
Different threads share parts of the virtual memory space
They communicate by reading and writing to shared variables
Core 1
Core 2
Core N
Shared memory

## Slide 8
/* variable declaration */
int partialSums [N];
int numbers [SIZE];
int result = 0;
/* initialise arrays */
...
/* parallel section */ # pragma omp parallel {
  /* get my processor id */
    int myId = omp_ get_ thread_ num ();
/* add my portion of numbers */
int startIdx = myId * SIZE/ N;
int end Idx = startIdx + SIZE/ N;
    for( int jdx = startIdx; jdx < end Idx; jdx++)
    partialSums[ myId] += numbers[ jdx];
}
/* sequential section */
for( int idx=0; idx < N; idx++)
result += partialSums[ idx];
OpenMP
code

## Slide 9: A Typical Shared Memory Program
Parent thread
Time
Spawn child threads
Child
threads
Thread join operation
Sequential
section
Initialization

## Slide 10: Message Passing Code
Cores communicate by sending messages to each other
They do not share memory.
There are two basic functions.
Function | Semantics
send(pid, val) | Send the integer val to the process with id, pid
receive(pid) | Receive an integer from process pid This is a blocking call If the pid is equal to ANYSOURCE, then the receive function returns with the value sent by any process

## Slide 11
/* start all the parallel processes */
Spawn AllParallelProcesses();
/* For each process execute the following code */
int myId = getMyProcessId ();
/* compute the partial sums */
int startIdx = myId * SIZE/ N;
int end Idx = startIdx + SIZE/ N;
int partialSum = 0;
for( int jdx = startIdx; jdx < end Idx; jdx++)
    partialSum += numbers[ jdx];
/* All the non - root nodes send their partial sums to the root */
if( myId != 0) {
        /* send the partial sum to the root */ send (0 , partialSum );
}
Message
passing
code

## Slide 12: Continuation
else {
/* for the root */ int sum = partialSum ;
    for ( int pid = 1; pid < N; pid ++) {
    sum += receive( ANYSOURCE );
    }
    /* shut down all the processes */
    shutDown AllProcesses();
    /* return the sum */
    return sum;
}

## Slide 13: Shared Memory vs Message Passing
Easy to program.
Issues with scalability
The code is portable across machines.
Shared memory
Message passing
Hard to program.
Scalable
The code may not be portable across machines.

## Slide 14: Amdahl’s Law
How much can we parallelize?
We are limited by the fraction of the sequential section: fseq
For P processors
Speedup
As ,

## Slide 15: Speedup vs #Processors
Number of processors (P)
Note the saturation of the speeudup

## Slide 16: Gustafson-Barsis’s Law
Old workload: W
New workload: Scale the parallel part by #procs (P)
Entity | Mathematical expression
New workload | 
Sequential Time () is a constant of proportionality | 
Parallel Time () | 
Entity | Mathematical expression
New workload | 

## Slide 17: Design Space of Multiprocessors: Flynn’s Classification
SISD
Single inst. single data
SIMD
Single inst. multiple data
MIMD
Multiple inst. multiple data
MISD
Multiple inst. single data

## Slide 18: Explanation of the Flynn’s Classification
SISD Processors
A regular single core processor
SIMD Processors
Single instruction stream, multiple data streams
Vector instruction set. Example: add v1, v2, v3
v1, v2, and v3 are vector registers
They pack multiple integers (let’s say 4)
A pairwise addition is performed
Summary: We can do 4 additions using just a single instruction

## Slide 19: Explanation II
MISD Processors
Used in airplanes: Run the same program on three separate processors that have different instruction sets. Compare the outputs and decide by voting.
MIMD Processors
SPMD Processors: Single program, multiple data. Run the same program on different cores with different data streams (most common)
MPMD Processors: Consider a processor with different accelerators. Each core or accelerator runs a different program.

## Slide 20
Hardware Threads

## Slide 21: Notion of Hardware Threads
We traditionally have processes that run on different cores.
Let’s say we have cores with large issue widths
  If processes have low ILP, then we waste issue slots
Run multiple processes simultaneously on the same core
Definition
Such processes that share cores are known as hardware threads.
They are not the same as software threads that share the virtual address space.

## Slide 22: Coarse-grained Multithreading
Run instructions from thread 1 for k cycles.
Then switch to thread 2, then to thread 3, thread 4, thread 1, ...
Separate program counters, ROBs and retirement register files per thread
Each instruction packet, rename table entry, LSQ entry, physical register is tagged with the thread id
If there is a high-latency event like an L2 miss, the core can switch to a new thread.
1
3
2
4

## Slide 23: Fine-grained Multithreading
Coarse-grained multithreading does not let the processor idle, if there is a high-latency event.
Fine-grained multithreading reduces k to 1-5 cycles.
We can tolerate low-latency events like L1 misses.
There is an additional overhead of excessive thread switching.

## Slide 24: Simultaneous Multithreading (SMT)
Run multiple hardware threads simultaneously
Dynamically split the issue slots between the threads
There are several heuristics for partitioning the issue slots
  Fairness
  Instruction criticality (higher priority to loads)
  Thread criticality: real time, non-real time
  Based on instruction type (expected ILP, etc.)
Hyperthreading  SMT with static partitioning (typically 50:50)

## Slide 25: Comparison of Different Hardware Multithreading Schemes
T
i
m
e
Coarse-grained
multithreading
Fine-grained
multithreading
Simultaneous
multithreading
Thread 1
Thread 2
Thread 3
Thread 4
issue
slots

## Slide 26: Contents
1.
Parallel Programming
2.
Theoretical Foundations
3.
4.
5.
AGENDA ITEM 06
Green marketing is a practice whereby companies seek to go above and beyond.
Cache Coherence
Memory Models
Data Races
6.
Transactional Memory

## Slide 27: Issues with Large Caches
Large caches’ access times can be between 10-50 cycles
  Requests need to traverse the NoC
If we have many cores, they will make parallel accesses.
We are dealing with large, slow, multi-ported caches.
This is not possible to build.
Create large distributed caches.

## Slide 28: Notion on a Distributed Cache
Make a set of small caches act like one single, large cache.
Each sister cache is small and fast.
Many parallel accesses.

## Slide 29: Shared vs Distributed Caches
We want a set of small L1 caches (sister caches) act like one, single, large L1 cache. How is this possible?
Consider accesses to a single memory address/variable, x
If we have a single physical location for x, then there is no advantage of a distributed design.
If we have multiple locations for storing the variable x, then the replicas have to contain the same value.
This is the problem of coherence.
Coherence  Make a set of locations behave like a single location.

## Slide 30: Consider Multiple Locations
Thread 1 | Thread 2
x = 1 | t1 = y
y = 1 | t2 = x
Assumptions
All global variables are initialized to 0. They start with u, v, x, y, or z.
All local variables are mapped to registers. They start with a ‘t’.
The delay between the execution of consecutive instructions can be indefinitely large. Instructions across threads can execute in any order.
Is the outcome <t1, t2> = <1,0> possible?
It for some reason bothers us because no sequential ordering of instruction executions can produce this outcome.

## Slide 31: This outcome is indeed valid on many machines
Thread 1 sets x to 1
It sends an update message on the NoC. The message gets caught in congestion.
Thread 1 sets y to 1. The corresponding message on the NoC is swiftly delivered.
Thread 2 reads y to be 1.
Thread 2 reads x as 0 (initialized value)
Thread 1 | Thread 2
x = 1 | t1 = y
y = 1 | t2 = x
This is indeed possible!

## Slide 32: One More Example
Can we read <t1, t2> = <0,0> ?
Thread 1 | Thread 2
x = 1 | y = 1
t1 = y | t2 = x
The loads are issued early, and the writes happen at commit time.

## Slide 33: Set of Valid Outcomes
Given a parallel program, what are the set of valid outcomes?
This depends on the system on which the program is running. It depends on ....
The pipeline
Memory system
NoC
Memory controller (for off-chip memory)
Every processor has a set of specifications that specify the allowed outcomes/behaviors. If the behavior is consistent with the specifications, the execution is said to be consistent.
This specification is known as the memory model or memory consistency model.

## Slide 34: Difference between Memory Consistency and Memory Coherence
A memory consistency model or a memory model is a policy that specifies the behavior of a parallel, multithreaded program. In general, a multithreaded program can produce a large number of outcomes depending on the relative order of scheduling of the threads, and the behavior of memory operations. A memory consistency model restricts the set of allowed outcomes for a given multithreaded program. It is a set of rules that defines the interaction of memory instructions between each other.
Coherence is a subset of the overall memory model that specifies the behavior with respect to a single location.

## Slide 35
Theoretical Foundations

## Slide 36: Every Observer has a Point of View
Queue
Cache
Observer
Timeline of memory requests seen by the observer:
Time
R1
R2
R3
t
start
t
comp
t
end
t
start
t
comp
t
end
t
start
t
comp
t
end
tstart | Start time
tend | End time
tcomp | Completion time

## Slide 37: Definition of an Execution
Operation
tid
type
read
write
tstart
tend
addr
value
Operation
Operation
Operation
Operation
Execution

## Slide 38: More about Executions
Sequential Execution
All the operations are ordered.
Legal Sequential Execution
Every read operation returns the value of the latest write operation to the same address.
The observer sitting on a memory location needs to observe a legal sequential execution.

## Slide 39: Observer sitting on a Core
In the case of a load, this relationship still holds 
However, things change for a store.
We don’t know when it will complete. The store will be put on the NoC. It may reach the cache bank a long time later.
The operation ends when the store leaves the ROB.
We can very well have 
Even in this case, the observer on the core expects to see a legal sequential execution
Otherwise, the execution will not make any sense ....

## Slide 40: Parallel Executions
Consider a parallel execution.
Term | Meaning
Rx1 | Read the value of x as 1
Wy2 | Set y = 2
Multiple threads: one observer per thread. Each observer records the local execution history of a thread.

## Slide 41: A Parallel Execution
Note the time line: ordered by the completion time.
3

## Slide 42: Issues with Parallel Executions
Atomicity  Every operation has a single completion time. It appears to execute instantaneously at that point of time.
Have multiple observers (one per each thread) with their points of view does not help.
It is better if we can think of parallel executions in terms of sequential executions  It is very intuitive.
For this, we need to introduce the notion of the equivalence of executions: P and S.

## Slide 43: Equivalence of Two Executions
Equivalence of two executions
Expression | Meaning
P ¦ T | All the operations issued by thread T (in the same order). This is an ordered sequence.
 | There is a one-to-one mapping between the two sequences of operations.
 | For all T,
Expression | Meaning
P ¦ T | All the operations issued by thread T (in the same order). This is an ordered sequence.
 | There is a one-to-one mapping between the two sequences of operations.

## Slide 44: Example of Execution Equivalence
1  1’, 2  2’, ... , 7  7’
Mapping

## Slide 45: Sequential Consistency
When is a parallel execution equivalent to some sequential execution?
Sequential Consistency (SC)
When a parallel execution is equivalent to a legal sequential execution and the order of operations in the sequential execution is as per program order, we say that the execution is sequentially consistent.
We can interleave the executions of different threads such that they are arranged sequentially, every read receives the value of the latest write, and for each thread the operations are arranged in program order.

## Slide 46: Key Properties of SC
Writes are atomic
Program order is preserved
SC = Atomicity + Program Order
Reordering accesses to different addresses might create havoc in multiprocessor systems.

## Slide 47: Examples of Single-variable Programs
T1 | T2 | T3
Wx1 | Rx0 | Rx1
Wx2 | Rx2 | Rx2
T1 | T2 | T3
Wx1 | Rx1 | Rx2
Wx2 | Rx2 | Rx1
Execution in SC
Execution that is not in SC
Rx0  Wx1  Rx1  Wx2  Rx2 (T2)  Rx2 (T3)
This behavior is non-intuitive. For x there appear to be different storage locations.
If we consider all the accesses to a single variable (memory location), let such an execution be always in SC. This is known as the PLSC (Per Location Sequential Consistency) constraint. It is needed to provide the illusion of a single memory location, even if we have a distributed cache.
PLSC

## Slide 48: SC for Multi-variable Programs
Can <x,y> = <0,0>?
T1 | T2
Wx1 | Wy1
Ry0 | Rx0
This execution is not in SC
T1 | T2
Wx1 | 
 | Rx0
Accesses w.r.t x
Accesses w.r.t y
T1 | T2
 | Wy1
Ry0 | 
Both are in PLSC
PLSC does not guarantee SC?

## Slide 49: Why not make all machines guarantee SC?
The outcome <x,y> = <0,0> is clearly not in SC.
This is because
  The loads will be sent early to the cache
  The stores will only be sent at commit time
  This means that both the loads will read x and y to be 0
If we still need SC then
  Loads will have to be issued at commit time
  All the benefits of OOO execution and the LSQ will go away
For high performance we need to sacrifice SC
  It prohibits many performance-enhancing optimizations
T1 | T2
x = 1 | y = 1
t1 = y | t2 = x
Threads can reorder accesses to different addresses.

## Slide 50: Non-atomic Writes
This execution is clearly not in SC
It is however in PLSC. Verify
However, the write to x appears to have different completion times for different threads. The write is non-atomic.
T1 | T2 | T3
Wx1 | while (x != 1) {} | while (y != 1) {}
 | Wy1 | Rx0
T1 | T2 | T3
Wx1 | Rx1 | Ry1
 | Wy1 | Rx0
T1 | T2 | T3
Wx1 | Rx1 | 
 |  | Rx0
T1 | T2 | T3
 |  | Ry1
 | Wy1 | 

## Slide 51: Non-Atomic Writes - II
This is possible in many architectures such as IBM and ARM machines
Thread 2 is basically reading the write to x early  before it is visible to Thread 3
This is possible if multiple locations store the variable x, and Core 2 is closer to Core 1 and Core 3 is much farther away.
In a system with an NoC, this can easily happen.
Given that this execution is in PLSC, let us accept it.

## Slide 52: Behaviors not in PLSC
This behavior is not in PLSC
SC implies PLSC, PLSC does not necessarily imply SC
Writes atomic w.r.t. one location need not be atomic w.r.t. accesses for multiple locations.
Such behaviors break the notion of shared memory completely
T1 | T2 | T3
Wx1 | Rx1 | Rx2
Wx2 | Rx2 | Rx1
Let us thus allow non-atomic writes as long as PLSC is preserved.

## Slide 53: Summary Till Now
SC is intuitive yet impractical
SC = Atomicity + Program order
PLSC is definitely required
SC implies PLSC (not the other way round)
In OOO machines, it is impractical
PLSC holds in systems that have non-atomic writes.
It is needed to provide the illusion of a single memory location in a distributed cache

## Slide 54: From PLSC to Coherence
Akin to the definition of SC, we can define PLSC as per-location program order + atomicity (viewed per location)
Program order basically means that processors or cache controllers are not allowed to reorder accesses to the same address.
Since caches have FIFO queues for requests, they already ensure program order.
Consider atomicity. Because of PLSC an observer at a memory address always sees atomic writes, but an observer on a core may see non-atomic writes because of intervening accesses to other addresses.
For a given address, let us look at the following orders of operations
  Global order  All observers record this order between operations
  Local order  A few observers do, and a few don’t

## Slide 55: Ordering between Accesses to the Same Variable across Threads (Observer at the Core)
Order | Implication
Read  Read | Does not matter
Write  Read | Given that a core can read another core’s write early, while other cores may not even see the write, this order may not be global all the time. A core does not know when a write reaches the sister caches present in other cores. Hence, it may not agree about the values read by other cores; this order is local.
Write  Write | If this order is not global, then the same variable will end up with multiple final states. This is not allowed. Hence, in all systems this order is global.
Read  Write | Writes are globally ordered. Assume one core records Wi  Ri  Wj . All the cores will record Ri  Wj because the core that issued Ri could not have seen Wj else it would have read a different value.

## Slide 56: Implications of PLSC (Observer at the Core)
Write  Write order is global
Read  Write order is global
Write  Read order is global only for machines with atomic writes.
Writes to the same location are globally ordered.
Write Serialization
Axioms of Coherence
Write Propagation
A write is eventually seen by all the threads.

## Slide 57
SC Using Synchronisation Instructions

## Slide 58: Communicating a Value between Threads
This code will work correctly on an SC machine. It will not work correctly on other machines with other memory models.
The ordering between the read and write in T2 may not hold.
A store instruction fully completes when all the threads can read the stored value
T1 | T2
value = 3 | while (status != 1) {}
status = 1 | temp = value
fence instruction  All the instructions fetched before the fence need to fully complete before the fence instruction executes. All the instructions after the fence instruction cannot execute until the fence instruction has completed.

## Slide 59: Code with fence Instructions
Regardless of the underlying memory model this code will always work
Memory barriers
  A fence is an example of a memory barrier
  Specifies rules of completion for instructions before and after the barrier (in program order)
  Store barrier  Ensures an ordering between store instructions before and after the barrier instruction.
T1 | T2
value = 3 | while (status != 1) {}
fence | fence
status = 1 | temp = value

## Slide 60: Acquire and Release Instructions
Acquire instruction  No instruction after the acquire instruction in program order can execute before it has completed.
Release instruction  The release instruction can only complete if all the instructions before it have been fully completed. Note that the release instruction allows instructions after it to execute before it has completed.

## Slide 61
Theory of Memory Models

## Slide 62: Where do we stand ...
Processors reorder instructions that access different addresses
Very problematic in multithreaded systems  non-intuitive behaviors
Writes can be non-atomic
How do we reason about the correctness of these systems?
SC gave us a mechanism where we could map a parallel execution
to a legal sequential execution (LSE). We could then reason on the LSE.
What about non-SC executions?

## Slide 63: Method of Execution Witnesses
A given piece of parallel code can have many different executions.
The valid outcomes are dependent on the memory model of the machine.
For each execution (valid or invalid), we can create an execution witness (a graph containing nodes and edges).
If we can convert the execution witness to a sequential execution that obeys the memory model, the execution is valid, otherwise it is invalid.
Parallel Execution
Execution Witness
Sequential Execution

## Slide 64: Execution Witness
It is a graph
The nodes are the instructions
We can have edges between the instructions based on the orders that are guaranteed by the memory model.
We can have two edges: global and local
These are happens-before edges  If means that event A happened first and then event B happened after that. It could be immediately later or after a very long time.
A global hb edge (ghb) is agreed to by all threads.
T1 | T2
x = 1 | y = 1
t1 = y | t2 = x
SC Execution | 
1 | x = 1
2 | t1 = y
3 | y = 1
4 | t2 = x
<t1,t2> = <0,1> | 

## Slide 65: Program Order (po) Edge
Edge | Description
poRW | Read  Write edge
poRR | Read  Read edge
poWR | Write  Read edge
poWW | Write  Write edge
poIS | read/write  synch operation
poSI | synch  read/write operation
All the edges are between memory operations issued
by the same thread regardless of their address.
Not always global. Global only in SC.
Global

## Slide 66: Example of a po edge
We create a node for each memory operation
We add edges between them (as per the memory model)
T1 | 
(a) | x = 1
(b) | y = 1
(c) | t1 = x
Wx1
Wy1
Rx1
(a)
(b)
(c)
po
po
Execution witness

## Slide 67: rf (read from) edge
If writes are atomic, the rfe edge is global. Not otherwise.
rfi is not global when we have optimizations like load-store forwarding where a core can read its own value before other cores can.
rf edge
rfe edge
rfi edge
Read and write ops in different threads
Read and write ops in the same thread
T1 | T2
(a) x = 1 | (b) t1 = x
t1 = 1
Wx1
(a)
Rx1
(b)
rfe

## Slide 68: Write Serialization (ws) Edge
This is always global. This is a direct consequence of PLSC and the requirements of coherence.
T1 | T2 | T3
(a) x = 1 | (b) x = 2 | (c) t1 = x (d) fence (e) t2 = x
t1 = 1, t2 = 2
Execution witness
Wx1
Wx2
Rx1
fence
Rx2
ws
rf
rf
po
po
(a)
(b)
(c)
(d)
(e)

## Slide 69: From-read (fr) Edge
This edge is global because of PLSC.
T1 | T2
x = 1 x = 2 | (c) t1 = x
t1 = 1
Execution witness
Wx1
Wx2
Rx1
ws
rf
fr
(a)
(b)
(c)

## Slide 70: Synchronization Edge: so
Assume y is a synchronization variable.
All updates to such synch variables are globally ordered.
T1 | T2
x = 1 y = 1 | (c) t1 = y (d) t2 = x
t1 = 1, t2 = 1
Wx1
Wy1
Ry1
po
rf
rf/so
(a)
(b)
(c)
Rx1
po

## Slide 71: Relationships between memory accesses
po
program order edge (same or different addresses)
rf
write  read, dependence (same address)
ws
write  write (same address)
fr
read  write (same address)
so
Synchronisation edge between synch operations.

## Slide 72: Summary: Memory Models
ws, fr, and so are always global
Let be global
Let 𝑔𝑝𝑜 ⊆𝑝𝑜 be global
Let be global
Let grf ⊆𝑟𝑓 be global
grf=rf and gpo=po only for SC
ws, fr, and so are always global
grf=rf and gpo=po only for SC

## Slide 73: Cycles in an Execution Witness
If a graph does not have a cycle, we can arrange all the nodes in a linear sequence such that
If there is a path from operation A to B in the graph, then A appears before B in the linear sequence.
This is a topological sort.
An acyclic execution witness
Sequential execution that respect ghb

## Slide 74: Implications of a Sequential Execution
For an arbitrary memory model
  We can now establish an equivalence between a parallel execution and a sequential execution.
It may not be legal.
The sad part is that it may not be legal if writes are not atomic.
At least the fact that we established an equivalence means that
the execution is feasible according to the memory model.

## Slide 75
Access to a Single Location Data and Control Dependences

## Slide 76: Access Graphs: All accesses to the same location
T1
(a) x = 1
(b) x = 2
(c) y = 3
(d) z = x + y
(e) x = 4
Wx1
(a)
Wx2
up
(b)
Rx2
(d)
up
up
Wx4
(e)
Instead of po edges, we have up edges  Edge between accesses to the same location in the same thread.

## Slide 77
PLSC is always respected regardless of the memory model.
Hence, the access graph never has cycles.

## Slide 78: Example
Note the up edges and the presence of the cycle.
T1 | T2 | T3
(a) x = 1 | (c) x = 2 | (d) t2 = x
(b) t1 = x |  | (e) t3 = x
<t1,t2,t3> = <2,1,0>?
Wx1
Wx2
Rx2
Rx1
Rx0
rf
up
ws
rf
up
fr
fr
(a)
(b)
(c)
(d)
(e)

## Slide 79: Data and Control Dependences
T1 | T2
(a) t1 = x | (d) t2 = y
(b) if (t1 == 1) { | (e) fence
(c) y = 2 } | (f) x = 1
Rx1
if-stmt
Wy2
Ry2
fence
Wx1
t1 = 1, t2 = 2
rfe
rfe
po
po
There is a clear breakdown of causality. Rx1 seems to be happening without a preceding write. This is a thin air read.
(a)
(b)
(c)
(d)
(e)
(f)

## Slide 80: Causal Graph
Three kinds of global edges: rf, gpo (all global program order edges), dep (dependences)
Rx1
if-stmt
Wy2
Ry2
fence
Wx1
rfe
rfe
po
po
(a)
(b)
(c)
(d)
(e)
(f)
dep
dep
To stop thin air reads

## Slide 81: Putting it all Together
Condition | Test
Satisfies the memory model | The execution witness is acyclic.
PLSC holds for all memory locations | All access graphs are acyclic.
No thin air reads | The causal graph is acyclic.

## Slide 82: Contents
1.
Parallel Programming
2.
Theoretical Foundations
3.
4.
5.
AGENDA ITEM 06
Green marketing is a practice whereby companies seek to go above and beyond.
Cache Coherence
Memory Models
Data Races
6.
Transactional Memory

## Slide 83
Write Update Protocol

## Slide 84: Enforce PLSC in Hardware
All writes to the same location are seen in the same order
A write ultimately completes
Bus based Model
Shared bus
Cache 1
Cache 2
Cache 3
Cache 4

## Slide 85: Write-Update Protocol
Every cache line has three states
State | Meaning
M | Modified
S | Shared with other sister caches
I | Invalid
Event | Message Notation
Event Type | Meaning
Rd | Read request
Wr | Write request
Evict | Evict the block
Wb | Write back data to the lower level
Update | Update the copy of the block

## Slide 86: Message Types
Message Type | Meaning
RdX | Generate a read miss message. Send it on the bus/NoC if required.
WrX | Generate a write miss message. Send it on the bus/NoC if required.
WrX.u | Get permission to write to a block that is already present in the cache.
Broadcast | Broadcast a write on the bus.
Send | Send a copy of the block to the requesting cache.

## Slide 87: Snoopy Protocols
Cache coherence protocols that use buses are known as Snoopy protocols.
All messages are essentially broadcast messages.
All the caches can read them (snoop on them).
These are easy to design
There are serious scalability issues. Such systems do not scale beyond 4 to 8 cores.

## Slide 88: Reads
If the block is not present, send a read miss message on the bus.
S state  If it is already present, don’t do anything. Just read it.
The S state allows seamless evictions
I
S
Evict | -
Rd | RdX
Rd | -

## Slide 89: Writes
I
M
Evict | Wb
Wr | WrX
Rd | -
Wr | Broadcast
If the block is not present, send a write miss message on the bus. Transition to the M state.
If it is already present, don’t do anything. Just read it.
M state  If we need to write, the write is broadcasted first to the rest of the sister caches.
The M state does not allow seamless evictions. We write back the data to the lower level, while evicting  Otherwise, the updates will be lost.
Broadcasting after every write is the issue.

## Slide 90: All the transitions due to read, write, and evict events
I
M
Evict | Wb
Wr | Wrx
Rd | -
Wr | Broadcast
S
Evict | -
Rd | RdX
Rd | -
Wr | Broadcast
Power hungry step

## Slide 91: Events Received from the Bus
RdX | Send
WrX | Send
S
Broadcast | Update
M
RdX | Send
WrX | Send
Broadcast | Update
Given that only one sister cache can use the bus at any time, a global order of writes is automatically enforced.
If the bus master disallows starvation, then all writes will ultimately
complete.

## Slide 92
Write Invalidate Protocol

## Slide 93: Single Writer Multiple Reader Model for each Cache Line
Single Writer
Multiple Readers
Ensures a global order of writes to the same memory location

## Slide 94: Write Invalidate Protocol (MSI Protocol)
I
S
M
Rd | RdX
Wr | WrX
Rd | -
Wr | WrX.u
Rd | -
Wr | -
Evict | -
Evict | Wb
Only one cache can contain
a block in the M state. At that point, no other cache has a valid copy.
Multiple caches can have the
block in the S state. They can all read from it.
Seamless reads and writes
Upgrade the status of the line

## Slide 95: Transitions because of Messages Received on the Bus
If any line is in the modified state and another cache requests for the block, then a state transition is necessary.
A writeback is necessary here. The S state has seamless evictions.

## Slide 96: MESI Protocol
Insight: Consider a core that reads a block, and the block is never shared. It will be read first in the shared state, and then an additional message (WrX.u) is required to transition to the M state.
Can we avoid this?
Add an additional Exclusive (E) state  The block is only present in one cache. If we are reading a block from the lower level, it enters the E state.
The rest remains the same.
MSI protocol  MESI protocol

## Slide 97: MESI (Read, Write, and Evict events)
I
S
E
M
Rd | RdX
Rd | RdX
(from lower
level)
Wr | WrX
Rd | -
Wr | WrX.u
Wr | -
Rd | -
Wr | -
Rd | -
(from sister cache)
Evict | -
Evict | -
Evict | Wb
New state
Seamless transition

## Slide 98: MESI (messages received from the bus)
The moment another cache requests for the data (read-only), we need to transition to the S state.

## Slide 99: Important Engineering Questions
Who supplies data if a sister cache sends a read miss or write miss message?
Answer:
The caches who have a copy of the block, arbitrate for the bus. The one who gets access to the bus first, sends the data. The rest snoop this value, and then cancel their request. This is an overhead in terms of time and power.
Do we have to write data back on an M  S transition?
Answer:
In the interest of performance and power, it will be the best if we can avoid it.

## Slide 100: MOESI (messages received from the bus)
Whenever, another cache requests for data, from an E or M state, the line moves to the O state.
In the O state, it sends data to other requesting caches.
We will discuss the Probe message in the next slide.
From the S state, no data is sent.

## Slide 101: MOESI
I
S
E
M
Rd | RdX
Wr | WrX
Rd | -
Wr | WrX.u
Wr | -
Rd | -
Wr | -
Rd | -
Evict | -
Evict | -
Evict | Wb
O
Rd | -
Wr | WrX.u
Evict | Wb
St
Reply | -
Se
Timeout | Probe
Reply | -
Timeout | Read from
lower level
Ignore the two temporary states – St and Se – for the time being.
Main problem: An eviction from the O state, leaves us with a state where there is no owner.
This makes the transitions from the I state tricky

## Slide 102: MOESI
I
S
E
M
Rd | RdX
Wr | WrX
Rd | -
Wr | WrX.u
Wr | -
Rd | -
Wr | -
Rd | -
Evict | -
Evict | -
Evict | Wb
O
Rd | -
Wr | WrX.u
Evict | Wb
St
Reply | -
Se
Timeout | Probe
Reply | -
Timeout | Read from
lower level
We first transition to the St state upon encountering a read miss
If a Reply is received, then the state transitions to the shared(S) state.
Otherwise, there is a timeout. A Probe message is sent. We transition to the Se state.
Again, if we receive a Reply from a cache (line in the S state), we transition to the S state.

## Slide 103: MOESI
I
S
E
M
Rd | RdX
Wr | WrX
Rd | -
Wr | WrX.u
Wr | -
Rd | -
Wr | -
Rd | -
Evict | -
Evict | -
Evict | Wb
O
Rd | -
Wr | WrX.u
Evict | Wb
St
Reply | -
Se
Timeout | Probe
Reply | -
Timeout | Read from
lower level
If there is a timeout in the Se state, we read from the lower level.
Transition to the E state.

## Slide 104
Directory
Protocol

## Slide 105: A Scalable Solution: Directory Protocol
  Do not have a bus
  Have a dedicated structure called a directory
  The directory co-ordinates the actions of the coherence protocol
  It sends and receives messages to/from all the caches and the lower level in the memory hierarchy
  Scalable
Cache
Cache
Directory
Cache
Cache
Lower Level in the Memory Hierarchy

## Slide 106: Structure of the Directory
State of the entry
Block address
List of sharers
  List of caches that contain a copy of the block.
  Typically, stored as a bit vector. If the ith bit is set, it means that the ith cache has a copy of the block.
Block Address
List of Sharers
Directory Entry
Directory
State

## Slide 107: Design of the Directory
What are the messages that the directory receives?
  RdX
  WrX and WrX.u (regular and upgrade)
  Evict
What should the directory do:
  RdX  Locate a cache that contains the block (sharer) and fetch the block
  WrX and WrX.u  Ask all sharers to invalidate their lines, give exclusive rights to the cache that wants to write
  Evict  Delete the cache from the list of sharers
  The basic protocol at the level of the caches remains the same. The state transitions of directory entries are as follows.

## Slide 108: State Transitions of a Directory Entry (from the U and S states)
U
S
E
RdX | 1. Send RdX to one of the
sharers. Ask it to forward
a copy.
2. sharers += {P}
WrX.u | 1. Send WrX.u to all sharers
(other than P)
2. sharers = {P}
WrX | 1. Send WrX to all sharers
2. Ask one of the sharers to
forward a copy.
3. sharers = {P}
WrX |
1. sharers = {P}
2. Read from LL
sharers={} | -
Evict | sharers -= {P}
RdX |
1. sharers = {P}
2. Read from LL
LL  Lower level
U  Uncached
P sends a message

## Slide 109
U
S
E
RdX | 1. Send RdX to the sharer. Ask it
to forward a copy of the block.
2. sharers += {P}
Evict |
1. sharers = {}
WrX | 1. Send WrX to the sharer
2. Ask the sharer to forward a copy
3. sharers = {P}
State Transitions of a Directory Entry (from the E state)

## Slide 110: Enhancements to the Directory Protocol
Let us list some of the common problems associated with directories
  We need an entry for each block in a program’s working set (lot of storage)
  In each directory entry, we need an entry for each constituent cache (storage overheads)
  The directory itself can become a point of contention
  Let us look at 

## Slide 111: Distributed Directories
Address
Space
Split the address space
Directory
Directory
Directory
Directory
Directory
Split the physical address space
A directory handles all the requests for the part of the address space it owns
Resolves the issue of the single point of contention.

## Slide 112: List of Sharers
Space-efficient Solutions
    Maintain a bit for a set of caches. Run a snoopy protocol inside the set.
    Store the ids of only k sharers. Have an overflow bit to indicate that there are more than k sharers. In this case, every message needs to be broadcasted. [Partially mapped scheme]
block address
1 1 0 0 0 0 0 0 1 0 0 0 1 0 1 1
How to maintain the list of sharers?
Solution 1 [Fully mapped scheme]:
  If there are N processors, have a bit vector of N processors.
  Each block is associated with a bit vector of sharers

## Slide 113: Size of the Directory
The directory should ideally be as large as the number of blocks in the programs’ working sets
Having an entry for every block in the physical address space is impractical
Practical Solution:
  Design a directory as a cache
  Keep the state of a limited number of blocks
  If an entry is evicted from the directory, invalidate it in all the caches

## Slide 114: A Few More Issues
False sharing  Consider a 64-byte block. It is possible that different threads access different memory words within the block.
  The block will keep bouncing between caches.
  These are false sharing misses.
  Use a smart compiler to place data more intelligently.
Race conditions
  In real hardware, there are a lot of interactions. It is possible that multiple messages of different types for the same block might arrive at the same time.
  Such concurrent events (race conditions) need to be handled. Hence, a practical cache coherence protocol has close to a 100 states.

## Slide 115
Critical
Sections and Atomic Operations

## Slide 116: Consider this piece of code
t1 = account.balance;
t2 = t1 + 100;
account.balance = t2;
Can this code be executed in parallel by multiple threads?

## Slide 117: What is the problem?
Each line corresponds to a line of assembly code
Assume corresponding lines execute in parallel.
The final answer is wrong. It should be 300, it is 200.
t1 = account.balance;
t2 = t1 + 100;
account.balance = t2;
100
200
200
100
200
200
t1 = account.balance;
t2 = t1 + 100;
account.balance = t2;

## Slide 118: Solution: Use Locks
lock();
t1 = account.balance;
t2 = t1 + 100;
account.balance = t2;
unlock();
Only one thread can execute this piece of code at any single point in time.

## Slide 119: Use Atomic Instructions to Implement Locks
For implementing lock and unlock functions.
We need atomic instructions
Either execute completely or not at all. Nobody observes a partial state.
Most atomic operations also act as a fence.
Atomic exchange operation
xchg reg, <mem>
Atomically exchanges their contents

## Slide 120: Assembly Level Implementation of the Lock and Unlock Functions
.lock:
mov r1, 1
xchg r1, 0[r0]
cmp r1, 0
bne .lock
ret
r0 contains the lock address
The xchg instruction contains a fence
Contains 0 if the lock is not acquired
1 if acquired
.unlock:
mov r1, 0
xchg r1, 0[r0]
ret
We store 0 at the lock address

## Slide 121: Implementation of Atomic Exchange
xchg r1, [r2]
  temp = r1, r1 = [r2], [r2] = temp
It involves 3 steps
  1 memory read + 1 memory write + register move
  All the operations need to happen atomically
  This is called a read-modify-write instruction (RMW)
Method
  Get exclusive access (M state) with write permissions for the memory address in r2
  Perform the read-modify-write operation
  Do not respond to any other requests from the local cache, or other caches, or the directory when the operation is in progress
  Respond to the directory or other caches only when the operation is over

## Slide 122: Spin Locks
We need to repeatedly try to acquire the lock
This is a spin lock
There are a lot of overheads:
  Every time we access the lock, it needs to be read in the M state.
  Too many invalidation messages
Test and Exchange Lock

## Slide 123: Test and Exchange Lock
.lock:
mov r1, 1
.test
/* test if the lock is free */
ld r2, 0[r0]
cmp r2, 0
bne .test
/* attempt an exchange only when the lock is free */
xchg r1, 0[r0]
cmp r1, 0
bne .test
ret
.unlock:
mov r1, 0
xchg r1, 0[r0]
ret

## Slide 124
Atomic Operation | Example | Explanation
Test and Set | tas r1, 8[r0] | if (8[r0] == 0) { 8[r0] = 1; r1 = 1; } else r1 = 0;
Fetch and Increment | fai r1, 8[r0] | r1 = 8[r0]; 8[r0] = r1 + 1;
Fetch and Add | faa r1, r2, 8[r0] | r1 = 8[r0]; 8[r0] = r1 + r2;
Compare and Set | cas r1, r2, r3, 8[r0] | if (8[r0] == r3) { 8[r0] = r2; r1 = 1; } else r1 = 0;
Load linked (ll) Store conditional (sc) | ll r1, 8[r0] .... mov r2, 1 sc r3, r2, 8[r0] | r1 = 8[r0] /* Use the ll instruction */ ... /* sc */ if (8[r0] is not written to since the last ll){ 8[r0] = r2; r3 = 1; } else r3 = 0;

## Slide 125: Lock-free Algorithms
Let us write the same code without locks.
If the thread goes to sleep after acquiring the lock, all the threads wait.
while (1) {
t1 = account.balance;
t2 = t1 + 100;
if (CAS (account.balance, t1, t2))
break;
}
It is possible for a thread to starve – never get the lock.

## Slide 126: How do we eliminate starvation?
Wait free algorithms
Basic Idea
A request, T, first finds another request, R, that is waiting for a long time
T decides to help R
This strategy ensures that no request is left behind
Also known as an altruistic algorithm
Answer:

## Slide 127: Summary of Consensus Numbers
Type of Operation | Consensus Number
Atomic exchange | 2
Test and Set | 2
Fetch and add | 2
CAS (Compare and Set) | 
LL/SC | 
Type of Operation | Consensus Number
Atomic exchange | 2
Test and Set | 2
Fetch and add | 2
CAS (Compare and Set) | 
LL/SC | 
Are all atomic operations equally powerful?
Consensus number
Consensus problem: each thread proposes a value – one among the proposed values is chosen. The consensus number is the maximum number of threads that can solve this problem using a wait-free algorithm.
The consensus problem forms the theoretical basis of most concurrent algorithms.

## Slide 128: Contents
1.
Parallel Programming
2.
Theoretical Foundations
3.
4.
5.
AGENDA ITEM 06
Green marketing is a practice whereby companies seek to go above and beyond.
Cache Coherence
Memory Models
Data Races
6.
Transactional Memory

## Slide 129: Memory Models
The memory model is dependent on the processor architecture. If there are very aggressive optimizations, then the memory model has to be very weak.
PLSC requires the ws and fr orders to be global. All popular architectures follow PLSC, and many disallow thin air reads.
The only orders that can be local are rf and po.

## Slide 130: Write-to-Read Order
T1
T2
(d) t2 = y
(e) t3 = x
(a) x = 1
(b) t1 = x
(c) y = 1
Wx1
Rx1
Execution witness
rfi
po
Rx0
Ry1
po
(a)
(b)
(e)
(d)
t1= 1, t2 = 1, t3 = 0 ?
Wy1
(c)
rfe
fr
rfi
LSQ forwarding and write buffers

## Slide 131: Non-atomic Writes
T1
T2
(b) t1 = x
(c) y = 1
(a) x = 1
Wx1
Rx1
Execution witness
rfe
po
Rx0
Ry1
po
(a)
(b)
(e)
(d)
t1= 1, t2 = 1, t3 = 0 ?
Wy1
(c)
rfe
fr
T3
(d) t2 = y
(e) t3 = x
rfe
If writes are atomic, this behavior is not allowed, otherwise it is.
We are seeing writes to different locations in different orders.
Create local tiles of caches.

## Slide 132: Write-to-Write Order
T1
T2
(c) t1 = y
(d) t2 = x
(a) x = 1
(b) y = 1
Wx1
Wy1
Execution witness
po
rfe
Ry1
Rx0
po
(a)
(b)
(c)
(d)
t1= 1, t2 = 0 ?
fr
Even if writes are atomic, this behavior is not allowed.
If the W W ordering is relaxed, we will see writes to different locations in different orders.
Non-blocking Caches

## Slide 133: Read-to-Read Order
T1
T2
(c) y = 1
(a) t1 = x
(b) t2 = y
Rx1
Ry0
Wy1
Execution witness
po
fr
(d) t3 = y
(e) x = 1
T3
Ry1
Wx1
po
rf
rf
(a)
(b)
(d)
(c)
(e)
t1 = 1, t2 = 0, t3 = 1?
If the R R ordering is relaxed, we will observe this behavior.
Issues loads OOO in the LSQ

## Slide 134: Read-to-Write Order
T1
T2
(c) t2 = y
(d) x = 1
(a) t1 = x
(b) y = 1
Rx1
Wy1
Execution witness
po
rf
Ry1
Wx1
po
(a)
(b)
(c)
(d)
t1= 1, t2 = 1 ?
rf
If the R  W ordering is relaxed, we will observe this behavior.
Speculative writes

## Slide 135: Special case of rfi in SC.
Can the rfi relation be relaxed in SC?
The proof is there in the book

## Slide 136: Summary of Memory Models
Relaxation | W  R | W  W | R  R | R  W | rfe | rfi
SC |  |  |  |  |  | 
TSO (Intel) |  |  |  |  |  | 
Processor consistency |  |  |  |  |  | 
PSO |  |  |  |  |  | 
Weak Ordering/ RC |  |  |  |  |  | 
IBM PowerPC |  |  |  |  |  | 
ARM |  |  |  |  |  | 
Ordering is
relaxed

## Slide 137: Contents
1.
Parallel Programming
2.
Theoretical Foundations
3.
4.
5.
AGENDA ITEM 06
Green marketing is a practice whereby companies seek to go above and beyond.
Cache Coherence
Memory Models
Data Races
6.
Transactional Memory

## Slide 138: Increment a Counter
Let us say that all we want to do is
counter++
t1 = counter;
t2 = t1 + 1;
counter = t2;
fetch_and_increment (counter)
Uses an atomic instruction

## Slide 139: Code with Locks
If we do not want to write code using atomic instructions, we need to encapsulate this code within a critical section.
t1 = counter;
t2 = t1 + 1;
counter = t2;
lock()
unlock()

## Slide 140: Critical Sections
T
1
T
1
T
2
T
2
T
2
time
Successfully locked
Unlocked
Failed to acquire a lock

## Slide 141: Why do we need to use locks?
If there are no shared variables, do we need to use locks?
When do we need locks then?
Answer:
Answer:
Two blocks of code need to be making conflicting and concurrent accesses to the same address.
Conflicting accesses
At least one access is a write

## Slide 142: Concurrent Accesses
Common sense meaning  At the same time.
Rx0
Wx1
Rx0
Wx1
Rx0
Wx1
Rx0
Wx1
T1
T2
Execution witness
(a)
(b)
(a)
(b)
(c)
(d)
(a)
(b)
(c)
ws
po
po
fr
fr
Ry1
Rx1
T1
T2
(c)
(a)
(c)
(d)
Wx1
Wy1
Ry1
Rx1
Execution witness
(d)
(a)
(b)
(c)
po
po
so/rf
rf
x++ ;
Code for T1 and T2
Code for T1
x = 1;
Wx1
Wy1
Code for T2
while (y != 1) {}
t1 = x;
y = 1;
(b)
(d)
(d)
y is a synch variable
Note the so edge

## Slide 143: Data Races
Two accesses are said to be concurrent when there is no path between them in the execution witness that contains an so edge.
A pair of conflicting and concurrent accesses to the same regular variable constitute a data race.
Data Race
If a piece of code does not have data races, what does it mean?

## Slide 144: Does SC Imply Data-Race-Freedom?
S2
Wx1
Rx0
S1
Rx0
S1
S2
Wx1
T1
T2
Execution 1
(a)
(b)
Rx1
S1
S2
Wx1
Execution 2
(d)
Rx1
S1
S2
Wx1
T1
T2
(c)
po
so
po
po
rf
po
Data
race

## Slide 145: Does Data-Race-Freedom imply SC?
If there are two conflicting accesses, there will be an so edge on at least one path between them in the execution witness.
They will thus be ordered by the so edge.
Let us add all the SC edges to the execution witness.
A cycle implies that there is a cycle between synch operations.
This is not possible. Synch operations follow SC.
Proof by contradiction.
Refer to the book for the detailed proof.
Salient Points

## Slide 146: What does having data races imply?
If we have a data race in a program, we can construct an SC execution that also has a data race.
Theorem
Proof  refer to the book
What does it imply?
If an automated tool cannot construct an SC execution
that has a data race, then it means that the program
is data race free.
Method to detect data races

## Slide 147: Summary of All the Results
Properties
SC does not imply data-race-freedom.
Data-race-freedom implies SC
Non-SC execution implies data races
If an automated tool cannot construct an SC execution that has a data race, then it means that the program is data race free.
Programming languages need to define data-race-free memory (DRF) memory models that provide synchronization primitives.
Programmers need to use them to write properly synchronized programs.
This means that all accesses to shared variables are protected with critical sections such that there are no concurrent, conflicting accesses.
Moral of the story
If there are no data races, the memory model doesn’t matter

## Slide 148
Methods to Detect Data Races

## Slide 149: Data Race Detection Algorithm
We need an algorithm that tests a piece of code for data races
  Exercise all possible control paths
  Create as many interleavings as possible
A data race must show up in an SC execution
  Try to find it …
How do we detect data races?

## Slide 150: Notion of Lock Sets
A lock is identified by the lock address.
L(v)
Set of locks held by this memory location, v.
L(T)
Set of locks held by thread, T.
After each access we modify the lock set.
Compute an intersection

## Slide 151: Standard Approach
Add annotations to multithreaded code. These annotations modify the lock set.
The locksets of threads are initially empty.
For each variable, its lockset initially has all the locks.
When a thread acquires a lock, we add the lock to its lock set.
When it releases a lock, we remove the lock.
As the program executes, , keeps getting updated.
At the end, if there is a variable with an empty lock set, it is probably involved in a data race.
If the lock set is empty, it means that there is no
synchronization between accesses to the variable.

## Slide 152: Notion of False Positives
Note that we will detect many scenarios that are actually not data races. For example, the basic algorithm will flag a data race when we consider read-only variables.
A few more examples
Example | Description
Initialization | We typically initialize variables without using locks
Read-only variables | Written once (during initialization) and read many times
Reader-writer pattern | Multiple threads read a variable concurrently.

## Slide 153: Modified State Diagram for each Variable
The first access has to be a write. We then move to the Exclusive state.
If a different thread reads it, move to the Shared state.
The Shared state allows reads (irrespective of the thread).
After a write, move to the Modified state.
In the Modified state, run the regular lock set algorithm.

## Slide 154: Notion of Vector Clocks
We can think of a multithreaded execution environment as a classical distributed system
Here, there is no notion of global time.
Every thread has a local clock.
The local clocks are updated any time there is an interaction between threads.
Assume there are n threads. Every thread maintains an n-element vector clock. Thread i’s vector clock is .
is the best estimate that i has for j’s local clock

## Slide 155: Comparability of Clocks
Two vector clocks are equal when
Two vector clocks are totally ordered when
Two vector clocks may not always be comparable

## Slide 156: Notion of a Message
A message represents an interaction between two threads.
Say if a thread i accesses a variable in memory, it updates its state, and then thread j accesses the variable (and its state)  This is an interaction that falls under the theoretical definition of a message.
Memory location
Event 1
Event 2
hb
x = 1
t1 = x

## Slide 157: More about Events
Increment the local clock (e.g., for thread i) before sending a message and after receiving a message.
Let’s say, thread i sends a message to thread j. When j receives the message, it updates its clock as follows.
The receiver is as at least as up to date as the sender. It records an additional receive event.

## Slide 158: Vector Clocks and Causality
Let’s say that there is a happens-before relationship between events ei and ej. We use vector clocks to track the interaction.
Event | Time
ei | Event in thread i at time Vi
ej | Event in thread j at time Vj
We have the following relationship
This happens because the receiver has all the sender’s updates
and without a chain of happens-before edges, two vector clocks
will not remain comparable.

## Slide 159: Vector Clock based Algorithm
Symbol | Meaning
 | Vector clock of the current thread
 | Vector clock of the current lock
 | Read clock of variable v
 | Write clock of variable v
 | Thread id
Symbol | Meaning
 | Vector clock of the current thread
 | Vector clock of the current lock
 | Read clock of variable v
 | Write clock of variable v
 | Thread id
Increment the vector clock of CT and CL

## Slide 160: Read Operation
Increment the local count of the thread clock
If no thread has overwritten the value after the transaction started, then the read is successful. Update the read clock.

## Slide 161: Write Operation
Increment the local count of the thread clock
If no thread has overwritten or read the value after the transaction started, then the read is successful. Update the read and write clocks.

## Slide 162: Contents
1.
Parallel Programming
2.
Theoretical Foundations
3.
4.
5.
AGENDA ITEM 06
Green marketing is a practice whereby companies seek to go above and beyond.
Cache Coherence
Memory Models
Data Races
6.
Transactional Memory

## Slide 163: Lock and Unlock functions have a problem
If we have one lock, then there is no parallelism in the system.
We can afford much more parallelism.
The only constraint is:
  We should not have two parallel accesses to the same account.
void updateBalance ( int amount , Account account ) {
lock ();
int temp = account.balance ;
temp = temp + amount ;
account.balance = temp ;
unlock ();
}
Disjoint access parallelism

## Slide 164: Code that Allows Disjoint Access Parallelism
void updateBalance ( int amount , Account account ) {
account.lock ();
int temp = account.balance ;
temp = temp + amount ;
account.balance = temp ;
account.unlock ();
}
Account specific locks
This is a scalable solution.
But, there is a problem. If we have code where we acquire multiple locks, we may have a deadlock.

## Slide 165: Deadlock Situation
Thread A acquires lock A
Thread B acquires lock B
Thread A waits for lock B
Thread B waits for lock A
Deadlock

## Slide 166: Create a Transaction
Provides disjoint access parallelism
Automatically manages all the locks and avoids deadlocks.
void updateBalance ( int amount , Account account ){
atomic { /* an atomic transaction */
int temp = account . balance ;
temp = temp + amount ;
account.balance = temp ;
}
}
The atomic block implements a transaction

## Slide 167: Properties of a Transaction
Atomicity: Either the entire transaction completes or fails.
Consistency: A consistent state is a valid state that is as per a given set of specifications (consistency model). The property of consistency says that if the full system was consistent before a transaction started, it should be consistent after it ended.
Isolation: It appears that while the transaction was executing, regular instructions or other transactions were not executing.
Durability: Once a transaction has finished, its results are written to stable storage.

## Slide 168: Transactional Memory
Hardware TM
Software TM
A memory system that provides support for transactions is known as a transactional memory (TM).
Two Types

## Slide 169: Basics of Transactional Memory
set of variables that are
read by the transaction
set of variables that are
written by the transaction
read set
write set
Term | Meaning
Ri | Read set of transaction i
Wi | Write set of transaction i
Rj | Read set of transaction j
Wj | Write set of transaction j

## Slide 170: When do transactions conflict?
There is a conflict if and only if
Wi ∩ Wj ≠ φ
Wi ∩ Rj ≠ φ
Ri ∩ Wj ≠ φ
OR

## Slide 171: Abort and Commit
Commit
  A transaction completed without any conflicts
  Finished writing its data to main memory
Abort
  A transaction could not complete
  due to conflicts
  Did not make any of its writes visible

## Slide 172: What happens after an abort?
The transaction restarts and re-executes
Might wait for a random duration of time to minimize future conflicts
  do {
    …
    …
    } while (! Tx.commit());
This is automatically handled by the transactional memory system

## Slide 173: Basics of Concurrency Control
A conflict occurs when the read-write sets overlap
A conflict is detected when the TM system
becomes aware of it
A conflict is resolved when the TM system either
  delays a transaction
  aborts it
occurrence
detection
resolution

## Slide 174: Pessimistic vs Optimistic Concurrency Control
pessimistic
concurrency
control
occurrence,
detection,
resolution
optimistic
concurrency
control
occurrence
detection
resolution

## Slide 175: Version Management
Eager version management
  Write directly to memory
  Maintain an undo log
Lazy version management
  Write to a buffer (redo log)
  Transfer the buffer to memory on a commit
commit
abort
flush undo log
writeback undo log
commit
abort
writeback
redo log
flush redo log

## Slide 176: Conflict Detection
Eager
  Check for conflicts as soon as a transaction accesses a memory location
Lazy
  Check at the time of
  committing a transaction

## Slide 177: Semantics of Transactions
Serializable
  Sequential consistency at the level of transactions
Strictly Serializable
  The sequential ordering is consistent with the real time ordering
  This means that if Transaction A starts after Transaction B ends, it should be ordered after it in the equivalent sequential ordering
  For concurrent transactions, their ordering does not matter
  Opacity
  Even aborted transactions need to see a consistent state – one produced by only committed transactions
What about aborted transactions?

## Slide 178: Opacity
If one transaction executes after the other, x will always be equal to y
Assume optimistic concurrency control: resolution at the end
Assume Thread 1 reads x=0
Then the transaction on thread 2 finishes
The transaction on thread 1 needs to be aborted (will read y=5)
However, it will be stuck in the while loop, it will never reach the end
Opacity will not y to be read as 5
atomic {
t1 = x;
t2 = y;
while (t1 != t2) {}
}
Thread 1
atomic {
x = 5;
y = 5;
}
Thread 2

## Slide 179: Mixed Mode Accesses: Transactional and Non-Transactional
Single Lock Atomicity (SLA)
Assume all the transactions are protected by a single lock
Transactions first acquire a hypothetical (global) lock
Same definition of data races
Reduces concurrency
Disjoint Lock Atomicity (DLA)
Uses more locks than SLA: (let’s say one per variable)
We a priori need to know the locks that a transaction is going to use
Transactional Sequential Consistency (TSC)
We can order all transactions (committed or aborted) and regular instructions in a sequential order
All the instructions are in program order (incl. within transactions)

## Slide 180: Software Transactional Memory
Concurrency Control
  Optimistic or Pessimistic
Version Management
  Lazy or Eager
Conflict Detection
  Lazy or Eager
choices

## Slide 181: Support Required
Augment every transactional object/ variable with meta data
object
object
metadata
Transaction that has locked the object
Read or write

## Slide 182: Maintaining Read–Write Sets
Each transaction maintains a list of locations that it has
  read in the read-set
  written in the write-set
Every memory read or write operation is augmented
  readTX (read, and enter in the read set)
  writeTX (write, and enter in the write set, make changes to the undo/redo log)

## Slide 183: Bartok STM
Every variable has the following fields
  version
  value
  lock
value
version
Transactional Variable
Eager version management, lazy conflict detection

## Slide 184: Read Operation
Read Operation
Record the version of the variable
Add the variable to the read set
Read the value

## Slide 185: Write Operation
Lock the variable
Abort if it is already locked
Add the old value to the
undo log
Write the new value

## Slide 186: Commit Operation
Check if the version of the variable is still the same
For each entry in the read set
No
Yes
For each entry in the write set
Increment the version
Release the lock
Abort

## Slide 187: Pros and Cons
simple
reads are simple
provide a strong
semantics for
transactions
does not
provide opacity
uses locks
writes are slow

## Slide 188: Subtle Points
With an undo log, aborts are more expensive than commits
A transaction can read intermediate values written by transactions
Opacity is thus not guaranteed
Locks are kept for a long time: lock  commit

## Slide 189: TL2 STM
Uses lazy version management  redo log
Uses a global timestamp (globalClock)
Locks variables only at commit time
Every transaction does the following (atomically) when it starts:
globalClock++ ;
Tx.rv = globalClock ;
Set the value of the transaction’s Tx.rv timestamp (read version)

## Slide 190: Read Operation
Read Operation: read (tX, obj)
obj in the redo log?
v1 = obj.timestamp
result = obj.value
v2 = obj.timestamp
if( (v1 != v2) || (v1 > Tx.rv) || obj.lock) abort();
addToReadSet(obj);
return result;
No
Yes
Return value in the redo log
Check if the value and timestamp are collected atomically
Collect a snapshot

## Slide 191: Write Operation
Add entry to the redo log if required
Perform the write
Writes are

## Slide 192: Commit Operation
For each entry in the write set
Lock object
abort
failure
Tx.wv = ++globalClock (atomic)
For each entry e in the read set
if (e.timestamp > Tx.rv)
abort
failure
writeback redo log
For each entry e in the write set
e.timestamp = Tx.wv
Release the lock

## Slide 193: Pros and Cons
simple
provides opacity
A redo log is slower
uses locks
holds locks for a
lesser amount of time
Commits are more expensive than aborts

## Slide 194: Subtle Points
We use two timestamps per transaction: Tx.rv and Tx.wv
  We have,
We first write the variables to permanent state
  Then, we update their timestamps
  If another transaction sees an updated timestamp, it is sure that the variable has been written to
  Finally, we release the locks. This allows later reads.
Provides opacity

## Slide 195
Hardware Transactional Memory

## Slide 196: Case for Hardware
STM systems do not handle non-transactional accesses
Acquiring and releasing locks is expensive
Maintaining undo and redo logs is difficult
Hardware is much faster …

## Slide 197: Hardware Support (mostly based on LogTM)
ISA Support
Add three new instructions: begin, abort, and commit
Version Management
HW schemes mostly use eager version management – undo log
The log has its dedicated set of addresses in virtual memory
Cache line
R
W
If (R=1) some word has been read
If (W=1) some word has been written

## Slide 198: Conflict Detection
Use the coherence protocol to detect conflicts
Let us say core D has a miss. It sends a read-miss to the directory.
The directory forwards it to core C.
C detects a conflict.
It sends a nack message to D (via the directory).
The transaction at D aborts.

## Slide 199: Eviction
What if there is an eviction?
If there is an eviction in the M state, the state at the directory is set to M@C. C is the number of the core that evicted the block.
Sets the overflow bit to 1.
Let us assume silent evictions from the S state.
Whenever the directory gets a request for a block in the M@C state, it forwards it to core C.
Core C may not have the block in the cache.
It will however infer a conflict because of the state of the block in the directory (the block is in its write set).
If it gets a normal request (not @C), it will assume that the line was in the S state.

## Slide 200: Example
Core D sends a read-miss message to the directory.
The directory forwards it to core C with the (M@C) directive
Core C infers a conflict
Sends a nack back to D (via the directory)

## Slide 201: Subtle Issues
Assume a block has been evicted.
If there is a conflicting request by a non-transactional access, the current transaction has to abort
If a transaction aborts, then we need to clean the read/write sets. Some blocks might have gone to lower levels of the memory hierarchy.
Since we restore the entire undo log, the correct state of the blocks is restored (in the L1 cache). Wrong values at lower levels do not matter.
After a transaction finishes, all the R, W, M@C, and overflow bits need to be cleared.

## Slide 202
Cache coherence protocols enforce the axioms of coherence.
If a program is data-race-free its execution is in SC.
Transactional memory is a very easy-to-use paradigm for writing data-race-free code (wrapped in atomic blocks).
A memory model is determined by two factors: write atomicity and program order. It is specified by the po, rf, fr, and ws relations.
Per-location sequential consistency (PLSC) is followed by
all systems today. It translates to the axioms of coherence.
There are two paradigms in parallel programming:
shared memory and message passing
Conclusion

## Slide 203
The End