## Slide 1: Cache Coherence: Directory Protocol
Smruti R. Sarangi, IIT Delhi

## Slide 2: Contents
Overview of the Directory Protocol
Details
Optimizations

## Slide 3: Basic Idea of a Coherence Protocol
Memory Level n
Memory Level n+2
Private Cache
Private Cache
Private Cache
Private Cache
Private Cache
Private Cache
Coherent memory: multiple private caches  appear as one large shared cache
Level n+1

## Slide 4: Limitations of the Snoopy Protocol
Fundamentally relies on a broadcast based mechanism
  The order of writes is determined by the order of grant accesses to the broadcast bus
  This is not a scalable solution
  Solution: We can have different broadcast buses for different sets of addresses
    Can work for 4-8 core systems (not beyond, too many conflicts)
    Ultimately: not scalable
  We cannot make efficient use of the NoC
Also not very power efficient
  All the cores need to keep on snooping the bus
  Need to migrate to a message based system

## Slide 5: Single Writer Multiple Reader Model for each Cache Line
Single Writer
Multiple Readers
Ensures a global order of writes to the same memory location

## Slide 6: Solution: Directory Protocol
  Don’t have a bus
  Have a dedicated structure called a directory
  The directory co-ordinates the actions of the coherence protocol
  It sends and receives messages to/from all the caches and the lower level in the memory hierarchy
  Scalable
Cache
Cache
Directory
Cache
Cache
Lower Level in the Memory Hierarchy

## Slide 7: State of Lines in the Shared Cache Bank
Every line that is shared has some state associated with it
  I  Invalid
  S  Shared (with some other cache)
  E  Exclusive (no other cache contains a copy of this line)
  M  Modified (no other cache contains a copy of this line + this cache has modified it)
Meaning of the states
  I  Nothing exists, content is not valid (cannot read or write)
  S  Can read the line, not write
  E  We know that no other cache contains a copy of the line. Cannot immediately write, can read.
  M  Can read or write
Let us explain some common scenarios with two simple examples
tag
coherence state
tag array entry

## Slide 8: Main Actions of the Protocol (Example: read)
We want to read a line from cache C1
Line is not in the S or E or M state
Send a message to the directory
Directory locates the line
Line is contained in another cache
Ask the other cache for a read permission
Other cache: transitions the line to the S state (if not already so). Returns acknowledgement + contents
Acknowledgement + contents of the line
Directory forwards the line to C1

## Slide 9: Main Actions of the Protocol (Example: write)
We want to write a line to cache C1
Line is not in the E or M state
Send a message to the directory
Directory locates all the caches that contain the line (sharers)
Line is present in other caches
Ask the other caches to invalidate the line
Other cache: transitions the line to the I state (if not already so). Returns acknowledgement + contents
Acknowledgement + contents of the line
Directory forwards the line to C1

## Slide 10: Contents
Overview of the Directory Protocol
Details
Optimizations

## Slide 11: Let us look at the protocol in some detail ...
There are three entities
  The Cache (contains some state for each line)
    It receives messages from the upper level (read or write)
    It receives messages from the NoC (read miss, write miss)
    Generates events or gets messages from the lower level  evictions
  The NoC
    Routes messages
  The directory
    Gets messages from caches, processes them
    Sends messages to caches (if required)

## Slide 12: Let us consider the cache’s point of view
readX  read miss on NoC, writeX  write miss on NoC
read  local read, write  local write
Let us consider the I (invalid, line not present) state
Standard format: event/action, (send: default sent to dir.)
I
E
I
S
No other cache contains the line
Some other cache contains the line
read/send readX
read/send readX

## Slide 13: More I state transitions
I
M
I
I
write/send writeX
readX or writeX/-

## Slide 14: S state transitions
S
read/-
readX/send value(?)
M
write/send writeX
I
writeX/send value(?)
evict/send evict
1) Support multiple readers (at a time), yet only one writer.
2)Also seamlessly evict lines.

## Slide 15: M State Transitions
M
read/-
write/-
S
readX/write-back+send data
I
writeX/send data
evict/send evict + write-back
1) Only one writer at a time
2) In the M  S transition, write back data to the lower level. This is done to enable seamless evictions in the S state.

## Slide 16: E State Transitions
E
read/-
S
readX/send data
I
writeX/send data
evict/send evict
1) We can seamlessly move to the M state. It is not necessary to send any messages.
M
write/send writeX

## Slide 17: Protocol Summary: readX and writeX
E
S
I
M
readX or writeX/-
writeX/send data(?)
readX/send data(?)
readX/write-back+send data
writeX/send data
readX/send data
writeX/send data

## Slide 18: Protocol Summary: read,write, and evict
E
S
I
M
read/send readX
read/send readX
write/send writeX
write,read/-
evict/send evict +
write-back
evict/send evict
read/-
write/send writeX
read/-
evict/send evict
write/-

## Slide 19: Design of the Directory
What are the messages that the directory receives?
  readX
  writeX
  evict
What should the directory do:
  readX  Locate a cache that contains the line(sharer) and fetch the line
  writeX  Ask all sharers to invalidate their lines, give exclusive rights to the cache that wants to write
  evict  Delete the cache from the list of sharers
Basic Design:
Line Address
List of Sharers
Directory Entry
Directory
State

## Slide 20: Actions of the Directory
Notation:
  readX.C  id of the cache
  List of sharers  S
  Directory line state  DirState
On receiving a readX
  Entry for line not present in the directory
    Create an entry, S = [readX.C], Read from the lower level
    Send an acknowledgement to the cache (state transition to the E state)
  Entry present
    DirState = Shared
      S = S U readX.C
      Send a readX message to one of the sharers to send the line’s contents to the requester
    DirState = Modified
      Send a readX message to the cache that is the exclusive owner
      S = S U readX.C
      DirState = Shared

## Slide 21: Actions of the Directory
On receiving a writeX
  Entry for line not present in the directory
    Create an entry, S = [writeX.C], Read from the lower level
    Send an acknowledgement to the cache (state transition to the M state)
  Entry present
    DirState = Shared
      Send a writeX message to all the sharers
      Ask one of the sharers to send a copy of the line to the requester
      S = [writeX.C]
      DirState = Modified
    DirState = Modified
      Send a writeX message to the cache that is the exclusive owner
      The exclusive owner needs to send the contents of the block to the requester
      S = [writeX.C]

## Slide 22: Actions of the Directory
On receiving an evict from cache, C
  S = S – C
  If (S == Empty), set the state as invalid

## Slide 23: Contents
Overview of the Directory Protocol
Details
Optimizations

## Slide 24: Enhancements to the Directory Protocol
Let us list some of the common problems associated with directories
  We need an entry for each line in a program’s working set (lot of storage)
  In each directory entry, we need an entry for each constituent cache (storage overheads)
  The directory itself can become a point of contention
  Let us look at 

## Slide 25: Distributed Directories
Address Space
Split the address space
Directory
Directory
Directory
Directory
Directory
Split the virtual address space
A directory handles all the requests for the part of the address space it owns
Resolves the issue of the single point of contention.

## Slide 26: List of Sharers
Problems with this solution:
  If there are a large number of processors and most of the entries are 0  space wasted
  Better solution:
    Maintain a bit for a set of caches. Run a snoopy protocol inside the set. OR
    Store the ids of only k sharers.
    Design the list of sharers as a linked list. Every block maintains a pointer to the next copy.
block address
1 1 0 0 0 0 0 0 1 0 0 0 1 0 1 1
How to maintain the list of sharers?
Solution 1:
  If there are N processors, have a bit vector of N processors.
  Each block is associated with a bit vector of sharers

## Slide 27: Size of the Directory
The directory should ideally be as large as the number of blocks in the programs’ working sets
Having an entry for every block in the virtual address space is impractical
Practical Solution:
  Design a directory as a cache
  Keep the state of a limited number of blocks
  If an entry is evicted from the directory, invalidate it in all the caches

## Slide 28: Question
A critical section has two functions: lock and unlock
Let us implement both of them with assembly instructions
  Assume register r2 contains the lock address
  The lock address can contain 1 (it is locked) or 0 (unlocked)
lock function
  Atomically exchange the contents of register r1 (=0), with [r2]
  If r1 = 0 after the exchange, we have the lock
  Otherwise keep repeating
Unlock function: release the lock
  Write 0 to [r2]
Implement a critical section with the help of the directory protocol.
.lock:
mov r1, 0
atomicxchg r1, [r2]
cmp r1, 0
bne .lock
.unlock:
fence
st [r2], 0
Why do you need
a fence?

## Slide 29: Atomic Exchange
atomicxchg r1, [r2]
  temp = r1, r1 = [r2], [r2] = temp
It involves 3 steps
  1 memory read + 1 memory write
  All 3 need to happen atomically
  This is called a read-modify-write instruction (RMW)
Method
  Get exclusive access (M state) with write permissions for the memory address in r2
  Perform the read-modify-write operation
  Do not respond to any other requests from the local cache, or other caches, or the directory when the operation is in progress
  Respond to the directory or other caches only when the operation is over
  The directory/requesting cache need to stall till they get valid responses from all caches that have the line in the M state