## Slide 1: Data Prefetching
Smruti R. Sarangi

## Slide 2: Data Prefetching
Instead of instructions let us now prefetch data
Important distinction
  Instructions are fetched into the in-order part of the OOO pipeline
  Data is fetched into the OOO pipeline
    As a result the IPC is slightly more resilient to data cache misses
    Nevertheless, prefetching is useful
  On the other hand
    x86 has instructions where a single instruction (with the rep prefix) can be used to load or store multiple bytes from memory
    Small i-cache footprint, yet large d-cache footprint

## Slide 3: Outline
Stride based Prefetching
Prefetching based Runahead Execution

## Slide 4: History based Prefetching
Consider the following piece of code
  For the arrays A and B, the addresses in each iteration differ by 4 bytes (assumed to be the size of an integer)
  For the array, C, consecutive accesses differ by 8 bytes
  This instruction will translate into multiple load/store RISC instruction
    There will be only on memory access per instruction
  The hardware will observe that for the same PC
    The memory address keeps getting incremented by a certain value (4 or 8 bytes in this case)
    This fixed increment is called a stride
for (i = 0; i < N; i++ ) {
...
A [i] = B[i] + C[2*i];
}

## Slide 5: Reference Prediction Table (RPT)
For each instruction
  keep trace of the address and the stride
  You can decide to prefetch N interations in advance
  State: initial  transient (not sure about the stride)  steady
Instruction Tag
Previous Address
Stride
State
PC
Memory address
Adder
Prefetched address

## Slide 6: Extensions
How many iterations to prefetch in advance?
  This depends upon the rest of the instructions in the for loop
  This ideally should be dynamically adjusted
  For a subset of prefetches
    Monitor the number of cycles between when a line is prefetched and it is actually used for the steady state
    Should not be negative
    Should be a small positive number
Extensions to the RPT scheme
  Track the next address for a linked list (If p is prefetched, prefetch *(p->next))

## Slide 7: Outline
Stride based Prefetching
Prefetching based Runahead Execution

## Slide 8: Runahead Mode
What happens when we do bad prefetching?
  We have misses. L1 misses can more or less be taken care of by an OOO pipeline
  L2 misses are bigger problems
What happens on an L2 miss
  You go to main memory (200-400) cycles
  What does the OOO pipeline do?
    The IW and ROB fill up
    It pretty much stalls
Idea: Do some work during the stalled period

## Slide 9: What can you do?
Enter runahead mode
  Return a junk value for the L2 miss
  Restart execution
  You will produce junk values (in the forward slice)
  That is still okay. Why
    You will prefetch data into the caches
Once when the L2 miss returns
  Flush the instructions in the forward slice of the L2 miss
  Re-execute them
  Very effective prefetching technique

## Slide 10: Operation
Before entering the runahead mode
  Take a checkpoint of the architectural register file
  Also, of the branch history register and return address stack
Start the runahead mode
  Add an invalid (INV) bit to each register
  The L2 miss generates an INV value
  All the instructions in its foward slice have an INV value
  The INV value is same as the poison bit (learnt earlier)
  Question:
    Do we restrict invalid values to the pipeline or let them propagate?

## Slide 11: Value Propagation
If till the pipeline  nullify all stores
If till the L1  do not evict INV data from the L1
Preferably not till the L2 (massive amount of state management)
Pipeline
L1
L2

## Slide 12: Let us take INV values till the L1
If we use the traditional L1 cache, there will be some problems
  We need to maintain both INV and non-INV data together
  What if they are on the same line (additional state required)
Solution: have an additional runahead cache that contains only INV data.
Pipeline
Runahead L1
L1

## Slide 13: Runahead L1 Cache
A store might have the INV flag set for two reasons
  Its address is INV. Ignore. Assume that the address is correct and access the runahead cache.
  A stores data is INV. Access the runahead cache
Perform the store
  Let us keep some additional state per line. Let us mark those words written by an INV store as INV.
Cache Line
INV Stores

## Slide 14: Loading a Value
First try forwarding in the LSQ
If not possible:
  Access the runahead cache and L1 cache in parallel
  The runahead cache gets preference
  Load the data. If the data is marked as INV, marked the load data as INV
  Otherwise, load data from the L1 cache
  If there is a miss, load data from the L2 (acts as prefetching)

## Slide 15: Operation (Contd...)
Keep fetching and retiring (in runahead mode) instructions
All the instructions before the speculated load (in program order) will retire
After that, all insts. are in runahead mode (will not retire)
As we fetch and execute more and more instructions, we in effect do more prefetching
What about updating branch predictors?
  Best option: Treat runahead instructions as normal instructions
Return from runahead mode
  Similar to a branch misprediction, restore the checkpoint

## Slide 16: THE END