## Slide 1: Power and Temperature
Smruti R. Sarangi
IIT Delhi

## Slide 2: Why is power consumption important?

## Slide 3: Scientific Reasons
High Power
High Temperature
Low Reliability

## Slide 4: Sources of Power Consumption

## Slide 5: Types of Power Dissipation
Dynamic power
  Power lost due to current flowing across resistors in the chip’s circuit
Leakage power
  Power that is lost in transistors when they are in the off state
Short circuit power
  Power lost when both the PMOS and NMOS transistors are on (during a logic transition)

## Slide 6
Dynamic Power

## Slide 7: Dynamic Power
Any electronic circuit can be decomposed (at any point in time), to an equivalent circuit with resistances, capacitances, current and voltage sources
Equivalent Circuit of an NMOS transistor
gate
source
body
drain
+
-
+
-

## Slide 8: Consider a simple case
While charging
  Energy dissipated in the resistance:
  Energy stored in the capacitor:
While discharging
  Energy dissipated by the resistance:
V
R
C
R
C
Charging
Discharging
Total energy dissipated in one charge-discharge cycle:

## Slide 9: Dynamic Power Analysis
What do we know up till now:
  For a simple circuit with a R and a C, the dynamic energy dissipation for a single charge-discharge cycle is: CV2
  What about for a larger circuit:
    Let us assume that in a given charge-discharge cycle: units 1 ... n are active
Energy dissipated: =
In general for a unit, if a fraction α (in terms of energy) is active at a given point of time, we can say that the energy dissipated is:
  α

## Slide 10: Energy vs Power
Power = Energy per unit time
For a given clock cycle
Let C refer to a lumped capacitance
is the activity factor (varies from 0 to 1)
V is the supply voltage
f is the frequency

## Slide 11: Are V and f related?
Let us look at some textbook results.
Alpha Power Law
For older processes (late nineties) (V >> Vth) and (α = 2)
Thus, we could say: , this will make
Olden Days
Nowadays
V is 2-3 times Vth , and α is between 1.1 and 1.3
Thus, this statement would be more correct:

## Slide 12: Voltage-Frequency Scaling
What happens if we increase the voltage
  We can also increase the frequency
  The power will also increase significantly
  We already know the relation between V and f
Quad-core AMD Opteron scaling levels:
Voltage | Frequency
1.25 V | 2.6 GHz
1.15 V | 1.9 GHz
1.05 V | 1.4 GHz
0.9 V | 0.8 GHz

## Slide 13
Leakage Power

## Slide 14: Leakage Power: Sources of Leakage Current
n
n
gate
drain
source
bulk
1. subthreshold current
2. Drain induced barrier lowering
3. Gate oxide tunneling
4. GIDL

## Slide 15: Leakage Power: Sources of Leakage Current
n
n
gate
drain
source
bulk
5. p-n junction current
6. hot carrier injection

## Slide 16: Description of the Mechanisms
Sub-threshold leakage
  When a transistor is turned off, there should be no current flowing between the source and drain
  This is the ideal case, and life is never ideal
  Little bit of leakage is there even in the off state
input
output
small amount of current flow even if the transistor is off

## Slide 17: DIBL and Gate Tunneling
DIBL (drain induced barrier lower)
  As the drain voltage increases, the threshold voltage decreases (Vth)
  Lower the Vth, more is the leakage
  The current flows between the drain-to-source terminals
Thin-oxide Gate Tuneling
  The gate oxide is very thin (<2 nm)
  Since the oxide layer is so thin, current tunnels from the gate to the body of the transistor
  NMOS leakage is much more than PMOS leakage (3-10X more)

## Slide 18: Other Mechanisms
Gate-Induced Drain Leakage (GIDL)
  Current flows from the drain terminal into the body of the transistor
  Can happen when the gate voltage is high (in NMOS)
  A high gate voltage increases the charge concentration in the areas near the gate.
P-N Junction Leakage
  Current flowing between the source-and-body and drain-and-body
Hot Carrier Injection
  Hot carriers are fast electrons that get trapped in the gate oxide
  This causes a shift in the threshold voltage, Vth
  Affects leakage current

## Slide 19: Some Equations
Most commonly used equation for leakage current (mainly sub-threshold leakage)
  vT  kT/q (k  Boltzmann’s constant, q  Coulomb’s constant, T  Temperature)
  Vth has a temperature dependence
  Typically reduces by 2.5 mV for every degree C rise in temperature
Conclusion: Leakage power is superlinearly dependent on temperature

## Slide 20
Short Circuit Power

## Slide 21: Consider a CMOS Inverter
When the input is 0: T1 is off, and T1 is on
When the input is 1: T1 is on, and T2 is off
During the transition: For a brief period, both are on
T2
T1

## Slide 22: Ballpark Figures
Dynamic Power
40-60%
Short Circuit Power
5-10 %
Leakage Power
20-40 %

## Slide 23
Temperature

## Slide 24: Power and Temperature
Methods of heat transfer
  Conduction
    Heat transferred between two objects when they are in contact
  Convection
    Heat transferred between an object and a flowing fluid
  Radiation (Not relevant)
Rate of change of temperature (u) is proportional to the second derivative of temperature over space

## Slide 25: Chip’s Package
The spreader helps to avoid temperature hot spots
The fan blows air over the heat sink
PCB
Silicon die
Heat sink
Heat spreader
Thermal interface material
Fan

## Slide 26
source: www.alamy.com

## Slide 28: Some Maths
T= AP
Let us divide the surface of the die into a M * M grid
Let N = M2
Let the vector P be a N*1 vector.
  P[i] is the power dissipated at the ith grid point
Similarly, let T be a N*1 vector for temperature
Let A be a N*N matrix that linearly relates power and temperature
As simple as that ....

## Slide 29: Leakage Temperature Feedback Loop
Needs several iterations to converge
Dynamic + Short Circuit Power
Leakage Power
Total Power
Temperature