## Slide 1: Temperature and Power Management
Smruti R. Sarangi

## Slide 2: Outline
Dynamic Power Management
  DVFS
  Clock gating
  big.LITTLE approach
  Fetch throttling
Leakage Power Management
Temperature Reduction

## Slide 3: DVFS Scaling
DVFS is one of the the most popular method of reducing power in processors.
Every processor has a DVFS table:
  Pairs of: voltage and frequency
  It is possible to choose one among several discrete DVFS settings
Internal Operation
  The processor gets cues from software (user or OS) regarding changing the DVFS settings
  The processor also might decide on its own

## Slide 4: Chip’s Power Grid and Frequency Control System
The quartz clock generates a fixed 133 MHz signal
PLL  phase locked loop
  It helps generate a clock signal that is synchronized with the quartz clock
  The frequency is a multiple of 133 MHz
For example, we can use it to generate a frequency of 133MHz * 16 = 2.13 GHz
The PLL takes 10s of micro-seconds to lock to a new frequency. During that time there is no usable clock signal.
Chip
Quartz clock
Power Supply
Voltage Regulator
PLLs
3.3V
0.8-1.2V

## Slide 5: Changing Voltage and Frequency
V0
V1
Voltage conversion
PLL lock time
PLL lock time
Voltage conversion
frequency
Voltage

## Slide 6: Hardware based DVFS
Estimate the amount of CPU activity
  If it is low  reduce the frequency
  If it is high  increase the frequency (if you need performance)
Estimating CPU activity
  Average L2 misses per instruction
  Commit(retirement) rate
We essentially need a model to correlate frequency and performance
  Option 1: Get it by profiling. Run small phases of the program, and record the IPC.
  Option 2: Method of stall rates: assumes that the stall cycles due to LLC misses is proportional to the frequency. Decrease the frequency till the LLC miss stalls are below a certain threshold.

## Slide 7: Software based DVFS
Video Codecs
Each frame needs to be processed in 33 ms
If we can do it in 20 ms
Reduce the frequency till we process it in 33 ms
Need a model to relate processing time and frequency
Regular programs
Classify them: hard real time, soft real time, interactive, periodic, batch
Real time tasks  set DVFS settings based on performance and deadlines
Interactive  Take the user’s perception into account
Periodic jobs  Take the periodicity into account
Batch  Take the user’s requirements into account

## Slide 8: Linux Speed Governors
Use the cpufreq utility
  Performance  maximum possible frequency
  Powersave  always run at minimum frequency
  Ondemand  Tries to maintain a constant rate of CPU utilization. Uses a set of thresholds for each DVFS setting.
  Conservative  Much more conservative than ondemand
  Interactive  Similar to Ondemand, but does not use thresholds. Uses a formula that relates CPU utilization to frequency.

## Slide 9: Clock Gating
Recall
  Dynamic power is only consumed during a transition.
32
31
30
3
2
1
29
4
G,P
32-31
G,P
30-29
G,P
2-1
G,P
4-3
G,P
32-29
G,P
4-1
G,P
32-25
G,P
24-17
G,P
16-9
G,P
8-1
G,P
32-17
G,P
16-1
G,P
32-1
Block 1
Block 16
Carry lookahead adder
Assume bit #4 changes
Only the small part of the circuit shown in red is affected
The rest of the elements do not dissipate any dnamic power

## Slide 10: Typical Structure of a Circuit
What if the clock signal is 0?
  The output of the registers do not change
  There are no state transitions in the logic
  No current flow and thus no dynamic power dissipation
Pipeline Register
Pipeline Register
Logic
clock

## Slide 11: Circuit with clock gating
If S = 0, the inputs to the logic circuit don’t change. The circuit is clock gated.
If S = 1, normal operation
Pipeline Register
Pipeline Register
Logic
clock
S

## Slide 12: Clock Gating
Present in almost all architectures
Guess/predict/deduce if a unit is off
  For example, an add instruction will not use the divider
  Clock-gate the divider
  Note that the divider will still have leakage
In processors such as Pentium 4
  They try to ensure that there is absolutely no deviation in timing by enabling clock gating
  Some times, we can aggressively clock gate. Instructions will have to wait till the unit is enabled.

## Slide 13: Other Architectural Techniques
ARM big.LITTLE Architecture, or Samsung’s dual quad processor
Have N big cores, and M small cores
  Depending on the nature of the task and its priority, choose:
  a big core  if it is important
  a little core  if it is not important, and power needs to be saved.
Fetch throttling
  Dynamically adjust the fetch/issue/commit rate  Based on power constraints
  Idea 1: After fetching low-confidence branches, reduce the fetch rate (decreases the number of potential wrong-path instructions)
  Idea 2: Reduce the fetch rate in the shadow of an L2 miss

## Slide 14: Outline
Dynamic Power Management
  DVFS
  Clock gating
  big.LITTLE approach
  Fetch throttling
Leakage Power Management
Temperature Reduction

## Slide 15: Power Gating
Brute force method: Just turn off the power
  Easier said than done
Functional Unit
Power Grid
Need to have power switches at each connection to the power grid
Power controllers

## Slide 16: Multiple Transistor Sizes
Transistors with shorter channels and transistors with longer channels
  Normal transistors: power  1 unit, time  1 unit
  Longer channel transistors: power  0.3 units, time  1.1 units
  Use normal transistors on the critical path, and slower transistors off the critical path
Gate sizing
  Delay , Power
  Slower transistors: smaller W/L ratio
  Same idea: Slower transistors off the critical path, Faster transistors on the critical path.

## Slide 17: Adaptive Body Biasing
Vth = Vth1 – K1 ⋅ Vdd – K2 ⋅ Vbs
Forward body biasing  Increase Vbs
  Reduce Vth
  Increase power, increase performance
Reverse body biasing  Decrease Vbs (even –ve)
  Increase Vth
  Decrease power, decrease performance
Same idea: forward body biasing in the critical path, reverse body biasing off the critical path

## Slide 18: Drowsy Caches
row of SRAM cells
Vdd = 1V
Allows read/writes
row of SRAM cells
Vdd = 0.3 V
Maintain the value, accesses not allowed
drowsy mode
Drowsy mode  Runs at 0.3 V. Maintains the value. Access it not allowed
Takes 1-2 cycles to enter/exit drowsy mode
Treat a set of lines as 1 unit
Turn it on/off as 1 unit
Once a set is turned on  Keep it on 1000-2000 cycles
  Take temporal and spatial locality into account

## Slide 19: Outline
Dynamic Power Management
  DVFS
  Clock gating
  big.LITTLE approach
  Fetch throttling
Leakage Power Management
Temperature Reduction

## Slide 20: Dynamic Thermal Management
Place thermal sensors all over the chip
Once a temperature hot-spot forms
  Traditional mechanisms: DVFS, power reduction, fetch throttling
Many new techniques for CMP (multicore) processors
Stop-n-go
  Temporarily stop a core (let it cool down)
Heat and run thread assignment
  Don’t allow hot cores to be close to each other
  If a thread’s activity increases, migrate it to a colder region of the chip