## Slide 1: OOO Pipelines
Smruti R. Sarangi

## Slide 2: Contents
In-order Pipelines
Out-of-order Pipelines: Motivation
Out-of-order Pipelines: Basics
Branch Prediction

## Slide 3: Pipelines
What do we know up till now:
In-order Pipelines
Instructions enter the pipeline in program order
Inst. Fetch
Operand Fetch
Execute
Memory
Access
Register
Writeback
5-Stage Pipeline

## Slide 4: Problems with Inorder Pipelines
Hazards
  Structural Hazards  Two instructions vie for the same resource (NOT possible in simple 5 stage pipelines)
  Data Hazards  Producer instruction is not ready when the consumer needs the data
  Control Hazards  Instructions are fetched from the wrong path of the branch
Inst.
Fetch
Operand Fetch
Execute
Memory
Access
Register
Writeback

## Slide 5: Data Hazards in In-order Pipelines
Instruction
Fetch
Operand Fetch
Execute
Memory
Access
Register
Writeback
ld r4, 4[r0]
add r5, r4, 1
Cycle N
Cycle N+1
Need data now
Earliest it can be generated
clock
Hazard

## Slide 6: Solution: Stall the Pipeline
Instruction
Fetch
Operand Fetch
Execute
Memory
Access
Register
Writeback
ld r4, 4[r0]
add r5, r4, 1
Cycle N
Cycle N+1
Need data now
Here is the data
clock
ld r4, 4[r0]
Cycle N+2

## Slide 7: Control Hazards
Inst.
Fetch
Operand Fetch
Execute
Memory
Access
Register
Writeback
beq .label
add r1, r2, r3
beq .label
sub r5, r6, r7
We know the status of the branch now
Cancel these instructions
Two instruction slots are wasted

## Slide 8: Contents
In-order Pipelines
Out-of-order Pipelines: Motivation
Out-of-order Pipelines: Basics
Branch Prediction

## Slide 9: Performance Equation
Is Computer A faster that computer B
  Wrong Answers:
  More is the clock speed, faster is the computer
  More is the RAM, faster is the computer
What does it mean for computer A to be faster than computer B
Short Answer: NOTHING
Performance is always with respect to a program. You can say that a certain program runs faster on computer A as compared to computer B.

## Slide 10: Performance Equation - II
Let us loosely refer to the reciprocal of the time per program as the performance
= * *
=
= (assume just 1 program)

## Slide 11: So, what does performance depend on …
#instructions in the program
  Depends on the compiler
Frequency
  Depends on the technology and the architecture
IPC
  Depends on the architecture, and the compiler

## Slide 12: How to improve performance?
There are 3 factors:
  IPC, instructions, and frequency
#instructions is dependent on the compiler  not on the architecture
Let us look at IPC and frequency
IPC
  What is the IPC of an in-order pipeline?
1 if there are no stalls, otherwise < 1

## Slide 13: What about frequency?
What is frequency dependent on …
Frequency = 1 / clock period
Clock Period:
  1 pipeline stage is expected to take 1 clock cycle
  Clock period = maximum latency of the pipeline stages
How to reduce the clock period
  Make each stage of the pipeline smaller by increasing the number of pipeline stages
  Use faster transistors

## Slide 14: Limits to Increasing Frequency
Assume that we have the fastest possible transistors
Can we increase the frequency to 100 GHz
Reasons

## Slide 15: Limits to increasing frequency - II
What does it mean to have a very high frequency?
Before answering keep these facts in mind:
Thumb Rule
P  power
f  frequency
T
Thermo-dynamics
P  power
T  Temperature
We need to increase the number of pipeline stages  more hazards, more forwarding paths
1
2
3

## Slide 16: How many pipeline stages can we have?
We are limited by the latch delay
Even with an infinite number of stages, the minimum clock period will be equal to the latch delay
Logic
Latch
Latch
Logic
Latch
Few stages
More stages
Even more stages

## Slide 17: Pipeline Stages vs IPC
CPI = 1/ IPC
CPI = CPIideal + stall_rate * stall_penalty
The stall rate will remain more or less constant per instruction with the number of pipeline stages
The stall penalty (in terms of cycles) will however increase
This will lead to a loss in IPC

## Slide 18: Summary: Why we cannot increase frequency?
Power
Temperature
Effect of the Latch Delay
Stall penalties will increase

## Slide 19: Since we cannot increase frequency …
Increase IPC

## Slide 20: Increase IPC
Issue more instructions per cycle
2, 4, or 8 instructions
Make it a superscalar processor  A processor that can execute multiple instructions per cycle

## Slide 21: In-order Superscalar Processor
Have multiple pipelines.
Inst. Fetch
Operand Fetch
Execute
Memory
Access
Register
Writeback
Inst. Fetch
Operand Fetch
Execute
Memory
Access
Register
Writeback
Inst. Fetch
Operand Fetch
Execute
Memory
Access
Register
Writeback
Instruction i
Instruction i+1
Instruction i+2

## Slide 22: In-order Superscalar Processor - II
There can be dependences between instructions
Have O(n2) forwarding paths for a n-issue processor
Complicated logic for detecting dependences, hazards, and forwarding
Still might not be enough ...
To get the peak IPC (= n) in an n-issue pipeline, we need to ensure that there are no stalls
There will be no stalls if there are no taken branches, and no data dependences between instructions.
Programs typically do not have such long sequences of instructions without dependences

## Slide 23: What to do ...
Don’t follow program order
Consider
Too many dependences
mov r1, 1
add r3, r1, r2
add r4, r3, r2
mov r5, 1
add r6, r5, 1
add r8, r7, r6

## Slide 24: Execute out of order
mov r1, 1
add r3, r1, r2
add r4, r3, r2
mov r5, 1
add r6, r5, 1
add r8, r7, r6
Execute on a 2-issue OOO processor

## Slide 25: Execution on a 2-issue OOO Processor
mov r1, 1
add r3, r1, r2
add r4, r3, r2
mov r5, 1
add r6, r5, 1
add r8, r7, r6
cycle 1
cycle 2
cycle 3
issue slot 1
issue slot 2

## Slide 26: Basic OOO idea
Create a pool of instructions
Find instructions that are mutually independent and have all their operands ready
Execute them out of order

## Slide 27: Contents
In-order Pipelines
Out-of-order Pipelines: Motivation
Out-of-order Pipelines: Basics
Branch Prediction

## Slide 28: Revisit the Example
mov r1, 1
add r3, r1, r2
add r4, r3, r2
mov r5, 1
add r6, r5, 1
add r8, r7, r6
Pool of Instructions
Issue ready and mutually independent instructions

## Slide 29: Pool of Instructions
Needs to be large enough such that the requisite number of mutually independent instructions can be found
Typical instruction pool sizes: 64 to 128
How do we create a large pool of instructions in a program with branches? We need to be sure that the instructions are on the correct path
for (i = 1; i < m; i++) {
for (j = 1; j < i; j ++ ) {
if (j %2 == 0) continue;
....
}
}

## Slide 30: Problems with creating an Instruction Pool
Typically 1 in 5 instructions is a branch
Predict the direction of the branches, and their targets

## Slide 31: Dependences between Instructions
Program Order Dependence
mov r1, 1
mov r2, 2
One instruction appears after the other in program order
The program order is the order of instructions that is perceived by a single cycle in-order processor executing the program.

## Slide 32: Data Dependences
RAW  Read after Write Dependence (True dependence)
mov r1, 1
add r3, r1, r2
It is a producer-consumer dependence.
The earlier instruction produces a value, and the later instruction reads it.

## Slide 33: Data Dependences - II
WAW  Write after Write Dependence (Output dependence)
mov r1, 1
add r1, r4, r2
Two instructions write to the same location
The later instruction needs to take effect after the former

## Slide 34: Data Dependences - III
WAR  Write after Read Dependence (Anti dependence)
add r1, r2, r3
add r2, r5, r6
Earlier instruction reads, later instruction writes
The later instruction needs to execute after the earlier instruction has read its values

## Slide 35: Control Dependences
The add instruction is control dependent on the branch(beq) instruction
If the branch is taken then only the add instruction will execute, not otherwise
beq .label
.....
.label
add r1, r2, r3

## Slide 36: Basic Results
In-order processors respect the program order dependences. Thus, they automatically respect all data and control dependences.
OOO processors respect only data and control dependences.

## Slide 37: Can output and anti dependences be removed?
Don’t you think that these dependences are there because we have a finite number of registers.
What if we had an infinite number of registers?
mov r1, 1
add r1, r4, r2
add r1, r2, r3
add r2, r5, r6

## Slide 38: Solution: Infinite number of registers
mov r1, 1
add r1, r2, r3
add r4, r1, 1
mov r2, 5
add r6, r2, r8
mov r1, 8
add r9, r1, r2
mov v1, 1
add v11, v2, v3
add v4, v11, 1
mov v12, 5
add v6, v12, v8
mov v21, 8
add v9, v21, v12
Code with architectural registers
Code with virtual registers

## Slide 39: Renaming
Program with real (architectural) registers
Program with virtual registers
RAW dependences
WAR dependences
WAW dependences
RAW dependences
Higher instruction level parallelism (ILP)

## Slide 40: Where are we now ...
Fetch + Decode + Rename + Reg. Read
Memory
Pool of Instructions
Execution Units
Issue
Write back results

## Slide 41: Issue with writeback
To an outsider should it matter if the processor is in-order or OOO
Answer is NO
Processor
Instructions
Register File
Memory
Update State

## Slide 42: Assume that there is an exception or interrupt
Languages like Java have dedicated functions that are called if there is a divide-by-zero in the code.
The question is:
  Would the sub instruction have executed when we enter the exception handler
mov r4, 10
mov r2, 0
div r3, r1, r2
sub r4, r4, 1
Divide by 0
Divide by zero handler

## Slide 43: Precise Exceptions
Assume that the exception handler decides to do nothing and return back
After this the sub instruction should be executed
This is exactly what will happen in an in-order processor
In an OOO processor there is a possibility that the sub inst. can execute out of order
Regular Instructions
÷ by 0
Exception
handler
sub
inst.

## Slide 44: Precise Exceptions - II
To an external observer
  The execution should always be correct
  Even in the presence of interrupts and exceptions
Regular Instructions
÷ by 0
Exception
handler
sub
inst.
Regular Instructions
÷ by 0
Exception
handler
sub
inst.
Correct
Wrong

## Slide 45: Precise Exceptions - III
We thus need precise exceptions
Assume that the dynamic instructions in a program (ordered in program order) are: ins1, ins2, ins3 ... insn
Assume that the processor starts the exception/interrupt handler after it has just finished writing the results of instruction: insk
Then instructions: ins1 ... insk should have executed completely and written their results to the memory/register file
AND, insk+1 onwards should appear to not have started their execution at all
Such an exception or interrupt is precise

## Slide 46: Precise Exceptions in OOO Processor
Now, in an OOO processor how can exceptions be precise?
We need a mechanism to ensure that instructions appear to execute in order to not an external observer
Anything can happen inside the processor
  But an external observer should not be able to make out if the processor is in-order or OOO

## Slide 47: Contents
In-order Pipelines
Out-of-order Pipelines: Motivation
Out-of-order Pipelines: Basics
Branch Prediction

## Slide 48: Timing
Fetch ith instruction
Fetch (i+1)th instruction
Fetch (i+2)th instruction
Predict (i+1)th instruction
Predict (i+2)th instruction
Predict (i+3)th instruction
There is no time to look at an instruction

## Slide 49: Branch Prediction
There are several things to predict:
  Predict if an instruction is a branch or not
  If it is a branch, predict its outcome
  If the branch is taken, predict its target
General structure of a predictor
Predictor
Program Counter (PC)
Prediction

## Slide 50: Is an instruction a branch or not?
Insights
  Given a PC, the status of the instruction (branch or not) does not change
  Can we use this information?
Approach
  The last time that we had seen a branch remember its PC
  Next time we see a PC, check if we have seen it before
  Also remember the type of the branch:
    Unconditional
    Conditional
    Function call
    Return

## Slide 51: Make a structure in hardware to remember ...
PC
32 - n
n
Type of the instruction
2n entries
Instruction Status Table (IST)

## Slide 52: Basic Method of Operation
When we see a branch instruction
  Access its corresponding entry in the table
  Record the branch type
When we see an instruction:
  Check the corresponding entry of the table
  Read the status of the instruction

## Slide 53: Instruction Status Table (IST)
If we choose the least significant 10 bits of the PC address, we will have 1024 entries in the IST
For a 32 bit PC, we cannot have a 232 entry table.
  Too big
  Too slow
  Too much of power
  Too much of area
We need to manage with a smaller table

## Slide 54: Destructive Interference
Two instructions can map to the same entry
Instruction A
Instruction B
Defined as destructive inteference

## Slide 55: Branch Aliasing
Possible for a branch and a non-branch instruction to map to the same entry
Possible for two branches to map to the same entry
Possible for two non-branches to map to the same entry
Need for disambiguation
  Augment each entry of the IST

## Slide 56: Disambiguation Between Addresses
PC
32 - n
n
Type of the instruction
2n entries
Branch type
32 – n

## Slide 57: Disambiguation
We can keep the status of only branches in the IST
However, for every instruction we need to check the IST
If there is no entry, then we need to predict that it is not a branch
  Can be wrong
  What to do 
Why does an IST work?
  Mainly because most pieces of code exhibit temporal locality
  In a given window of time instructions tend to repeat themselves

## Slide 58: Predict the Direction of the Branch
If a branch is unconditional  no need to predict (taken)
If a branch is a call/return  no need to predict (taken)
If a branch is conditional  need to predict
Predictor
Program Counter (PC)
Taken or Not Taken

## Slide 59: Example Code
void foo() {
for (i=0; i < 5; i++) {
...
}
}
C
Assembly
.foo:
mov r0, 0
.loop: cmp r0, 5
beq .exit
add r0, r0, 1
b .loop
Predict

## Slide 60: Simple Bimodal Predictor
PC
32 - n
n
Outcome of the branch
2n entries
Predictor Table

## Slide 61: Bimodal Predictor - II
Each entry saves the last recorded outcome of the branch
  taken or not-taken
What is the problem:
  The beq instruction is evaluated 6 times
  Assume the default is not-taken
  First 5 times  correctly predicted not-taken
  6th and last time  incorrectly predicted to be taken
Now assume we call the function foo() once again
  The first time  we will predict taken. This is wrong
  Again the last time will be wrong
  Correct prediction rate: 2/6

## Slide 62: Increasing Accuracy
What is the problem?
  The beq instruction is fundamentally biased towards: not-taken
  One exception at the end of the for loop cannot change its inherent behavior
Let us add some hysteresis
  Instead of having a single bit in each entry, have a 2 bit counter
Saturating Counter
00
01
10
11
Increment
Decrement

## Slide 63: Saturating Counters
Algorithm for updates:
  If a branch is taken, increment the saturating counter
  If it is not taken, decrement the counter
For prediction:
  00 and 01  not taken
  10 and 11  taken
00
01
10
11
Predict: Not Taken
Predict: Taken

## Slide 64: Bimodal Predictor with Saturating Counters
PC
32 - n
n
Outcome of the branch
2n entries
Predictor Table
2-bit saturating counter
Logic

## Slide 65: Will it help?
1st Time: Predict not-taken. Correct. Starts with 01. Moves to 00
2nd Time: Predict not-taken. Correct. Remains at 00
...
6th Time: Predict not-taken. Wrong. Starts with 00. Moves to 01
.foo:
mov r0, 0
.loop: cmp r0, 5
beq .exit
add r0, r0, 1
b .loop
Misprediction rate: Down from 2/6 to 1/6

## Slide 66: Can we do better?
void foo() {
for (i=0; i < 5; i++) {
...
if (i == 4) {
foobar();
}
}
}
C
Assembly
What if we had?
.foo:
mov r0, 0
.loop: cmp r0, 5
beq .exit
add r0, r0, 1
cmp r0, 4
bne .loop
call .foobar
b .loop

## Slide 67: Global History Register (GHR)
Let us have a shift register that records the history of the last n branches
We record: 1  taken branch, 0  not taken branch
Let us consider a 2-bit GHR
We have two conditional branches in the running example
  beq .exit
  bne .loop

## Slide 68: Status of the GHR
Beginning of 2nd Iteration
  01
Beginning of 4th Iteration
  01
Beginning of 5th iteration
  01
Beginning of 6th iteration
  00
.foo:
mov r0, 0
.loop: cmp r0, 5
beq .exit
add r0, r0, 1
cmp r0, 4
bne .loop
call .foobar
b .loop

## Slide 69: Gap Predictor
PC
32 - n
n
Outcome of the branch
2n+k entries
k-bit GHR
Logic
n
k
PHT: Pattern History Table

## Slide 70: Gap Predictor
We create 2k times more entries in the predictor table
Captures the global branch history
In this case, we can remove the misprediction after the 5th iteration (6th time the instruction beq .exit is evaluated)
The accuracy is expected to increase.
In general we can create different combinations of:
  The PC bits and the GHR’s branch history

## Slide 71: Another way of combining information: GShare
PC
32 - n
n
Outcome of the branch
2max(n,k) entries
k-bit GHR
Logic
XOR

## Slide 72: Can we design a class of predictors?
G  Global, P  Pattern
All four combinations are possible
  Gag
  Gap
  Pag
  Pap

## Slide 73: Gag Predictor
Outcome of the branch
2k entries
k-bit GHR
Logic
k

## Slide 74: Pag predictor
PC
Outcome of the branch
2k entries
k-bit GHR
Logic
n1
k-bit GHR
k

## Slide 75: Pap predictor
PC
32 - n
n
Outcome of the branch
2n+k entries
k-bit GHR
Logic
n1
k-bit GHR
n
k

## Slide 76: Tournament Predictor
Different predictors have different accuracies for different programs
How to know which predictor is best for which program?
What to do?
  Answer: Use two predictors, and choose between them
Predictor 1
Predictor 2
Choose

## Slide 77
PC
n bits
Choose
Predictor 1
Predictor 2
Prediction

## Slide 78: Operation of a Tournament Predictor
Prediction
  Find the entry in the chooser table
  Choose the predictor
  Use its prediction
Training
  Train both the predictors
  Train the entry in the chooser array if we chose the wrong predictor
Modification: We can either use 1 bit in each entry of the chooser table or use a 2-bit saturating counter

## Slide 79: Other methods of prediction
Reduce aliasing
  Incorporate a few tag bits in each entry of the predictor
  Have multiple predictors for different subsets of branches
  Include a bias bit with every branch (its most likely direction), and just predict if we need to agree with the bias bit or not (agree predictor)
  Ensure that all entries of the PHT are uniformly used
Better use of bits
  Separate high confidence and low confidence branches. Dedicate more bits to low confidence branches
Examples of other predictors:
  Bi-mode, Agree, Skew, YAGS, TAGE

## Slide 80: Prediction and Compression
Consider a sequence of <PC,outcome> pairs
Let’s say compress this sequence using a standard program: zip, rar
Is the prediction accuracy related to the compression ratio (size of compressed file/ size of original file)
  YES
Take a course on information theory
  Read about the Fano’s inequality
  See this link

## Slide 81: Predict the Branch Target
Predictor
PC of the taken branch
Target

## Slide 82: Use the IST. Let us call it the Branch Target Buffer (BTB)
PC
32 - n
n
Type of the instruction
and target
2n entries
Branch type
32 – n
target

## Slide 83: Calls and Returns
foo
foobar
foobarbar
call
call
ret
ret
0xFC0
0xFF4
foobarbarbar
ret
call
0xBF8
How to predict return addresses?
Solution: Use a stack

## Slide 84: Return address stack (RAS)
foo
foobar
foobarbar
call
call
ret
ret
0xFC0
0xFF4
foobarbarbar
ret
call
0xBF8
0xFC0
0xFF4
0xBF8
Stack

## Slide 85: Summary: The Branch Prediction System
PC
BTB
Type & Target
Branch
Predictor
PC
RAS
Choose
the next PC
next PC