## Slide 1: Advanced Caches
Smruti R. Sarangi

## Slide 2: Time to go deeper into the memory system
Processor
L1
L2
Main Memory
Let us mainly focus on the L2 cache

## Slide 3: Outline
Modeling and simulating caches
Structure of a large L2 Cache
Non-uniform Caches
  S-NUCA
  D-NUCA
  R-NUCA

## Slide 4: Modeling and Simulating Caches
Should I use a 4KB, 2-way assoc cache or 8KB, 1-way assoc cache?
  First, we need to find the access times of both caches
  Convert access time into clock cycles
  Simulate both the configurations: find the faster one
To find the time it takes to access a cache
  We need to use a simulation tool
  Most popular simulation tool  Cacti (designed by HP labs)
Along with that
  We need power and area data as well
  Cacti 6.0 provides all of these
  It has a web interface also: http://quid.hpl.hp.com:9081/cacti/

## Slide 5: Structure of a Cache
Decoder
Address
Tag Array
Data Array
wordlines
column muxes
SRAM cell
sense amps
Comparators
valid output
mux drivers
Output driver
data output
output drivers

## Slide 6: Usage
cacti C B A
  C  cache size in bytes
  B  block size in bytes
  A  associativity
  Number of sub-banks (a bank is a sub-cache) (more later ..., assume 1 for now)
Hidden inputs
  bo  output width (differs for 32/64 bit machines)
  bwidth  input address width (differs for 32/64 bit machines)
Cacti
inputs
area,time,power

## Slide 7: Sample input and output

## Slide 8: How does Cacti work?
Given the inputs it tries to create the most optimal (often fastest) cache
What can happen?
Caches can get very asymmetric. rows >> columns, or columns >> rows (>>  significantly more than)
slow design
fast design

## Slide 9: How to make it fast?
Create sub-arrays of SRAM cells
  Ndwl  Number of vertical cut lines
  Ndbl  Number of horizontal cut lines
  Total number of subarrays created  Ndwl * Ndbl
  Also to improve the aspect ratio, map more sets per wordline
    It will increase the number of column multiplexers  slowdown
    Will decrease the number of rows, and thus the size of the address decoder  speedup
    Number of sets mapped to a wordline  Nspd
The optimal values of Ndwl , Ndbl, and Nspd are found out by Cacti

## Slide 10: Banks and Sub-arrays
A large cache can be split into multiple banks
  A bank is a cache in its own right. It has its own tag and data array.
  Different banks can be accessed simultaneously
  Given an address, we first need to map it to a bank, and then access that specific bank
  Advantage of banking  faster banks and more parallel access
  Disadvantage of banking  Higher area, and additional delay in deciding the bank
Each bank can then be split into sub-arrays
  Subarrays do not allow parallel(concurrent) access
Multilevel hierarchical organizations are also possible (Cacti 5.0 +)
  Bank  sub-banks Mats  4 sub-arrays
  Wire routing delay and SRAM array access delay determine the degree of hierarchy

## Slide 11: Multi-Ported Structures
Approach 1: Change the SRAM Cell  Area intensive & slow
Approach 2: Use banking
Better  faster, and does not need more area.

## Slide 12: Examples: (2-way assoc, 64B line size, 1 array, 32 nm) Access Time vs Cache Size
Chart: 
| 4096 | 8192 | 16384 | 32768 | 65536 | 131072
Access Time | 0.42 | 0.43 | 0.44 | 0.46 | 0.5 | 0.55

## Slide 13: Area vs Cache Size
Chart: 
| 4096 | 8192 | 16384 | 32768 | 65536 | 131072
Area | 0.14 | 0.17 | 0.187 | 0.22 | 0.28 | 0.56

## Slide 14: Cache Size vs Power
Chart: 
| 4096 | 8192 | 16384 | 32768 | 65536 | 131072
Power | 0.149 | 0.15 | 0.155 | 0.17 | 0.19 | 0.25

## Slide 15: Outline
Modeling and simulating caches
Structure of a large L2 cache
Non-uniform Caches
  S-NUCA
  D-NUCA
  R-NUCA

## Slide 16: Structure of a Modern Processor
Typical L2 caches in a chip are fairly large: order of MBs
  It is thus necessary to divide them into many banks
  We thus have an array of banks
  A lot of modern chips have many cores (OOO pipelines) also (more later)
  There are many ways to organize cores and cache banks
Checkerboard Layout
Rim Layout
Core
Cache bank

## Slide 17: How do you pass messages in such a system?
Need an on-chip network
  Also called Network-on-chip (NoC)
First create groups of co-located cores and cache banks
  Called a tile
  Associate a network element (router) with each tile. Elements in each tile are connected to each other using regular electrical links. All of them are also connected to the router (one per each tile).
Router
Communication Element

## Slide 18: Passing Messages - II
Connect all the routers with an on-chip network
Routers are connected by electrical links (or hops)
Sending a message
Source
Destination

## Slide 19: A Network Router
Router
Router
Router
Router
Router
Local Tile

## Slide 20: Network Delays
Two routers are connected with a set of wires
  We cannot have many wires in parallel
  We typically cannot have more than 64-128 wires in parallel
  Means, we cannot send more than 64-128 bits at a time
  64-128 bits  8-16 bytes
  Each such packet is also called a flit in an NoC
If we are reading a 64 byte cache line
  We need to break it into 4-8 flits
  Send one flit after the other
  A lot of networks typically a head flit and a tail flit also
Head flit
Body flit
Body flit
Tail flit

## Slide 21: Network Delays
Flits typically 1 cycle to traverse a hop
  Sending delay by the transmitter
  Signal propagation time
  Receiving delay
What does the router do?
  If the flit belongs to the local time  send it to the local tile
  Figure out the next router to send the packet to
  Take congestion and deadlocks into account
  Router has a delay of 2-3 cycles
Total delay: at least 3-4 cycles

## Slide 22: Network Delays
How long will it take to go from one end to the other in this network?
6 hops, assume 4 cycles per hop  24 cycles

## Slide 23: Non Uniform Caches
L2/L3 caches are large.
  If you find data in a nearby bank  a couple of cycles
  If it is a remote bank  20-50 cycles (depending on the size of the network and the degree of congestion)
Cache access times can be very variable depending on where the data is
  This is called a non-uniform cache (NUCA cache)
  Can we take advantage of this non-uniformity?
  ANSWER: Place frequently used data closer

## Slide 24: Outline
Modeling and simulating caches
Structure of a large L2 cache
Non-uniform Caches
  S-NUCA
  D-NUCA
  R-NUCA

## Slide 25: S-NUCA (static NUCA)
Simplest scheme:
  Map cache lines to cache banks
  Give a cache line  we know which cache bank it maps to
How to do the mapping
  Solution 1:
  Solution 2:
  Tradeoffs: Bank locality vs homogenizing bank accesses
Byte within a block
Set id
Bank id
Tag
Byte within a block
Bank id
Set id
Tag

## Slide 26: D-NUCA (Dynamic NUCA)
Let us now look at a method of bringing frequently used data closer
Bank set  sets of banks
Bank set 1
Bank set 8

## Slide 27: Operation of the Protocol
Given an address  Map it to a bank set
Search the bank set
  If you find the line, declare a cache hit
  Otherwise declare a miss and fetch it from the lower level
Three search strategies
  Sequential
  Two-way
  Broadcast
Byte within a block
Set id
Bank set id
Tag

## Slide 28: Search Strategies: Start from the home bank (closest to the core in the bank set)
Sequential Search
Two-way Search
Broadcast Search
start from home bank

## Slide 29: After a Hit/Miss Decision
Hit decision
  Send the block to the requesting core
  Promote the block  Move it closer to the home bank (Migration)
  Bring it to a nearer bank (closer to the home bank)
  If there is an empty block in the set in the new bank  no problem
  Otherwise swap the blocks
  Bringing blocks closer to the home bank (consistent with temporal locality)
Miss decision
  Fetch the block from the lower level
  Either insert it into the nearest bank or the farthest bank (depends on the strategy)

## Slide 30: Eviction and Migration
Assume that a block needs to be evicted
  Solution 1: Move it to the lower level
  Solution 2: Move it away from the home bank. Need to tag each line with the id of the requesting core
Advantages
  Keeps data close to requesting cores
  Brings data closer depending upon usage
  Gives a block multiple chances  Upon an eviction move it to block slightly further away
Search policy, location, migration and eviction are important design decisions

## Slide 31: R-NUCA
Break down accesses into three types
  Instructions (read only)
  Data-private
  Data-shared
Since instructions are read-only, thus they can be replicated
Data cannot be replicated (very complex)
Use OS mechanisms to map pages as: instruction, data-private, and data-shared
  Save this information in the TLBs

## Slide 32: Instructions
Create small clusters of 4 tiles
  Can be overlapping or non-overlapping
If they are overlapping
  A tile can be a part of multiple clusters
Search protocol
  Consider the 2 bits in the block address above the set index bits
  2 bits  4 combinations
  For each combination store the id of the tile that we need to search
  Note that a tile can be a part of multiple clusters
  Ensure that for all the tiles in the cluster that we search  all the blocks with the same value of the 2 bits map to the same cluster
If there is a miss in the cluster search in a designated remote bank (SNUCA)
Overlapping clusters

## Slide 33: Mapping Clusters in R-NUCA – Rotational Interleaving
RIDs are contiguous along each row
Differ by n/2 (for n = 4) across a column
Let A = (a1, a2) be 2 bits in the block address to the left (more significant) of the set index
Compute ( RID - A )
Result: 0 (current), -1 (right), 1 (left), 2 or -2 (down)
Access the bank. This is where the instruction line should be kept.
11
00
01
10
01
10
11
00
11
00
01
10
01
10
11
00
Randomly assign a RID of 00 to a tile
Cluster

## Slide 34: Data
Private data  Store it only within the bank in the tile
Shared data  Use SNUCA
Advantages:
  Limited replication ensures good instruction hit rates
  Does not add the complexity of maintaining replicas for read-write data

## Slide 35: THE END