## Slide 1: OOO Pipelines - II
Smruti R. Sarangi
IIT Delhi

## Slide 2: Contents
Renaming
Instruction Window
Wakeup and Bypass
Load Store Queue
Reorder Buffer and Precise Exceptions

## Slide 3: Renaming (architectural registers  virtual registers)
Consider a 4-issue processor
  4 instructions are being renamed each cycle
  4 instructions have 8 read operands, and 4 write operands
Each read operand, needs to read its value from a virtual register
Each write operand needs to be assigned a new virtual register
Dependences between the instructions need to be taken care of
There are two main approaches
  Renaming with a physical register file
  Renaming with reservation stations

## Slide 4: Renaming with a physical register file
Every ISA has a set of registers that are visible to software
  These are called architectural registers
  x86 has 8
  x86-16 has 16
  ARM has 16
  MIPS has 32
To ensure precise exceptions, the architecture registers should appear to be updated in-order
However, inside the processor we need to do renaming to eliminate output and anti dependences

## Slide 5: Physical Register File
Physical register file
R1
R2
R16
Architectural register file

## Slide 6: Physical Register File
If we have 16 architectural registers, we can have 128 physical registers
In this case, architectural registers exist in principle. There is no separate architectural register file.
Each architectural register is mapped to one and only one physical register at any point in time.
112 physical registers are unmapped. They either are empty or contain a value that will be overwritten by a later instruction

## Slide 7: Example
r series  architecture, p series  physical
At the beginning ri is mapped to pi
With time the mapping changes
p12 contains the value of r1 till the value is overwritten. p13 contains the new value. At this p12 contains an interim value
mov r1, 1
add r1, r2, r3
add r4, r1, 1
mov r2, 5
add r6, r2, r8
mov r1, 8
add r9, r1, r2
mov p11, 1
add p12, p2, p3
add p41, p12, 1
mov p21, 5
add p61, p21, p8
mov p13, 8
add p91, p13, p21

## Slide 8: Example - II
We need 16 physical registers to contain the latest values of architectural registers
112 physical registers can possibly contain interim values that might be required by instructions in the OOO pipeline (also called in-flight instructions)
More are the number of physical registers  more are the number of instructions that can simultaneously be in flight  more is the ILP
Renaming: convert architectural register id  physical register id

## Slide 9: Rename Stage
Three Structures
  Register Address Table (RAT)  Translate architectural register id to physical register id
  Dependency Check Logic (DCL)  Take care of dependences between instructions issued in the same cycle
  Free List or Free Queue  Maintain a list of unmapped physical registers

## Slide 10: Register Alias Table
RAT table
Architectural register ids
Physical register ids

## Slide 11: Free List
It is queue of unmapped physical register file ids
An entry is removed from it when we need to assign it to an architectural register id
When is an entry added to it? LATER
Update the RAT with the new mapping
Physical register id

## Slide 12: Operation of the RAT Table
add r1, r2, r3
14
r1
29
34
r2
r3
add p32, p29, p34
free list
32
mov r3, r1
28
mov p28, p32

## Slide 13: Dependency Check Logic
Let us say r1 is mapped to p11
The second instruction needs to read the mapping of r1 as p11
What if both instructions are sent to the RAT together?
add r1, r2, r3
add r4, r1, 1

## Slide 14: Dependency Check Logic - II
from RAT
px
from RAT
px
1) add r1, r2, r3
2) add r4, r1, 1
3) add r3, r4, r6
py
All mappings from the RAT
inst 2
inst 3
r1  px
r4  py
r3 pz

## Slide 15: Available bit in the rename table entry
We need some more information in each entry
  A available bit
  It indicates whether the result can be found in the physical register file and the rest of the pipeline or not
physical register id
available bit
rename table entry

## Slide 16: Contents
Renaming
Instruction Window
Wakeup and Bypass
Load Store Queue
Reorder Buffer and Precise Exceptions

## Slide 17: Dispatch
Till the rename stage, instructions proceed in-order
Dispatch  Send the instruction to the instruction window (IW)
Rename
Instruction Window

## Slide 18: Instruction Window
Status of an instruction in the window
opcode  type of operation: add, subtract, multiply
tag  physical register id
ready bit  does the physical register file contain the corresponding value
opcode
src tag1
ready
bit 1
src tag2
ready
bit 2
dest tag
imm1
imm2
valid

## Slide 19: At any point in the instruction window
Instructions waiting for an operand to be ready
Instructions whose operands are ready

## Slide 20: Select and Execute
Select unit
Instruction
Window
Register File Read
Execution Unit 1
Execution Unit 2
Execution Unit 3
Execution Unit 4

## Slide 21: Select Unit
Interface
Select unit
grant
request

## Slide 22: Tree Structured Select Unit
requests
requests
requests
Root Node
Request
Granted Request
Request Granted

## Slide 23: Select Unit for Multiple Resources
What if we have 2 adders, 2 multipliers, and 1 divider
Solution:
  Have a separate select unit for each class of instructions
  For a select unit that caters to multiple FUs (functional units)
  Two options: Option 1  Chain select units
Select
Unit 1
request
grant
request
grant
Select
Unit 2
grant
XOR

## Slide 24: Option 2: Multiple request signals
Send multiple request signals (up to n)
Every level sends at most n requests to the root
The root selects at most n requests, and issues grant signals
This circuit is more complicated than serial select circuits

## Slide 25: Select policies
Random
Oldest First
Type of opcode
  The adder processes adds, subtracts, loads, and stores
  Choose the type of instruction
    For example, reduce the priority of stores
    Or, increase the priority of loads

## Slide 26: Read operands from the register file and Issue to the execution units
Select unit
Instruction
Window
Register File Read
Execution Unit 1
Execution Unit 2
Execution Unit 3
Execution Unit 4
2k read ports
port  interface to the external world
k  issue width

## Slide 27: Execute
Select unit
Instruction
Window
Register File Read
Execution Unit 1
Execution Unit 2
Execution Unit 3
Execution Unit 4

## Slide 28: Case of Load and Store Instructions
First, the instructions are sent to the adder to compute the effective address. In this case: 4 + (contents of r3), 10 + (contents of r5)
Next, they are sent to a load-store unit
  Sends the loads and stores to the data cache
  Loads can execute immediately
  Stores update the processor’s state (remember precise exceptions)
  We cannot afford to write the value of stores on the wrong path
ld r1, 4[r3]
st r2, 10[r5]

## Slide 29: Pipeline Stages
Fetch
B. Pred
Decode
Rename
Reg. Read
Dispatch
Select
Execute

## Slide 30: Contents
Renaming
Instruction Window
Wakeup and Bypass
Load Store Queue
Reorder Buffer and Precise Exceptions

## Slide 31: Wakeup
How does an instruction in the IW know that its operands are ready
The producer instructions need to let it know
Once a producer finishes executing
  Broadcast the tag (destination physical register id) to the entries of the IW
  Each entry marks its corresponding operand as ready if the tag matches
  This is called wakeup

## Slide 32: Instruction Window
tag bus
tag bus

## Slide 33: Instruction Window - II
src tag 1
tag
ready bit 1
src tag 2
tag
ready bit 2

## Slide 34: Broadcast multiple tags at once

## Slide 35: When should we broadcast the tag?
Rename
Reg. Read
Dispatch
Select
Execute
add r1, r2, r3
add r4, r1, r5
Option 1
(2)
(1)
Reg. Write
Option 2
(2)
(1)
Option 3
(2)
(1)

## Slide 36: Let us consider Option 3
Allows back-to-back (in consecutive cycles) execution
What needs to be done:
  When (1) is in the Reg. read stage, (2) needs to be in the select stage
  This is possible if we broadcast the tag for (1) when it is in the reg-read stage
  (2) picks up the tag, wakes up, and gets selected for the next cycle

## Slide 37: 1-cycle latency for producer
Rename
Reg. Read
Dispatch
Select
Execute
Reg. Write
Broadcast
Tag
Rename
Reg. Read
Dispatch
Select
Execute
Reg. Write
Wakeup
(2)
(1)
Forward

## Slide 38: 2-cycle latency for producer
Rename
Reg. Read
Dispatch
Select
Execute
Reg. Write
Broadcast
Tag
Rename
Reg. Read
Dispatch
Select
Execute
Wakeup
(2)
(1)
Forward
Execute
Wait

## Slide 39: Structure of the Pipeline
Rename
Reg. Read
Dispatch
Select
Execute
Reg. Write
Wakeup
Broadcast
Tag

## Slide 40: Forwarding Logic in the Execution Unit
Also called bypass paths
Functional Unit
from the Register File

## Slide 41: When should we mark the available bit?
Option 1: Along with the register write
Rename
Reg. Read/BCast
Dispatch
Select/ Wakeup
Execute
Reg. Write
Some instructions that have
arrived after the broadcast might wait forever
Difficult - Begin

## Slide 42: When should we mark the available bit?
Option 2: Along with the broadcast
Rename
Reg. Read/BCast
Dispatch
Select/ Wakeup
Execute
Reg. Write
The instructions being written to the IW, will miss the broadcast and the update of the available bit

## Slide 43: What to do?
Let us fix solutions 1 and 2
Basic features of a new solution:
  Realization: Instructions being written to the IW will miss the broadcast
  These instructions would have also read the available bit to be 0
  As a result: they will wait forever
What does the teacher do if some students in the class are sleeping?
  ANSWER: Take one more class
What is the solution here:
  Double broadcast

## Slide 44: Double Broadcast
Both solutions 1 and 2 can be fixed, if two broadcast messages are sent
Let us look at one solution
  Set the available bit to 1 along with sending the Broadcast message
  There might be some instructions that miss the broadcast
  Log the Broadcasted tags in a temporary structure
  Also record all the instructions that are being dispatched in a separate structure called the dispatch buffer
In the next cycle
  Match the tags with entries in the dispatch buffer.
  If there is a match, update the corresponding IW entry
  Clear the entries for the last cycle in the dispatch buffer
Difficult - End

## Slide 45: Contents
Renaming
Instruction Window
Wakeup and Bypass
Load Store Queue
Reorder Buffer and Precise Exceptions

## Slide 46: Load-Store Queue (LSQ): Actually maintain two queues
Load queue  Queue of all load instructions
Store queue  Queue of all store instructions
Allocate an entry at decode time (allocated in order)
Don’t ask when to deallocate an entry (ask later)
When the effective address is computed, update the entry
And follow these steps:

## Slide 47: Updating the Address of a Load
Search earlier entries in both queues
Find the latest entry (among all earlier entries), which matches the following criteria
  I. Unresolved (address not known) store
  II. Store to the same address (if address is known  store value is known)
  III. Load to the same address, value fetched from memory
Load Queue
Store Queue
Time
Search

## Slide 48: Updating the address of a Load - II
Case I: Unresolved store
  Option 1: Wait
  Option 2: Speculate and move ahead to cases II and III
Case II: Store to the same address
  Store  load forwarding
Case III: Load to the same address, value known
  Load  load forwarding
None of these cases
  Send the load instruction to memory

## Slide 49: Load: Obtain data from memory
Write the data to the corresponding register
Broadcast a tag for wakeup (if required)
Save the data in the LSQ entry

## Slide 50: Updating the address/data of a store
Search backwards (towards later entries) till we find a store that is either unresolved or has the same address. Let such an entry have index i (-1 if none found).
Find all loads between current store and i , with the same address. Store  load forward
If there are loads with a different address, mark them as ready
Load Queue
Store Queue
Time
Search

## Slide 51: Contents
Renaming
Instruction Window
Wakeup and Bypass
Load Store Queue
Reorder Buffer and Precise Exceptions

## Slide 52: Precise Exceptions
For an external observer
  Instructions need to appear to execute in order
  At any point of time the instruction flow can be stopped
Processor
Instructions in order
Instructions in order

## Slide 53: New Structure: Reorder Buffer (ROB)
Reorder Buffer (entry)
  Contains 1 entry for every instruction that has been fetched
  After decoding an instruction, we enter it in the ROB
  If there are no free entries, the PIPELINE stalls
  Instructions are entered into the ROB in order
  The ROB is essentially an in order queue
Updating an entry
  Whenever an instruction finishes its execution, we update the entry of the ROB
  Mark it ready

## Slide 54: Removing Entries from the ROB (Commit/Retire)
Every processor has a commit width
  Number of instructions to commit per cycle
  Let the commit width be W
  2, 4, or 6 (typical values)
  Start from the top of the ROB and access the next W entries
  Stop at the first entry, which is not ready or continue till we reach the Wth entry
  Commit all the entries that we find to be ready
ROB
Fetch
and
Execute
update
entry
create
entry
commit

## Slide 55: What does it mean to commit an entry?
Remove it from the ROB
AND
Depends on the type of instruction
Consider instructions with a register destination
  Inst J: r1  r2 + r3
  Assume that r1 is mapped to py
  Before this instruction r1 was renamed it was mapped to px
When can we free px?
  After J commits, there are no instructions earlier than J in the pipeline
  There is no instruction that requires the value in px
  px can be reclaimed, and added to the free list

## Slide 56: Updates to renaming
Whenever we see an instruction of the form:
  Instruction J: r1  ...
  Remember the previous mapping of r1 by reading the rename table
  Assume that r1 was mapped to px
  Save this mapping in the ROB entry for instruction J
  When J is committed, unmap px, and return it to the free list
This can be done for all instructions that have a destination operand as a register: ALU instructions, load instruction

## Slide 57: Store Instructions
When should a store be written to memory?
  ANS: When we are sure that it is not in the wrong path of a branch, or no interrupt will come before it
  Only possible at commit time.
  Solution: Send stores to memory at commit time.
  At the same time remove them from the store queue

## Slide 58: What do we in the case of an interrupt?
Let us treat interrupts, exceptions, and branch mispredictions in the same category
We will clearly have some instructions in the pipeline that are on the wrong path. They should not be committed
Use the ROB:
  Mark the instruction that has had an exception, or suffered from a misprediction in the ROB
  In the case of an interrupt mark the top most entry in the ROB
  Wait till the marked instruction retires
  Initiate the recovery sequence
  More on the next slide 

## Slide 59: Flushing the Pipeline
Fetch
Rest of the Pipeline
ROB
Insts
Branch misprediction
Flush the ROB, LSQ, IW
and all pipeline registers

## Slide 60: Recovery Sequence
  Flush the pipeline
  Remove the entries from the IW, LSQ, and ROB
  Remove entries from all pipeline registers and other temporary structures (not the rename table or register file though)
Restore the state
  Architectural register state for the last committed instruction
  The contents in the rest of the physical registers does not matter

## Slide 61: Approach 1: Retirement Register File (RRF)
RRF  Maintain the state of all architectural registers at commit time
Each entry of the ROB gets augmented with the value of the destination
Write the value of the destination register at commit time.
The RRF maintains a checkpoint at commit time
ROB
RRF
PRF

## Slide 62: Approach 2: Retirement RAT (RRAT)
Why do we need to write the values into the RRF?
Aren’t just the mappings sufficient.
Maintain a copy of the mapping of the destination register in the ROB entry
  Eg: r1  r2 + r3, r1 gets mapped to py
  Maintain r1  py in the ROB entry
  Update the RRAT with this mapping
At the time of recovery
  Restore the mappings in the RRAT to the RAT
ROB
RAT
RRAT

## Slide 63: Approach 3: RAT Checkpointing (SRAM based)
Consider the following design
At every branch let us maintain a checkpoint
Set of 16, 7-bit ids
In each entry of the RAT have a shift register, where each entry of the shift register is 7 bits wide
To create a checkpoint, shift the entries in each row.
The last entries of each shift register represent the current architectural state
Remove the last entries once the corresponding instructions commit
16 entries
7 bit (1 out of 128 phys. regs)

## Slide 64: RAT
Arch reg. id
Latest Mapping
Architectural State

## Slide 65: Approach 4: RAT Checkpointing (CAM based)
A CAM (content addressable memory) is like a hash table
  You address each element not by an index, but by a subset of its content
  It is slower than a structure that is addressed by an index
CAM based RAT
128 entries
arch. reg id
7 bit physical reg id
4 bit arch. reg id, valid bit, 7 bit phys. reg id,
SRAM and CAM: Refer to Chapter 6 of the reference: Computer Organisation and Architecture
[Sarangi, McGrawHill, ’15]

## Slide 66: CAM based RAT
At any point of time, 16 bits are set to 1. They contain the current mapping (latest state)
The architectural state is also a set of 16 entries in the RAT table.
We can save a checkpoint by saving the set of valid bits in a 128 bit vector.
For every branch, we can take a snapshot of the valid bits.
The best way to achieve this is to have a shift register in each row of the RAT table, where each entry is 1 bit wide
Use the same idea as the SRAM based RAT

## Slide 67: [PROBLEM]
Ideally in a CAM based scheme, we should be storing 128 x 5 bits as the checkpoint.
However
  We are only storing 128 x 1 bits as the checkpoint
  How are we doing this?
  Are there any implications on correctness?
Can you prove this formally.

## Slide 68: [Activity]
Understand the operation of a circular queue implemented using an array
  Uses a head and tail pointer
How do we implement the following operations?
  enqueue
  dequeue
  copy the first element, and then shift. This is required in our SRAM and CAM based designs.

## Slide 69: Pros and Cons
RRF
  + point  Simple to implement. Transferring the checkpoint is easy
  - point  Extra register writes every cycle. More power
  - point  Need to save the value in the ROB. More space.
RRAT
  + point  Requires less space in the ROB than the RRF
  - point Has activity every cycle. More power
SRAM based RAT
  + point  Activity only on a branch. Shift.
  - point  Each row of the RAT is wider. Shift operations.
CAM based RAT
  + point  Shift operations are easy. Shift only 1 bit.
  - point  The CAM per se is a slower structure than a SRAM.