## Slide 1: Instruction Prefetching Smruti R. Sarangi

## Slide 2: Contents
Motivation for Prefetching
Simple Schemes
Recent Work
  Proactive Instruction Fetching
  Return Address Stack Directed Prefetching
  Pentium 4 Trace Cache

## Slide 3: Journey till now ...
Processor
Optimized
I-Cache
D-Cache
L2 Cache
Main Memory
2-4 cycles
10-50 cycles
200-400 cycles
Rest of the System

## Slide 4: Misses in the Caches
We can incur a large performance penalty if there is a miss in the i-cache
  For the next 10-50 cycles, there will be no instructions to fetch if there is an L2 hit
  If there is a miss in the L2, we have nothing to do for hundreds of cycles
  The pipeline will have bubbles (idle cycles), IPC will suffer
What is the solution?
  Prefetch the memory addresses
  Meaning: Predict memory addresses that will be accessed in the future. Fetch them from the lower levels of the memory hierarchy before they are required.

## Slide 5: Patterns in Programs
Temporal Locality
  Tend to use the same data (cache lines) repeatedly
Spatial Locality
  High probability of accessing data in the same memory region (similar range of addresses) once again

## Slide 6: Contents
Motivation for Prefetching
Simple Schemes
Recent Work
  Proactive Instruction Fetching
  Return Address Stack Directed Prefetching
  Pentium 4 Trace Cache

## Slide 7: Instruction Prefetching
1
Find patterns in the i-cache access sequence
Leverage this pattern for prefetching
2

## Slide 8: Next line prefetching
Pattern: Spatial locality
If cache line X is accessed, there is a high probability of accessing lines: X+1 and X+2
Reason: The code of most functions spans multiple i-cache lines
Leverage this pattern: If a cache line X incurs an i-cache miss, read X and the next 2 lines from the L2 cache

## Slide 9: Markov prefetching
Pattern: i-cache miss sequences have high repeatability
The miss sequence of a core looks like this:
High correlation between consecutive misses
Leverage this pattern for prefetching
X | Y | …. | X | Y | … | X | Y | … | X | Y | …
Miss sequence:

## Slide 10: Markov prefetching
Record the i-cache miss sequence in a table
Given that cache line X incurs a miss, predict the line which will incur a miss next
Cache line | Option 1 |  | Option 2 | 
 | Address | Frequency | Address | Frequency
X | Y | 3 | Z | 1
X | Y | …. | X | Y | … | X | Z | … | X | Y | …
Miss sequence:
higher probability
Markov table:

## Slide 11: Markov Predictors - II
We can instead have an n-history predictor that takes the last n misses into account
Whenever there is a miss, access a prefetch table. Find the next few addresses to prefetch. Issue prefetch instructions.
Also, update the frequencies of the entries for the last n-1 misses.
All prefetch requests go to a prefetch queue. These requests are subsequently sent to the L2 cache (lower priority).

## Slide 12: Call Graph Prefetching
Pattern: The function access sequence has high repeatability
Leverage this pattern: predict and prefetch the function that may be called next

## Slide 13: Call graph prefetching
......
......
......
......
prepare_page( )
......
......
update_page( )
......
......
unlock_page( )
......
…
if NOT IN MEMORY {
read_from_disk( )
}
lock_page( )
......
......
......
......
create_record
prepare_page
read_from_disk
lock_page
......
......
......
......
update_page
unlock_page

## Slide 14: Call graph prefetching
create_record
prepare_page
read_from_disk
lock_page
update_page
unlock_page
1
2
3
1
2

## Slide 15: Call graph prefetching
prefetch prepare_page
......
......
......
……
prepare_page( )
prefetch update_page
......
......
update_page( )
prefetch unlock_page
......
......
unlock_page( )
......
create_record
......
......
......
......
prepare_page( )
......
......
update_page( )
......
......
unlock_page( )
......
create_record
becomes

## Slide 16: Call Graph History Cache
Each entry in the data array contains a list of functions to be subsequently executed.
The index maintains a pointer to a function in the data array entry.
Tag Array
Data Array
Function id
Index
func 1
func 2
func 3
func 4
func 5

## Slide 17: Operation (Function Call)
Function Call.
X calls Y
Access the entry of Y in the CGHC
Does it exist?
NO
Create entry
Prefetch the first function in Y’s call sequence
YES
Put Y in X’s call sequence at the appropriate index

## Slide 18: Operation (Function return)
Y returns to X
Reset the index of Y to 1
Access X’s call sequence
Increment the index
Prefetch the next function in the call sequence

## Slide 19: Patterns:
Technique | Pattern
Next line prefetching | Spatial locality
Markov prefetching | i-cache miss sequence has high repeatability
Call graph prefetching | Function access sequence has high repeatability

## Slide 20: Contents
Motivation for Prefetching
Simple Schemes
Recent Work
  Proactive Instruction Fetching
  Return Address Stack Directed Prefetching
  Pentium 4 Trace Cache

## Slide 21: Proactive Instruction Fetch
Insight:
  Instructions on the wrong path lead to spurious prefetches
  Corrupt the state of the prefetcher
Divide addresses into spatial regions
  Each region has a trigger address (first instruction in the region)
Commit Stage
Compactor

## Slide 22: Compactor
Operation
  Compares the block address of the retiring instruction with the block address with the previously retired instruction. If same, discard.
  The spatial compactor creates a region of blocks. A region has N blocks preceding the trigger and M blocks after the trigger.
    The trigger is the first accessed block in a spatial region.
  For each region we maintain a bit vector (1 bit for each block). When that block is accessed, we set the bit.
  If the program access a block in another spatial region. Send the trigger PC, bit vector to the temporal compactor.
  Example:
Bit Vector
A-2
A
A+2
Access Block A-2
Access Block A
Access Block A+2
1
1
1

## Slide 23: Temporal Compactor
Maintains a list of spatial regions (let’s say last 4)
Codes typically have a lot of temporal locality
  If the given record matches any one of the stored records, discard this record
  AND promote this record (most recently used)
  otherwise, discard the least recently used record
  create a new record, and also send to the history buffer

## Slide 24: History Buffer
Circular buffer  Stores retired instructions
Each entry stores  trigger PC, bit vector of the spatial region
Index table saves a mapping
  Trigger PC  most recent record in the history buffer
Operation:
  Two kinds of instruction fetches  Instructions that were prefetched, and instructions that were not prefetched
  When a core fetches an instruction that was not prefetched
    Trigger the prefetching mechanism
    Search for the PC in the index table
  If we find an entry prefetch the instruction stream (proactive)

## Slide 25: Stream Address Buffer
The stream address buffer maintains a list of all the blocks that need to be prefetched
This information is calculated based on the information saved in the history buffer
PC
History Buffer
Stream Address Buffer
L1 Cache

## Slide 26: Contents
Motivation for Prefetching
Simple Schemes
Recent Work
  Proactive Instruction Fetching
  Return Address Stack Directed Prefetching
  Pentium 4 Trace Cache

## Slide 27: Motivation
I-cache misses are a crucial determinant of performance
  Particularly in server based applications
  Can determine 10-30% of the overall performance
PIF (proactive instruction fetching) has high storage overheads
  History Buffer
  Stream Address Buffer
Reduce storage overheads
  Use the RAS (return address stack) instead
  It effectively captures the context of the current program

## Slide 28: RDIP: Basic Idea
Three steps
  Record the i-cache misses in a given program context (sequence of function calls)
  Predict the next program context based on the current context.
  Prefetch cache misses associated with the next context
Representing program context
  Take all the entries and XOR them together (32 bits)
  Signature of the path taken to reach the current function
  Assume a caller calls multiple callees. After returning from each callee the state of the RAS is identical.
    Solution: Take signatures before processing return instructions.

## Slide 29: Miss Table
Miss Table
  Signature  Set of i-cache misses
  Maintain a buffer of the last k misses
  Whenever the call signature changes update the miss table
  Compress each set of misses using a scheme similar to PIF
  When updating a miss table entry: merge the sequence of misses with the sequence already stored

## Slide 30: Program Context Prediction
Instead of logging misses with the current signature log them with a previous signature
  To increase lookahead, log them with the previous k signatures
    Maintain a circular buffer with the last k signatures
  Keeps things simple: just issue prefetches for the entry corresponding to the current signature

## Slide 31: Contents
Motivation for Prefetching
Simple Schemes
Recent Work
  Proactive Instruction Fetching
  Return Address Stack Directed Prefetching
  Pentium 4 Trace Cache

## Slide 32: Trace Cache
Execution of a typical program
Basic Block 1
Basic Block 2
Basic Block 3
Basic Block 4
Basic block  A set of instructions with a single point of entry and a single point of exit
We fetch a sequence of basic blocks from the i-cache
Such a sequence is called a trace
Let us have a cache that stores such traces. We have the option of sequentially reading out a full trace
This is called a trace cache (first major use: Pentium 4, circa 2000)

## Slide 33: Earlier approaches
Traditional approach
  A cache line contains contiguous cache blocks
Peleg and Weiser
  Store successive basic blocks per cache line
  Trace segments cannot span multiple cache lines
Melvin et al.
  CISC instruction sets decode instructions into micro-ops
  The idea is to store decoded micro-ops for each instruction in a cache line
  Saves some decoding effort
Can we combine and augment these solutions?

## Slide 34: Structure of a Solution
A trace consists of multiple cache lines
It is a linked list of cache lines (each line is a trace segment)
We need a method to place a marker to terminate a trace, and start a new trace.
Trace Head
Trace Body
Trace Body
Trace Tail

## Slide 35: Operation
Lookup a fetched address. See if it is a trace head
If yes, start prefetching the trace
Each line of the trace contains a pointer to its previous trace segment and successive trace segment
The entire data line need not contain valid instructions
  Never distribute micro-ops of a macro instruction across cache lines
  Terminate a data line if you encounter more branch microps than a threshold
Trace segment termination
  Encounter an indirect branch
  Interrupt or branch misprediction notification
  Maximum length of trace (64 sets) reached

## Slide 36: Bird’s eye view of traces
Head
Head
Body
Body
Body
Body
Body
Body
Tail
Tail
Way 0
Way 1
Way 2
Way 3
Set 1
Set 2
Set 3
Set 4
Set 5

## Slide 37: Hardware Support
Augment each entry in the tag array
  Trace head, body, and tail information
How to store the id of the next trace segment member
  Store the index of the line
  Store the way index, and the set index (if a different set)
There is also a need to do some predecoding within the same line
  Save some additional pointers: uIP (identifying the next microinstruction), NLIP (next macro instruction),

## Slide 38: Execution Mode
Starts in the idle state
  Transition to the head lookup state.
  Lookup the fetched address in the tag array. See if it is a trace head.
Once we find a head
  Transition to the body lookup state
  By default the next trace segment is in the next set. The way is specified in the current line
  Keep reading the micro-ops and send to the processor
  If there is any interrupt/branch misprediction, abandon, back to head lookup
Once we reach the tail
  Transition to the tail state
  Restart from the head lookup state

## Slide 39: Other States
During this process several things can go wrong
  Encounter a macro-instruction (very complex CISC instruction)
  Transition to the MS (microcode sequencer state)
  For that particular instruction, read its micro-operands from microcode memory and insert them into the pipeline
  Then transition to the body lookup state
Body miss state
  Enters this state when there is a cache miss while reading a trace segment
  Abandon and start building a trace

## Slide 40: Building a Trace
During trace building, we do not read from the trace cache
We start in the fetch request state
  Send the PC to the lower level for its contents
  After the line comes back wait for it to get decoded
  After the instruction is decoded into several uOPs, place them in the fill buffer
  Keep doing till a data line termination condition is encountered
  After that write the contents of the fill buffer to the trace cache
There are many methods to find an entry in the trace cache to write to:
  Next set
  Next way in the current set
  Other heuristic: least used entry
Keep building till a trace end condition is encountered

## Slide 41: Important Claims
A separate trace segment reader, and a separate builder
The trace cache state machine
Notion of partially building a trace and storing it in the fill buffer