## Slide 1: Compute Express Link (CXL)
Prof. Smruti R. Sarangi
https://srsarangi.github.io/

## Slide 2: History
Formed by Intel 2019
Now managed by a consortium
Three generations of specifications: 1.0, 2,0, 3.0
Uses PCIe as the base physical layer
CPU  Device
CPU  Memory

## Slide 3: Introduction to CXL
CXL is a protocol that is built on top of PCIe (PCI Express)
Dynamic multi-protocol technology
I/O semantics: CXL.io
Caching protocol: CXL.cache
Device memory access: CXL.mem
Accelerators
Memories
Network interfaces
Cores
Persistent Memory

## Slide 4: Why CXL?
Coherent access to host/device memory
Scalable memory: PCIe is 5X faster than DDR
Pool memory by using remote memory
Fine-grained data sharing: leverage local accesses

## Slide 5
Outline
Switching
Background and Overview
Link Layer
Transaction Layer
Power, Security, Reliability

## Slide 6: PCI Express
Motherboards needs a bus to connect the I/O elements
  There were many buses in use in the late nineties. Two of them were very popular.
    PCI (Peripheral Component Interconnect)
    AGP (Accelerated Graphics Port)
A standardisation effort led to the PCI-Express (PCI-X) bus
A PCI Lane is a :
  High speed serial bus.
  Does not use parallel links because of the possibility of different amounts of delay across the links. Synchronisation across links is difficult.
Full duplex comm: 3.94 GB/s (serial lane), 7.56 GB/s (3.x)

## Slide 7
PCI Express (Peripheral Component Interconnect Express)
Usage
As a mother board bus
Specification
PCI Express specifications (link)
Topology
Connection
Point to point with multiple lanes
Lane
A single bit full duplex channel with data striping
Number of Lanes
1 to 32
Physical Layer
Signalling
LVDS based differential signalling
Encoding
8 bit/10 bit
Timing
Source synchronous
Data Link Layer
Frame Size
128 bytes
Error Correction
32-bit CRC
Transactions
Split transaction bus
Bandwidth
8 GB/s per lane (approx.) (version 6.0)
Network Layer
Routing Nodes
Switches

## Slide 8: Flex Bus
Choose between native PCIe and CXL
CPU
PCIe
CXL
CXL card
PCIe card
CXL accelerator
CXL Switch
CPU/memory/accelerator
Switch

## Slide 9: FlexBus Layers
cache and mem
Transaction Layer
cache and mem Link Layer
Logical Layer
Electrical Layer
PCIe/CXL.io Trans. Layer
PCIe/CXL.io Data Link Layer
ARB/MUX

## Slide 10: Example CXL System
Host
I/O Devs
Core
Core
Coherence + Mem logic
Mem Ctrl.
PCIe and CXL
Host Memory
Accelerator
CXL
Mem Ctrl.
Logic
Device Memory
CXL.mem
Caching logic
CXL.cache
DTLB
CXL.io

## Slide 11: Types of CXL Devices
Type 1 device: Rely on the host’s memory
  Need a fully coherent cache to access the host’s memory
  Supports devices using the cxl.cache link layer: devices can cache host memory
  Any memory consistency model can be implemented on top of it.
  Special feature: Unlimited number of atomic operations
Type 2 device: Local memory + host’s memory
  Support all three protocols: io, cache and mem
  They additionally have memory (DDR, HBM, etc.)
  The device has cache + memory (device-managed coherence)
  The device memory can be private to it, or it can be shared with the host

## Slide 12: Type 3 CXL Device
Supports the CXL.io and CXL.mem protocols
Does not operate on host memory
Serve as a memory expander
No compute elements
Instead of participating in cache coherence, it services requests sent from the host

## Slide 13: Comparison of all Three CXL Memory Devices
 | Type 1 | Type 2 | Type 3
Purpose | Accelerator | Accelerator with local memory | Memory expander
Local memory | No (mostly) | Yes | Yes
Coherence | Yes (host) | Yes (host + local) | No
Protocols | io and cache | io, cache and memory | io and memory
Use case | Network adapter, compression engine | GPUs, AI/ML accelerators | Persistent memory, DRAM modules

## Slide 14: Complex Interconnections + Virtualization
1 Device  16 Isolated Logical Devices
Each logical device has a Logical Device Identifier (LD-ID)
Multi-Logical Device (MLD)
1 Device Memory  Exposed to multiple hosts
Can use a single link or multiple links
Pooled Memory and Shared Fabric
Matrix connection between logical devices and memories

## Slide 15: Example Topology
Head 0
Head 1
Head 2
A “Head” is a CXL port on a Type 3 device
LD0
LD1
LD2
LDn
Pooled Memory

## Slide 16: CXL Fabric
Switch
Switch
Switch
Switch
Host
Host
Acc
Acc
Host
MLD
Memory
Expander

## Slide 17
Outline
Switching
Background and Overview
Link Layer
Transaction Layer
Power, Security, Reliability

## Slide 18
CXL.cache

## Slide 19: CXL.cache
The granularity of data transfer is always 64 bytes
Snoops to maintain coherence (H2D or D2H)
The channels operate independently (deadlock potential)
There can be no assumption made on the delivery times of messages
  The sender may run out of link-layer credits
Request
Response
Data
D2H
H2D
Bidirectional caching

## Slide 20: Host and Device Bias
Host bias  The host manages the coherence.
Device bias  The device manages the coherence. The host needs permission from the device to access the block.
Bias Table
  Tracks bias data at the granularity of pages
  Allows bias transitions

## Slide 21: Ex: Host Bias
Host
Coherence logic
Host attached memory
Device
Host-managed device memory
Coherence logic
CXL
Always ask the host for coherence info.

## Slide 22: Device to Host Requests (Upstream)
CXL.cache Read (Device wants to read from the host)
Request  Response  Data (2 x 32 bytes)
CXL.cache Read0
Do not receive any data messages after the response
Examples: cache flush (zero the data, relevant in persistent memory and atomics)
CXL.cache Write (host asks the device to send the write)
Request  Response (GO and WritePull)  Data
CXL.cache Read0-Write
Device let’s go of ownership first and then forwards the data
First zero the data on the host, and then write to it
Device Coherence Engine (DCOH)

## Slide 23: Host to Device Responses
WritePull  Host needs to get the data from the device
GO messages  Global Observation message. Coherence message.
  Locks the host until the transaction is over (avoid race conditions)
An orderly transfer of ownership is ensured. Otherwise race conditions will lead to errors.
  Only one snoop pending per cache line
  Multiple reads, evicts and writes to the same cache line are strictly regulated
  Only one outstanding evict per cache line. Multiple reads are fine. Preferably, single write.
The GO message establishes the ordering
Downstream

## Slide 24: Example Device to Host Interaction
Device
Host
Wr Request
GO + WritePull
Data

## Slide 25: Host to Device: Snoop Requests
SnpData
Read requests (no ownership)
Transition to shared, send data
SnpInv
Require ownership
Meant for write requests
Leads to invalidations
SnpCur
Get current version of the line
No change in the cache state

## Slide 26: Example Interaction: Host to Device
Device
Host
SnpData
RspSFwdM
Wait for the data
Data

## Slide 27: Device to Host Response
Mnemonic | Meaning
RspIHITI | Line not found
RspVHITV | Hit and no state change
RspIHITSE | Hit (not modified), now cleared
RspSFWDM | Downgraded to shared
RspIFWDM | Modified  Invalid transition at the device
RspVFWDV | Returning the current data

## Slide 28
CXL.mem

## Slide 29: CXL.mem
The memory controller can be on the host CPU, device or on a separate chip
CPUs and other CXL devices can access device memory
CXL.mem
(transactional interface)
CPU
Memory
HDM-H: Host-only coherent (Type 3 devices)
HDM-D: Device coherent (Type 2 devices)
HDM-DB: Device coherent using back-invalidate (Type 2 or 3 devices)
Master
Subordinate
Back-invalidate: other cached copies are invalidated

## Slide 30: M2S and S2M Transactions
Request without data
Request with data
Back-invalidate response
M2S
S2M
Response without data
Response with data
Back-invalidate snoop
Device
Snoop filter
Which address is cached where?

## Slide 31: Transaction Ordering
Snoops cannot overtake earlier GO messages
Back-invalidate snoop: The device snoops the host (and possibly invalidates it)
There are strict rules for ordering transactions in the D2H and H2D links.
Examples

## Slide 32
Scenario 1: Simple snoop request (Type 1 and Type 2 devices)
32
Host
DCOH
Device
Rd addr. X
SnpData
Data + Response
Cmp (complete)
Data X
Hit
shared

## Slide 33
Scenario 2: Inv snoop request (Type 1 and Type 2 devices)
33
Host
DCOH
Device
Rd X + SnpInv
SnpInv
Data + Response
Cmp (complete)
Data X
Hit
Invalidate

## Slide 34
Scenario 3: Non-cacheable Read (Type 1 and Type 2 devices)
34
Host
DCOH
Device
Rd X + SnpCur
SnpCur
Data + Response
Cmp (complete)
Data X
Hit

## Slide 35
Scenario 4: Direct Write from Host
35
Host
DCOH
Device
Wr, SnpInv
Cmp
Miss
Dev Mem
Write
Cmp

## Slide 36
Scenario 5: Weakly Ordered Write
36
Host
DCOH
Device
Wr, SnpInv
SnpInv
Data + Response
Cmp
Hit
Dev Mem
Invalidate
Write
Cmp

## Slide 37
Host
DCOH
Device
Dev Mem
Host bias
Scenario 6: Device Read to Device-Attached Memory
RdAny
RdForward
Device bias
Data
Data
Data
Read
Read
RdAny
Data
Device bias
Subsequent reads

## Slide 38
38
Host
DCOH
Device
Dev Mem
Device bias
Scenario 7A: Device Write to Device Memory (Device Bias)
Write
WrPull
Data
Write
Cmp
Cmp

## Slide 39
39
Host
DCOH
Device
Dev Mem
Host bias
Scenario 7B: Device Write to Device Memory (Host Bias)
WrBack
Data
WrPull
Data Write
Cmp
Cmp

## Slide 40
Peer cache
Host
DCOH
Device Mem.
Rd X
BISnp Y
SnpInv Y
Data +
response
Rd X
Data X
Wr Y
Wr Y
Cmp
Cmp (complete)
Data X
X displaces Y
Invalidate
Scenario 8: Miss in the Snoop Filter

## Slide 41
Telemetry

## Slide 42: QoS Telemetry
Each memory device indicates its current load level (DevLoad) along with every response
  Load balancing, power management, request rate throttling
QoS 
Memory device
Req.
Response
QoS
Light
Optimal
Moderate
Severe
Memory device
Multiple QoS classes
Performance isolation

## Slide 43: How is Telemetry Used?
Dynamic feedback-based control.
LoadMax (sent by memory device) | Level of Request Throttling
Light | 
Optimal | 
Moderate | 
Severe | 
Adjust ever T ns. T is slightly more than the host->device->host round-trip time
Flow control at the “egress” port also exerts some back-pressure.
Conflict
Devices can themselves take “breaks” and perform maintenance tasks: refresh, wear levelling, etc.

## Slide 44: Flow Control vs Device Load
When the device’s request queue length is increasing
  Responses take more time
  The device’s load is high
  Severe or Moderate Load messages take longer to send
  The host does not throttle the traffic on time
  This leads to more messages and the queue filling up even faster
A reverse effect happens when the queue length decreases
  “Light Load” messages take a long time to reach the host
  The queue drains even faster
Consider a clogged egress port
Include egress port information in the QoS data

## Slide 45
CXL.io

## Slide 46: CXL.io
Uses non-coherent I/O load semantics
For all devices, CXL.io is mandatory
Supports strict ordering like sequential consistency (relaxed in CXL 3)
Three flow-control classes: writes (P), reads and config messages (NP) and completions (C)
  Writes and reads may bypass reads
Need two virtual channels for ensuring QoS
Device discovery
Status reporting
Address translation
DMA

## Slide 47: Software Support
The firmware lists and configures CXL resources at boot time
Many such devices are assigned host physical address ranges
These are often memory devices, and cannot be removed seamlessly
Coherent Device Address Table
  Internal NUMA domains
  Memory ranges
  Bandwidth
  Latency
Support hot addition and removal

## Slide 48
Outline
Switching
Background and Overview
Link Layer
Transaction Layer
Power, Security, Reliability

## Slide 49: Link Layer
Intermediate stage between CXL.io and Flex Bus
Runs on top of the PCIe Data Link Layer
68B (used with CXL.io) and 256B modes available
  66B in the link layer and 2 bytes in the ARB/MUX layer
  Physical layer support up to 32 GT/s
  256B supports any legal transfer rate (>32 GT/s)
Standard supports only x16 links and higher
The framed I/O packet is forwarded to the Flex Bus Layer

## Slide 50: cxl.cachemem
Flit size: 528 bits (66 bytes)
Flit header (4 B)
12-B Header
16-B Generic Slot
16-B Generic Slot
16-B Generic Slot
CRC (2 B)
Protocol flit
16-B Generic Slot
16-B Generic Slot
16-B Generic Slot
CRC (2 B)
16-B Generic Slot
Data flit

## Slide 51: Packing Flits and Transactions
Data chunks may roll over to the next data flit
Fairness between cxl.cache and cxl.mem transactions
Slots need to be tightly packed
Control and all-data flits cannot be interleaved
Control flits can be sent even without any credits (do not follow rules)
Data flit
Control flit
Protocol flit
Link layer control types | Description
RETRY | Retry operation flit
LLCRD | Credit and ack information
IDE | Integrity and data encryption
INIT | Link layer initialization

## Slide 52: Reliable Transmission (Retry Buffer)
There is a retry buffer (RB) that stores flits that have not been acknowledged (there can be CRC errors)
Every flit has a sequence number
The sender periodically retries sending flits that could not be sent
There is additional state to manage the buffer (treated as a circular queue)
If the sender’s RB is filling up, the receiver can be forced to send pending acknowledgements
Receiver also sets a timer to remind it to send acknowledgements

## Slide 53: RETRY State Machines
State | Meaning
RETRY_LOCAL_NORMAL | Default state
RETRY_LLREQ | Receiver has detected a CRC error
RETRY_LOCAL_IDLE | Waiting for a RETRY message
RETRY_ABORT | RETRY attempt failed
State | Meaning
RETRY_REMOTE_NORMAL | A flit other than RETRY request is received
RETRY_LLRACK | RETRY acknowledgement is not sent yet
Receiver
Sender

## Slide 54: 256 Byte Flits
Reliability is handled by the physical layer (PCIe)
Standard and Latency Optimized (LO)
Standard flit
  Fourteen 16-byte data chunks
  2B header, 14B (more header information)
  16B error correction (CRC and FEC (forward error correction))
LO flit
  In the middle of the flit, we store the following (Slots 7 and 8, bits 112 to 144)
  CRC and header information

## Slide 55: Correctness and Integrity
If the sender is running out of credits, force the receiver to return all the credits that it can
Indicate empty flits
Viral
Indicates that there is a fatal error. All downstream devices need to also go viral and stop sending messages. They need to take error containment actions.
Poison
Indicates that the data that is being sent (or was/will be sent is incorrect). The poison bits identify
the bits that are erroneous.

## Slide 56
ARB/Mux

## Slide 57: ARB/MUX
Arbitrates between requests
Merges state transition requests (like power states)
For each link, a vLSM (virtual Link State Management) state machine is maintained.
  Plays a role in link training: #lanes, data rates, signal quality, low-power mode
  Links are regularly retrained
  LMPs (Link Management Packets) are sent to set the status of links and find their status
Link Layer
PCI.e/CXL.io LL
CXL cache and mem
ARB/MUX

## Slide 58: Resource Allocation and Partitioning
An ARB/MUX can get multiple requests
  Link layers send requests to the ARB/MUX
  CXL.io may request some lanes
  CXL.mem may request for some more
  The combined total may be more than the number of lanes available.
  This is where efficient resource allocation is required. ARB can negotiate.
  Links can be upsized and downsized
Any error in any Link Management Packet initiates link retraining

## Slide 59
Outline
Switching
Background and Overview
Link Layer
Transaction Layer
Power, Security, Reliability

## Slide 60: Switches
Switches have a very important role to play in the CXL fabric
CXL/PCIe
VCS: Virtual CXL Switch
VCS
VCS
VCS
VCS
Composite
Switch
vPPB
vPPB
vPPB
vPPB
vPPB
Fabric Manager

## Slide 61: PCIe-PCIe Bridge (PPB)
A switch may connect different PCIe buses
We thus need a PPB and virtual vPPBs to connect them. Internally, the upstream ports and downstream ports may be multiplexed.
Upstream ports always have priority over downstream ports
Normally, a hierarchy of vPPB devices is created within a switch
Allows hot-plugging: addition and removal of devices
The switch supports dynamic binding: input-output connections
  Implemented by the Fabric Manager

## Slide 62: A More Complex Example (Composite Switches)
vPPB
vPPB
vPPB
PCIe/CXL device
PCIe/CXL device
Phy port
VCS 0
vPPB
vPPB
vPPB
MLD Device
PCIe/CXL device
Phy port
VCS 1
Fabric Manager

## Slide 63: Composable CXL System
CXL Switch
CXL Switch
CXL Switch
CXL Switch
CXL Switch
CPU
Acc
Mem
Acc
Acc
Mem
Mem
Acc
Mem

## Slide 64: More about Switches
Role of the fabric manager: Bind devices to virtual ports (vPPBs)
vPPBs can be bound and unbound from physical ports
SLD vs MLD
  SLD  Single logical device
  MLD  Multiple logical devices, pooled logical devices
In an MLD
  Each LD can be connected to a vPPB
  Complicated connections are possible
PPB
vPPB
vPPB
MLD

## Slide 65: Contd …
The Fabric Manager (FM) is notified when a device is added or removed
It is used to tunnel commands to an LD in an MLD
Set QoS parameters
Supports multi-headed devices: multiple devices can access the same memory region
PPB
vPPB
vPPB
MLD – LD1
MLD – LD2

## Slide 66: CXL PBR Switches
Every switch has a mailbox for control messages
Switch  Several upstream ports + downstream ports + mailbox
PBR  Port-based routing
  Can build on existing PCIe tree of devices
  Each switch can be connected to other PBR switches, and Type 1/2/3 devices
  Devices don’t need special support
  Dynamic routing for congestion avoidance
  Supports tree, mesh, ring, star, butterfly and multi-dimensional topologies
HBR  Hierarchy-based Routing
  Offers tree-based routing

## Slide 67: CXL Fabric Architecture
Scale from node to rack-level
  Simple load/store semantics
  Non-coherent I/O
Supports up to 4096 ports
CXL Fabric
Fabric manager
Host
Host
Host
Host
Dev
Dev
Dev
Dev

## Slide 68: Example Topology
CXL Fabric
Fabric manager
Acc
Acc
Acc
Acc
GFD
GFD
GFD
GFD
Host
Host
Host
Host
Fabric attached memory

## Slide 69: Host and Device Memory Address Spaces
An MLD has separate device addresses (DPAs) for each host
A Global Fabric-attached Device/Memory (GFD/GFAM) translates the Host Physical Address (HPA) to a DPA
  It has a decoder and a decoding table per host (or group of hosts)
The GFAM address space is split into segments
  Each segment is associated with a GFD
Host
Virtual
address
Switch/
Edge Port
Fabric
Switches
Downstream edge port
G-FAM
Device

## Slide 70
Outline
Switching
Background and Overview
Link Layer
Transaction Layer
Power, Security, Reliability

## Slide 71
Power
Management

## Slide 72: Power Management
Hierarchical power management architecture
Thermal and power management decisions are executed locally
  However, the decision to enter a low-power state needs to be taken in consultation with other entities
  A high-bandwidth memory cannot arbitrarily lower its bandwidth (power) without letting the host processor know
  Similarly, the processor cannot enter a low-power state while accessing high-bandwidth memory
All the changes need to be notified to connected entities
  Hosts need to convey latency tolerance values to devices

## Slide 73: Phase 1 and Phase 2
68B flit mode requires the ARB/MUX to initiate power-state synchronization across its two ends
Once the negotiation ends, enter a specific low-power state.
Phase 1
Phase 2
Initiated by the ARB/MUX of the downstream component
There is an optional Phase 3: Bring the electrical links to an idle state. Wait for outstanding state-change requests to complete.

## Slide 74
Security

## Slide 75: Security
Confidentiality
Integrity
Replay
Tasks
Key establishment
Key negotiation
Device attestation

## Slide 76: Trusted Computing Base (TCB)
CXL Link
Security logic
Security logic
Encryption logic
Integrity check logic
Key-exchange protocol
Reset/debug/link power mgmt
Threats
Analyze data
Perform record-replay
Reorder/delete
Insert malicious packets
Replace trusted devices

## Slide 77: Security Details
Link layer control flits are not protected
Link CRC is computed on encrypted data flits
Uses 256-bit AES-GCM encryption
Key refresh:
  Running a different VM on an accelerator
  After key wear-out
AES-GCM
Plaintext
Addl. Data (A)
IV
Key
Ciphertext

## Slide 78: Encryption Details
In CXL Cachemem:
  The 32-bit header bits are the additional data
  They are integrity-protected
  The rest of the flit is a part of the plaintext
Flit aggregation
  We can aggregate K flits
  Compute the CRC of the contents (PCRC) and append to the plaintext
  Encrypt it
  The encrypted hash is known as the MAC

## Slide 79: Encryption Mechanism
Flit content
PCRC
Plaintext
AESCntr(K)
A
CRC
0v
0u
len(A)64
len(C)64
C
C
IV
Proc
GHash
AESCntr(K)
MAC

## Slide 80: Modes
Containment mode
Data is released only after the integrity check. Non-speculative.
Skid mode
Use the data speculatively.
Aggregation flit count: 68B (5), 256B (2)
Integrity checking can go on in the background.
Aggregation flit count: 68B (128), 256B (32)
In both cases, epochs can be terminated early

## Slide 81: Switch Support
Model A
The host performs key-exchange (KE) with the CXL switch first.
Model B
First perform KE with the switch.
Model C
Out-of-band management model for setting up and configuring keys.
The host next performs KE with all the downstream devices.
The switch performs KE with all downstream devices.
Performs public-key-based device attestation and reports the status to the host.
cachemem protocols rely on session keys (subsequently generated)

## Slide 82: Trusted Execution Environments (TEE)
Trusted I/O virtualization
  Expand the TCB of each TEE to include CXL devices
  PCI-SIG TEE Device has many protocols defined for PCIe devices
  CXL focuses more on Type 3 devices (memory expanders)
Confidential Computing
  Date in use, Data in transit, Data at rest
Threat model
  Messages need not arrive in order
  Nothing that happens inside the TEE is externally visible
  Targets are directly connected to the host [Limitation]
  Target maintains separation between hosts

## Slide 83: Contd…
Data at rest
  Requires memory encryption
  Host or device-initiated encryption is allowed
  A memory region has a single initiator
  It is the job of the initiator to maintain all the encryption keys
Memory ranges can be recycled – keys and hosts can be changed
Device should support clearing or randomizing memory ranges
Dynamic capacity changes
  Different memory ranges can have different keys

## Slide 84
Reliability

## Slide 85: Reliability, Availability and Serviceability (RAS)
Protocol and link errors are detected and then reported to the host.
Generate PCI_ERR messages (can be reported to the OS)
Poison  Return data tagged as poisoned. Depends on the requester.
Viral  More severe error conditions. Contain and isolate the error.
  Send it to all downstream entities.
  Start a sequence of resets
CRC and Retry
Retraining
Hot-plugging
Data poisoning
CXL Isolation
Viral

## Slide 86: Handling Viral Conditions
Switch
  If any of the downstream ports of a VCS is viral, so is the VCS and the upstream port
  All cachemem traffic has its viral bit set
  Other VCSs are unaffected
  CXL.io traffic continues as usual
  If the switch is affected, then multiple VCs maybe set to viral
  If a VCS is connected to an MLD device, then LDs are made viral

## Slide 87: Device
Device
  Potentially wrong data cannot be written to persistent storage
  Needs to self-isolate
  Commit all writes before receiving the viral message
  Stop all writes that causally succeed the viral message
  Keep responding to snoops
  Complete pending host accesses
  Complete all accesses to the device’s volatile memory
  If the device has had a fault, then take steps to contain the error
  Communicate the viral status in all cachemem messages (to the host)

## Slide 88: References
Compute Express Link Specification, August 2023, Revision 3.1
Das Sharma, D., Blankenship, R., & Berger, D. (2024). An Introduction to the Compute Express Link (CXL) Interconnect. ACM Computing Surveys, 56(11), 1-37.

## Slide 89
The End