## Slide 1
Chapter 11:
Power and Temperature

## Slide 2: Background Required to Understand this Chapter
OOO Pipelines
Caches
Basic Physics
Chapters 4 and 7

## Slide 3: Do computers consume a lot of power?
We have moved from a few Watts to a few Megawatts ...

## Slide 4: How hot do CPUs get?
This Photo by Unknown Author is licensed under CC BY-NC-ND

## Slide 5: Why do we care?
High power consumption raises energy bills and cooling costs
Reduces the battery life
High power  high temperature
Causes an unpleasant experience in mobile phones
Increases fan noise (in desktops/ servers)
Decreases reliability
Cooling costs of a data center are 20-40% of the total energy consumption

## Slide 6: Contents
1.
Power Consumption Model
2.
Temperature Model
3.
4.
AGENDA ITEM 06
Green marketing is a practice whereby companies seek to go above and beyond.
Power Management
Temperature Management

## Slide 7: Types of Power Consumption
Power Consumption
Dynamic Power
Leakage Power

## Slide 8
Dynamic Power

## Slide 9: Consider an Inverter Pair
Input
Output
I1
I2
T1
T2
T3
T4
If the input maintains its value, then all the nodes in the circuit maintain their values (voltages). There is no flow of current.
There is a flow of current, only if a conducting path forms from Vdd to ground, or between the gate of T3/T4 and Vdd/ground (via T1 and T2, respectively).
Any flow of current leads to an I2R heat loss.

## Slide 10: Dynamic Power Dissipation
No dynamic power is dissipated if the inputs maintain their values
The power dissipation is a function of the number of voltage transitions
Each leads to a passage of current and subsequent I2R heat loss
Power simulation tools estimate the number of 1  0 and 0  1 transitions in the circuit. Each transition has an energy cost.

## Slide 11: Basic Idea: Convert an Electronic Circuit into an RC Network
Equivalent Circuit of an NMOS transistor
gate
source
body
drain
+
-
+
-
The equivalent circuit has resistors, capacitors, current, and voltage sources

## Slide 12: Simple Capacitor Charging and Discharging
V
R
C
Vo
switch (2)
switch (1)
Assume that at t = 0, we connect switch (1)
The capacitor gets charged
Total energy provided:
Energy dissipated as heat:
Energy stored in C:

## Slide 13: More about Capacitor (Dis)Charging
While discharging, the stored energy is dissipated as heat
An entire charge-discharge cycle dissipates units of energy
If we have a charge-discharge event every cycle, then
However, every cycle we may not have a charge-discharge event
  Hence, the energy dissipated is
  Here, is the activity factor: between 0 and 1

## Slide 14: Dynamic Power Analysis
What do we know up till now?
  For a simple circuit with a R and a C, the dynamic energy dissipation for a single charge-discharge cycle is: CV2
  What about for a larger circuit?
    Let us assume that in a given charge-discharge cycle: units 1 ... n are active
Energy dissipated =

## Slide 15: Relationship between V and f
Let us look at some textbook results.
Alpha Power Law
For older processes (late nineties) (V >> Vth) and (α = 2)
Thus, we could say: , this will make
The good old days
Nowadays
V is 2-3 times Vth , and α is between 1.1 and 1.3
Thus, this statement would be more correct:

## Slide 16: The Metric
ED2 is a fundamental property of the system.
It can be used to compare different designs.
In this case: ED2 for B is 0.97 times the ED2 of A
Let us say that we have two designs: A and B. As compared to design A,
B is 10% faster yet consumes 20% more energy. Which design is better?
Old model
Approximate

## Slide 17: Short-Circuit Power
T1
T2
short
circuit
current
There is a brief period when both the transistors are conducting.
This is the short-circuit current.
Typically, 10% of the overall dynamic power

## Slide 18
Leakage Power

## Slide 19
Leakage (or static) power is any source of power dissipation that is not present in an ideal transistor.
No current should flow through the gate. However, there might be a small amount of leakage.
Same is the case for a transistor in the off state.
Examples

## Slide 20: Major Leakage Mechanisms
Six different popular leakage mechanisms

## Slide 21: I1: P-N Junction Reverse Bias Current
The p side is connected to a low voltage source and the n side is connected to a high voltage source
Typical scenario in an NMOS transistor (reverse bias)
Main leakage mechanism: Band-to-band Tunnelling (BTBT)
n-type
p-type
drain
substrate

## Slide 22: Band-to-band Tunnelling (BTBT)
Electrons can only occupy a fixed set of energy levels
For doped semiconductors, the Fermi level separates the valence and conduction bands
Electrons can act as charge carriers only in the conduction band
A high electric field forces electrons to tunnel from the valence band of the p-typed region to the conduction band of the n-typed region
Fermi level
Valence band
Conduction band
Electron energy
Metal
Semiconductor
Insulator

## Slide 23: I2: Subthreshold Leakage
Term | Meaning
 | Zero bias mobility
 | Width
 | Subthreshold swing coefficient
 | Gate voltage
 | Drain-source voltage
Term | Meaning
 | Zero bias mobility
 | Width
 | Subthreshold swing coefficient
 | Gate voltage
 | Drain-source voltage
Term | Meaning
 | Gate oxide capacitance
 | Length
 | Threshold voltage
 | Boltzmann’s constant
 | Temperature (in Kelvins)
Term | Meaning
 | Gate oxide capacitance
 | Length
 | Threshold voltage
 | Boltzmann’s constant
 | Temperature (in Kelvins)
The gate voltage needs to be lower than the threshold voltage
A tiny amount of current still flows from the drain to the source

## Slide 24: More about Subthreshold Leakage
The dependence is theoretically exponential.
However, in the 40-80 C range, a linear, piecewise linear, or quadratic assumption is good enough
The relationship between the subthreshold leakage current and the temperature has been a subject of extensive study.
The key term is
Short-channel devices
The source-drain are relatively close to each other. Vth is influenced by VDS.
As increases, it reduces the threshold voltage, and this increases the subthreshold leakage current.

## Slide 25: I3: Gate Oxide Tunnelling
  The gate oxide is very thin (<2 nm)
    Increases the electric field
  Since the oxide layer is so thin, charge carriers tunnel through the thin gate oxide
Fowler-Nordheim Tunnelling: Electrons move into the conduction band of the oxide layer because of an external electric field.
DirectTunnelling: Electrons directly tunnel from the surface of the silicon layer to the gate.

## Slide 26: I4: Hot-Carrier Injection
Electrons escape across the Si-SiO2 interface
In the case of a positively charged gate
  Some electrons can move from the substrate to the gate
  This is not quantum mechanical tunnelling  just plain old kinetic energy

## Slide 27: I5: Gate-Induced Drain Leakage (GIDL)
Condition: Gate-to-drain voltage < 0
Positively charged holes migrate towards the gate oxide layer and accumulate there
Holes migrate into the substrate. Causes a current flow from the drain to the substrate.
n-type
p-type
drain
substrate
n-type
source
gate
Hole accumulation

## Slide 28: I6: Punchthrough Current
Consider transistors with short channels
Possible that the drain-substrate and source-substrate interfaces are reverse biased
The depletion regions can merge
Basically, now the drain and source are connected by a depletion region
Creates a new conductive path that is poorly controlled by the gate
n-type
p-type
drain
substrate
n-type
source
gate

## Slide 29: Ballpark Figures
Dynamic Power
Major component
50-70%
Short Circuit Power
Small (insignificant)
5-10%
Leakage Power
Managed at operating temperatures
20-30%

## Slide 30: Contents
1.
Power Consumption Model
2.
Temperature Model
3.
4.
AGENDA ITEM 06
Green marketing is a practice whereby companies seek to go above and beyond.
Power Management
Temperature Management

## Slide 31: Diagram of a Silicon Chip Package
Heat spreader
Heat sink
Heat spreader
Silicon chip
PCB
Heat
flow
Most of the heat flows vertically through the heat sink (to the ambient)
The heat spreader homogenizes the temperature profile (made of a Ni-Cu alloy)
The heat sink has a large surface area
Lateral heat conduction and flow through the PCB account for 20-30% of the total heat flow (typically)

## Slide 32: Chip Package (Heat Sink and Fan)
Photo by Zane Lee on Unsplash

## Slide 33: The Motherboard
Photo by Jim Varga on Unsplash

## Slide 34: Three Heat Transfer Mechanisms
Conduction
Convection
Radiation
Need contact
Dissipated by the movement of fluids
Dissipated as EM waves

## Slide 35: Some Basic Physics
Fourier’s Law of Heat Conduction
Area of a face: A
3D view
3D version
Power (in Watts)

## Slide 36: A Little Bit of Algebra
Heat (in W) that remains within the volume
(x-axis)
Total heat that remains within the volume, dV

## Slide 37: Some More Algebra
Definition
Total heat that remains within the volume, dV
Rate of internal heat generation for the given volume
Q’
<Total thermal power that enters> + <is generated> within the volume dV

## Slide 38: Another way of looking at Pst
The stored power increases the temperature of dV
density
specific heat
Rate of temperature rise
Equating both the expressions of Pst
Steady state profile
Equating the time derivative and second-order spatial derivatives

## Slide 39: How do we solve the Fourier equation?
Answer:
We can use the Finite Difference Method (FDM). Convert the partial differential equation into a regular system of linear equations.
For element i at time t, we are creating an algebraic equation

## Slide 40: Steady State Solution
This can be converted to a set of linear equations (we can consider all three axes: x, y, and z). We will finally get 
Steady state Fourier’s equation
Discretize a chip into a grid of N cells
Two N-element vectors: T (temperature) and P (power)
N x N matrix A (derived from the principles shown in the previous slide)
Linear transformation

## Slide 41: Transient Solution
 Linear transformation
Let us refer to the time derivative of T as T’
G and C are N x N element matrices
Second derivative  linear transformation
Power
vector
Time derivative
Matrix form of the equation
Solve this equation for all time steps:
For the kth time step:
Transient form

## Slide 42: Electrical Analog of the Problem
Replace temperature with voltage and power with current
The matrix G is the conductance matrix: relates voltage to current
stands for the derivative of temperature (voltage)
Consider a capacitor. I (current/power) = C dV/dt
The C matrix thus stands for thermal capacitance
Thermal problem
Electrical problem

## Slide 43: Electrical Analog
Add thermal resistances between grid cells
Capacitors are added to ground
Solve for the voltages using a regular circuit simulator
Map the solved voltages to temperatures

## Slide 44: Finite Element Method (FEM)
Convert the differential equation into an integral equation. Multiply the original differential equation with a test function, v().
Divide the domain into a set of triangles, rectangles, cuboids or tetrahedrons. Each such basic structure is an element. The points at which elements are connected as nodes.
Create a set of algebraic equations.
  fk is the value of f(x) (function to be computed) at node k
  Let vk(x) be a basis function corresponding to node k
  Let us express:
Express as a system of linear equations and solve
Accurate yet slow

## Slide 45: Green’s Functions
1
Linearity and Superposition
If the total power profile is P = Px+ Py, the final thermal profile is T = Tx + Ty
2
Shift Invariance
For large parts of the chip, the effect of a small power source on its immediate neighborhood is the same.
Exceptions: The rim and corners
FEM and FDM are very slow.
Divide the chip into an NxN grid
Let us apply 1W of power at the point (xp, yq) (function G)
G(x,y) is radially symmetric.
This means G(x,y) = G(-x,-y)

## Slide 46: Green’s Functions
Using the properties of linearity and shift invariance
Green’s function
Continuous
form
Each power source reduces to the Dirac delta function (impulse)
Its value is 0 at all points other than the origin
This is nothing but the 2D convolution operation
Add the effect of all power sources
Green’s function

## Slide 47: Green’s Function
Green’s function
Power profile
Temperature profile
This is a much faster operation than conventional vector-matrix multiplication. O(n2)  O(n) (quadratic to linear)

## Slide 48: Leakage Temperature Feedback Loop
Needs several iterations to converge
Dynamic + Short Circuit Power
Leakage Power
Total Power
Temperature
Can we compute a leakage-aware Green’s function?

## Slide 49: Contents
1.
Power Consumption Model
2.
Temperature Model
3.
4.
AGENDA ITEM 06
Green marketing is a practice whereby companies seek to go above and beyond.
Power Management
Temperature Management

## Slide 50: DVFS – Dynamic Voltage Frequency Scaling
CPUs can run with different voltage-frequency configurations
Increasing frequency  increasing voltage
Most processors use a DVFS table
Frequency | Voltage
1.6 GHz | 1.484 V
1.4 GHz | 1.420 V
1.2 GHz | 1.276 V
1.0 GHz | 1.164 V
0.8 GHz | 1.036 V
0.6 GHz | 0.956 V
DVFS table, Intel Pentium M processor
Can be HW controlled
SW controlled, cpufreq utility on Linux

## Slide 51: Chip’s Power Grid and Frequency Control System
The quartz clock generates a fixed 133 MHz signal
PLL  phase locked loop
  It helps generate a clock signal that is synchronized with the quartz clock
  The frequency is a multiple of 133 MHz
Quartz clock
PLLs
3.3V
0.8-1.2V
Power Supply
Voltage Regulator
CPU
For example, we can use it to generate a frequency of 133 MHz * 16 = 2.13 GHz

## Slide 52: Changing Voltage and Frequency
V0
V1
Voltage conversion
PLL lock time
PLL lock time
Operation
Steady state
Voltage
Voltage conversion

## Slide 53: Hardware-based DVFS
Estimate the amount of CPU activity
If it is low, then reduce the frequency
If it is high, then increase the frequency
Measure the power consumption and temperature
If they are low, then increase the frequency
If they are high, then reduce the frequency

## Slide 54: Software-based DVFS
Each frame needs to be processed in 33 ms
If we can do it in 20 ms
Reduce the frequency till we process it in 33 ms
Need a model to relate processing time and frequency
Classify them: hard real time, soft real time, interactive, periodic, batch
Real time tasks  set DVFS settings based on performance and deadlines
Interactive  Take the user’s perception into account
Periodic jobs  Take the periodicity into account
Batch  Take the user’s requirements into account
Regular programs
Video Codecs

## Slide 55: Linux Speed Governor
  Performance  maximum possible frequency
  Powersave  always run at minimum frequency
  Ondemand  Tries to maintain a constant rate of CPU utilization. Uses a set of thresholds for each DVFS setting.
  Conservative  Much more conservative than ondemand
  Interactive  Similar to Ondemand but does not use thresholds. Uses a formula that relates CPU utilization to frequency.
Linux cpufreq utility

## Slide 56: Clock Gating
Clk
Clk
gate
Functional
unit
Clk input
Dynamic power is dissipated because of voltage transitions
The best way to stop transitions and disable a circuit is by disabling the clock
Set it to 0
Predict if a unit will be idle in the future. Gate its clock.
Use past history
Forecast in the decode stage

## Slide 57: Correctness Problems
How do we verify such a circuit?
Answer:
In a lot of designs, the internal states with and without clock gating need to be identical. Much easier to verify
Does it introduce spurious clock edges?
Answer:
If the clock is at 1, and we gate it, we introduce a premature 1 0 transition. This condition has to be avoided.

## Slide 58: Clock Gating Example
Carry lookahead adder
32
31
30
3
2
1
29
4
G,P
32-31
G,P
30-29
G,P
2-1
G,P
4-3
G,P
32-29
G,P
4-1
G,P
32-25
G,P
24-17
G,P
16-9
G,P
8-1
G,P
32-17
G,P
16-1
G,P
32-1
Block 1
Block 16
Assume bit #4 changes
Only the small part of the circuit shown in red is affected.
The rest of the elements do not dissipate any dynamic power.
They can be clock gated.

## Slide 59: Issue and Fetch Throttling
This is a power vs IPC tradeoff
The fetch rate and issue rate can be dynamically adjusted based on the dynamic power that is being dissipated
This will reduce the IPC (use a feedback-based mechanism)
However, there will be a point till which the reduction in IPC is acceptable (given that Pdyn is reducing)

## Slide 60: Reducing Leakage Power: Power Gating
Ground grid
Sleep trans.
Power grid
Ground grid
Sleep trans.
Power grid
Use transistors to turn off the supply.
We can have two transistors for each island of transistors: connected to the power grid and ground grid
If a circuit is unused, power-gate it: Zero leakage power

## Slide 61: Issues to Keep in Mind
The current available to the functional units (FUs) after adding the sleep transistors.
Large sleep transistors take time to switch on and off. The FU is unusable during this time.
There will be some leakage through the sleep transistors (not much though).
Abrupt changes in the current usage may destabilize the power and ground grids  add decoupling capacitors
Sleep transistors will effectively reduce the supply voltage and raise the ground voltage.
We have to predict well in advance about when a certain FU is unused and can be power gated.
A power-gated FU loses its state.

## Slide 62: Use Multiple Transistor Sizes
Transistors with shorter channels and transistors with longer channels
  Normal transistors: power  1 unit, time  1 unit
  Longer channel transistors: power  0.3 units, time  1.1 units
  Use normal transistors on the critical path, and slower transistors off the critical path (save power)
Gate sizing
  Delay , Power (W  Width of the transistor)
  Slower transistors: smaller W/L ratio (L  Length of the channel)
  Same idea: Slower transistors off the critical path, Faster transistors on the critical path.
Compare

## Slide 63: Adaptive Body Biasing
Forward body biasing  Increase Vbs
  Reduce Vth
  Increase leakage power, increase switching speed
Reverse body biasing  Decrease Vbs (even –ve)
  Increase Vth
  Decrease leakage power, decrease switching speed
Same idea: forward body biasing in the critical path, reverse body biasing off the critical path
Vth = Vth0 – K1 ⋅ Vdd – K2 ⋅ Vbs
The threshold voltage is dependent on the supply voltage and the source-body voltage

## Slide 64: Drowsy Caches
Row of SRAM cells
Vdd = 1V
Allows read/writes
Row of SRAM cells
Vdd = 0.3 V
Maintain the value, accesses not allowed
Drowsy mode
Drowsy mode  Runs at 0.3 V. Maintains the value. Accesses are not allowed
Takes 1-2 cycles to enter/exit drowsy mode (access time increases)
Treat a set of lines as 1 unit
Turn it on/off as 1 unit
Once a set is turned on  Keep it on for 1000-2000 cycles
  Take temporal and spatial locality into account

## Slide 65: Circuit Diagram
Drowsy signal
Word line (WLE) enable
Power line
Drowsy
Drowsy
Vdd-low
Vdd
Latch
Word line (WL)
Switch between
low voltage (Vdd-low)
and high voltage (Vdd)
T3
T4
Drowsy signal = 1, WLE = 0  T1 is on, T2 is off, T3 is on, T4 is off, Power line = Vdd-low , WL = 0
Drowsy signal = 0, WLE = 1  T1 is off, T2 is on, T3 is off, T4 is on, Power line = Vdd, WL = 1
T1
T2
drowsy mode

## Slide 66: Contents
1.
Power Consumption Model
2.
Temperature Model
3.
4.
AGENDA ITEM 06
Green marketing is a practice whereby companies seek to go above and beyond.
Power Management
Temperature Management

## Slide 67: Dynamic Thermal Management
Place thermal sensors all over the chip
Once a temperature hotspot forms
  Traditional mechanisms: DVFS, power reduction, fetch throttling
Stop-n-go
  Temporarily stop a core (let it cool down)
Heat and run thread assignment
  Don’t allow hot cores to be close to each other
  If a thread’s activity increases, migrate it to a colder region of the chip (leakage is (slightly) a nonlinear function of temperature)

## Slide 68: Temperature-Aware Task Mapping
It is not a good idea to have two cores nearby
There will be lateral heat conduction leading to higher temperature
Leakage increases nonlinearly with temperature
The spreader finds it hard to dissipate and distribute the heat
Optimization problem: Minimize the peak temperature subject to performance constraints.

## Slide 69
Temperature is modeled using the Fourier’s heat conduction
equations using the FEM, FDM, and Green’s functions
Power consumption can be reduced using a combination
of DVFS, clock gating, power gating, and throttling
Leakage power is dissipated at non-ideal interfaces: there is current
flow when there should be none.
Dynamic power consumption is proportional to the number of state transitions.
The major power consumption mechanisms in modern CPUs are dynamic power and leakage power
Conclusion

## Slide 70
The End