## Slide 1
Chapter 2:
Out-of-Order Pipelines

## Slide 2: Background Required to Understand this Chapter
Assembly Languages
Basic Processor Design
Basic Pipeline Design
http://www.cse.iitd.ac.in/~srsarangi/archbooksoft.html

## Slide 3
Outline
1.
In-Order Pipelines
2.
Performance Considerations
3.
Out-of-Order Pipelines

## Slide 4: A Simplified Diagram of a Processor with 5 Stages
Fetch
unit
Instruction
memory
Immediate
and branch
unit
Register
file
Control
unit
op2
op1
ALU
unit
Branch
unit
flags
Memory
unit
Data
memory
Register
write unit
Interconnection
element
Instruction
fetch stage
Operand fetch and
decode stage
Execute stage
Memory access
stage
Register write-back
stage
[IF] Instruction fetch
[OF] Operand fetch and decode
[EX] Execute
[MA] Memory access
[RW] Register write-back

## Slide 5: Pipelines
For more efficiency, we can pipeline the design. This will eliminate idleness in the processor.
In-order Pipelines
Instructions enter the pipeline in program order
Inst. Fetch
Operand Fetch
Execute
Memory
Access
Register
Write-back
5-Stage Pipeline

## Slide 6: Pipelined Version of the Processor
Note the positions of the pipeline latches.
IF-OF
Fetch
unit
Instruction
memory
Immediate
and branch
unit
Register
file
Control
unit
OF-EX
op2
op1
ALU
Unit
Branch
unit
flags
EX-MA
Memory
unit
Data
memory
MA-RW
Register
write unit

## Slide 7: Problems with In-order Pipelines
Hazards
  Structural Hazards  Two instructions vie for the same resource (NOT possible in simple 5-stage pipelines)
  Data Hazards  An instruction stands to read or write the wrong data.
  Control Hazards  Instructions are fetched from the wrong path of the branch
Inst. Fetch
Operand Fetch
Execute
Memory
Access
Register
Write-back

## Slide 8: Pipeline Diagrams
IF
OF
EX
MA
RW
1
Reads wrong
values
1
1
1
1
2
2
2
2
2
1
2
3
4
5
6
add r1, r2, r3
add r4, r1, r3
1
2

## Slide 9: Pipeline Interlocks
IF
OF
EX
MA
RW
1
1
1
1
1
2
2
2
3
3
1
2
3
4
5
6
Pipeline
bubble
3
2
2
3
2
3
7
An interlock inserts a nop instruction (bubble) in the pipeline

## Slide 10: Forwarding from the MA to the EX stage  No stalls
IF
OF
EX
MA
RW
1
1
1
1
1
2
2
2
1
2
3
4
5
6
2
2
1: add r1, r2, r3
2: add r5, r1, r4
(a)
(b)

## Slide 11: Forwarding Multiplexers
ALU
Latch
Memory
access unit
Forwarded input
Input 1
Input 2
EX stage
MA stage

## Slide 12: We need 4 Forwarding Paths
Forwarding Paths | Example
RW  MA | ld r1, 8[r2] st r1, 8[r3]
RW  EX | ld r1, 8[r2] sub r5, r6, r7 add r3, r2, r1
RW  OF | ld r1, 8[r2] sub r5, r6, r7 sub r8, r9, r10 add r3, r2, r1
MA  EX | add r1, r2, r3 sub r5, r1, r4
Forward as late as possible

## Slide 13: Final View of the Pipelined Processor with Forwarding Multiplexers
IF-OF
Fetch
unit
Instruction
memory
Immediate
and branch
unit
Register
file
Control
unit
OF-EX
op2
op1
ALU
unit
Branch
unit
flags
EX-MA
Memory
unit
Data
memory
MA-RW
Register
write unit
op2
We add 6 forwarding multiplexers

## Slide 14: Data Hazards in In-order Pipelines with Forwarding
ld r4, 4[r0]
add r5, r4, 1
Need the value in r4 now
Earliest it can be generated
clock
Load-use Hazard
Inst. Fetch
Operand Fetch
Execute
Memory
Access
Register
Write-back

## Slide 15: Solution: Stall the Pipeline
ld r4, 4[r0]
add r5, r4, 1
Cycle N
Cycle N+1
Need the value of r4 now
Here is the data
clock
ld r4, 4[r0]
Cycle N+2
Inst. Fetch
Operand Fetch
Execute
Memory
Access
Register
Write-back

## Slide 16: Control Hazards
beq .label
add r1, r2, r3
beq .label
sub r5, r6, r7
We know the status of the branch now. Assume it is taken.
Cancel these instructions
Two instruction slots are wasted
Inst. Fetch
Operand Fetch
Execute
Memory
Access
Register
Write-back

## Slide 17
Outline
1.
In-Order Pipelines
2.
Performance Considerations
3.
Out-of-Order Pipelines

## Slide 18: Performance Equation - I
Is Computer A faster that Computer B
  Wrong Answers:
    More is the clock speed, faster is the computer
    More is the RAM, faster is the computer
What does it mean for computer A to be faster than computer B
Short Answer: NOTHING
Performance is always with respect to a program. You can say that a certain program runs faster on computer A as compared to computer B.

## Slide 19: Performance Equation - II
IPC is the number of instructions per cycle
Let us loosely refer to the reciprocal of the time per program as the performance
= * *
=
= (assume just 1 program)

## Slide 20: So, what does performance depend on …
#instructions in the program
  Depends on the compiler
Frequency
  Depends on the transistor technology and the architecture
    If we have more pipeline stages, then the time to traverse each stage reduces roughly proportionally
    Given that each stage needs to be processed in one clock cycle, smaller the stage, higher the frequency
    To increase the frequency, we simply need to increase the number of pipeline stages
IPC
  Depends on the architecture and the compiler
  A large part of this book is devoted to this aspect.

## Slide 21: How to improve performance?
There are 3 factors:
  IPC, #instructions, and frequency
  #instructions is dependent on the compiler  not on the architecture
Let us look at IPC and frequency
IPC
  What is the IPC of an in-order pipeline?
1 if there are no stalls, otherwise < 1
Forwarding
Having more not-taken branches in the code
Faster instruction and data memories
Methods to increase IPC

## Slide 22: What about frequency?
What is frequency dependent on …
Frequency = 1 / clock period
Clock Period:
  1 pipeline stage is expected to take 1 clock cycle
  Clock period = maximum latency of the pipeline stages
How to reduce the clock period?
  Make each stage of the pipeline smaller by increasing the number of pipeline stages
  Use faster transistors

## Slide 23: Limits to Increasing Frequency
Assume that we have the fastest possible transistors
Can we increase the frequency to 100 GHz?
Reasons

## Slide 24: Limits to increasing frequency - II
What does it mean to have a very high frequency?
Before answering, keep these facts in mind:
Thumb Rule
P  power
f  frequency
T
Thermo-dynamics
T  Temperature
We need to increase the number of pipeline stages  more hazards, more forwarding paths
1
2
3

## Slide 25: How many pipeline stages can we have?
We are limited by the latch delay
Even with an infinite number of stages, the minimum clock period will be equal to the latch delay
Logic
Latch
Latch
Logic
Latch
Few stages
More stages
Even more stages

## Slide 26: Pipeline Stages vs IPC
CPI = CPIideal + stall_rate * stall_penalty
The stall rate will remain more or less constant per instruction with the number of pipeline stages
The stall penalty (in terms of cycles) will however increase
This will lead to a net increase in CPI and loss in IPC
As we increase the number of stages, the IPC goes down.

## Slide 27: Summary: Why we cannot increase frequency by increasing the number of pipeline stages?
Power
Temperature
Effect of the Latch Delay
Stall penalties will increase

## Slide 28: Since we cannot increase frequency …
Increase IPC

## Slide 29: Increase IPC
Issue more instructions per cycle
2, 4, or 8 instructions
Make it a superscalar processor  A processor that can execute multiple instructions per cycle

## Slide 30: In-order Superscalar Processor
Have multiple in-order pipelines.
Inst. Fetch
Operand Fetch
Execute
Memory
Access
Register
Write-back
Inst. Fetch
Operand Fetch
Execute
Memory
Access
Register
Write-back
Inst. Fetch
Operand Fetch
Execute
Memory
Access
Register
Write-back
Instruction i
Instruction i+1
Instruction i+2
Inst. Fetch
Inst. Fetch
Inst. Fetch

## Slide 31: In-order Superscalar Processor - II
There can be dependences between instructions
Have O(n2) forwarding paths for an n-issue processor
Complicated logic for detecting dependences, hazards, and forwarding
Still might not be enough ...
To get the peak IPC (= n) in an n-issue pipeline, we need to ensure that there are no stalls
There will be no stalls if there are no taken branches, and no data dependences between instructions.
Programs typically do not have such long sequences of instructions without dependences

## Slide 32: Contents
Outline
1.
In-Order Pipelines
2.
Performance Considerations
3.
Out-of-Order Pipelines

## Slide 33: What to do ...
Don’t follow program order
Too many dependences
mov r1, 1
add r3, r1, r2
add r4, r3, r2
mov r5, 1
add r6, r5, 1
add r8, r7, r6

## Slide 34: Execute out of order
mov r1, 1
add r3, r1, r2
add r4, r3, r2
mov r5, 1
add r6, r5, 1
add r8, r7, r6
Execute on a 2-issue OOO processor
Execute 2 instructions in parallel

## Slide 35: Continuation ...
mov r1, 1
add r3, r1, r2
add r4, r3, r2
mov r5, 1
add r6, r5, 1
add r8, r7, r6
cycle 1
cycle 2
cycle 3
issue slot 1
issue slot 2
In Out-of-order (OOO) processors, the execution is not as per program order. It is as per the data dependence order  the consumer is executed always after the producer.

## Slide 36: Basic Principle of OOO Processors
Create a pool of instructions
Find instructions that are mutually independent and have all their operands ready
Execute them out-of-order
ILP
Instruction level parallelism
The number of ready and independent instructions
we can simultaneously execute.

## Slide 37: Revisit the Example
mov r1, 1
add r3, r1, r2
add r4, r3, r2
mov r5, 1
add r6, r5, 1
add r8, r7, r6
Pool of Instructions
Issue ready and mutually independent instructions

## Slide 38: Pool of Instructions: Instruction Window
Needs to be large enough such that the requisite number of mutually independent instructions can be found.
Typical instruction window sizes: 64 to 128
How do we create a large pool of instructions in a program with branches? We need to be sure that all the instructions are on the correct path
for (i = 1; i < m; i++) {
for (j = 1; j < i; j ++ ) {
if (j %2 == 0) continue;
....
}
}
Example

## Slide 39: Problems with creating an Instruction Pool
Typically 1 in 5 instructions is a branch
Predict the directions of the branches, and their targets

## Slide 40
Motivation for Branch Prediction
1
2
3
4
We need
high IPC
This means that
we need a large
instruction window
It will have a
lot of branches.
We need to predict
ALL the branches
correctly.

## Slide 41: The Maths of Branch Prediction
Number of instructions | n
Number of branches | n/5
Probability of predicting any given branch incorrectly | p
Probability of predicting ALL the branches correctly | 
Probability of making at least a single mistake (branch misprediction) in a pool of n instructions. | 
Number of instructions | n
Number of branches | n/5
Probability of predicting any given branch incorrectly | p
Probability of predicting ALL the branches correctly | 
Probability of making at least a single mistake (branch misprediction) in a pool of n instructions. | 

## Slide 42: For (n=100) : A plot of Pn vs p
If Pn = 10%, p has to be as low as 0.5% !!!

## Slide 43
If we need a large instruction window, we need a very accurate branch predictor. The accuracy of the branch predictor limits the size of the instruction window.

## Slide 44
Nature of Dependences

## Slide 45: Dependences between Instructions
Program Order Dependence
mov r1, 1
mov r2, 2
One instruction appears after the other in program order
The program order is the order of instructions that is perceived by a single cycle in-order processor executing the program.

## Slide 46: Data Dependences
RAW  Read after Write Dependence (True dependence)
mov r1, 1
add r3, r1, r2
It is a producer-consumer dependence.
The earlier instruction produces a value, and the later instruction reads it.

## Slide 47: Data Dependences - II
WAW  Write after Write Dependence (Output dependence)
mov r1, 1
add r1, r4, r2
Two instructions write to the same location
The later instruction needs to take effect after the former

## Slide 48: Data Dependences - III
WAR  Write after Read Dependence (Anti dependence)
add r1, r2, r3
add r2, r5, r6
Earlier instruction reads, later instruction writes
The later instruction needs to execute after the earlier instruction has read its values

## Slide 49: Control Dependences
The add instruction is control dependent on the branch(beq) instruction
If the branch is taken then only the add instruction will execute, not otherwise
beq .label
.....
.label
add r1, r2, r3

## Slide 50: Basic Results
In-order processors respect all program order dependences. Thus, they automatically respect all data and control dependences.
OOO processors respect only data and control dependences.

## Slide 51: Can output and anti dependences be removed?
Don’t you think that these dependences are there because we have a finite number of registers.
What if we had an infinite number of registers?
mov r1, 1
add r5, r6, r7
add r1, r4, r2
add r8, r9, r10
add r1, r2, r3
add r5, r6, r7
add r2, r5, r6
add r8, r9, r10
Set r1
Set r1
Use r1
Use r1
Use r1
Avatar 1
Avatar 2

## Slide 52: Solution: Assume infinite number of physical registers
mov r1, 1
add r1, r2, r3
add r4, r1, 1
mov r2, 5
add r6, r2, r8
mov r1, 8
add r9, r1, r2
mov p11, 1
add p12, p2, p3
add p41, p12, 1
mov p21, 5
add p61, p21, p8
mov p13, 8
add p91, p13, p21
Code with architectural registers
Code with physical registers
Architectural register
Physical register
Format in this example: rx is mapped to px<avatar number>

## Slide 53: Renaming
Program with real (architectural) registers
Program with physical registers
RAW dependences
WAR dependences
WAW dependences
RAW dependences
Higher instruction level parallelism (ILP)

## Slide 54: Where are we now ...
Fetch + Decode + Rename
Instruction
Memory
Pool of Instructions
Execution Units
Issue + Reg.
read
Write back results
Branch Predictor

## Slide 55: Issue with Write-back
To an outsider should it matter if the processor is in-order or OOO
NO
Processor
Instructions
Register File
Memory
Update State

## Slide 56: Assume that there is an exception or interrupt
Languages like C or Java have dedicated functions that are called if there is a divide-by-zero in the code.
The question is:
  What if the sub instruction has executed when we enter the exception handler?
  An in-order processor will never do this.
mov r4, 10
mov r2, 0
div r3, r1, r2
sub r4, r4, 1
Divide by 0
Divide by zero handler

## Slide 57: Precise Exceptions
Assume that the exception handler decides to do nothing and return back
After this the sub instruction should be executed
This is exactly what will happen in an in-order processor
In an OOO processor there is a possibility that the sub inst. can execute out of order
The outsider (exception handler) will see a different view as compared to the view it will see with an in-order processor.
Regular Instructions
÷ by 0
Exception
handler
sub
inst.
Flow of actions

## Slide 58: Precise Exceptions - II
To an external observer
  The execution should always be correct and as per program order
  Even in the presence of interrupts and exceptions
Regular Instructions
÷ by 0
Exception
handler
sub
inst.
Regular Instructions
÷ by 0
Exception
handler
sub
inst.
Correct
Wrong

## Slide 59: Precise Exceptions - III
We thus need precise exceptions
Assume that the dynamic instructions in a program (ordered in program order) are: ins1, ins2, ins3 ... insn
Assume that the processor starts the exception/interrupt handler after it has just finished writing the results of instruction: insk
Then instructions: ins1 ... insk should have executed completely and written their results to the memory/register file
AND, insk+1 and later instructions should not appear to have started their execution at all
Such an exception or interrupt is precise
ins1
ins2
ins3
insk
Exception
insk+1

## Slide 60: Precise Exceptions in an OOO Processor
Processor
(Out-of-order execution)
Register File
Memory
Update State
In program order

## Slide 61
In-order pipelines have a limited IPC because
of hazards and branches
Multi-issue in-order pipelines do not solve the
problem. Reason: dependences and interlocks
Hence, we issue instructions out-of-order (OOO). We need
a large instruction window to find sufficient independent insts.
To sustain a large instruction window, we need a very
accurate branch predictor.
To expose additional ILP, we can remove WAR/WAR
hazards. Finally, we need to have precise exceptions.
Conclusion

## Slide 62
The End