## Slide 1
Chapter 3:
The Fetch and Decode
Stages

## Slide 2: Background Required to Understand this Chapter
Basic Boolean Logic
Need for Branch Prediction
RISC and CISC ISAs
http://www.cse.iitd.ac.in/~srsarangi/archbooksoft.html

## Slide 3
Background

## Slide 4: The Fetch Stage
Decoder
PC
Instruction
packet
Branch prediction and fetch logic
Branch outcomes
i-cache
The branch prediction and fetch logic computes the addresses of the instructions to be fetched in the next cycle
The corresponding instructions are fetched from the i-cache
They are sent down the pipeline

## Slide 5: Reading 4 instructions in one go from the i-cache
Cache
lines
Cache
lines
i
j
Instructions
Instructions
They might be in different cache lines
Assume no branches

## Slide 6: Timing: Fetching a single instruction per cycle
Fetch ith instruction
Fetch (i+1)th instruction
Fetch (i+2)th instruction
Predict (i+1)th instruction
Predict (i+2)th instruction
Predict (i+3)th instruction
There is no time to look at an instruction. We just know its PC.
Clock

## Slide 7: Timing: Fetching 4 instructions simultaneously
Fetch 4 instructions
Predict the addresses of the next 4
This is very hard to do. Why?
Clock
Fetch 4 instructions
Predict the addresses of the next 4
Fetch 4 instructions
Predict the addresses of the next 4

## Slide 8: Branches in a Bundle of 4 Instructions
If we have branches in a bundle of 4 instructions, the instructions will not be contiguous
To predict the second branch, we need to first predict the first branch
Regular inst.
Branch
Regular inst.
Regular inst.
Regular inst.
Branch
Regular inst.
Branch
One branch
Two branches

## Slide 9: Branch Prediction: Three Problems
Predictor
Program Counter (PC)
Prediction
Predict if an instruction is a branch or not.
If it is a branch, predict is direction.
Predict its target.

## Slide 10: Contents
1.
Prediction of the Instruction Type
2.
Prediction of the Branch Outcome
3.
Prediction of the Branch Target
4.
Decode Stage

## Slide 11: Is an instruction a branch or not?
Insights
  Given a PC, the status of the instruction (branch or not) does not change.
  Can we use this information?
Approach
  The last time that we had seen a branch remember its PC
  Next time we see a PC, check if we have seen it before
  Also remember the type of the branch:
    Unconditional branch
    Conditional branch  depends on the result of a previous compare instruction
    Function call
    Return

## Slide 12: Make a structure in hardware to remember ...
PC
32 - n
n
Type of the instruction
2n entries
Instruction Status Table (IST)
Assume a 32-bit PC address
Assumption

## Slide 13: Basic Method of Operation
When we see a branch instruction
  Access its corresponding entry in the table
  Record the branch type
When we see an instruction:
  Check the corresponding entry of the table
  Read the type of the instruction
Why do we choose the n least significant bits?

## Slide 14: Instruction Status Table (IST)
If we choose the least significant 10 bits of the PC address, we will have 1024 entries in the IST
Why 10 bits?
For a 32-bit PC, we cannot have a 232 entry table.
  Too big
  Too slow
  Too much of power
  Too much of area
We need to manage with a smaller table

## Slide 15: Destructive Interference
Two instructions can map to the same entry; same last n bits.
Instruction A
Instruction B
Defined as destructive inteference

## Slide 16: Branch Aliasing
Possible for a branch and a non-branch instruction to map to the same entry
Possible for two branches to map to the same entry
Possible for two non-branches to map to the same entry
Need for disambiguation
  Augment each entry of the IST

## Slide 17: Disambiguation Between Addresses
PC
32 - n
n
Type of the instruction
2n entries
Branch type
32 – n
Add a (32-n) bit tag

## Slide 18: Disambiguation
We can keep the status of only branches in the IST
However, for every instruction, we need to check the IST
If there is no entry, then we need to predict that it is not a branch
  Can be wrong
  What to do 
Why does an IST work?
  Mainly because most pieces of code exhibit temporal locality
  In a given window of time instructions tend to repeat themselves

## Slide 19: Contents
1.
Prediction of the Instruction Type
2.
Prediction of the Branch Outcome
3.
Prediction of the Branch Target
4.
Decode Stage

## Slide 20: Predict the Direction of the Branch (Outcome)
If a branch is unconditional  no need to predict (taken)
If a branch is a call/return  no need to predict (taken)
If a branch is conditional  need to predict
Predictor
Program Counter (PC)
Taken or Not Taken

## Slide 21: Example Code
void foo() {
for (i=0; i < 5; i++) {
...
}
}
C
Assembly
.foo:
mov r0, 0
.loop: cmp r0, 5
beq .exit
add r0, r0, 1
b .loop
Predict
This branch has roughly similar behavior most of the time. Predominantly not taken.

## Slide 22: Simple Bimodal Predictor
PC
32 - n
n
Outcome of the branch
2n entries
Predictor Table
Remember the last outcome.
Current prediction = last outcome

## Slide 23: Bimodal Predictor - II
Each entry saves the last recorded outcome of the branch
  taken or not-taken
What is the problem:
  The beq instruction is evaluated 6 times
  Assume the default is not-taken
  First 5 times  correctly predicted not-taken
  6th and last time  incorrectly predicted to be taken
Now assume we call the function foo() once again
  The first time  we will predict taken. This is wrong
  Again the last time will be wrong
  Misprediction rate: 2/6

## Slide 24: Increasing Accuracy
What is the problem?
  The beq instruction is fundamentally biased towards not-taken
  One exception at the end of the for loop cannot change its inherent behavior
Let us add some hysteresis
  Instead of having a single bit in each entry, have a 2-bit counter
Saturating Counter
00
01
10
11
Increment when taken
Decrement when not taken

## Slide 25: Saturating Counters
Algorithm for updates:
  If a branch is taken, increment the saturating counter
  If it is not taken, decrement the counter
For prediction:
  00 and 01  not taken
  10 and 11  taken
00
01
10
11
Predict: Not Taken
Predict: Taken
State | Name
00 | Strongly not taken
01 | Weakly not taken
10 | Weakly taken
11 | Strongly taken

## Slide 26: Bimodal Predictor with Saturating Counters
PC
32 - n
n
Outcome of the branch
2n entries
Predictor Table
2-bit saturating counter
Logic

## Slide 27: Will it help?
1st Time: Predict not-taken. Correct. Starts with 01. Moves to 00
2nd Time: Predict not-taken. Correct. Remains at 00
...
6th Time: Predict not-taken. Wrong. Starts with 00. Moves to 01
.foo:
mov r0, 0
.loop: cmp r0, 5
beq .exit
add r0, r0, 1
b .loop
Misprediction rate: Down from 2/6 to 1/6

## Slide 28: Why do saturating counters work?
In this case, we have a degree of hysteresis. The status of the branch (beq .exit) moves between the strongly not taken and weakly not taken states.
If a branch is strongly biased towards one direction, but once in a while changes its direction, we should use saturating counters.
They capture stable behavior with occasional anomalies.

## Slide 29: Can we do better?
void foo() {
for (i=0; i < 5; i++) {
...
if (i == 4) {
foobar();
}
}
}
C
Assembly
What if we had?
.foo:
mov r0, 0
.loop: cmp r0, 5
beq .exit
cmp r0, 4
bne .inc
call .foobar
.inc: add r0, r0, 1
b .loop

## Slide 30: Global History Register (GHR)
Let us have a shift register that records the history of the last n branches encountered by the processor
  We have one bit for each branch (regardless of the PC)
We record: 1  taken branch, 0  not taken branch
Let us consider a 2-bit shift register also known as the GHR
  GHR  Global History Register
We have two conditional branches in the running example
    beq .exit
    bne .inc
Global history register (GHR)

## Slide 31: Status of the GHR
Beginning of the 2nd Iteration
  01
Beginning of the 4th Iteration
  01
Beginning of the 5th iteration
  01
Beginning of the 6th iteration
  00
.foo:
mov r0, 0
.loop: cmp r0, 5
beq .exit
cmp r0, 4
bne .inc
call .foobar
.inc: add r0, r0, 1
b .loop
Use the GHR information to also decide the direction of the branch.

## Slide 32: GAp Predictor
PC
32 - n
n
Outcome of the branch
2n+k entries
k-bit GHR
Logic
n
k
PHT: Pattern History Table

## Slide 33: GAp Predictor - II
We create 2k times more entries in the predictor table
Capture the global branch history
Use both the global history as well as local (per PC) history to make the prediction.
The accuracy is expected to increase.
  The branch in the last iteration was predicted correctly
In general we can create different combinations of:
    The PC bits and the GHR’s branch history
We have a branch that has an alternating pattern: taken, not-taken, taken, ... . Will a GAp predictor capture the pattern?

## Slide 34: Can we design a class of predictors?
GAg
GAp
PAg
PAp
G  Global history, P  Per PC pattern history

## Slide 35: GAg Predictor
Outcome of the branch
2k entries
k-bit GHR
Logic
k
Only the global history

## Slide 36: PAg predictor
PC
Outcome of the branch
2k entries
k-bit GHR
Logic
n1
k-bit GHR
k

## Slide 37: PAp predictor
PC
32 - n
n
Outcome of the branch
2n+k entries
k-bit GHR
Logic
n1
k-bit GHR
n
k

## Slide 38: Another way of combining information: GShare
PC
32 - n
n
Outcome of the branch
2max(n,k) entries
k-bit GHR
Logic
XOR

## Slide 39: Tournament Predictor
Different predictors have different accuracies for different program snippets
For a very biased branch a bimodal predictor with saturating counters is the best
For an alternating pattern, a PAp predictor works very well
How to know which predictor is the best for which piece of code?
What to do?
  Answer: Use two predictors, and choose between them
Predictor 1
Predictor 2
Choose

## Slide 40: Tournament Predictor
PC
n bits
Choose
Predictor 1
Predictor 2
Prediction

## Slide 41: Operation of a Tournament Predictor
Prediction
  Find the entry in the choice array
  Choose the predictor based on the value of a saturating counter
  Use its prediction  because of the saturating counter, we automatically choose the predictor that performs the best for a given PC.
Training
  Train both the predictors
  Train the entry in the choice array if we chose the wrong predictor
  If both the predictions are the same, we don’t modify the choice array
  If they differ, we increment the counter if Predictor 1 was correct and decrement it if it was incorrect.

## Slide 42: Other methods of prediction
Reduce aliasing
  Incorporate a few tag bits in each entry of the predictor
  Have multiple predictors for different subsets of branches
  Include a bias bit with every branch (its most likely direction), and just predict if we need to agree with the bias bit or not (agree predictor)
Better use of bits
  Separate high confidence and low confidence branches. Dedicate more bits to low confidence branches
Examples of other predictors:
  Bi-mode, Agree, Skew, YAGS, TAGE

## Slide 43: Skewed Branch Predictor
Address bits
Global history
Func 1
Func 2
Func 3
Pred1
Pred2
Pred3
Majority
Prediction

## Slide 44: Prediction and Compression
Consider a sequence of <PC,outcome> pairs
Let’s compress this sequence using a standard program: zip, rar
Is the prediction accuracy related to the compression ratio (size of compressed file/ size of original file)?
  YES
Take a course on information theory
  Read about the Fano’s inequality

## Slide 45: Contents
1.
Prediction of the Instruction Type
2.
Prediction of the Branch Outcome
3.
Prediction of the Branch Target
4.
Decode Stage

## Slide 46: Predict the Branch Target
Predictor
PC of the taken branch
Target

## Slide 47: Use the IST. Let us call it the Branch Target Buffer (BTB)
PC
32 - n
n
Type of the instruction
and target
2n entries
Branch type
32 – n
target

## Slide 48: Calls and Returns
foo
foobar
foobarbar
call
call
ret
ret
0xFC0
0xFF4
foobarbarbar
ret
call
0xBF8
How to predict return addresses?
Solution: Use a stack

## Slide 49: Return address stack (RAS)
foo
foobar
foobarbar
call
call
ret
ret
0xFC0
0xFF4
foobarbarbar
ret
call
0xBF8
0xFC0
0xFF4
0xBF8
Stack

## Slide 50: Summary: The Branch Prediction System
PC
BTB
Type & Target
Branch
Predictor
PC
RAS
Choose
the next PC
next PC

## Slide 51: Contents
1.
Prediction of the Instruction Type
2.
Prediction of the Branch Outcome
3.
Prediction of the Branch Target
4.
Decode Stage

## Slide 52: The Process of Decoding
Expand all the immediate values to 32 or 64-bit values
Extract all the fields
Compute the branch target (if branch is taken)
Add all implicit sources (such as for the return instruction)
Create the instruction packet

## Slide 53: Issues with CISC Instructions
Do not have a fixed length
In x86 the length varies from 1 to 15 bytes
It is hard to fetch multiple instructions at once
  Need to know the boundaries of instructions
  It is hard for OOO pipelines to process them
    Most CISC processors internally convert from CISC to RISC
CISC Instructions
Decode
unit
CISC
instructions
RISC
instructions (μOPs)

## Slide 54: Regular Decoder vs Microcode Cache
x86 has some very complex instructions
Consider the rep movsd instruction
  It can be used to copy n elements from one location to the other  all in one single instruction
  Such instructions map to a large number of μOPs
In comparison, simple add and sub instructions with register operands map to a single μOP.
Microcode Cache
Decoder
CISC
instruction
μOPs
μOPs

## Slide 55: Predecoding CISC Instructions
When we read in an instruction into the i-cache
  We predecode it
   We annotate each byte with additional information
  When we read the bytes from the i-cache, we can use this additional information to decide the instruction boundaries. [Narayan and Tran, 1999]
Lower levels of memory
Predecode unit
i-cache

## Slide 56: Predecoding - II
Start bit  Starting byte of an instruction
End bit  Last byte of an instruction
Functional bit  Interpretation depends on the implementation.
two-ROP and three-ROP bits  Number of μOPs in an instruction
8 bits
start bit
end bit
functional
bit
two-ROP
three-ROP

## Slide 57: Optimizing Operations on the Stack Pointer
There is a pattern here.
  We either modify the stack pointer by adding or subtracting a constant
  The load and store instructions access the stack pointer.
  Update the stack pointer locally or get the memory address directly
Example code
sub sp, sp 8
st r1, 0[sp]
st r2, 4[sp]
....
ld r2, 4[sp]
ld r1, 0[sp]
add sp, sp, 8
Have a copy of the sp register in the decode stage itself.

## Slide 58: Add a csp register in the decode stage
The decode
unit
Subsequent
pipeline stages
csp
Stack pointer
calculation logic
Instruction
packet
Modify the stack pointer / compute the memory address

## Slide 59: Corner Cases
When we encounter such instructions, we set the value of csp to null.
  Treat sp as a regular register in the OOO pipeline.
  Accumulate the difference, Δ, between the value returned by the load addr and the current value of the stack pointer.
  When the load instruction returns with its value: set csp  addr + Δ
ld sp, 12[r1]

## Slide 60: Advantages
Load instructions to the stack can be issued early because we compute the address at decode time.
For load and store instructions to the stack, the address need not be computed in the pipeline.
We can get rid of many instructions that update the stack pointer. This will effectively reduce the dynamic instruction count in the rest of the pipeline.

## Slide 61: Instruction Compression
Instruction caches have a limited size: typically 32 to 64 KB
The performance is extremely sensitive to their size
Hence, we wish to pack as many instructions as possible
Approach 1: Reduced-width instructions
  Support a limited number of opcodes
  Avoid encoding complicated flags and options
  Reduced view of architectural registers
  Reduce the size of the immediate fields
  Implicit operand (accumulators): add r1, r2 (r1  r1 + r2)

## Slide 62: Instruction Compression
i-cache
Dictionary
To the fetch
stage
The compiler or profiler identifies sequences of frequently executed instructions
Each sequence is replaced with a code word
The code word uses fewer bits
The code word  sequence mapping is stored in a separate hardware structure: dictionary
Reduces code size. We can even store decoded instructions

## Slide 63
We can use past history to predict if a PC is a branch or not.
Saturated counters are used to capture steady-state behavior that can have occasional anomalies.
Often, the context determines the direction of branches. A global history predictor such as GAp or PAp is useful in this case.
The BTB records the branch type and the target.
Decode time optimizations are required to increase performance.
Conclusion

## Slide 64
The End