## Slide 1
Chapter 4:
The Issue, Execute, and
Commit Stages

## Slide 2: Background Required to Understand this Chapter
In-Order Pipelines
Precise Exceptions
OOO Pipelines: Basic idea
http://www.cse.iitd.ac.in/~srsarangi/archbooksoft.html

## Slide 3: Contents
1.
Instruction Renaming
2.
Instruction Dispatch, Wakeup, Select
3.
The Load-Store Queue (LSQ)
4.
Instruction Commit

## Slide 4: Renaming (architectural registers  physical registers)
Consider a 4-issue processor
  4 instructions need to be renamed each cycle
  4 instructions have 8 read operands, and 4 write operands
Each read operand, needs to read its value from a physical register
Each write operand needs to be assigned a new physical register
Dependences between the instructions need to be taken care of
There are two main approaches
  Renaming with a physical register file
  Renaming with reservation stations

## Slide 5: Renaming with a physical register file
Every ISA has a set of registers that are visible to software
    These are called architectural registers
    x86 has 8
    x86-64 has 16
    ARM has 16
    MIPS has 32
To ensure precise exceptions, the architectural registers should appear to be updated in-order
However, inside the processor we need to do renaming to eliminate output and anti dependences

## Slide 6: Physical Register File and the Process of Renaming
Physical register file
R1
R2
R16
Architectural register file

## Slide 7: Physical Register File
Consider a system with16 architectural registers and128 physical registers
In this case, architectural registers exist in principle. There is no separate architectural register file.
Each architectural register is mapped to one and only one physical register at any point in time.
112 physical registers are unmapped. They either are empty or contain a value that will be overwritten by a later instruction
Why are 112 registers unmapped?

## Slide 8: Example
r series  architecture, p series  physical
At the beginning ri is mapped to pi
With time, the mapping changes
p12 contains the value of r1 till the value is overwritten. p13 contains the new value. At this point, p12 contains an interim value
mov r1, 1
add r1, r2, r3
add r4, r1, 1
mov r2, 5
add r6, r2, r8
mov r1, 8
add r9, r1, r2
mov p11, 1
add p12, p2, p3
add p41, p12, 1
mov p21, 5
add p61, p21, p8
mov p13, 8
add p91, p13, p21

## Slide 9: Example - II
We need 16 physical registers to contain the latest values of architectural registers
112 physical registers can possibly contain interim values that might be required by instructions in the OOO pipeline (also called in-flight instructions like p12)
More is the number of physical registers  higher is the number of instructions that can simultaneously be in flight  more is the ILP
Renaming: convert architectural register id  physical register id

## Slide 10: Rename Stage
Three Structures
  Register Alias Table (RAT)  Translate architectural register id to physical register id
  Dependence Check Logic (DCL)  Take care of dependences between instructions renamed in the same cycle
  Free List or Free Queue  Maintain a list of unmapped physical registers

## Slide 11: Register Alias Table
RAT table
Architectural register ids
Physical register ids
Rename multiple instructions at once
We get a stream of physical register ids
  Eliminates WAW and WAR hazards

## Slide 12: Operation of the RAT Table
add r1, r2, r3
14
r1
29
34
r2
r3
add p32, p29, p34
Free list
32
mov r3, r1
28
mov p28, p32
RAT table

## Slide 13: Free List
It is a queue of unmapped physical register file ids
An entry is dequeued from it when we need to assign it to an architectural register id
When is an entry added to it? LATER
Update the RAT with the new mapping
Physical register id
Free list

## Slide 14: Dependence Check Logic
Let us say r1 is mapped to p11
The second instruction needs to read the mapping of r1 as p11
What if both instructions are sent to the RAT together?
add r1, r2, r3
add r4, r1, 1

## Slide 15: Dependence Check Logic - II
1) add r1, r2, r3
2) add r4, r1, 1
3) add r3, r4, r6
from RAT
px
inst 2
from RAT
py
px
inst 3
r1  px
r4  py
r3  pz
Mappings from the free list
All mappings from the RAT

## Slide 16: Available bit in the rename table entry
We need some more information in each entry
  An available bit (avlbl)
  It indicates whether the result can be found in the physical register file and the rest of the pipeline or not.
    If not, the instruction has to wait in the instruction window.
physical register id
avlbl bit
rename table entry

## Slide 17: Contents
1.
Instruction Renaming
2.
Instruction Dispatch, Wakeup, Select
3.
The Load-Store Queue (LSQ)
4.
Instruction Commit

## Slide 18: Dispatch
Till the rename stage, instructions proceed in-order.
Dispatch  Send the instruction to the instruction window (IW)
Rename
Instruction Window

## Slide 19: Instruction Window
Status of an instruction in the window
opcode  type of operation: add, subtract, multiply
tag  physical register id
ready bit  does the physical register file contain the corresponding value
opcode
src tag 1
ready
bit 1
src tag 2
ready
bit 2
dest tag
imm1
imm2
valid

## Slide 20: At any point in the instruction window
Instructions waiting for an operand to be ready
Instructions whose operands are ready

## Slide 21: Select and Execute
Select unit
Instruction
Window
Register File Read
Execution Unit 1
Execution Unit 2
Execution Unit 3
Execution Unit 4

## Slide 22: Wakeup
How does an instruction in the IW know that its operands are ready?
The producer instructions need to let it know
Once a producer finishes executing
  Broadcasts the tag (destination physical register id) to the entries of the IW
  Each entry marks its corresponding source operand as ready if the tag matches
  This is called wakeup

## Slide 23: Instruction Window
Tag bus

## Slide 24: Instruction Window - II
src tag 1
tag
Ready bit 1
src tag 2
tag
Ready bit 2

## Slide 25: Broadcast multiple tags at once
src 1
ready 1
src 2
ready 2
Tag bus 1
Tag bus 2

## Slide 26
Instruction Select

## Slide 27: Select Unit
Select unit
grant
request
Instruction window (IW)
Once an IW entry has all its operands ready, it is marked as ready.
It asserts its attached grant line
The select unit chooses one among the ready instructions

## Slide 28: Tree Structured Select Unit: Each node is a choice box
requests
requests
requests
Root Node
Request
Granted Request
Request Granted

## Slide 29: Select Unit for Multiple Resources
What if we have 2 adders, 2 multipliers, and 1 divider?
Solution:
  Have a separate select unit for each class of instructions
  For a select unit that caters to multiple FUs (functional units)
  Three options: Option 1  chain select units
Select
Unit 1
request
grant
request
grant
Select
Unit 2
grant
XOR

## Slide 30: Option 2: Multiple request signals
Send multiple request signals (up to n)
Every level sends at most n requests to the root
The root selects at most n requests, and issues grant signals
This circuit is more complicated than serial select circuits
  The choice boxes need more elaborate logic

## Slide 31: Option 3: Asymmetric Select Units
Have two select units with different policies.
Select unit 1:
  Each choice box gives priority to its left input
Select unit 2:
  Each choice box gives priority to its right input

## Slide 32: Select Policies
Random
Oldest First
Type of opcode
  Load instructions typically have higher priority than stores.
  Other priorities can also be learnt based on execution patterns.
The select policy has an important implication on performance. We should select those instructions that are the most performance critical.

## Slide 33
Tag Broadcast

## Slide 34: RAW Dependences in our Pipeline
Consider consecutive instructions with RAW dependences
add r1, r2, r3
add r4, r1, r5
We want back-to-back execution – Execution in consecutive cycles.

## Slide 35: What does this imply?
Assume we have slightly optimized our pipeline to have
wakeup and select in the same cycle.

## Slide 36: When should we broadcast the tag?
Rename
Reg. Read
Dispatch
Wakeup/Select
Execute
Option 1
(2)
(1)
Reg. Write/
Broadcast
Option 2
(2)
(1)
Option 3
(2)
(1)

## Slide 37: Let us consider Option 3 – Early Broadcast
Allows back-to-back (in consecutive cycles) execution
What needs to be done:
  When (1) is in the Reg. read stage, (2) needs to be in the select stage
  This is possible if we broadcast the tag for (1) when it is in the reg-read stage
  (2) picks up the tag, wakes up, and gets selected for the next cycle

## Slide 38: Classic Example of Forwarding in an OOO Pipeline
Rename
Reg. Read
Dispatch
Execute
Reg. Write
Broadcast
Tag
Rename
Reg. Read
Dispatch
Select
Execute
Reg. Write
Wakeup
(2)
(1)
Forward
Rename
Reg. Read
Dispatch
Select
Execute
Reg. Write
Broadcast
Tag
Rename
Reg. Read
Dispatch
Wakeup
Execute
Select
Wakeup
Broadcast
Tag

## Slide 39: 2-cycle latency for producer: Load-use Hazard
Rename
Reg. Read
Dispatch
Wakeup
Execute
Reg. Write
Broadcast
Tag
Rename
Reg. Read
Dispatch
Wakeup
Execute
Select
(2)
(1)
Forward
Execute
Wait
Select

## Slide 40: Structure of the Pipeline
Rename
Reg. Read
Dispatch
Wakeup
Execute
Reg. Write
Select
Broadcast
Tag
For different instructions, we broadcast the tags at different points of time.
If the execution requires k cycles, we broadcast the tag k cycles after getting selected.

## Slide 41: Forwarding Logic in the Execution Unit
Also called bypass paths
Functional Unit
from the Register File

## Slide 42: When should we mark the avlbl bit?
Option 1: Along with the register write
Rename
Reg. Read/
Broadcast
Dispatch
Select/ Wakeup
Execute
Reg. Write
Some instructions that have
arrived after the broadcast might wait forever

## Slide 43: When should we mark the available bit?
Option 2: Along with the broadcast
Rename
Reg. Read/
Broadcast
Dispatch
Select/ Wakeup
Execute
Reg. Write
The instructions being written to the IW will miss the broadcast and the update of the avlbl bit

## Slide 44: What to do?
Let us fix solutions 1 and 2
Basic features of a new solution:
  Realization: Instructions being written to the IW will miss the broadcast
  These instructions would have also read the avlbl bit as 0
  As a result: they will wait forever
What does the teacher do if some students in the class are sleeping?
  ANSWER: Take one more class
What is the solution here:
  Double broadcast

## Slide 45: Double Broadcast
Both solutions 1 and 2 can be fixed, if two broadcast messages are sent
Let us look at one solution
  Set the avlbl bit to 1 along with sending the Broadcast message
  There might be some instructions that miss the broadcast
  Log the Broadcasted tags in a temporary structure
  Also record all the instructions that are being dispatched in a separate structure called the dispatch buffer
In the next cycle
  Match the tags with entries in the dispatch buffer.
  If there is a match, update the corresponding IW entry
  Clear the entries for the last cycle in the dispatch buffer

## Slide 46
Register Read and Execute

## Slide 47: Read operands from the register file and Issue to the execution units
Select unit
Instruction
Window
Register File Read
Execution Unit 1
Execution Unit 2
Execution Unit 3
Execution Unit 4

## Slide 48: Execute
Select unit
Instruction
Window
Register File Read
Execution Unit 1
Execution Unit 2
Execution Unit 3
Execution Unit 4

## Slide 49: Contents
1.
Instruction Renaming
2.
Instruction Dispatch, Wakeup, Select
3.
The Load-Store Queue (LSQ)
4.
Instruction Commit

## Slide 50: Case of Load and Store Instructions
First, the instructions are sent to the adder to compute the effective address. In this case: 4 + (contents of r3), 10 + (contents of r5)
Next, they are sent to a load-store unit
  Sends the loads and stores to the data cache
  Loads can execute immediately
  Stores update the processor’s state (remember precise exceptions)
  We cannot afford to write the value of stores on the wrong path
    Hence, for stores we wait.
ld r1, 4[r3]
st r2, 10[r5]

## Slide 51: Requirements: Loads and Stores
Stores wait
They need some storage space
Loads first check this dedicated space
Loads cannot directly be sent to the cache
There might be stores before them that are unresolved
Unresolved stores might be to the same address

## Slide 52
Key requirements
Stores have to be sent to the memory system in program order. This is needed for precise exceptions.
We need dedicated storage space  store queue
Stores can only be sent when they are guaranteed
to be on the correct path. A store needs to be the earliest
instruction in the pipeline when it is sent.
Loads first check the store queue. The store queue is
like a cache.
Loads cannot be sent to the memory system until all the stores before it are resolved and do not write to the same
address.

## Slide 53: Load-Store Queue (LSQ)
Allocate an entry at decode time (allocated in order)
Don’t ask when to deallocate an entry (ask later)
When the effective address is computed, update the entry
Time
Load
Store

## Slide 54: Resolved and Unresolved Eentries
Load
Store
Unresolved – address not computed
Resolved – address computed

## Slide 55: Compute Address of a Store – Case I
A
A’
A
A
Load
Store
Unresolved – address not computed
Resolved – address computed
Scan later entries
1. Resolve
2. Forward
3. Stop

## Slide 56: Compute Address of a Store – Case II
A
A’
A
A
Load
Store
Unresolved – address not computed
Resolved – address computed
Scan later entries
1. Resolve
2. Forward
3. Stop

## Slide 57: Compute Address of a Load – Case I
A
A’
A
A
Load
Store
Unresolved – address not computed
Resolved – address computed
Scan earlier entries
2. Stop
1. Resolve

## Slide 58: Compute Address of a Load – Case II
A
A’
A
A’’
A
Load
Store
Unresolved – address not computed
Resolved – address computed
Scan earlier entries
1. Resolve
2. Forward

## Slide 59: Summary of the Discussion
Type | Search direction | Action: Condition
Loads | Search all the stores before it | Terminate and forward value: Store to the same address Terminate: Store with an unresolved address Go to d-cache: Conditions (1) and (2) not met
Stores | Search all the loads and stores after it | Terminate: Store to the same address Terminate: Store with an unresolved address Forward value: Load from the same address

## Slide 60: Actual Implementation
For the purpose of efficiency, have two queues:
  One load queue
  One store queue
Load queue
Store queue
New load entry
New store entry
LSQ

## Slide 61: Both are arranged as a circular queue
head
tail
Entries
Consume
Produce

## Slide 62: Organization
tail
head
Load queue
tail
head
Store queue
Load queue entry
Load address
Index of the tail ptr in the store queue when the entry was added
Store queue entry
Memory address and value
Index of the tail ptr in the load queue when the entry was added

## Slide 63: Basic Search Operations
Search all the stores before a load
Search all the stores after a store
Search all the loads after a store
Represent locations as a bit vector. If a queue has N entries, we have N bits: one bit per each entry.
Create a bit vector called prec – all the locations before a given location after set to 1.

## Slide 64: Implementation of functions: before
head
tail
j
prec(head)
1
1
0
0
0
0
0
0
prec(j)
1
1
1
1
0
0
0
0
before(j)
0
0
1
1
0
0
0
0
Entries before j
in the queue
Compute quickly in HW

## Slide 65: Expressions for other cases
Wraparound
tail
head
j

## Slide 66
Wraparound
tail
head
j
j
tail
head
after function

## Slide 67: Operation of the LSQ
Type | Search direction | Action: Condition
Loads | Search all the stores before it | Terminate and forward value: Store to the same address Terminate: Store with an unresolved address Go to d-cache: Conditions (1) and (2) not met
Stores | Search all the loads and stores after it | Terminate: Store to the same address Terminate: Store with an unresolved address Forward value: Load from the same address
We need to maintain a few more bit-vectors
  resvd: bit-vector to store whether an entry is resolved or unresolved
  match: all the entries that match a given address (we can use a CAM array for this purpose, Chapter 7)
Example: All matching/unresolved stores before a load:

## Slide 68: Wrap-up
We can compute various functions and find a set of locations of interest.
We need to find either the first or last location.
How do we do this quickly in hardware?
Can we use a select unit?

## Slide 69: Contents
1.
Instruction Renaming
2.
Instruction Dispatch, Wakeup, Select
3.
The Load-Store Queue (LSQ)
4.
Instruction Commit

## Slide 70: Precise Exceptions
For an external observer
  Instructions need to appear to execute in order
  At any point of time, the instruction flow can be paused, and resumed later.
Processor
Instructions in order
Instructions in order

## Slide 71: New Structure: Reorder Buffer (ROB)
Reorder Buffer (entry)
  Contains 1 entry for every instruction that has been fetched
  After decoding an instruction, we enter it in the ROB
  If there are no free entries, the OOO pipeline stalls
  Instructions are entered into the ROB in program order
  The ROB is essentially an in-order queue
Updating an entry
  Whenever an instruction finishes its execution, we update the entry of the ROB
  Mark it ready
Removing an entry
It is called retiring or committing
This happens in program order (keep reading ... )

## Slide 72: Removing Entries from the ROB (Commit/Retire)
Every processor has a commit width
  Number of instructions to commit per cycle
  Let the commit width be W
  2, 4, or 6 (typical values)
  Start from the top of the ROB and access the next W entries
  Stop at the first entry, which is not ready or continue till we reach the Wth entry
  Commit all the entries that we find to be ready
ROB
Fetch
and
Execute
Update
entry
Create
entry
Commit

## Slide 73: What does it mean to commit an entry?
Remove it from the ROB
AND
Depends on the type of instruction
Consider instructions with a register destination
  Inst J: r1  r2 + r3
  Assume that r1 is mapped to py
  Before this instruction, r1 was mapped to px
When can we free px?
  After J commits, there are no instructions earlier than J in the pipeline
  There is no instruction that requires the value in px
  px can be reclaimed, and added to the free list

## Slide 74: Updates to renaming
Whenever we see an instruction of the form:
  Instruction J: r1  ...
  Remember the previous mapping of r1 by reading the rename table
  Assume that r1 was mapped to px
  Save this mapping in the ROB entry for instruction J
  When J is committed, unmap px, and return it to the free list
This can be done for all instructions that have a destination operand as a register: ALU instructions, load instruction

## Slide 75: Load and Store Instructions
When should a store be written to memory?
  ANS: When we are sure that it is not in the wrong path of a branch, or no interrupt will come before it
  Only possible at commit time.
  Solution: Send stores to memory at commit time.
  At the same time remove them from the store queue
When should a load be removed from the LSQ?
At commit time 

## Slide 76: What do we in the case of an interrupt?
Let us treat interrupts, exceptions, and branch mispredictions in the same category
We will clearly have some instructions in the pipeline that are on the wrong path. They should not be committed
Use the ROB:
  Mark the instruction that has had an exception, or suffered from a misprediction, in the ROB
  In the case of an interrupt mark the topmost entry in the ROB
  Wait till the marked instruction retires
  Initiate the recovery sequence
  More on the next slide 

## Slide 77: Flushing the Pipeline
Fetch
Rest of the Pipeline
ROB
Insts
Branch misprediction
Flush the ROB, LSQ, IW
and all pipeline registers

## Slide 78: Recovery Sequence
  Flush the pipeline
  Remove the entries from the IW, LSQ, and ROB
  Remove entries from all pipeline registers and other temporary structures (not the rename table or register file though)
Restore the state
  Architectural register state for the last committed instruction and the PC
  The contents in the rest of the physical registers does not matter

## Slide 79: Approach 1: Retirement Register File (RRF)
RRF  Maintain the state of all architectural registers at commit time
Each entry of the ROB gets augmented with the value of the destination register
Write the value of the destination register at commit time.
The RRF maintains a checkpoint at commit time
ROB
RRF
PRF

## Slide 80: Approach 2: Retirement RAT (RRAT)
Why do we need to write the values into the RRF?
Aren’t just the mappings sufficient.
Maintain a copy of the mapping of the destination register in the ROB entry
  Eg: r1  r2 + r3, r1 gets mapped to py
  Maintain r1  py in the ROB entry
  Update the RRAT with this mapping
At the time of recovery
  Transfer the mappings in the RRAT to the RAT
ROB
RAT
RRAT
Prove that this can be done.

## Slide 81: Approach 3: RAT Checkpointing (SRAM based)
Consider the following design
At every branch let us maintain a checkpoint
Set of 16, 7-bit ids
In each entry of the RAT, have a shift register, where each entry of the shift register is 7 bits wide
To create a checkpoint, shift the entries in each row.
The last entries of each shift register represent the current architectural state
Remove the last entries once the corresponding instructions commit
16 entries
7 bit (1 out of 128 phys. regs)

## Slide 82: RAT
Arch reg. id
Latest mapping
Architectural state

## Slide 83: Approach 4: RAT Checkpointing (CAM based)
A CAM (content addressable memory) is like a hash table
  You address each element not by an index, but by a subset of its content
  It is slower than a structure that is addressed by an index
CAM based RAT
128 entries
arch. reg id
7-bit physical reg id
4 bit arch. reg id, valid bit, 7 bit phys. reg id,
SRAM and CAM: Refer to Chapter 6 of the reference: Computer Organisation and Architecture
[Sarangi, McGrawHill, ’15]

## Slide 84: CAM based RAT
At any point of time, 16 bits are set to 1. They contain the current mapping (latest state)
The architectural state is also a set of 16 entries in the RAT table.
We can save a checkpoint by saving the set of valid bits in a 128 bit vector.
For every branch, we can take a snapshot of the valid bits.
The best way to achieve this is to have a shift register in each row of the RAT table, where each entry is 1 bit wide
Use the same idea as the SRAM based RAT

## Slide 85: CAM based checkpointing, one 1 bit per row

## Slide 86: Pros and Cons
RRF
+ point  Simple to implement. Transferring the checkpoint is easy
- point  Extra register writes every cycle. More power
RRAT
+ point  Requires less space in the ROB than the RRF
SRAM based
+ point  Activity only on a branch. Shift operation.
CAM
- point  Need to save the value in the ROB. More space.
- point Has activity every cycle.
- point  Each row of the RAT is wider. Cannot resume from non-branch points.
+ point  Shift operations are easy. Shift only 1 bit.
- point  The CAM per se is a slower structure than an SRAM.

## Slide 87
Renaming is done using the RAT table that stores a mapping between an arch. register and a physical reg.
We additionally need a free list and dependence check logic.
The LSQ manages the dependences between loads and
stores. It forwards data between in-flight loads and stores.
The ROB is used to keep track of in-flight instructions.
Instructions are committed when they complete.
Conclusion
The scheduler comprises the wakeup, select, and broadcast logic. We often perform an early broadcast to avoid stalls.

## Slide 88
The End