## Slide 1
Chapter 7:
Caches

## Slide 2: Background Required to Understand this Chapter
RC and CMOS Circuits
Memory cells, latches and digital logic
Branch Prediction
Chapter 3
CMOS Logic

## Slide 3: Contents
Simpler Version of an OOO Processor
Compiler based Techniques
EPIC based Techniques: Intel Itanium
1.
Overview of Memory Systems
2.
Modelling Caches
3.
4.
5.
6.
Advanced Cache Design
Trace Caches
Instruction Prefetching
Data Prefetching

## Slide 4: How do we read books?
Read the books on the desk more frequently.
Keep books on similar topics on the desk.

## Slide 5: Patterns in Real Life
Temporal Locality
  Tend to read the same book over and over again.
  The person will rarely fetch a book from the cabinet
Spatial Locality
  High probability of fetching and reading books on similar topics
Generalize to the memory hierarchy
Temporal locality
Access the same address over and over again.
Spatial locality
Access similar (proximate) addresses in the same window of time.

## Slide 6: Laptop  desk  shelf Principle
Laptop
Fastest
Most frequently read books and documents are in the laptop.
Desk
Slightly slower
Slightly less frequent documents are on the desk
Shelves
Slowest
Rarely accessed books are in the shelf
Increasing
storage
space

## Slide 7: Apply a similar idea and create a memory hierarchy (use temporal locality)
Processor
I-cache
D-cache
L2 Cache
Main Memory
2-4 cycles
10-50 cycles
200-400 cycles
Inclusive cache hierarchy: each cache contains a subset of addresses that are stored in the lower level.

## Slide 8: Use Spatial Locality
Store data at the granularity of blocks: 32 to 128 bytes A block is also called a cache line
We treat the block as an indivisible, atomic unit
Even if we read or write one byte, we fetch the entire block
A cache simply
contains a
set of blocks
along with some
metadata per block
block
We don’t want to maintain separate per-byte state in a block
Hence, we never fetch a subset of a block
While writing we wait for the block to be fist loaded into the cache.

## Slide 9: Storing Blocks in a Cache
Block address
Byte
offset
26 bits
6 bits
Problem
In a 32-bit memory system, design a cache with a 64-byte block size. Total size: 64 KB
Break the address into two parts: block address and byte offset

## Slide 10: A Simple Mapping
Index
Byte
offset
10 bits
6 bits
Number of cache lines = 64 KB/ 64 B = 1024
Rest of the bits (tag)
16 bits
Aliasing is possible

## Slide 11: Direct Mapped (DM) Cache: Solves the problem of aliasing
Have a separate tag and data array
Access the tag and data array in parallel
If the tag matches, read or update the corresponding data block
There will be a lot of destructive interference.

## Slide 12: Fully Associative (FA) Cache
Array of CAM (content addressable memory) cells in each row
CAM
cell
CAM
cell
CAM
cell
match
line
The match line is set to 1 only if all the CAM cells (contain 1 bit) match the corresponding input bit
Problem with a DM cache  bind a block to a single cache line
We can use a CAM array to implement a fully associative (FA) cache where a block can be stored in any cache line
Input bits

## Slide 13: Fully Associative Cache - II
A block can be stored in any cache line
Disadvantage: Such caches are slow and power hungry

## Slide 14: Compromise Solution: Set Associative Cache
Divide the 1024 cache lines into 256 sets
  Each set contains 4 cache lines
Map a block to a set
  Within the set it can be stored in any cache line
  A flexible design that is fast and reduces the probability of aliasing
We access the tag array
  Read all the tags in the set
  If one of them matches the tag part of the address: declare a hit
  Else it is a miss

## Slide 15: Diagram of a Set Associative Cache

## Slide 16
Basic Operations in a Cache

## Slide 17: The read Operation
Along with looking up the tag, read all the blocks of the set in parallel
If there is a hit, choose one of the read blocks (performance optimization)
If there is a miss, read the block from the lower level and find an empty line in the set
If there is no empty line, evict a block in the set to create space for the new block
lookup
data read
lookup
miss
Lower level
cache
hit
replace
insert
evict
read block
insert
Time
Lower level
cache
if write
back cache

## Slide 18: The Valid bit and Modified bit
Enhance the tag array to contain two important bits
  Valid bit  Does this line contain valid data?
  Modified bit  Has any byte in the block been modified?
Write-through scheme
Propagate every write to the lower level
We can seamlessly evict the block
Write-back scheme
Set the modified bit, if there is a write access.
At the time of eviction  If the line is modified, write it back to the lower level.
Consumes a lot of power

## Slide 19: Write Operation (write-back cache)
If there is a hit, the access is straight-forward. Set the modified bit.
If there is a miss, write to the block, and try to insert it.
If there is no space, find a replacement candidate, and evict it
lookup
data write
hit
lookup
miss
Lower level
cache
replace
insert
evict
Lower level
cache
insert
write
block
Time

## Slide 20: Write Operation (write-through cache)
In a write-through cache, we can seamlessly evict a line
However, at the time of writing, the write needs to be propagated to the lower level.
Because the hierarchy is inclusive, there will be a hit at the lower level.
lookup
data write
hit
lookup
miss
Lower level
cache
replace
insert
evict
Lower level
cache
insert
write
block
Time

## Slide 21: Cache Replacement Policies
Random replacement
FIFO (first in, first out) replacement
LRU  Least recently used
  Impractical because we need to maintain timestamps
  Use Psuedo LRU
    Have a 3-bit saturating counter with each tag
    Increment on every access
    Periodically decrement all counters
    Choose the entry in the set with the least counter

## Slide 22
Mathematical Analysis

## Slide 23: Average Memory Access Time

## Slide 24
Simple Optimizations

## Slide 25: Basic Strategy
Reduce hit time
Reduce miss rate
Reduce miss penalty
Three kinds of misses
Cold or compulsory misses
Misses incurred the first time we read or write a block
Capacity misses
Misses incurred because of the limited size of the cache
Misses incurred because of destructive interference
Conflict misses

## Slide 26: Simple Optimizations
Reduce hit time
Reduce compulsory misses
Reduce capacity misses
Small and simple caches
Increases the miss rate
Increase the block size, prefetching
A large block size reduces the number of blocks
Prefetching, better compiler algorithms

## Slide 27: Simple Optimizations – II
Conflict misses
Increase the associativity
Increases the latency and power consumption
Victim cache
CPU
L1
L2
Victim
The small victim cache
stores frequently evicted
blocks. If a block is not found
in the L1 cache, it is searched
in the victim cache before
searching the L2 cache.

## Slide 28: Static Optimizations – III
Reduce the miss penalty
  We typically request for 4 bytes in a 64-byte block
  Transfer those 4 bytes first and then transfer the remaining 60 bytes subsequently (critical word first)
  Let the processor resume when the 4 bytes arrive (early restart)

## Slide 29
Virtual Memory

## Slide 30: What does a process assume about the memory system?
Process  Running instance of a
program.
It owns a large contiguous chunk of the memory space. Within
this chunk it can access and modify any location at will.
Kernel
0xFFFF FFFF
0xC000 0000
Stack
Heap
BSS
Data
Text
Memory Map

## Slide 31: Two Important Questions
How do we support multiple processes concurrently? A typical machine runs 100s of processes concurrently. Wouldn’t they be able to access each other’s data?
Can we access memory that is larger than the size of the physical memory?
Overlap Problem
Size Problem

## Slide 32: Solution to the Size and Overwrite Problems
Virtual Memory
The processor generates virtual addresses
Convert virtual to actual (physical) addresses
This solves both the problems

## Slide 33: Address Translation
What do we need to ensure?
Unless intended, two processes never access the same physical address
The physical address might point to a location outside main memory (solution to the size problem)
Address
Translation
Virtual address (32 bits)
Physical address (32 bits)

## Slide 34: Basic Idea
Divide the virtual memory space (addresses that programmers and compilers see)
  Into 4 KB pages
Divide the physical memory into 4 KB frames
Map pages to frames
Ensure that the mapping solves the size and overwrite problems

## Slide 35: Overlap Problem: Map in such a way that there are no overlaps
Process 1
Process 2
Physical
address
space
Page
Frame
Map pages to frames such that there are no overlaps.

## Slide 36: Size Problem: Create an array of frames in the hard disk called swap space
Process 1
Main
memory
Page
Swap
space
Frame
Create an array in the hard disk or other form of stable storage. This is the swap space.
If a page points to a frame in the swap space, we need to bring the frame to main memory.

## Slide 37: Page Tables and TLBs
The mappings are stored in a dedicated data structure called the page table.
The page table takes several cycles to access. This is a slow process.
Have a fast hardware structure called the TLB to cache the most frequent mappings
The processor accesses the TLB first, uses the mapping if it is there. Otherwise, it accesses the page table.

## Slide 38: Flowchart for a memory access
TLB hit?
Yes
Memory
access
Send mapping
to processor
Frame in
memory?
Yes
No
Populate
TLB
No
Send mapping
to processor
Free frame
available?
No
(1) Evict a frame
to swap space
(2) Update its page
table
Yes
Create/update mapping
in the page table
Populate
TLB
Send mapping
to processor
Read in the new frame
from swap space (if possible),
or create a new empty frame

## Slide 39: Contents
Simpler Version of an OOO Processor
Compiler based Techniques
EPIC based Techniques: Intel Itanium
1.
Overview of Memory Systems
2.
Modelling Caches
3.
4.
5.
6.
Advanced Cache Design
Trace Caches
Instruction Prefetching
Data Prefetching

## Slide 40
SRAM Array

## Slide 41: Cross-Coupled Inverters
Cross-coupled inverters
Cross-coupled inverters
implemented using CMOS logic
Q
Q
Q
Q

## Slide 42: Basic SRAM Cell
Word line (WL)
BL
BL
(Bit line)
W
1
W
2
Q
Q
Word line
transistor
Each cell is connected to a bit line pair. They have complementary values.

## Slide 43
Decoder
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
SRAM
cell
Row
address
BL
BL
WL
WL
WL
Write
driver
Write
driver
Data in
Sense amplifier
Sense amplifier
Data out
Data in
Column mux/demux
Column
address
SRAM Array

## Slide 44: Structure of a Cache
Address
Tag Array
Data Array
wordlines
column muxes
SRAM cell
sense amps
Comparators
hit/miss
mux drivers
Output driver
data output
Decoder

## Slide 45: Precharging Trick
Do we wait for one bit line
to go to 0 V and the other to
reach 1 V?
This will take too much time.
SRAM cell
Sense
Amplifier
BL
BL
Assume ground is 0 V and the supply is 1 V

## Slide 46: Precharging trick – II
To figure out which side is heavier, do we have to wait for one of the stones to hit the ground?
Keep measuring the slope of the rod. Once it is more than a threshold (noise value), declare the result.

## Slide 47: Precharging Trick – III
We don’t have to wait for the voltage values to reach the final values.
Here is the noise margin
Precharging step: Set the voltage of the bit line pair to 0.5 V using powerful precharge drivers
A dedicated sense amplifier senses the difference in the voltage
It sets the output, once the difference crosses the threshold

## Slide 48: The Sense Amplifier
Bit Line (BL)
Bit Line (BL)
Output
AMP1
AMP2
AMP3
T1
T2

## Slide 49
CAM Array

## Slide 50
Word line (WL)
BL
BL
W1
W2
A
A
match line
T1
T2
T3
T4
Q
Q
A CAM Cell
Checks whether Q = A

## Slide 51: Truth Tables
Q |  | T1 | T2
0 | 0 | off | off
0 | 1 | off | on
1 | 0 | on | off
1 | 1 | on | on
Q |  | T1 | T2
0 | 0 | off | off
0 | 1 | off | on
1 | 0 | on | off
1 | 1 | on | on
 |  | T3 | T4
0 | 0 | off | off
0 | 1 | off | on
1 | 0 | on | off
1 | 1 | on | on
 |  | T3 | T4
0 | 0 | off | off
0 | 1 | off | on
1 | 0 | on | off
1 | 1 | on | on

## Slide 52: CAM Array
Decoder
Row
address
BL
BL
Write
driver
Write
driver
Data in
Sense amplifier
Sense amplifier
Data out
Data in
Column mux/demux
Column
address
A
A
1
1
CAM mode
BL
BL
A
A
2
2
BL
BL
A
A
n
n
WL
WL
WL
match
match
Priority encoder
Matching
index
CAM
cell

## Slide 53
The Cacti Tool

## Slide 54: Modeling and Simulating Caches
  First, we need to find the access times of both caches
  Convert access time into clock cycles
  Simulate both the configurations: find the faster one
To find the time it takes to access a cache
  We need to use a simulation tool
  Most popular simulation tool  Cacti (designed by HP labs)
Along with that
  We need power and area data as well
  Cacti 6.0 provides all of these
Should I use a 4 KB, 2-way assoc. cache or an 8 KB, 1-way assoc. cache? Should I allow concurrent accesses?

## Slide 55: Idea that will not work: Multi-ported structures
Re-design the SRAM cell  slower and larger
WL1
WL2
BL1
BL2
BL1
BL2

## Slide 56: Usage
cacti C B A
  C  cache size in bytes
  B  block size in bytes
  A  associativity
  Number of banks (a bank is a sub-cache) (more later ..., assume 1 for now)
Hidden inputs
  bo  output width (32 or 64 bits)
  bwidth  input address width (32 or 64 bits)
Cacti
inputs
area,time,power

## Slide 57: Sample input and output

## Slide 58: How does Cacti work?
Given the inputs, it tries to create the most optimal (often fastest) cache
What can happen?
Caches can get very asymmetric. rows >> columns, or columns >> rows (>> means significantly more than)
Slow design
Fast design

## Slide 59: How to make it fast?
  Set the aspect ratio first:
    Number of sets mapped to a wordline  Nspd
    A higher Nspd will increase the number of column multiplexers  slowdown
    However, it will decrease the number of rows, and thus the size of the address decoder  speedup
Then create subarrays of SRAM cells
  Ndwl  Number of vertical cut lines
  Ndbl  Number of horizontal cut lines
  Total number of subarrays created  Ndwl * Ndbl
The optimal values of Ndwl , Ndbl, and Nspd are found out by Cacti

## Slide 60: Partitioning an SRAM array
Large SRAM array
Ndwl
Ndbl
A * B * Nspd bytes

## Slide 61: Banks and Subarrays
A large array can be split into multiple banks
  A bank is an independent array.
  Different banks can be accessed simultaneously
  Given an address, we first need to map it to a bank, and then access that specific bank
  Advantage of banking  faster banks and more parallel access
  Disadvantage of banking  More area, and additional delay in deciding the bank. Higher wire routing overhead.
  We split each bank into multiple subarrays
  Compute the three parameters: Ndwl, Ndbl, Nspd

## Slide 62: Arrange the Subarrays in a Hierarchy
Each bank can then be split into subbanks
  Subbanks do not allow parallel (concurrent) access
  A subbank stores a full block (Advantage: read the block in one go)
Each subbank is further divided into mats and subarrays
Each mat supplies a portion of a block (enhanced parallelism)
Subarrays in a mat share a decoder or predecoder
Array
Bank
Subbank
Mat
Subarray

## Slide 63: Summary
First set the aspect ratio: Nspd
Then compute Ndwl and Ndbl  Total Ndwl * Ndbl subarrays
Divide the cache into equal-sized banks
  Keep in mind the probability of bank conflicts
  A bank is a fully independent array with its separate address and data lines
Hierarchy: bank  subbank  mat  subarray
subbanks do not allow independent or concurrent accesses
Enhanced intra-block parallelism
  A mat stores a part of a block. It contains multiple subarrays.
  subarrays share their decoding logic in a mat.

## Slide 64: Examples: (2-way assoc, 64B line size, 1 bank, 32 nm) Access Time vs Cache Size
Chart: 
| 4096 | 8192 | 16384 | 32768 | 65536 | 131072
Access Time | 0.42 | 0.43 | 0.44 | 0.46 | 0.5 | 0.55
Little variation. Because of Cacti’s optimizations.

## Slide 65: Area vs Cache Size
Chart: 
| 4096 | 8192 | 16384 | 32768 | 65536 | 131072
Area | 0.14 | 0.17 | 0.187 | 0.22 | 0.28 | 0.56
Roughly linear scaling

## Slide 66: Cache Size vs Power
Chart: 
| 4096 | 8192 | 16384 | 32768 | 65536 | 131072
Power | 0.149 | 0.15 | 0.155 | 0.17 | 0.19 | 0.25
Little variation. Because of Cacti’s optimizations.

## Slide 67
Elmore Delay Model

## Slide 68: Time and Power Modelling
How to compute the delay of a cache?
Replace it by its equivalent RC model.
RC model of a wire

## Slide 69: Assumptions
Let us only consider RC trees
We only consider voltage sources that provide step inputs. 0  1 or 1  0
Elmore Delay Model

## Slide 70: Example: RC Tree
V
C
1
R
1
R
2
R
3
C
2
C
3
R
4
R
5
C
4
C
5
2
3
1
4
5
0
ground
1  0 transition

## Slide 71: Replace Capacitors with Current Sources
V
C
1
R
1
R
2
R
3
C
2
C
3
R
4
R
5
C
4
C
5
2
3
1
4
5
0
-C3 dV3(t)/dt

## Slide 72: Principle of Superposition
AIM: Compute the voltage at node Vx at time t.
Methodology:
  The aim is to find  voltage at terminal i because of the current source placed at terminal j
  While considering one current source, disconnect the rest of the current sources (replace by an open circuit)

## Slide 73: Generalize the Result
Let Pij denote the RC circuit in the shared path from from 0i and 0 j
0
i
j
RC circuit
Definition

## Slide 74: Elmore’s Assumption
Superposition
Elmore’s Assumption

## Slide 75: Using Elmore’s Approximation
Solution

## Slide 76: Results Derived by using the Elmore Delay Model
The latency of a wire is proportional to the square of its length.
The bit line and word line can be modelled very easily.
Full SRAM banks can be modeled as a sequence of simple elements.

## Slide 77: Contents
Simpler Version of an OOO Processor
Compiler based Techniques
EPIC based Techniques: Intel Itanium
1.
Overview of Memory Systems
2.
Modelling Caches
3.
4.
5.
6.
Advanced Cache Design
Trace Caches
Instruction Prefetching
Data Prefetching

## Slide 78: Pipelined Caches
Let us say that a cache takes 5 cycles to access.
Do we wait for 5 cycles for the next access?
Pipeline the cache.
Even if the latency is high, we can achieve a high throughput.

## Slide 79: Tasks Involved in a Read Operation
Tag array
access
Data array
access
Tag
comparison
Data block
selection
Tag array
access
Data array
access
Tag
comparison
Data block
selection
Stage 1
Stage 2
Stage 3
Pipeline
latches
Pipelined Implementation

## Slide 80: More on Pipelining
We simply add new pipeline buffers
The SRAM access can be pipelined by adding latches after the decoder
  This is very expensive in terms of area and power.
The write access can be pipelined
  Access tag array  Compare the tags  Effect the write in the data array

## Slide 81: Non-Blocking Caches
Let us say that there is a cache miss.
  Do later cache access stall?
Cache accesses need not be blocked. We simply need to record all accesses to the missed block.
MSHR
Miss Status Holding Register

## Slide 82: Design of an MSHR
MSHR
Miss queue
Address
Miss queue entry
Read/
write
Word
address
Tag
Store
value
For every address we have an associated miss queue  Ordered in FIFO order

## Slide 83: Operation of an MSHR
When there is a miss in a cache, an entry is created in its MSHR. If there are no free entries, the request blocks.
  We also create an entry in the miss queue.
  This is a primary miss.
If at the same time, another miss arrives, it will be called a secondary miss.
  If it is a write, we just append it to the tail of the miss queue.
  If it is a read, we search for earlier writes in the miss queue to the same set of bytes. If we find an entry, the value is forwarded. Else, we enqueue the entry.

## Slide 84: Skewed Associative Caches
Conflict misses are the main problem
Solution:
  Have multiple subcaches
  Use different indexing functions for each subcache
Address
f
1
f
2
f
3
f
4
Subcache 1
Subcache 2
Subcache 3
Subcache 4

## Slide 85: Basic Insight
Consider two addresses
If most likely
If they conflict in one subcache most likely they will not conflict in another subcache
Reduce conflict misses
Overheads
These functions need to be computed
Replacements are tricky

## Slide 86: Replacements
Assume that we want to add the block B at address A
We will first check if ... are free
If not, we evict the block B’ with address A’ stored at . We insert block B in the first subcache at
We try to accommodate B’ at or or
If none of these locations are free, we choose one of the locations randomly. Let’s say, it is We insert B’ there by evicting block B’’. Again we try to accommodate B’’.
We repeat this process a few times before finally giving up and evicting a block.
Cuckoo search

## Slide 87: Way Prediction
Default mechanism in set-associative caches
  Read all the tags and blocks in a set (simultaneously)
  Compare the tag part of the address with each of the tags
We do more work that what is required.
Predict the way in which the tag will be found
Access that way first
If the tags don’t match, access the rest of the ways
Fast and power-efficient

## Slide 88: Way Prediction Techniques
Predict based on the program counter
Use a branch predictor-like mechanism
Problems: Memory addresses for an instruction might keep changing
Approach 1
Approach 2
Use an estimate of the memory address to predict the way
If the address is available use it, else use some other piece of information.

## Slide 89: Way Prediction Techniques – II
Combine the value of the base address with the offset (like GShare). We may use additional PC bits
Then use a branch predictor-like mechanism to predict the way
Load instruction
ld r2, 12[r1]
Read registers
Compute the address
Check for LSQ forwarding
Access the d-cache
r1 XOR 12
Way prediction

## Slide 90: Loop Tiling
How do we run large loops that access large arrays on a system with caches?
How is a 2D array stored?
Row-major order: Store the first row, then the second, then the third and so on.
Column-major order: first column, second column, and so on

## Slide 91: Basic Matrix Multiplication
for (i=0; i<N; i++) {
for (j=0; j<N; j++) {
sum = 0;
for (k=0; k<N; k++)
sum += A[i][k] * B[k][j];
C[i][j] = sum;
}
}
Matrix Multiplication
Not suitable when arrays are large, and caches are comparatively much smaller.

## Slide 92: Tile the Multiplication
(a)
(b)
i
j
i
j
ii,kk
kk,jj
ii, jj
Operate on blocks of data

## Slide 93: Tiled loops
/* Iterate through the tiles */
for (ii =0; ii <N; ii +=b) {
for (jj =0; jj <N; jj +=b) {
for (kk =0; kk <N; kk +=b) {
/* iterate within a tile */
for (i=ii; i < ( ii+b) ; i++) {
for (j=jj; j < ( jj+b) ; j++) {
for (k=kk; k < ( kk+b) ; k++) {
C[i][j] += A[i][k] * B[k][j];
...
b
b
Fits within the cache

## Slide 94
Prove that the algorithm is correct.

## Slide 95: VIPT (Virtually Indexed Physically Tagged) Caches
We need to spend an additional cycle translating the address after we have computed it.
What if we don’t need any translation to access the correct set in the L1 cache?
Compute address
Translate address
Access the d-cache
Possible

## Slide 96: VIPT Caches
Page id
Offset
Frame id
Offset
Virtual address
Physical
address
Offset
Index
Byte offset
Tag
Access all the ways in the set while the address translation mechanism is working. It will compute the tag.

## Slide 97: The Design of the VIPT Cache
Offset
Index
Tag
Tag array
Data array
Address
translation
(a) VIPT cache
Multiplexer
Output
Access tag array
Read data array
Address
translation
Tag comparison
Select data block
Time
(b) Timeline
Overlap

## Slide 98: Contents
Simpler Version of an OOO Processor
Compiler based Techniques
EPIC based Techniques: Intel Itanium
1.
Overview of Memory Systems
2.
Modelling Caches
3.
4.
5.
6.
Advanced Cache Design
Trace Caches
Instruction Prefetching
Data Prefetching

## Slide 99: Trace Cache
Execution of a typical program
Basic Block 1
Basic Block 2
Basic Block 3
Basic Block 4
Basic block  A set of instructions with a single point of entry and a single point of exit
We fetch a sequence of basic blocks from the i-cache
Such a sequence is called a trace
Let us have a cache that stores such traces. We have the option of sequentially reading out a full trace
This is called a trace cache (first major use: Pentium 4, circa 2000)
If the trace is accurate, we need not predict branches or decode instructions

## Slide 100: Early Approaches
Traditional approach
  A cache line contains contiguous cache blocks
Peleg and Weiser
  Store successive basic blocks per cache line
  Trace segments cannot span multiple cache lines
Melvin et al.
  CISC instruction sets decode instructions into micro-ops
  The idea is to store decoded micro-ops for each instruction in a cache line
  Saves some decoding effort
Can we combine and augment these solutions?

## Slide 101: Structure of a Solution
A trace consists of multiple cache lines
It is a linked list of cache lines (each line is a trace segment)
We need a method to place a marker to terminate a trace and start a new trace.
Trace Head
Trace Body
Trace Body
Trace Tail

## Slide 102: Design of the Trace Cache
Tag array
Data array
m
OPs
Controller
Fill buffers
NLIP
m
IP

## Slide 103: Storage of Traces
Store trace segments in consecutive sets
Each trace segment stores the number of the way in the next set
Each data line can store up till 6 decoded micro-instructions
Head
Head
Body
Body
Body
Body
Body
Body
Tail
Tail
Way 0
Way 1
Way 2
Way 3
Set 1
Set 2
Set 3
Set 4
Set 5

## Slide 104: Basic Rules
Rules for storing trace segments in a data line
  Never distribute micro-ops of a macro instruction across cache lines
  Terminate a data line if you encounter more branch micro-ops than a threshold
Termination of the trace creation process
  Encounter an indirect branch
  Interrupt or branch misprediction notification
  Maximum length of trace (64 sets) reached

## Slide 105: The Tag Array
Field | Meaning
Type | Trace head, body, or tail
Next way | Index of the way for the next trace segment (next set)
Prev way | Index of the way of the previous trace segment (prev. set)
NLIP | Address of the next CISC instruction
μIP | Index into the table of micro-instructions
Tag
valid
bit
Type
Next way
Prev way
NLIP
μIP

## Slide 106: State Diagram (reading a trace)
Head lookup
Body lookup
Tail
Body miss
Miss
Start a new trace
Search for head
Read micro-
instructions
Complex instruction
encountered
Return
Search for head

## Slide 107: State Diagram (creating a trace)
Fetch from i-cache
Wait for
m
OPs
Bypass
m
OPs
m
OPs reach
the fill buffer
Trace segment
end condition
Transfer
Trace not
ended
Head lookup
Trace end
condition
detected
Read micro
instructions
Complex
instruction
Trace not
ended
Trace end
condition
detected

## Slide 108: Contents
Simpler Version of an OOO Processor
Compiler based Techniques
EPIC based Techniques: Intel Itanium
1.
Overview of Memory Systems
2.
Modelling Caches
3.
4.
5.
6.
Advanced Cache Design
Trace Caches
Instruction Prefetching
Data Prefetching

## Slide 109: Misses in the Caches
We can incur a large performance penalty if there is a miss in the i-cache
  For the next 10-50 cycles, there will be no instructions to fetch, if there is an L2 hit
  If there is a miss in the L2, we have nothing to do for hundreds of cycles
  IPC will suffer
What is the solution?
  Prefetch memory addresses
  Meaning: Predict memory addresses that will be accessed in the future. Fetch them from the lower levels of the memory hierarchy before they are actually required.

## Slide 110: Instruction Prefetching
1
Find patterns in the i-cache access sequence
Leverage this pattern for prefetching
2

## Slide 111: Precautions
Do not prefetch too soon.
Do not prefetch too late.

## Slide 112: Next Line Prefetching
Pattern: Spatial locality
If cache line X is accessed, there is a high probability of accessing lines: X+1 and X+2
Reason: The code of most functions spans multiple i-cache lines and we have spatial locality
Leverage this pattern: If a cache line X incurs an i-cache miss, read X and the next k lines from the L2 cache
If k is too high, we might fill the cache with useless data.
Almost all prefetching algorithms operate on the miss sequence, not on the access sequence.

## Slide 113: Markov prefetching
Pattern: i-cache miss sequences have high repeatability
The miss sequence of a core typically looks like this:
High correlation between consecutive misses
Leverage this pattern for prefetching
X | Y | …. | X | Y | … | X | Y | … | X | Y | …
Miss sequence:

## Slide 114: Markov prefetching
Record the i-cache miss sequences in a table
Given that cache line X incurs a miss, predict the line which will incur a miss next
Cache line | Option 1 |  | Option 2 | 
 | Address | Frequency | Address | Frequency
X | Y | 3 | Z | 1
X | Y | …. | X | Y | … | X | Z | … | X | Y | …
Miss sequence:
Higher probability
Markov table:

## Slide 115: Markov Predictors - II
We can instead have an n-history predictor that takes the last n misses into account
Whenever there is a miss, access a prefetch table. Find the next few addresses to prefetch. Issue prefetch instructions.
Also, update the frequencies of the entries for the last n-1 misses.
All prefetch requests go to a prefetch queue. These requests are subsequently sent to the L2 cache (lower priority).

## Slide 116: Call Graph Prefetching
Pattern: The function call sequence is predictable
Leverage this pattern: predict and prefetch the function that may be called next

## Slide 117: Call Graphs
......
......
......
......
prepare_window( )
......
......
update_window( )
......
......
clear_window( )
......
....
set_buttons()
....
set_textboxes()
......
......
......
......
show_screen
set_buttons()
set_textboxes()
......
......
......
......
clear_window
update_window( )
prepare_window

## Slide 118: Call Graphs - II
show_screen
prepare_window
set_buttons
set_textboxes
update_window
clear_window
1
2
3
1
2

## Slide 119: Call Graph based Prefetching (in software)
prefetch prepare_window
......
……
prepare_window()
prefetch_update_window
......
......
update_window( )
prefetch clear_window
......
......
clear_window( )
......
show_screen
......
prepare_window( )
......
......
update_window( )
......
......
clear_window( )
......
......
show_screen
becomes
The compiler analyzes the code and inserts instructions to prefetch the code of functions.

## Slide 120: Hardware Approach Call Graph History Cache (CGHC)
Each entry in the data array contains a list of functions to be subsequently executed.
The index maintains a pointer to a function in the data array entry.
The index is initially 1. We prefetch the code of func1. After returning from func1, we set the index to 2, and prefetch the code for func2.
Tag Array
Data Array
Function id
Index
func 1
func 2
func 3
func 4
func 5

## Slide 121: Operation (Function Call)
Function Call.
X calls Y
Access the entry of Y in the CGHC
Does it exist?
NO
Create entry
Prefetch the first function in Y’s call sequence
YES
Put Y in X’s call sequence at the appropriate index (if required)

## Slide 122: Operation (Function return)
Y returns to X
Reset the index of Y to 1
Access X’s call sequence
Increment the index
Prefetch the next function in the call sequence

## Slide 123: Patterns
Technique | Pattern/Insight
Next line prefetching | Spatial locality
Markov prefetching | i-cache miss sequence has high repeatability
Call graph prefetching | Function access sequence has high repeatability

## Slide 124: Contents
Simpler Version of an OOO Processor
Compiler based Techniques
EPIC based Techniques: Intel Itanium
1.
Overview of Memory Systems
2.
Modelling Caches
3.
4.
5.
6.
Advanced Cache Design
Trace Caches
Instruction Prefetching
Data Prefetching

## Slide 125: Data Prefetching
Instead of instructions, let us now prefetch data
Important distinction
  Instructions are fetched into the in-order part of the OOO pipeline
  Data is fetched into the OOO pipeline
    As a result, the final IPC is slightly more resilient to data cache misses
    Nevertheless, prefetching is very useful
    i-cache hit rates are typically very high, whereas d-cache hit rates are much lower
    Hence, the margin for improvement is significant.

## Slide 126: Stride based Prefetching
Consider the following piece of code
  For the arrays A and B, the addresses in each iteration differ by 4 bytes (assumed to be the size of an integer)
  For the array, C, consecutive accesses differ by 8 bytes
  This instruction will translate into multiple load/store RISC instructions
    There will be only one memory access per instruction
  The hardware will observe that for the same PC
    The memory address keeps getting incremented by a certain value (4 or 8 bytes in this case)
    This fixed increment is called a stride
for (i = 0; i < N; i++ ) {
...
A [i] = B[i] + C[2*i];
}

## Slide 127: Reference Prediction Table (RPT)
For each instruction
  Keep track of the address and the stride
  We can decide to prefetch N iterations in advance
  State: initial  transient (not sure about the stride)  steady
Instruction Tag
Previous Address
Stride
State
PC
Memory address
Adder
Prefetched address

## Slide 128: Extensions
How many iterations do we prefetch in advance?
  This depends upon the rest of the instructions in the for loop
  This ideally should be dynamically adjusted
  For a subset of prefetches
    Monitor the number of cycles between when a line is prefetched and it is actually used
    Should not be negative
      It is being prefetched too late. We will not get the desired benefits.
    Should be a small positive number
      The data arrives just before it is needed.

## Slide 129: Pointer Chasing
...
/* traverse the linked list */
node * temp = start_node ;
while ( temp != NULL ) {
prefetch (temp -> next ); /* prefetch the next node */
process ( temp );
temp = temp -> next ;
}
Linked list accesses cannot be characterized by strides.
We can insert code to prefetch subsequent linked list nodes.

## Slide 130: Runahead Mode
What happens when we do incorrect prefetching?
  We have misses because we do not prefetch the correct data and we displace useful data. L1 misses can more or less be taken care of by an OOO pipeline
  L2 misses are bigger problems
What happens on an L2 miss
  We go to main memory (200-400) cycles
  What does the OOO pipeline do?
    The IW and ROB fill up
    It pretty much stalls
Idea: Do some work during the stalled period

## Slide 131: What can we do?
Enter runahead mode
  Return a junk value for the request that misses in the L2 cache
  Restart execution with the junk value
  We will produce junk values (in the forward slice)
  That is still okay. Why?
    We will have a lot of instructions in the pipeline that can be executed correctly because they are not in the forward slice of the mispredicted load.
    We will prefetch data into the caches, and train the predictors
Once when the L2 miss returns
  Flush the instructions in the forward slice of the L2 miss
  Re-execute them
  Very effective prefetching technique

## Slide 132: Operation
Before entering the runahead mode
  Take a checkpoint of the architectural register file + the branch history register + return address stack
Start the runahead mode
  Add an invalid (INV) bit to each register
  The L2 miss generates an INV value
  All the instructions in its foward slice have an INV value
  The INV value is same as the poison bit (learnt earlier)
  Question:
    Do we restrict invalid values to the pipeline or let them propagate?

## Slide 133: Value Propagation
If till the pipeline  nullify all stores
If till the L1  do not evict INV data from the L1. Invalidate it later.
Preferably not till the L2 (massive amount of state management)
Pipeline
L1
L2

## Slide 134: Let us take INV values till the L1
If we use the traditional L1 cache, there will be some problems
  We need to maintain both INV and non-INV data together
  What if they are on the same line (additional state required)
Solution: have an additional runahead cache that contains only INV data.
Pipeline
Runahead L1
L1

## Slide 135: Runahead L1 Cache
A store might have the INV flag set for two reasons
  Its address is INV. Ignore.
  A stores data is INV. Access the runahead cache, and also prefetch.
Perform the store
  Let us keep some additional state per line. Let us mark those words written by an INV store as INV.
Cache Line
INV Stores

## Slide 136: Loading a Value
First try forwarding in the LSQ
If not possible:
  Access the runahead cache and L1 cache in parallel
  The runahead cache gets preference
  Load the data. If the data is marked as INV, marked the load data as INV
  Otherwise, load data from the L1 cache
  If there is a miss, load data from the L2 (acts as prefetching)

## Slide 137: Operation (Contd...)
Keep fetching and retiring (in runahead mode) instructions
All the instructions before the speculated load (in program order) will retire
After that, all instructions are in runahead mode (will not retire)
As we fetch and execute more and more instructions, we in effect do more prefetching
What about updating branch predictors?
  Best option: Treat runahead instructions as normal instructions
Return from runahead mode
  Similar to a branch misprediction, restore the checkpoint

## Slide 138: Helper Threads
In a multicore processor, we can spawn threads (lightweight processes) on other cores
For some of the memory addresses, the threads can execute the backward slice of the load – instructions that determine the address of the load.
The computed address can be prefetched.
Requires some compiler support to identify the critical loads.

## Slide 139
Trace caches can be used to increase the IPC of the core by
storing frequently executed traces. We can save on decoding.
Both instruction and data prefetching techniques are
heavily used in modern processors to improve the IPC.
Caches use a variety of optimization techniques: pipelining,
non-blocking execution using MSHRs, way prediction, tiling, etc.
We typically use the Elmore delay model to estimate the
latency and power consumption of data and tag arrays.
Caches are divided into a tag array and data array.
We can have three kinds of caches: FA, SA, and DM.
Conclusion

## Slide 140
The End