## Slide 1
Chapter 8:
The On-chip Network

## Slide 2: Background Required to Understand this Chapter
Pipelining
Caches
Basic graph theory
Chapter 2 and 7

## Slide 3: Contents
1.
Overview of an NoC
2.
Message Transmission
3.
4.
5.
6.
Routing
Design of a Router
Non-Uniform Cache Architectures
Performance Aspects

## Slide 4: Layout of a Modern Chip
A mix of cores, cache banks, and memory controllers.
Different layouts are suitable for different kinds of workloads.
Core
Cache
bank
Memory
controllers
(a) Checkerboard layout
(b) Rim layout

## Slide 5: Definition of a Node
Any object that can send or receive a message.
Core
Cache Bank
Memory Controller
Accelerator

## Slide 6: Router
Every communicating node has a router that orchestrates the communication on its behalf.
Node
Router
Router
Channel
Data buffers

## Slide 7: Key Question
How do the routers communicate with
each other?

## Slide 8: Connection between two routers with a single link.
Source
Receiver
Unbuffered link
D is the delay
l is the length of the wire
Quadratic relationship
Long wires are very slow

## Slide 9: Buffered Wires
Source
Receiver
Buffered link
Buffers
s = number of segments
d = delay of a buffer
Delay is linear in terms of
the length

## Slide 10: Multi-layer Interconnects
Metallic layers
Vias

## Slide 11: Types of Interconnects in Silicon Chips
1. Local wires  These are used to connect transistors within the same functional unit.
2. Intermediate wires  Used to connect transistors across adjoining functional units.
3. Global wires  Used to connect transistors across the chip.
Most intermediate and global wires are typically buffered.

## Slide 12: Simple yet Naïve Solution
Connect the routers using a bus (single set of copper wires)
Bus
Node
Node
Node
Node
Bus master
The bus master needs to grant permission to a node to transmit a message.
It becomes a point of contention.
Slow and not scalable

## Slide 13
Layout of a multicore processor
Cache bank
Core
Memory
controller
Router
Tile
Need a complex topology

## Slide 14
Create a Network on Chip (NoC)
Arrange a set of nodes as tiles
A router sends and receives all the messages for its tile
A router also forwards messages originating at other routers to their destination
Routers are referred to as nodes. Adjacent nodes are connected with links.
The routers and links form the on chip network, or NoC.

## Slide 15
Bisection Bandwidth
  Number of links that need to be snapped to divide an NoC into two equal parts (ignore small additive constants). Indicative of path diversity between two nodes. More is the path diversity more is the congestion tolerance.
Diameter
  Maximum optimal distance between any two pair of nodes (again ignore small additive constants)
Aim : Maximise bisection bandwidth, minimise diameter
A Few Definitions

## Slide 16
Example Topologies

## Slide 17
Chain
Ring
No path diversity
Limited path diversity
Chain and Ring

## Slide 18
Fat Tree
Links get wider towards the root. This ensures that the root does not become a bottleneck

## Slide 19
Mesh
Every node has a degree of 4 other than at the rims and corners

## Slide 20
Torus
Every node has a degree of 4
The long links cause an issue.

## Slide 21
Folded Torus
Problem of long links gets solved.

## Slide 22: High-Radix Topologies
Nodes are connected to more than 4 neighbors
Additional path diversity
Low diameter
Hard to implement it in an NoC
  Much easier to implement in a cluster computer
  Hypercubes
  Clos network
  Butterfly

## Slide 23
Hypercube
H
0
H
1
H
2
H
3
H
4
0
000
001
010
011
110
111
101
100
(a)
(b)
(d)
(c)
(e)
0
1
00
01
10
11

## Slide 24
Properties of a Hypercube
If a hypercube has N nodes
  Diameter  log2(N)
  Bisection bandwidth  N/2
It is a recursive data structure
  Connect two copies of an order (N-1) hypercube
    by connecting corresponding nodes together.

## Slide 25
Clos Network (nr inputs and outputs)
r = 3
m = 4
n = 4
Three-layer network
4x4 switch
3x3 switch
r n x m
m r x r
r m x n

## Slide 26
Properties of a Clos Network
If m >= n, we can always connect an unused input terminal to an unused output terminal by rearranging the rest of the connections.
If m >= 2n – 1, we can do the same without rearranging the rest of the connections.

## Slide 27
Butterfly
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
00
01
10
11
00
01
10
11
00
01
10
11
Only uses 2x2 switches
Efficient implementations with high-radix routers exist.

## Slide 28
Summary
Topology | #Switches | #Links | Diameter | Bisection Bandwidth
Chain | 0 | N-1 | N-1 | 1
Ring | 0 | N | N/2 | 2
Fat Tree | N-1 | N log(N)* | 2 log(N) | N/2*
Mesh | 0 | 2N - 2√N | 2√N – 2 | √N
Torus | 0 | 2N | √N | 2√N
Folded Torus | 0 | 2N | √N | 2√N
Hybercube | 0 | N log(N)/2 | log(N) | N/2
Butterfly | N log(N)/2 | N + N log(N) | log(N) + 1 | N/2
* Assume that the size of each link is equal to the number of leaves in its subtree |  |  |  | 

## Slide 29: Contents
1.
Overview of an NoC
2.
Message Transmission
3.
4.
5.
6.
Routing
Design of a Router
Non-Uniform Cache Architectures
Performance Aspects

## Slide 30: Hierarchy of messages sent in a NoC
Packet
Flit
Phit
Message

## Slide 31: Description
Message  Set of bytes sent from a sending node to a receiving node
Packet  A message is broken into multiple packets.
    All the bytes in a packet take the same route.
Flit  Flow control digit: size is 8 bytes or 16 bytes. An atomic unit of bytes. A router never breaks a flit.
Phit  Physical digit. While transmitting a flit, it might take multiple cycles. If we can send 32 bits at a time, then transmitting a 128-bit flit will take 4 cycles. In each cycle we send a 32-bit phit.
Head flit
Body flit
Body flit
Tail flit

## Slide 32: Flow Control
Buffers at the sender’s side
Buffers at the receiver’s side
Transmission of a single flit
What do we do if we do not have enough buffer space at the receiver’s side?
We are not allowed to drop a flit.
Have some information at the sender about the free buffer space available at the receiver.

## Slide 33: Credit Based Flow Control
The sender (A) maintains an estimate of the number of free buffers at the receiver (B).
If the sender thinks that the receiver has enough free buffers, then only it sends a flit.
Once the receiver frees a buffer it sends a credit to the sender
Term | Meaning
 | Time it takes a single phit across the A  B link
 | Time it takes to send the flit from A  B
 | Time it takes to process a message.
 | Total credit round trip delay
Term | Meaning
 | Time it takes a single phit across the A  B link
 | Time it takes to send the flit from A  B
 | Time it takes to process a message.
 | Total credit round trip delay

## Slide 34: Assumptions
The routers are clock synchronized.
  Time is measured in the units of “router cycles”. All delays are an integral number of router cycles.
We first receive a message, then process it, and then add it to a buffer.
All the status messages (credits, on, off, etc.) are 1 phit each

## Slide 35: Process of Sending Credits
Node A
Node B
Buffer freed
Credit received
Processing
Flit received
time t
Round trip delay

## Slide 36: Properties of Credit Based Flow Control
From a buffer getting freed to receiving the next flit (because of the credit that was sent), it takes units of time.
We can receive a maximum of flits in this time period.
If the size of the buffer at B is at least () flits, then A will not stall (assuming B can send credit messages as soon as possible)
  We need to send a credit message, whenever a buffer becomes free.
  Not power efficient
Disadvantage

## Slide 37: Improvement: On-Off Flow Control
Channel: A  B
Improvement over normal credit-based flow control
Off-threshold (NOFF)
  If we have NOFF free buffers in B, then it immediately sends a message to A to stop sending
On-threshold (NON)
    If the number of free buffers in B is equal to NON , then it sends a message to A to start sending

## Slide 38: Graphical Description

## Slide 39: Analysis: Off message
How long is the risky period (during which packets are sent to B), after B has sent the OFF message?
(t + tph + tpr) – (t – tf - tpr) = tph + tf +2tpr = tD
A
B
t + tph
t
t - tf - tpr
t + tph + tpr
Risky
period
After sending the OFF message, B can receive tD/tf flits
flit
OFF message
It needs to have enough buffer space available

## Slide 40: The equation for NOFF
Because we cannot drop flits, we have:

## Slide 41: Analysis: ON message
Necessary condition:
If NON = NOFF + 1
After we receive 1 message, we will have to send an OFF message
Very inefficient
To avoid frequent ON and OFF messages, there should be a sizeable gap between the thresholds, such that we can transmit in one go without frequent stop-and-start messages.

## Slide 42: Better estimate for NON
A
B
OFF message
ON message
Shadow of an ON message
Assume NON is equal to the number of buffers  We cannot send a single message in this period.
This means that N (number of buffers) should be far greater than NON
N – NON is the number of buffers with messages. It should be more than a threshold.

## Slide 43: Better estimate for NON - II
We can keep transmitting flits in the shadow of an ON message. We will have enough flits.
We thus have:
If B has N flit buffers and the following conditions hold:

## Slide 44
Transmission of Messages
on the NoC

## Slide 45: Circuit Switching
Reserve buffer space in the routers along the way
Once the entire path is reserved, then send a message
After sending the message, clear the buffers
Source
Destination
Very slow

## Slide 46: Space-time diagram
L = Length of the message in flits
K = Number of hops/ cycles to reach the destination (assumption: 1 cycle per hop)
B = channel bandwidth: flits per cycle
K = 3, L = 2, B = 1
Total time:
3K + L/B - 1
S
1
2
D
1
2
3
Takes 1 cycle to traverse a hop. B divides L and B ≥ 1
Assumptions

## Slide 47: Advantages and Disadvantages
Once a circuit is established, we can transfer as may bytes as we want.
This is good for bulk transfers.
Large overheads for a single transfer.
Locks up resources for more time than the actual requirement.

## Slide 48: Packet based Flow Control: Store and Forward (SAF)
Router
Send a packet to a router (set of flits), store the entire packet, and then forward it to the next router.
Router
Router
M
L/B
Hops
Cycles
M
M
M
M
M
K * L / B cycles

## Slide 49: SAF Protocol
When the flits are being sent, we wait for the entire packet to be buffered.
This is a waste of time. We can send flits to the next router on the way.
Analysis: Total time required  K * L/B

## Slide 50: Virtual Cut-Through Routing (VCT)
Router
Router
Router
Even though we send flits before the entire packet is buffered, we need to ensure that there is space
for the entire packet.

## Slide 51: Problems in the VCT Scheme
A
B
C
D
Flit from packet 1 destined to C
Flit from packet 2 destined to D
Flit from packet 3 destined to a node
beyond D
We cannot send any flit from packet 1 till the router at B is totally empty because we need to buffer the entire packet.

## Slide 52: Comparison of Circuit Switching with Packet-level Switching
Scheme | Time in cycles
Circuit Switching | 3K + L/B – 1
Store and Forward (SAF) | K * L/B
Virtual Cut Through (VCT) | K + L/B - 1

## Slide 53: Solution: Buffer at the Flit Level
A
B
C
D
Wormhole Flow Control
We do not have to wait for space to be created to buffer the entire packet.
The flow control is at the level of flits.
Does not solve all our problems.

## Slide 54: Problem with Wormhole Flow Control
A
B
C
D
Flit from packet 1 Route: A  B  C
Head of the Line Blocking
The black flits can go to C, however, the orange flits are
blocking them.

## Slide 55: Solution: Virtual Channels (VCs)
Multiplex a single physical channel among different virtual channels. Have a separate buffer queue for each virtual channel.
A
B

## Slide 56: Virtual Channels: Two per physical channel
A
B
C
D
Each physical channel split into two virtual channels.
No HoL blocking.

## Slide 57: Virtual Channels: Pros and Cons
There is no head of the line (HoL) blocking.
Increases throughput significantly.
We can multiplex a single physical channel among different virtual channels.
Increases the complexity of the router.
We now need to assign the virtual channels in a router (additional work).

## Slide 58: Contents
1.
Overview of an NoC
2.
Message Transmission
3.
4.
5.
6.
Routing
Design of a Router
Non-Uniform Cache Architectures
Performance Aspects

## Slide 59: Aim of Routing
Send a message from a sender to a receiver
  Via a path of intermediate routers
  Good to have a choice of multiple routes  path diversity
What is a good route?
  Shortest path?
  Shortest time?
Good routes typically minimize the latency, and are also fair  do not unnecessarily penalize other packets

## Slide 60: Problems to avoid …
Deadlocks
Livelocks
Starvation

## Slide 61: Avoid Deadlocks
Photo by Jens Herrndorff on Unsplash

## Slide 62: Meaning of a Deadlock
No car can make any progress.

## Slide 63: Deadlock in an NoC
Assume a buffer size of 1 flit
No progress …

## Slide 64
Flits continuously get transmitted, but they never reach their destination
  They keep moving in infinite loops
These routing algorithms never terminate.
A certain flit never makes progress (never moves towards its destination). It has the lowest priority, its router always transmits other flits.
Both the problems can be solved by implementing ageing. The longer a flit stays in a router, the higher is its priority.
Livelock
Starvation
Solution: Ageing

## Slide 65: Dealing with Deadlocks
Deadlock in a circuit-switched system.
Packet | Source | Destination | Holds channel | Wants channel
P1 | D | B | 1 | 2
P2 | A | C | 2 | 3
P3 | B | D | 3 | 4
P4 | C | A | 4 | 1
Deadlock

## Slide 66: Resource Dependence Graph (RDG)
There is an arrow from Pi to channel j, if the packet Pi is waiting for channel j to become free.
There is an arrow from channel j to packet Pi, if the packet Pi holds the right to transmit on channel j.
A cycle in the RDG implies a deadlock.

## Slide 67: Channel Dependence Graph (simplified version of the RDG)
There is an arrow from Channel A
to Channel B if the packet (message)
that owns Channel A is waiting to
get access to Channel B.
A cycle in the CDG implies a deadlock.

## Slide 68: We can even have deadlocks with virtual channels 
10  0th VC of physical channel 1
11  1st VC of physical channel 1

## Slide 69: Turn Graphs
Disadvantage of CDGs and RDGs
They lose the orientation information of the channels.
Basic Steps
Consider a path C in the channel graph.
The TG contains all the nodes and channels belonging to C. It preserves the orientations of the channels. It does not contain any other channel.
We insert a new node called the channel node in the middle of each edge/channel.
There is a path C in the CDG  There is a path having the same channel nodes in the TG (and vice versa)
A cycle in the CDG  A cycle in the TG

## Slide 70: Illustration of a TG (Turn Graph)
Original Graph
A
B
D
C
Channel | Src  Dest
1 | A  B
2 | B  C
3 | C  D
4 | D  A
CDG
1
2
3
4
TG
A
B
D
C
1
2
3
4

## Slide 71: Properties of the TG
Every edge in the CDG translates to either a set of collinear nodes in the TG, or a turn in the TG.
Every cycle in the CDG is also a cycle in the TG.
Every cycle in the CDG can be translated to a sequence of straight paths and turns in the corresponding TG
Aim:
Ensure that there are no cycles in the turn graph (TG).
Try to introduce routing protocols that are provably deadlock free (their TGs will never have cycles).

## Slide 72: Dimension-Ordered Routing (X-Y Routing)
Route along the x-axis first
Then send the message along the y-axis
If we have n dimensions, we can order them, and route the message first along dimension 1, then dimension 2, and so on.

## Slide 73: Assume that the TG has a cycle
We either have a clockwise cycle.
Or an anti-clockwise cycle.
The Ck Ck+1 turn is not allowed. A packet is traversing in the y
direction first, and then in the x direction.
Hence, the TG does not have any cycles  No deadlocks
Example: anti-clockwise cycle
Can be proven for all the other cases

## Slide 74: Problems with X-Y routing
X-Y routing has no path diversity. The route is fixed.
The algorithm cannot adapt to congestion.
It is simple.

## Slide 75: Oblivious Routing (Valiant’s Algorithm)
Choose a point P at random
Send the message from the source to P, and then from P to the destination.
Deals with congestion much better by providing path diversity.
The routes can be very long and sub-optimal.

## Slide 76: Minimally Oblivious Routing
Create a window around B.
Send the message from the source to P (any node within the window),
and then from P to the destination.
Reduced path diversity.
The computed routes are not very long.

## Slide 77: Adaptive Routing: Theory of Turns
We can have two kinds of
cycles: clockwise and anti-
clockwise.
There are 8 possible turns.
Out of these we can allow only 6
turns (at the most). We have to
remove one turn from each cycle
to prevent a cycle from forming in
the turn graph.
Clockwise
Anticlockwise

## Slide 78: Types of Routing Algorithms based on Turns
X-Y Routing
Only 4 allowed turns
Disallow one of the turns in each cycle.
We have 4 choices per cycle:
(clockwise or anti-clockwise). We thus have a total choice of 16 combinations.
There are 16 such routing algorithms that eliminate one turn from each cycle

## Slide 79: Examples of Popular Routing Algorithms
Name | Turns Disallowed | Allowed Turns
West-first | N  W, S  W | 
North-last | N  W, N  E | 
Negative-first | N  W, E  S | 
High path diversity, and congestion avoidance capability

## Slide 80: Date line based method where we have 2 VCs per physical channel
Inject the packet into VC 0
It keeps travelling in VCs numbered 0 till it crosses the date line.
Then it shifts to VCs labelled 1. It continues on these VCs till it reaches the destination.
There are no deadlocks.
A flit on a VC numbered 1 will never wait for a VC numbered 0. A cyclic wait is not possible.

## Slide 81: Contents
1.
Overview of an NoC
2.
Message Transmission
3.
4.
5.
6.
Routing
Design of a Router
Non-Uniform Cache Architectures
Performance Aspects

## Slide 82: Interface
Router
N
S
E
W
Local
(L)
N
S
E
W
Local
(L)

## Slide 83: Input Buffers
All the flits are buffered first.

## Slide 84: For multiple VCs (per physical channel) we can have a single, large buffer.
VC0
VC1
VC2

## Slide 85: Route Computation

## Slide 86
Destination | Direction
1 | W
2 | N
3 | E
4 | W
6 | E
7 | S ¦ W
8 | S
9 | S ¦ E
Each node maintains a routing table (node table). Specifies the next hop for the final destination.
This table shows the routing decisions for the North-last algorithm at Node 5. Note that in some cases we have a
choice of two routes.
Make a decision based on congestion information. Take into account the delay incurred in sending flits the last time the channel was used.
L
Example of a Routing Table

## Slide 87: Router Pipeline till Now
Buffer Write
Route Computation
VC Allocation in the physical channel

## Slide 88: Next Step: Allocate switch ports
Design of an m x n switch

## Slide 89: This part of the router’s pipeline
Allocate Switch Ports
Reserve a path to the output port
Fairness is important.
Switch Traversal
Latency is critical.
Release Resources
Once the tail flit leaves the router. Reclaim the VC.

## Slide 90: Hierarchical Designs for Switches
Bigger switches
Smaller switches

## Slide 91: Area-Latency Tradeoffs
For an m x n switch:
Latency = m + n
Area = m * n
Design |  | Area cost | Latency cost
Level 1 | Level 2 |  | 
10 x 5 | -- | 50 | 15
Five 2 x 1 | 5 x 5 | 35 | 13
Two 5 x 2 | 4 x 5 | 40 | 16

## Slide 92: Dimension Sliced Switch (Used for X-Y Routing)
Since no turns are allowed from (N/S) to (E/W), we can create two
separate switches.
The lower router sends flits in a horizontal direction.
For any turn to the y-axis, it sends the flits to the upper router.
N
S
The upper router only routes flits on the y-axis, and delivers flits to the local tile.

## Slide 93: Allocation and Arbitration
An arbiter chooses one out of N requests for resource allocation.
Similar to instruction select logic.
An allocator creates a one-to-one mapping between N requests and M resources.
Can either be created by chaining together arbiters.
Or by creating a custom structure.

## Slide 94: Matching between resources and requests
Condition 1: Every request is mapped to at most a single resource.
Condition 2: Every resource is mapped to at most a single request.
Condition 3: Request Ri is mapped to resource Sj if f(Ri, Sj) is true. The f(R,S) function is true if request R is interested in resource S.
R1
R2
S1
S2
R1
R2
S1
S2
R1
R2
S1
S2
Not mapped
Sub-optimal matching
Optimal matching
Interest
Match

## Slide 95: Round Robin Arbiter
D
D
D
Grant 1
Grant 3
Grant 1
Grant 2
Grant 2
Grant 3
Priority 1
Request 1
Grant 1
G
1
G
2
G
3
Priority 2
Request 2
Grant 2
Priority 3
Request 3
Grant 3

## Slide 96
This is a simple scheme.
No way of enforcing a priority between requests.
If an agent is not interested, it is still given a chance.

## Slide 97: Matrix Arbiter
If a given agent is not interested, then it sets all the entries in its row to 0, and all the entries in its column to 1 (other than diagonal elements).
In every cycle the request is granted to the agent, which has 1s in all of the entries in its row other than the diagonal element.
Once the ith agent is done servicing its request, it sets all the entries in its row to 0, and sets all the entries in its column to 1 (other than the diagonal elements). This means that it relegates itself to the lowest priority.
Agents
Agents
i
j
Agent i has a priority over agent j

## Slide 98: Matrix Arbiter

## Slide 99: A Separable Allocator
Possible that all the requests get selected for the same resource
in the first column of switches.
Rij = ith agent is interested
in the jth resource
Matching is not maximal.

## Slide 100: Wavefront Allocator
Start by giving a row and column token to each diagonal element.
Every round move the row token 1 step to the left, and the column token 1 step down (with wraparounds).

## Slide 101
Example showing the movement of tokens.

## Slide 102
Grabbed two tokens
Grabbed two tokens

## Slide 103: Properties of the Wavefront Allocator
Once a token is absorbed, it is put out of circulation.
  This means that no cell in the same row (agent) or column (resource) can get both the tokens.
  This means that the matching that is produced is correct as per our criteria.
It produces maximal matchings
  There is no matching that could have been done but was missed.
  Every cell gets the two tokens at some point of time, if no cell in the same row or column has been allotted its request. At that point of time that cell can be allotted the request.

## Slide 104
Router Pipeline Optimizations

## Slide 105
BW
RC
VA
SA
ST
Abbrev. | Name
BW | Buffer Write
RC | Route Computation
VA | VC Allocation
SA | Switch Allocation
ST | Switch Traversal
F1 is the head flit
Rest are body flits

## Slide 106: Lookahead routing: Compute the route for the next hop.
Let’s say that we already know that from Node 1 we will go to Node 2.
Then when we are at Node 1, we compute the decision that Node 2 will take.
Similarly, when we are at Node 2, we compute the decision that Node 3 will take.
This routing decision is sent along with the packet.
Benefit: Removes Route Computation from the critical path.
1
2
3
4
5
A route

## Slide 107: Pipeline diagrams

## Slide 108: Bypassing
If the router queues are empty
  Attempt to directly traverse the switch
  If there is a conflict, then resort to the conventional method
RC
VA
ST
Bypassing

## Slide 109: Speculative VC Allocation
Assume that we will find a free VC.
After finding a free VC, send this information along with the head flit.
If we do not find a VC, then follow the conventional method.
VA
SA
ST
RC
BW
Speculative VC Allocation

## Slide 110: Late VC Selection
Maintain a queue of free VCs with each outgoing link
When a head flit traverses the switch, assign it a VC from the queue
If a free VC is not available, cancel the process, and restart the conventional process

## Slide 111: Design of the Router
Credits

## Slide 112: Contents
1.
Overview of an NoC
2.
Message Transmission
3.
4.
5.
6.
Routing
Design of a Router
Non-Uniform Cache Architectures
Performance Aspects

## Slide 113: Non-Uniform Caches
L2/L3 caches are large.
  If we find data in a nearby bank  a couple of cycles
  If it is a remote bank  20-50 cycles (depending on the size of the network and the degree of congestion)
Cache access times can be extremely variable depending on where the data is
  This is called a non-uniform cache (NUCA cache)
  Can we take advantage of this non-uniformity?
  ANSWER: Place frequently used data closer

## Slide 114: S-NUCA (static NUCA)
Simplest scheme:
  Map cache blocks to cache banks
  Give a cache block  find which cache bank it maps to
  Tradeoffs: Bank locality vs homogenizing bank accesses
Byte within a block
Set id
Bank id
Tag
Byte within a block
Bank id
Set id
Tag
Mapping 1
Mapping 2

## Slide 115: D-NUCA (Dynamic NUCA)
Let us now look at a method of bringing frequently used data closer
Bank set  sets of banks
Organize banks as columns (each column is a bank set)

## Slide 116: Operation of the Protocol
Given an address  Map it to a bank set
Search the bank set
  If we find the block, declare a cache hit
  Otherwise, declare a miss and fetch it from the lower level
Three search strategies
  Sequential
  Two-way
  Broadcast
Byte within a block
Set id
Bank set id
Tag

## Slide 117: Search Strategies: Start from the home bank (closest to the core in the bank set)

## Slide 118: After a Hit/Miss Decision
Hit decision
  Send the block to the requesting core
  Promote the block  Move it closer to the home bank (Migration)
  Bring it to a nearer bank (closer to the home bank)
  If there is an empty block in the set in the new bank  no problem
  Otherwise swap the blocks
  Bringing blocks closer to the home bank (consistent with temporal locality)
Miss decision
  Fetch the block from the lower level
  Either insert it into the nearest bank or the farthest bank (depends on the strategy)

## Slide 119: Eviction and Migration
Assume that a block needs to be evicted
  Solution 1: Move it to the lower level
  Solution 2: Move it away from the home bank. Need to tag each line with the id of the requesting core
Advantages
  Keeps data close to the requesting cores
  Brings data closer depending upon usage
  Gives a block multiple chances  Upon an eviction move it to bank slightly further away
Search policy, location, migration and eviction are important design decisions

## Slide 120: Advanced Designs
Private data  Store it only within the bank in the tile
Shared data  Use SNUCA
Read-only data  Replicate
Advantages:
  Limited replication ensures good instruction hit rates
  Replicating all data is tricky  need to synchronize replicas

## Slide 121: Contents
1.
Overview of an NoC
2.
Message Transmission
3.
4.
5.
6.
Routing
Design of a Router
Non-Uniform Cache Architectures
Performance Aspects

## Slide 122: Performance Evaluation Techniques
Evaluation Metrics
  Latency
  Throughput
  Energy or Power
  Area and routing complexity
Simulators
Architectural Simulators
Trace based
Dynamic workload based
Standalone Simulators
Synthetic traffic based

## Slide 123: Architectural Simulation
Program
Traces of network data + addresses
Simulate NoC
Simulate the network routers and links.
Get latency, throughput, and power/energy statistics.
Can
Slow
simulate NoCs accurately for real workloads

## Slide 124: Synthetic Traffic Generation
Consider a mesh (for the sake of simplicity)
Every node has an (x,y) coordinate
Synthetic traffic: set of sourcedestination pairs
Sx
Sy
Dx
Dy
Simple Patterns
Pattern | Src  Dest | Remarks
Random | src  random | Random traffic simulation
Bit-Complement |  | Used to test the NoC throughput
Transpose |  | Direction of traffic: perpendicular to the diagonal
Bit-Reverse | D[i] = S[2n – 1 – i] | Just reverse the bits. Used in FFTs
Pattern | Src  Dest | Remarks
Random | src  random | Random traffic simulation
Bit-Complement |  | Used to test the NoC throughput
Transpose |  | Direction of traffic: perpendicular to the diagonal
Bit-Reverse | D[i] = S[2n – 1 – i] | Just reverse the bits. Used in FFTs
S
D

## Slide 125: Bit-Rotation
Similar to a right shift.

## Slide 126: Shuffle and Tornado Patterns
Similar to a left shift.
Pattern | Src  Dest | Remarks
Tornado |  | Seen while solving a system of differential equations
Pattern | Src  Dest | Remarks
Tornado |  | Seen while solving a system of differential equations
Shuffle

## Slide 127: Faster approach: Synthetically generate traffic

## Slide 128
Conclusion
Modern NoCs have a complex network of nodes and
links. Hierarchy: message  packet  flit  phit
Key issues in NoCs: deadlocks, livelocks, starvation
Deadlock-free routing protocols avoid some turns. This stops a
clockwise and anti-clockwise cycle from forming.
The router has five stages: BW  RC  VA  SA  ST
For evaluating the performance of an NoC, we use
trace-based simulation or use synthetic traffic generators.

## Slide 129
The End