## Slide 1: Processor Design
The Language of Bits
Prof. Smruti Ranjan Sarangi IIT Delhi
Basic Computer Architecture
Chapter 6: RISC-V Assembly Language

## Slide 2
Download the pdf of the book
www.basiccomparch.com
videos
Slides, software, solution manual
Print version
(Publisher: WhiteFalcon, 2021)
Available on e-commerce sites.
The pdf version of the book and all the learning resources can be freely downloaded from the website: www.basiccomparch.com
2nd version

## Slide 3: Outline
RISC-V Machine Model
Integer Instructions
Control Transfer and Memory Instructions
Floating Point Instructions
Instruction Encoding
Code snippets beautified with carbon.app (https://carbon.now.sh)

## Slide 4: Requirements of a Modern ISA
Compatible with all kinds of devices: 32, 64, 128 bits
No licensing requirement
Large software developer community
Extensibility: Possible to add all kinds of novel extensions: vector, crypto, AI/ML, etc.
Why did the need for RISC-V arise?
Project begins in Berkeley
2010
Creative Commons License
2015
Maintained by the RISC-V Foundation

## Slide 5: RISC-V Machine Model
Name | Description
RV32 | 32-bit ISA
RV32E | 32-bit ISA (embedded version)
RV64 | 64-bit ISA
RV64E | 64-bit ISA (embedded version)
RV128 | 128-bit ISA
Mnemonic | Meaning
E | Embedded version
I | Base integer ISA
M | Integer multiplication/division instructions
A | Atomic instructions
F | Single-precision floating point
D | Double-precision floating point
V | Vector Instructions
Different variants of the instruction set
Extensions

## Slide 6: More about Extensions
Integer variants of the ISA
  RV32I is a regular 32-bit ISA with integer instructions
  RV64I, RV128I
RV32IMA  integer, mul/div, atomic instructions
RV32I1p3
  Major version number: 1
  Minor version number: 3
G  base integer ISA, additional integer insts, FP instructions, basic synch. instructions
  Popular format: RV32G

## Slide 7: Embedded and Compressed Instructions
We quickly run out of letters !!!
The `Z’ series was introduced
  Zfa  Additional floating-point instructions
Embedded version
  Does not reduce the instruction width (still 32 bits)
  Reduces the number of registers by 50%
Compressed version
  Width = 16 bits
  Access only 8 registers
  Limited opcode support, smaller immediate values
Even in 64 and 128-bit formats, instructions are 32 bits.
48 and 64-bit instructions are getting ratified

## Slide 8: RISC-V Integer Registers
Register | Mnemonic | Description
x0 | zero | Hardwired to zero
x1 | ra | Return address
x2 | sp | Stack pointer
x3 | gp | Global pointer
x4 | tp | Thread pointer (thread-local storage
x5-7 | t0-2 | Temporary registers
x8 | s0/fp | Saved register/frame pointer
Register | Mnemonic | Description
x9 | s1 | Saved register
x10-11 | a0-1 | Function args/ return values
x12-17 | a2-7 | Function args
x18-27 | s2-11 | Saved registers
x28-31 | t3-6 | Temporary registers
x0 is hardwired to 0
There is a dedicated pc register
Bi-endian

## Slide 9
x0/zero
x1
x2
x3
x4
x5
x6
x7
x8
x9
RV32
RV64
RV128
x31
0
32
64
127
PC
0
32
64
127
View of Registers

## Slide 10: Outline
RISC-V Machine Model
Integer Instructions
Control Transfer and Memory Instructions
Floating Point Instructions
Instruction Encoding

## Slide 11: Moving values to registers
Semantics | Example | Explanation
addi rd, rs1, imm | addi x1, x0, 5 | x1 ← 0 + 5
add rd, rs1, rs2 | add x1, x0, x3 | x1 ← 0 + x3
Register x0/ zero is hardwired to 0
Moving a value to a register is accomplished by adding it to zero
Immediates are normally 12 bits in RISC-V
The addi instruction adds an immediate to a register (could be zero)
The regular add instruction can be used
  If the first source register is set to zero  Moving a value from one register to another
There is no subi instruction because the immediate is signed

## Slide 12: Loading Immediates Directly
The lui instruction can load a 20-bit immediate directly into the upper 20 bits.
  Note that other instructions only load the lower 12 bits
The li assembler directive can load a 32-bit value directly
  Translated to two instructions (internally)
We can either use the x-series registers or the mnemonics
  The mnemonics are normally preferred because it is possible to honor the register-usage semantics.
Semantics | Example | Explanation
lui rd, imm (20-bit) | lui x1, 5 | x1 ← 5 << 12
li rd, imm (32-bit) | li t0, 0xABCD1234 | t0 ← 0xABCD1234

## Slide 13
Add 409932 + 409823.

## Slide 14
Using assembler directives like li makes writing assembly code easier
Add 409932 + 409823.

## Slide 15: Add/Sub Instructions
Semantics | Example | Explanation
add rd, rs1, rs2 | add x1, x2, x3 | x1 ← x2 + x3
addi rd, rs1, imm | addi x1, x2, 5 | x1 ← x2 + 5
sub rd, rs1, rs2 | sub x1, x2, x3 | x1 ← x2 - x3

## Slide 16
Compute 4 + 5 - 19.

## Slide 17
Swap two numbers stored in x1 and x2 (resp.).

## Slide 18: Multiplication and Division
Part of the ‘M’ extension
The default mul instruction computes the lower 32 bits
The product ideally requires 64 bits
  The mulh and mulhu instructions can be used to compute the upper 32 bits
The HW dynamically recognizes a consecutive mul-mulh instruction pair, and replaces it with a single multiplication
Semantics | Example | Explanation
mul rd, rs1, rs2 | mul x1, x2, x3 | x1 ← x2 * x3
div rd, rs1, rs2 | div x1, x2, x3 | x1 ← x2 / x3
rem rd, rs1, rs2 | rem x1, x2, x3 | x1 ← rem (x2 / x3)

## Slide 19: Division Rules
Division Operation | Quotient | Remainder
4 ÷ 3 | 1 | 1
4 ÷ (-3) | -1 | 1
(-4) ÷ 3 | -1 | -1
(-4) ÷ (-3) | 1 | -1
Round towards 0
Sign of the remainder is the same as the sign of the dividend
Consecutive division and remainder instructions (with the same operands) can be fused.

## Slide 20
Multiply 3 with (-17).

## Slide 21
Compute 123 + 1.

## Slide 22
Divide -50 / 3.
Dynamically fused by hardware.

## Slide 23: Logical and Shift Instructions
Semantics | Example | Explanation
and rd, rs1, rs2 | and x1, x2, x3 | x1 ← x2 AND x3
andi rd, rs1, imm | andi x1, x2, 6 | x1 ← x2 AND 6
or rd, rs1, rs2 | or x1, x2, x3 | x1 ← x2 OR x3
ori rd, rs1, imm | ori x1, x2, 9 | x1 ← x2 OR 9
xor rd, rs1, rs2 | xor x1, x2, x3 | x1 ← x2 XOR x3
xori rd, rs1, imm | xori x1, x2, 9 | x1 ← x2 XOR 9
sll rd, rs1, rs2 | sll x1, x2, x3 | x1 ← x2 << x3
srl rd, rs1, rs2 | srl x1, x2, x3 | x1 ← x2 >> x3
sra rd, rs1, rs2 | sra x1, x2, x3 | x1 ← x2 >>> x3
slli rd, rs1, imm | slli x1, x2, 3 | x1 ← x2 << 3
srli rd, rs1, imm | srli x1, x2, 3 | x1 ← x2 >> 3
srai rd, rs1, imm | srai x1, x2, 3 | x1 ← x2 >>> 3
right-shift arithmetic

## Slide 24: Generic Format of Shift Instructions
Generic format
sll
srl
sra
slli
srli
srai
rd
rd
rd
rd
rd
rd
rs1
rs1
rs1
rs1
rs1
rs1
rs2
rs2
rs2
imm
imm
imm
,
,
,
,
,
,
,
,
,
,
,
,
,
,
,
,
,
,

## Slide 25
Compute the bitwise OR of A and B. Let A = 4 and B = 1.

## Slide 26
Compute t1 = t2 + t3 × 4
Strength reduction
Multiplications are slow. Shifts are much faster.

## Slide 27: Outline
RISC-V Machine Model
Integer Instructions
Control Transfer and Memory Instructions
Floating Point Instructions
Instruction Encoding

## Slide 28: Conditional Control Transfer Instructions
Semantics | Example | Explanation
beq rs1, rs2, label | beq x1, x2, .foo | Branch to the . foo label if x1 = x2
bne rs1, rs2, label | bne x1, x2, .foo | Branch to the .foo label if x1 ≠ x2
bge rs1, rs2, label | bge x1, x2, .foo | Branch to the .foo label if x1 ≥ x2
blt rs1, rs2, label | blt x1, x2, .foo | Branch to the .foo label if x1 < x2
bgeu rs1, rs2, label | bgeu x1, x2, .foo | Similar to bge, considers unsigned values.
bltu rs1, rs2, label | bltu x1, x2, .foo | Similar to blt, considers unsigned values.
Semantics | Example | Explanation
slt rd, rs1, rs2 | slt x1, x2, x3 | if (x2 < x3) set x1 to 1
slti rd, rs1, imm | slti x1, x2, 5 | if (x2 < 5) set x1 to 1
sltu rd, rs1, rs2 | sltu x1, x2, 5 | if (x2 <unsigned x3) set x1 to 1
sltui rd, rs1, imm | sltui x1, x2, x3 | if (x2 <unsigned 5) set x1 to 1

## Slide 29: Control Transfer Instructions
RISC-V does not have a flags register.
Instead, the flags are stored in a register that the programmer specifies.
Compare 2 and 5 and store the comparison result in t2. [t2 = (2 < 5)]

## Slide 30
Add two 64-bit numbers (stored in two 32-bit registers) Note: sltu does an unsigned comparison.
t0 < t4 → there is a carry

## Slide 31
Add all the numbers from 1 to 10.

## Slide 32: Unconditional Branches
The jal instruction performs the role of an unconditional branch and a call instruction:
  The return address is explicitly specified (there is no default)
  If the return addr. register is zero, then this is a regular unconditional branch instruction
  Otherwise, it is a call instruction
jalr is like a return instruction
  In this case, the return address is stored in rd
  If the return addr. register is zero, then nothing is stored. Functions like an indirect branch.
Semantics | Example | Explanation
jal rd, label | jal x1, func | Jump to the func label and store the return address in x1
jalr rd, rs1, offset | jalr x1, x2, 20 | Jump to the address x2 + 20 and store the return address in x1

## Slide 33
Check if the number stored in a1 is a square or not?

## Slide 34
Check whether the number stored in a1 is a prime number.

## Slide 35
Find the number of ones in a 32-bit number stored in a1.

## Slide 36: A Program with a Simple Function Call
Return value

## Slide 37
Compute xn and store the result in a0.
Initialization
Computation

## Slide 38: Load-Store Instructions
Semantics | Example | Explanation
lw rd, imm(rs1) | lw x1, 32(sp) | x1 ← mem[sp + 32]
sw rs2, imm(rs1) | sw x1, 32(sp) | mem[sp+32] ← x1
la rd, label | la x1, pi | x1 ← address(pi)
The lw and sw instructions load and store 32-bit values
There is a need for an assembler directive (la)
  Assign a constant to a label
  Load the label directly to a register
  Generate assembly statements to load the constant to a register

## Slide 39: Load Instruction
lw x1, imm(x5)

## Slide 40: Store Instruction
Register
file
Memory
x5
x1
imm
sw x1, imm(x5)

## Slide 41
Load a0 with the contents of the memory address
sp − s0 × 4 − 12.
Load 17 into the register s0.

## Slide 42
Create a copy of a 10-element array. Assume the starting address of the original array is stored in a1 and that of the destination array is stored in a2.

## Slide 43
Compute the sum of the elements in a 10-element array. Assume that the base address of the array is stored in a1. Store the result in a0.

## Slide 44: Contd…
Add the array element to a0

## Slide 45
Compute the result of the factorial function using a recursive algorithm.

## Slide 46: Contd …

## Slide 47: Outline
RISC-V Machine Model
Integer Instructions
Control Transfer and Memory Instructions
Floating Point Instructions
Instruction Encoding

## Slide 48: Floating Point Registers
Register | Mnemonic | Description
f0-7 | ft0-7 | Temporary registers
f8-9 | fs0-1 | Saved registers
f10-11 | fa0-1 | Arguments/return values
f12-17 | fa2-7 | Function arguments
f18-27 | fs2-11 | Saved registers
f28-31 | ft8-11 | Temporary registers
No register is hardwired to 0
It is not possible to load values into FP registers directly
They can only be initialized by loading values from memory (like x86)

## Slide 49: Floating Point Control and Status Register
Mnemonic | Explanation
NV | Invalid operation
DZ | Divide by zero
OF | Overflow
UF | Underflow
NX | Inexact
Rounding Mode | Mnemonic | Meaning
000 | RNE | Round to nearest, prefer even LSBs
001 | RTZ | Round towards zero
010 | RDN | Round down (towards -∞)
011 | RUP | Round up (towards +∞)
100 | RMM | Round to nearest (prefer maximum abs. val.)
101,110 |  | Invalid. Reserved for future use
111 | DYN | Select a rounding mode dynamically (frm field)
Reserved
Rounding mode (frm)
8
31
7
5
24
3
Accrued exceptions (fflags)
NV
DZ
OF
UF
NX
1
1
1
1
1
4
0

## Slide 50: Floating Point Load and Store Operations
We load the contents into memory first, and then transfer it to a FP register.
Semantics | Example | Explanation
flw rd, imm(rs1) | flw f1, 32(sp) | f1 ← mem[sp + 32]
fsw rs2, imm(rs1) | fsw f1, 32(sp) | mem[sp+32] ← f1

## Slide 51: Load the value of a constant val into the floating point register fs1.
Define the constant.
Store its address in a1
Load into an FP register.

## Slide 52: Arithmetic Instructions
Semantics | Example | Explanation
fadd.s rd, rs1, rs2 | fadd.s f1, f2, f3 | f1 ← f2 + f3
fsub.s rd, rs1, rs2 | fsub.s f1, f2, f3 | f1 ← f2 - f3
fmul.s rd, rs1, rs2 | fmul.s f1, f2, f3 | f1 ← f2 × f3
fdiv.s rd, rs1, rs2 | fdiv.s f1, f2, f3 | f1 ← f2 ÷ f3
fmin.s rd, rs1, rs2 | fmin.s f1, f2, f3 | f1 ← min(f2 , f3)
fmax.s rd, rs1, rs2 | fmax.s f1, f2, f3 | f1 ← max(f2 , f3)
fsqrt.s rd, rs1 | fsqrt.s f1, f2 | f1 ←
Semantics | Example | Explanation
fadd.s rd, rs1, rs2 | fadd.s f1, f2, f3 | f1 ← f2 + f3
fsub.s rd, rs1, rs2 | fsub.s f1, f2, f3 | f1 ← f2 - f3
fmul.s rd, rs1, rs2 | fmul.s f1, f2, f3 | f1 ← f2 × f3
fdiv.s rd, rs1, rs2 | fdiv.s f1, f2, f3 | f1 ← f2 ÷ f3
fmin.s rd, rs1, rs2 | fmin.s f1, f2, f3 | f1 ← min(f2 , f3)
fmax.s rd, rs1, rs2 | fmax.s f1, f2, f3 | f1 ← max(f2 , f3)
fsqrt.s rd, rs1 | fsqrt.s f1, f2 | 
.s is for single precision
.d is for double precision

## Slide 53
Compute , and store the result in fa0.

## Slide 54: Multiplication and Conversion Instructions
Semantics | Example | Explanation
fmadd.s rd, rs1, rs2, rs3 | fmadd.s f1, f2, f3, f4 | f1 ← f2 * f3 + f4
fmsub.s rd, rs1, rs2, rs3 | fmsub.s f1, f2, f3, f4 | f1 ← f2 * f3 - f4
fcvt.s.w rd, rs1 | fcvt.s.w f1, x5 | f1 ← (float) x5
fcvt.w.s rd, rs1 | fcvt.w.s x5, f1 | x5 ← (int) f1
fmadd.s and fmsub.s are compound instructions: multiply + add/subtract
The convert instruction (fcvt) is another way of loading and storing FP values

## Slide 55
Compute π × e + 4, and store the result in ft0. Convert the result to an integer and store the result in a0.
Need to convert 4 to 4.0 first

## Slide 56: Floating Point Comparison Instructions
Same as integer comparison
Semantics | Example | Explanation
flt.s rd, rs1, rs2 | flt.s s1, f2, f3 | if (f2 < f3) set s1 to 1
fle.s rd, rs1, rs2 | fle.s s1, f2, f3 | if (f2 ≤ f3) set s1 to 1
feq.s rd, rs1, rs2 | feq.s s1, f2, f3 | if (f2 == f3) set s1 to 1

## Slide 57
First, initialize a0 = 0, then set a0 = 17 if e < π.
Perform the comparison and store the result in t0
Check the result of the comparison.

## Slide 58: Outline
RISC-V Machine Model
Integer Instructions
Control Transfer and Memory Instructions
Floating Point Instructions
Instruction Encoding

## Slide 59
Format/Type | Structure | Instructions
R | rd, rs1, rs2 | add, sub, mul, div, rem, and, or, xor, sll, srl, sra, slt, sltu
I | rd, rs1, imm rd, imm(rs1) | addi, andi, ori, xori, slli, srli, srai, slti, sltiu lw, jalr
S | rs2, imm(rs1) | sw
U | rd, imm | lui
Instruction Formats in 32-bit RISC-V
Define a new instruction type for store instructions
The default immediate size is 12 bits
The U-type supports a 20-bit immediate

## Slide 60
add, slt and xor
opcode
rd
funct3
funct7
rs1
7
7
3
5
5
rs2
5
R-Type
Differentiate between opcodes
Further differentiation between opcodes (add, sub)
opcode
rd
funct3
funct7
rs1
7
12
3
5
5
imm
I-Type
12-bit immediate field

## Slide 61
20
opcode
rd
7
5
U-Type
imm
opcode
imm[4..0]
funct3
imm[11..5]
rs1
7
7
3
5
5
rs2
5
S-Type
Split the immediate
Split the immediate
Do not define a new format
20-bit immediate

## Slide 62
opcode
rd
7
5
20
J-Type
imm[19..12]
imm[10..1]
20
11
opcode
imm[..]
funct3
imm[10..5]
rs1
7
7
3
5
5
rs2
5
B-Type
11
12
4..1
Format | Structure | Instructions
B | rs1, rs2, imm | beq, bne, blt, bge, bltu, bgeu
J | rd, imm | jal
immediate bits: LSB is 0
 Do not represent it
immediate bit
immediate bits: LSB is 0

## Slide 63
opcode
rd
width
funct7
rs1
7
12
3
5
5
imm
LOAD-FP
12-bit immediate field
opcode
imm[4..0]
width
imm[11..5]
rs1
7
7
3
5
5
rs2
5
STORE-FP
#bytes loaded/stored

## Slide 64: FP Instructions
opcode
rd
rm
funct5
rs1
7
5
2
3
5
5
rs2
fmt
5
opcode
rd
rm
rs3
rs1
7
5
2
3
5
5
rs2
fmt
5
precision
Used by all FP arithmetic, compare and conversion instructions.
rounding mode
Fused multiply-add instruction

## Slide 65
THE END