## Slide 1
Chapter 8: Computer Arithmetic (Part II)
Prof. Smruti Ranjan Sarangi IIT Delhi
Basic Computer Architecture
PowerPoint Slides

## Slide 2
Download the pdf of the book
www.basiccomparch.com
videos
Slides, software, solution manual
Print version
(Publisher: WhiteFalcon, 2021)
Available on e-commerce sites.
The pdf version of the book and all the learning resources can be freely downloaded from the website: www.basiccomparch.com
2nd version

## Slide 3: Outline
Addition
Multiplication
Division
Floating Point Addition
Floating Point Multiplication
Floating Point Division

## Slide 4: Integer Division
Let us only consider positive numbers
  N = DQ + R
    N → Dividend
    D → Divisor
    Q → Quotient
    R → Remainder
Properties
  [Property 1:] R < D, R >= 0
  [Property 2:] Q is the largest positive integer satisfying the equation (N = DQ +R) and Property 1

## Slide 5: Reduction of the Divison Problem
We have reduced the original problem to a smaller problem

## Slide 6: How to Reduce the Problem
We need to find Qn
We can try both values – 0 and 1
  First try 1
  If : N – D2n-1 >= 0, Qn = 1 (maximize the quotient)
    Otherwise it is 0
Once we have reduced the problem
  We can proceed recursively

## Slide 7: Iterative Divider
Initial: V holds the dividend (N), U = 0
U
V
Divisor(D)
(U-D)

## Slide 8: Restoring Division
Algorithm 3: Restoring algorithm to divide two 32 bit numbers
Data: Divisor in D, Dividend in V, U = 0
Result: U contains the remainder (lower 32 bits), and V contains the quotient
i ← 0
for i < 32 do
i ← i + 1
/* Left shift UV by 1 position */
UV ← UV << 1
U ← U - D
if U ≥ 0 then
q ← 1
end
else
U ← U + D
q ← 0
end
/* Set the quotient bit */
LSB of V ← q
end

## Slide 9: Example
00000
111X
after shift:
end of
iteration:
00000
1110
1
00000
0111
beginning:
U
V
00001
110X
after shift:
end of
iteration:
00001
1100
2
00011
100X
after shift:
end of
iteration:
00000
1001
3
00001
001X
after shift:
end of
iteration:
00001
0010
4
Divisor (D)
0011
Dividend (N)
00111
Remainder(R)
0001
Quotient(Q)
0010

## Slide 10: Restoring Division
Consider each bit of the dividend
Try to subtract the divisor from the U register
  If the subtraction is successful, set the relevant quotient bit to 1
  Else, set the relevant quotient bit to 0
Left shift

## Slide 11: Proof
Let us consider the value stored in UV (ignoring quotient bits)
After the shift (first iteration)
  UV = 2N
After line 5, UV contains
  UV – 2nD = 2N – 2nD = 2 * (N – 2n-1 D)
If (U – D) >= 0
  N' = N – 2n-1D.
  Thus, UV contains 2N'

## Slide 12: Proof - II
If (U – D) < 0
  We know that (N = N')
  Add D to U → Add 2nD to UV
  partial dividend = 2N = 2N'
In both cases
  The partial dividend = 2N'
After 32 iterations
  V will contain the entire quotient

## Slide 13: Proof - III
At the end, UV = 232 * N32 (Ni is the partial dividend after the ith iteration)
N31 = DQ1 + R
  N31 – DQ1 = N32 = R
Thus, U contains the remainder (R)

## Slide 14: Time Complexity
n iterations
  Each iteration takes log(n) time
  Total time : n log(n)

## Slide 15: Restoring vs Non-Restoring Division
We need to restore the value of register U
  Requires an extra addition or a register move
Can we do without this ?
  Non Restoring Division

## Slide 16
Algorithm 4: Non-restoring algorithm to divide two 32 bit numbers
Data: Divisor in D, Dividend in V, U = 0
Result: U contains the remainder (lower 32 bits), and V contains the quotient
i ← 0
for i < 32 do
i ← i + 1
/* Left shift UV by 1 position */
UV ← UV << 1
if U ≥ 0 then
U ← U − D
end
else
U ← U + D
end
if U ≥ 0 then
q ← 1
end
else
q ← 0
end
/* Set the quotient bit */
lsb of V ← q
end
if U <0 then
U ← U + D
end

## Slide 17
00000
111X
after shift:
end of
iteration:
11101
1110
1
00000
0111
beginning:
U
V
11011
110X
after shift:
end of
iteration:
11110
1100
2
11101
100X
after shift:
end of
iteration:
00000
1001
3
00001
001X
after shift:
end of
iteration:
11110
0010
4
Divisor (D)
0011
Dividend (N)
00111
Remainder(R)
0001
Quotient(Q)
0010
0001
0010
end (U=U+D):
U
V

## Slide 18: Idea of the Proof
Start from the beginning : If (U – D) >= 0
  Both the algorithms (restoring and non-restoring) produce the same result, and have the same state
If (U – D) < 0
  We have a divergence
  In the restoring algorithm
    value(UV) = A
  In the non-restoring algorithm
    value(UV) = A - 2nD

## Slide 19: Proof - II
In the next iteration (just after the shift)
  Restoring : value(UV) = 2A
  Non - Restoring : value(UV) = 2A - 2n+1D
If the quotient bit is 1 (end of iteration)
  Restoring :
    Subtract 2nD
    value(UV) = 2A - 2nD
  Non Restoring :
    Add 2nD
    value(UV) = 2A – 2n+1D + 2nD = 2A - 2nD

## Slide 20: Proof - III
If the quotient bit is 0
  Restoring
    partial dividend = 2A
  Non restoring
    partial dividend = 2A – 2nD
  Next iteration (if quotient bit = 1) (after shift)
    Restoring : partial dividend : 4A
    Non restoring : partial dividend : 4A – 2n+1D
Keep applying the same logic ….

## Slide 21: Outline
Addition
Multiplication
Division
Floating Point Addition
Floating Point Multiplication
Floating Point Division

## Slide 22: Adding Two Numbers (same sign)
Recap : Floating Point Number System
Normalised form of a 32 bit (normal) floating point number.
Normalised form of a 32 bit (denormal) floating point number.
A = (−1)S × P × 2−126, (0 ≤ P < 1) (7.23)
Symbol
Meaning
S
Sign bit (0(+ve), 1(-ve))
P
Significand (form: 1.xxx(normal) or 0.xxx(denormal))
M
Mantissa (fractional part of significand)
E
(exponent + 127(bias))
Z
Set of integers
A = (−1)S × P × 2E−bias, (1 ≤ P < 2, E ∈ Z, 1 ≤ E ≤ 254) (7.22)

## Slide 23: Addition
Add : A + B
  Unpack the E fields → EA , EB
  Let the E field of the result be → EC
Unpack the significand (P)
  P contains → 1 bit before the decimal point, 23 mantissa bits (24 bits)
  Unpack to a 25 bit number (unsigned)
    W → Add a leading 0 bit, 24 bits of the signficand

## Slide 24: Addition - II
With no loss of generality
  Assume EA >= EB
Let significands of A and B be PA and PB
Let us initially set W ← unpack (PB)
We make their exponents equal and shift W to the right by (EA – EB) positions

## Slide 25: Renormalisation
Let the significand represented by register, W, be PW
  There is a possibility that PW >= 2
  In this case, we need to renormalise
    W ← W >> 1
    EA ← EA + 1
The final result
  Sign bit (same as sign of A or B)
  Significand (PW), exponent field (EA)

## Slide 26: Example
Example: Add the numbers: 1.012 * 23 + 1.112 * 21
Answer:
The decimal point in W is shown for enhancing readability. For simplicity, biased notation not used.
A = 1.01 * 23 and B = 1.11 * 21
W = 01.11 (significand of B)
E = 3
W = 01.11 >> (3-1) = 00.0111
W + PA = 00.0111 + 01.0100 = 01.1011
Result: C = 1.011 * 23

## Slide 27: Example - II
Example: Add : 1.012 * 23 + 1.112 * 22
Answer:
The decimal point in W is shown for enhancing readability. For simplicity, biased notation not used.
A = 1.01 * 23 and B = 1.11 * 22
W = 01.11 (significand of B)
E = 3
W = 01.11 >> (3-2) = 00.111
W + PA = 00.111 + 01.0100 = 10.001
Normalisation: W = 10.001 >> 1 = 1.0001, E = 4
Result: C = 1.0001 * 24

## Slide 28: Rounding
Assume that we were allowed only two mantissa bits in the previous example
  We need to perform rounding
Terminology :
  Consider the sum(W) of the significands after we have normalised the result
  W ← (P + R) * 2-23 (R < 1)

## Slide 29: Rounding - II
P represents the significand of the temporary result
R (is a residue)
Aim :
  Modify P to take into account the value of R
  Then, discard R
  Process of rounding : P → P'

## Slide 30: IEEE 754 Rounding Modes
Truncation
  P' = P
  Example in decimal : 9.5 → 9, 9.6 → 9
Round to +∞
  P' = ⎡P +R⎤
  Example in decimal : 9.5 → 10, -3.2 → -3

## Slide 31: IEEE 754 Rounding - II
Round to -∞
  P' = ⌊P+R⌋
  Example in decimal : 9.5 → 9, -3.2 → -4
Round to nearest
  P' = [P + R]
  Example in decimal :
    9.4 → 9 , 9.5 → 10 (even)
    9.6 → 10 , -2.3 → -2
    -3.5 → -4 (even)

## Slide 32: Rounding Modes – Summary
Rounding Mode
Condition for incrementing the significand
Sign of the result (+ve)
Sign of the result (-ve)
Truncation
Round to +∞
Round to −∞
Round to Nearest
R > 0
(R > 0.5)||(R = 0.5 ∧ lsb(P) = 1)
R > 0
(R > 0.5)||(R = 0.5 ∧ lsb(P) = 1)
∧ (logical AND), R (residue)

## Slide 33: Implementing Rounding
We need three bits
  lsb(P)
  msb of the residue (R) → r (round bit)
  OR of the rest of the bits of the residue (R) → s (sticky bit)
Condition on Residue
Implementation
R > 0
R = 0.5
R > 0.5
r ∨ s = 1
r ∧ s = 1
r ∧ s = 1
r (round bit), s(sticky bit)

## Slide 34: Renormalisation after Rounding
In rounding : we might increment the significand
  We might need to renormalise
  After renormalisation
    Possible that E becomes equal to 255
    In this, case declare an overflow

## Slide 35: Addition of Numbers (Opposite Signs)
C = A + B
  Same assumption EA >= EB
Steps
  Load W with the significand of B (PB)
  Take the 2's complement of W (W = -B)
  W ← W >> (EA – EB)
  W ← W + PA
  If (W < 0) replace it with its 2's complement. Flip the sign of the result.

## Slide 36: Addition of Numbers (Opposite Signs)-II
Normalise the result
  Possible that W < 1
  In this case, keep shifting W to the left till it is in normal form. (simultaneously decrement EA)
Round and Renormalise

## Slide 37
A=0?
C=B
B=0?
C=A
Y
Y
N
sign(A) = sign(B)?
Swap A and B
such that E <= E
A
B
W
P >> (EA – EB)
Y
N
W
W + P
W
- W (2's complement)
Normalize W and
update E
Round W
B
A
E
E
A
, S
sign(A)
N
W < 0?
W
- W (2's complement)
S = S
Y
N
Normalize W and
update E
Overflow or
underflow?
Overflow or
underflow?
N
N
Report
Y
Report
Y
Construct C out
of W, E, and S
C
C = A + B

## Slide 38: Outline
Addition
Multiplication
Division
Floating Point Addition
Floating Point Multiplication
Floating Point Division

## Slide 39: Multiplication of FP Numbers
Steps
  E ← EA + EB - bias
  W ← PA * PB
  Normalise (shift left or shift right)
  Round
  Renormalise

## Slide 40
A=0?
C=0
B=0?
C=0
Y
Y
N
Normalize W and
update E
Round W
E
E + E - bias
A
sign(A) sign(B)
N
Normalize W and
update E
Overflow or
underflow?
Overflow or
underflow?
N
N
Report
Y
Construct C out
of W, E, and S
C
C = A * B
S
B
Overflow or
underflow?
Report
Y
P
A
W
P
B
*
N
Report
Y

## Slide 41: Outline
Addition
Multiplication
Division
Floating Point Addition
Floating Point Multiplication
Floating Point Division

## Slide 42: Simple Division Algorithm
Divide A/B to produce C
  There is no notion of a remainder in FP division
Algorithm
  E ← EA – EB + bias
  W ← PA / PB
  normalise, round, renormalise
Complexity : O(n log(n))

## Slide 43: Goldschmidt Division
Let us compute the reciprocal of B (1/B)
  Then, we can use the standard floating point multiplication algorithm
Ignoring the exponent
  Let us compute (1/PB)
If B is a normal floating point number
  1 <= PB < 2
  PB = 1 + X (X < 1)

## Slide 44: Goldschmidt Division - II

## Slide 45
No point considering Y32
Cannot be represented in our format

## Slide 46: Generating the 1/(1-Y)
We can compute Y2 using a FP multiplier.
  Again square it to obtain Y4, Y8, and Y16
  Takes 4 multiplications, and 5 additions, to generate all the terms
  Need 4 more multiplications to generate the final result (1/1-Y)
Compute 1/PB by a single right shift

## Slide 47: GoldSchmidt Division Summary
Time complexity of finding the reciprocal
  (log(n))2
Time required for all the multiplications and additions
  (log(n))2
Total Time : (log(n))2

## Slide 48: Division using the Newton Raphson Method
Let us focus on just finding the reciprocal of a number
Let us designate PB as b (1 <= b < 2)
  Aim is to compute 1/b
Let us create a function f(x) = 1/x – b
  f(x) = 0, when x = 1/b
Problem of computing the reciprocal
  same as computing the root of f(x)

## Slide 49: Idea of the Method
Start with an arbitrary value of x → x0
  Locate x0 on the graph of f(x)
  Draw a tangent to f(x) at (x0 , f(x0))
  Let the tangent intersect the x axis at x1
  Draw another tangent at (x2, f(x2))
Keep repeating
  Ultimately, we will converge to the root

## Slide 50: Newton Raphson Method
x0
x0,f(x0)
x1
x2
root
x
f(x)
x1,f(x1)

## Slide 51: Analysis
f(x) = 1/x – b
  f’(x)= d f(x) / d(x) = -1 / x2
  f'(x0) = -1/x02
Equation of the tangent : y = mx + c
  m = -1/x02
  y = -x/x02 + c
At x0, y = 1/x0 - b

## Slide 52: Algebra
The equation of the tangent is :
  y = -x/x02 + 2/x0 – b
  Let this intersect the x axis at x1

## Slide 53: Intersection with the x-axis
Let us define : E(x) = bx – 1
  E(x) = 0, when x = 1/b

## Slide 54: Evolution of the Error

## Slide 55: Bounding the Error
1 <= b < 2 (significand of a normal floating point number)
  Let x0 = ½
  The range of (bx0 – 1) is [-1/2, 0]
  Hence, |E(x0)| <= ½
  The error thus reduces by a power of 2 every iteration

## Slide 56: Evolution of the Error - II
E(x) = bx – 1 = b (x – 1/b)
  x – 1/b is the difference between the ideal value and the actual estimate (x). This is near 2-32, which is too small to be considered.
No point considering beyond 5 iterations
Since, we are limited to 23 bit mantissas
Iteration
max(e (x)
0
1
2
1
1
2
2
2
1
2
4
3
1
2
8
4
1
2
16
5
1
2
32

## Slide 57: Time Complexity
In every step, the operation that we need to perform is :
  xn = 2xn-1 – bxn-12
  Requires a shift, multiply, and subtract operation
  O(log(n)) time
Number of steps: O(log(n))
Total time : O( log (n)2 )

## Slide 58
THE END