## Slide 1: Processor Design
The Language of Bits
Prof. Smruti Ranjan Sarangi IIT Delhi
Basic Computer Architecture
PowerPoint Slides
Chapter 9: Processor Design

## Slide 2
Download the pdf of the book
www.basiccomparch.com
videos
Slides, software, solution manual
Print version
(Publisher: WhiteFalcon, 2021)
Available on e-commerce sites.
The pdf version of the book and all the learning resources can be freely downloaded from the website: www.basiccomparch.com
2nd version

## Slide 3: Outline
Overview of a Processor
Detailed Design of each Stage
The Control Unit
Microprogrammed Processor
Microassembly Language
The Microcontrol Unit

## Slide 4: Processor Design
The aim of processor design
  Implement the entire SimpleRisc ISA
  Process the binary format of instructions
  Provide as much of performance as possible
Basic Approach
  Divide the processing into stages
  Design each stage separately

## Slide 5: A Car Assembly Line
Similar to a car assembly line
  Cast raw metal into the chassis of a car
  Build the Engine
  Assemble the engine and the chassis
  Place the dashboard, and upholstery

## Slide 6: A Processor Divided Into Stages
Instruction Fetch (IF)
  Fetch an instruction from the instruction memory
  Compute the address of the next instruction
Instruction
Fetch
(IF)
Operand
Fetch
(OF)
Execute
(EX)
Memory
Access
(MA)
Register
Write
(RW)

## Slide 7: Operand Fetch (OF) Stage
Operand Fetch (OF)
  Decode the instruction (break it into fields)
  Fetch the register operands from the register file
  Compute the branch target (PC + offset)
  Compute the immediate (16 bits + 2 modifiers)
  Generate control signals (we will see later)

## Slide 8: Execute (EX) Stage
The EX Stage
  Contains an Arithmetic-Logical Unit (ALU)
    This unit can perform all arithmetic operations ( add, sub, mul, div, cmp, mod), and logical operations (and, or, not)
  Contains the branch unit for computing the branch condition (beq, bgt)
  Contains the flags register (updated by the cmp instruction)

## Slide 9: MA and RW Stages
MA (Memory Access) Stage
  Interfaces with the memory system
  Executes a load or a store
RW (Register Write) Stage
  Writes to the register file
  In the case of a call instruction, it writes the return address to register, ra

## Slide 10: Outline
Outline of a Processor
Detailed Design of each Stage
The Control Unit
Microprogrammed Processor
Microassembly Language
The Microcontrol Unit

## Slide 11: Instruction Fetch (IF) Stage
pc
Instruction
memory
4
branchPC
Fetch unit
control signal
1 - input 1
0 - input 0
Multiplexer
isBranchTaken
triggered by a negative
clock edge
32
32
32
inst
1
0
1
0
32

## Slide 12: The Fetch unit
The pc register contains the program counter (negative edge triggered)
We use the pc to access the instruction memory
The multiplexer chooses between
  pc + 4
  branchTarget
It uses a control signal → isBranchTaken

## Slide 13: isBranchTaken
isBranchTaken is a control signal
  It is generated by the EX unit
Conditions on isBranchTaken
Instruction
Value of isBranchTaken
non-branch instruction
0
call
1
ret
1
b
1
beq
branch taken – 1
branch not taken – 0
bgt
branch taken – 1
branch not taken – 0

## Slide 14: Data Path and Control Path
The data path consists of all the elements in a processor that are dedicated to storing, retrieving, and processing data such as register files, memory, and the ALU.
The control path primarily contains the control unit, whose role is to generate the appropriate signals to control the movement of instructions, and data in the data path.

## Slide 15: Control Path
We will currently look at the hardwired control path.
Data path elements
Interconnection network
Control path

## Slide 16: Operand Fetch Unit
Inst.
Code
Format
Inst.
Code
Format
add
00000
add rd, rs1, (rs2/imm)
lsl
01010
lsl rd, rs1, (rs2/imm)
sub
00001
sub rd, rs1, (rs2/imm)
lsr
01011
lsr rd, rs1, (rs2/imm)
mul
00010
mul rd, rs1, (rs2/imm)
asr
01100
asr rd, rs1, (rs2/imm)
div
00011
div rd, rs1, (rs2/imm)
nop
01101
nop
mod
00100
mod rd, rs1, (rs2/imm)
ld
01110
ld rd, imm[rs1]
cmp
00101
cmprs1, (rs2/imm)
st
01111
st rd, imm[rs1]
and
00110
and rd, rs1, (rs2/imm)
beq
10000
beq offset
or
00111
or rd, rs1, (rs2/imm)
bgt
10001
bgt offset
not
01000
not rd, (rs2/imm)
b
10010
b offset
mov
01001
mov rd, (rs2/imm)
call
10011
call offset
ret
10100
ret

## Slide 17: Instruction Formats
Each format needs to be handled separately.
Format
Definition
branch
op (28-32)
offset (1-27)
register
op (28-32)
I (27)
rd (23-26)
rs1 (19-22)
rs2 (15-18)
immediate
op (28-32)
I (27)
rd (23-26)
rs1 (19-22)
imm (1-18)
op → opcode, offset → branch offset, I → immediate bit, rd → destination register
rs1 → source register 1, rs2 → source register 2, imm → immediate operand

## Slide 18: Register File Read
First input → rs1 or ra(15) (ret instruction)
Second input → rs2 or rd (store instruction)
rs2
op1
op2
inst[15:18]
inst[23:26]
isSt
Register
file
read port 1
read port 2
A
D
A
D
A
D
address
data
1
0
inst
isRet
1
0
rd
rs1
inst[19:22]
ra(15)

## Slide 19: Register File Access
The register file has two read ports
  1st Input
  2nd Input
The two outputs are op1, and op2
  op1 is the branch target (return address) in the case of a ret instruction, or rs1
  op2 is the value that needs to be stored in the case of a store instruction, or rs2

## Slide 20: Immediate and Branch Unit
Compute immx (extended immediate), branchTarget, irrespective of the instruction format.
For the branchTarget we need to choose between the embedded target and op1 (ret)
shift by 2 bits
and extend sign
pc
calculate
immediate
imm
inst[1:18]
immx
27
32
18
32
inst
branchTarget

## Slide 21: OF Unit
rs1
rs2
op2
inst[19:22]
inst[15:18]
shift by 2 bits
and extend sign
pc
calculate
immediate
imm
inst[1:18]
immx
(opcode, I bit)
inst[27:32]
Control
unit
Fetch unit
Operand fetch unit
Execute
unit
27
32
18
32
6
rd
inst[23:26]
isSt
reg. operands
imm. operands
Register
file
read port 1
read port 2
A
D
A
D
A
D
address
data
inst
1
0
1
0
ra(15)
isRet
branchTarget
op1

## Slide 22: EX Stage – Branch Unit
Generates the isBranchTaken Signal
flags
flags.E
isBeq
flags.GT
isBgt
isUBranch
isBranchTaken
branchPC
branchTarget
op1
1
0
isRet
from OF

## Slide 23: ALU
Choose between immx and op2 based on the value of the I bit
op1
op2
immx
ALU
(Arithmetic
logic unit)
s
isImmediate
aluSignals
aluResult
A
L
U
a
n
d
m
e
m
i
n
s
t
s
1
0
A
B

## Slide 24: Inside the ALU
Adder
isAdd
isLd
isSt
isSub
isCmp
Multiplier
isMul
A
B
A
B
Divider
isDiv
A
B
isMod
Logical
unit
isOr
isNot
isAnd
Mov
isMov
B
flags
Shift
unit
isLsl
isLsr
isAsr
A
B
A
B
aluResult

## Slide 25: Disabling some Inputs
We do not want all the units of the ALU to be active at the same time because of we want to save power
The instruction will only use 1 unit
Power is dissipated when the inputs or outputs make a transition (0 → 1, 1 → 0)
  We shall avoid a transition by not letting the new inputs to propagate to units that do not require them
  They will thus have the old inputs (no switching)

## Slide 26: Use a Transmission Gate
output = input (if S = 1)
Otherwise, the output is totally disconnected from the input
S
S

## Slide 27: EX Unit
op1
op2
immx
Execute unit
ALU
(Arithmetic
logic unit)
s
isImmediate
aluSignals
flags
aluResult
flags.E
isBeq
flags.GT
isBgt
isUBranch
isBranchTaken
ALU and mem insts
1
0
A
B
branchPC
branchTarget
op1
1
0
isRet
from OF

## Slide 28: MA Unit
ldResult
aluResult
Memory unit
isLd
isSt
Data memory
mar
mdr
32
32
32
mar
mdr
memory
data reg.
memory
address reg.
op2

## Slide 29: RW Unit
register writeback unit
ldResult
aluResult
32
32
result
isLd
read port 1
read port 2
write port
rd (inst[23:26])
A
D
A
D
A
D
Register
file
isWb
E
A
D
address
data
E
enable
10
pc
32
01
00
isCall
0
1
ra(15)
isCall
4

## Slide 30
pc
1
0
Instruction
memory
1
0
ALU
f
l
a
g
s
Immediate and
branch target
Register
file
unit
Data memory
Memory
unit
mar
i
s
B
e
q
i
s
B
g
t
i
s
U
B
r
a
n
c
h
pc + 4
rs1
rs2
rd
Instruction
1
0
immx
op2
op1
Branch
Control
unit
isSt
isImmediate
aluSignals
isLd
isSt
mdr
isWb
isBranchTaken
B
A
1
0
ra(15)
isRet
01
isRet
01
isLd
data
rd
00
10
4
isCall
ra(15)
0
1
pc
data
reg

## Slide 31: Outline
Outline of a Processor
Detailed Design of each Stage
The Control Unit
Microprogrammed Processor
Microassembly Language
The Microcontrol Unit

## Slide 32: The Ha rdwired Control Unit
Given the opcode and the immediate bit
  It generates all the control signals
Control
unit
opcode
inst[28:32]
I bit
inst[27]
control
signals

## Slide 33: Control Signals
SerialNo.
Signal
Condition
1
isSt
Instruction: st
2
isLd
Instruction: ld
3
isBeq
Instruction: beq
4
isBgt
Instruction: bgt
5
isRet
Instruction: ret
6
isImmediate
I bit set to 1
7
isWb
Instructions: add, sub, mul, div, mod,
and, or, not, mov, ld, lsl, lsr, asr, call
8
isUBranch
Instructions: b, call, ret
9
isCall
Instructions: call

## Slide 34: Control Signals – II
10
isAdd
Instructions: add, ld, st
11
isSub
Instruction: sub
12
isCmp
Instruction: cmp
13
isMul
Instruction: mul
14
isDiv
Instruction: div
15
isMod
Instruction: mod
16
isLsl
Instruction: lsl
17
isLsr
Instruction: lsr
18
isAsr
Instruction: asr
19
isOr
Instruction: or
20
isAnd
Instruction: and
21
isNot
Instruction: not
22
isMov
Instruction: mov
aluSignal

## Slide 35: Control signal Logic
op5
op3
op5
op4
op2
op1
opcode
I
immediate bit
Serial No.
Signal
isSt
isLd
isBeq
isBgt
isRet
isImmediate
isWb
isUbranch
isCall
Condition
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
I
~(op5 + op5.op3.op1.(op4 + op2)) +
op5.op4.op3.op2.op1
op5.op4.(op3.op2 + op3.op2.op1)
op5.op4.op3.op2.op1
1
2
3
4
5
6
7
8
9

## Slide 36: Control Signal Logic - II
isAdd
isSub
isCmp
isMul
isDiv
isMod
isLsl
isLsr
isAsr
isOr
isAnd
isNot
isMov
aluSignals
op5.op4.op3.op2.op1 + op5.op4.op3.op2
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1
op5.op4.op3.op2.op1

## Slide 37: Outline
Outline of a Processor
Detailed Design of each Stage
The Control Unit
Microprogrammed Processor
Microassembly Language
The Microcontrol Unit

## Slide 38: Microprogramming
Idea of microprogramming
  Expose the elements in a processor to software
  Implement instructions as dedicated software routines
Why make the implementation of instructions flexible ?
  Dynamically change their behaviour
  Fix bugs in implementations
  Implement very complex instructions

## Slide 39: Microprogrammed Data Path
Expose all the state elements to dedicated system software – firmware
Write dedicated routines in firmware for implementing each instruction
Basic idea
  1 SimpleRisc Instruction → Several micro instructions
  Execute each micro instruction
  We require a microprogram counter, and microinstruction memory

## Slide 40: Fetch Unit
The pc is used to access the instruction memory.
The contents of the instruction are saved in the instruction register (ir)
Shared bus
pc
Instruction memory
ir

## Slide 41: Decode Unit
Divide the contents of ir into different fields
  I, rd, rs1, rs2, immx, and branchTarget
Shared bus
ir
rd
rs1
rs2
I
Immediate
unit
immx
calc.
offset
branchTarget
pc

## Slide 42: The Register File
regSrc (id of the source/dest register)
regData (data to be stored)
regVal (register value)
Register
file
regSrc
regData
regVal
args
Shared bus

## Slide 43: ALU
A, B → ALU operands
args → ALU operation type
aluResult → ALU Result
Shared bus
ALU
A
B
aluResult
flags
flags.E
flags.GT
args

## Slide 44: Memory Unit
Shared bus
Data
memory
mar
mdr
ldResult
args

## Slide 45: Microprogrammed Data Path
Shared bus
pc
Instruction memory
ir
rd
rs1
rs2
I
Immediate
unit
immx
calc.
offset
branchTarget
Register
file
regSrc
regData
regVal
ALU
A
B
aluResult
flags
flags.E
flags.GT
Data
memory
mar
mdr
ldResult
μ control
unit
opcode
args
args
args

## Slide 46: Outline
Outline of a Processor
Detailed Design of each Stage
The Control Unit
Microprogrammed Processor
Microassembly Language
The Microcontrol Unit

## Slide 47: Internal Registers
SerialNo.
Register
Size
(bits)
Function
1
pc
32
program counter
2
ir
32
instruction register
3
I
1
immediate bit in the instruction
4
rd
4
destination register id
5
rs
1
4
id of the first source register
6
rs
2
4
id of the second source register
7
immx
32
immediate embedded in the
instruction (after processing
modifiers)
8
branchTarget
32
branch target, computed as the
sum of the PC and the offset
embedded in the instruction
9
regSrc
4
contains the id of the register
that needs to be accessed in the
register file
10
regData
32
contains the data to be written
into the register file

## Slide 48: Internal Registers - II
11
regVal
32
value read from the register file
12
A
32
first operand of the AlU
13
B
32
second operand of the ALU
14
flags.E
1
the equality flag
15
flags.GT
1
the greater than flag
16
aluResult
32
the ALU result
17
mar
32
memory address register
18
mdr
32
memory data register
19
ldResult
32
the value loaded from memory

## Slide 49: Microinstructions
Basic Instructions
mloadIR → Loads the instruction register (ir) with the contents of the instruction.
mdecode → Waits for 1 cycle. Meanwhile, all the decode registers get populated
mswitch → Loads the set of micro instructions corresponding to a program instruction.

## Slide 50: Move Microinstructions
mmov r1, r2 : r1 ← r2
mmov r1, r2, <args> : r1 ← r2, send the value of args on the bus
mmovi r1, <imm> : r1 ← imm

## Slide 51: Add and Branch Microinstructions
madd r1, imm, <args>
  r1 ← r1 + imm
  send <args> on the bus
mbeq r1, imm, <label>
  if (r1 == imm), μpc = addr(label)
mb <label>
  μpc = addr(label)

## Slide 52: Summary of Microinstructions
SerialNo.
Microinstruction
Semantics
1
mloadIR
ir ← [pc]
2
mdecode
populate all the decode registers
3
mswitch
jump to the μpc corresponding to
the opcode
4
mmov reg1, reg2, < args >
reg1 ← reg2, send the value of
args to the unit that owns reg1,
< args > is optional
5
mmovi reg1, imm, < args >
reg1 ← imm, < args > is optional
6
madd reg1, imm, < args >
reg1 ← reg1+imm, < args > is
optional
7
mbeq reg1, imm, < label >
if (reg1 = imm) μpc ← addr(label)
8
mb <label>
μpc ← addr(label)

## Slide 53: Implementing Instructions in Microcode
The microcode preamble
  Load the program counter
  Decode the instruction
  Add 4 to the pc
  Switch to the first microinstruction in the microcode sequence of the prog. instruction
.begin:
mloadIR
mdecode
madd pc, 4
mswitch

## Slide 54: 3 Address Format ALU Instruction
/* transfer the first operand to the ALU */
mmov regSrc, rs1, <read>
mmov A, regVal
/* check the value of the immediate register */
mbeq I, 1, .imm
/* second operand is a register */
mmov regSrc, rs2, <read>
mmov B, regVal, <aluop>
mb .rw
/* second operand is an immediate */
.imm:
mmov B, immx, <aluop>
/* write the ALU result to the register file*/
.rw:
mmov regSrc, rd
mmov regData, aluResult, <write>
mb .begin

## Slide 55: The mov Instruction
mov instruction
/* check the value of the immediate register */
mbeq I, 1, .imm
/* second operand is a register */
mmov regSrc, rs2, <read>
mmov regData, regVal
mb .rw
/* second operand is an immediate */
.imm:
mmov regData, immx
/* write to the register file*/
.rw:
mmov regSrc, rd, <write>
/* jump to the beginning */
mb .begin

## Slide 56: The not Instruction
not instruction
/* check the value of the immediate register */
mbeq I, 1, .imm
/* second operand is a register */
mmov regSrc, rs2, <read>
mmov B, regVal, <not> /* ALU operation */
mb .rw
/* second operand is an immediate */
.imm:
mmov B, immx, <not> /* ALU operation */
/* write to the register file*/
.rw:
mmov regData, aluResult
mmov regSrc, rd, <write>
/* jump to the beginning */
mb .begin

## Slide 57: The cmp Instruction
cmp instruction
/* transfer rs1 to register A */
mov regSrc, rs1, <read>
mov A, regVal
/* check the value of the immediate register
mbeq I, 1, .imm
/* second operand is a register */
mmov regSrc, rs2, <read>
mmov B, regVal, <cmp> /* ALU operation */
mb .begin
/* second operand is an immediate */
.imm:
mmov B, immx, <cmp> /* ALU operation */
mb .begin

## Slide 58: The nop Instruction
mb .begin

## Slide 59: The ld Instruction
ld instruction
/* transfer rs1 to register A */
mmov regSrc, rs1, <read>
mmov A, regVal
/* calculate the effective address */
mmov B, immx, <add> /* ALU operation */
/* perform the load */
mmov mar, aluResult, <load>
/* write the loaded value to the register file */
mmov regData, ldResult
mmov regSrc, rd, <write>
/* jump to the beginning */
mb .begin

## Slide 60: The st Instruction
st instruction
/* transfer rs1 to register A */
mmov regSrc, rs1, <read>
mmov A, regVal
/* calculate the effective address */
mmov B, immx, <add> /* ALU operation */
/* perform the store */
mmov mar, aluResult
mmov regSrc, rd, <read>
mmov mdr, regVal, <store>
/* jump to the beginning */
mb .begin

## Slide 61: beq and bgt Instructions
beq instruction
/* test the flags register
mbeq flags.E, 1, .branch
mb .begin
.branch:
mmov pc, branchTarget
mb .begin
bgt instruction
/* test the flags register
mbeq flags.GT, 1, .branch
mb .begin
.branch:
mmov pc, branchTarget
mb .begin

## Slide 62: call Instruction
call instruction
/* save PC + 4 in the return address register */
mmov regData, pc
mmovi regSrc, 15, <write>
/* branch to the function */
mmov pc, branchTarget
mb .begin

## Slide 63: ret Instruction
ret instruction
/* save the contents of the return
address register in the PC */
mmovi regSrc, 15, <read>
mmov pc, regVal
mb .begin

## Slide 64: Example
Change the call instruction to store the return address on the stack. The
preamble need not be shown.
Answer:
stack based call instruction
/* read the stack pointer */
mmovi regSrc, 14, <read>
madd regVal, -4 /* decrement the stack pointer */
/* set the memory address to the stack pointer */
mmov mar, regVal
/* update the stack pointer */
mmov regData, regVal, <write> /* update stack pointer */
/* write the return address to the stack */
mmov mdr, pc, <store>
/* jump to the beginning */
mb .begin

## Slide 65: Outline
Outline of a Processor
Detailed Design of each Stage
The Control Unit
Microprogrammed Processor
Microassembly Language
The Microcontrol Unit

## Slide 66: Shared Bus
Decode unit
pc
Reg. file, ALU, Mem unit
Reg. file, ALU, Mem unit
pc
µ imm
Microcontrol unit
Shared bus
Write bus
Read bus
isMBranch

## Slide 67: Encoding an Instruction
Vertical Microprogramming (45 bit inst.)
  3 bits → type of instruction
  5 bits → source register
  5 bits → destination register
  12 bits → immediate
  10 bit → branch target in microcode memory
  10 bit → args value
    3 bits → (unit id)
    7 bits → operation code

## Slide 68: Horizontal Microprogramming
Encoding
    10 bits → branch target
    12 bits → immediate
    10 bits → args
    33 bits → bit vector of all the control signals
Total size of the encoded instruction : 65 bits

## Slide 69: Vertical Microprogramming
μ
pc
Microprogram
memory
Decode
unit
Execute
unit
Data path
control
signals
1
μbranchTarget
Shared bus
switch
μ
mux
opcode

## Slide 70: Horizontal Microprogramming
μ
pc
Microprogram
memory
Execute
unit
Data path
control
signals
1
μbranchTarget
Shared bus
switch
isMBranch
opcode
μ
mux
M1

## Slide 71
THE END