## Slide 1
Processor Design
The Language of Bits
Prof. Smruti Ranjan Sarangi IIT Delhi
Basic Computer Architecture
PowerPoint Slides
Chapter 10: Principles of Pipelining

## Slide 2
Download the pdf of the book
www.basiccomparch.com
videos
Slides, software, solution manual
Print version
(Publisher: WhiteFalcon, 2021)
Available on e-commerce sites.
The pdf version of the book and all the learning resources can be freely downloaded from the website: www.basiccomparch.com
2nd version

## Slide 3: Outline
Overview of Pipelining
A Pipelined Data Path
Pipeline Hazards
Pipeline with Interlocks
Forwarding
Performance Metrics
Interrupts/ Exceptions

## Slide 4: Up till now ….
We have designed a processor that can execute all the SimpleRisc Instructions
We have look at two styles :
  With a hardwired control unit
  Microprogrammed control unit
    Microprogrammed data path
    Microassembly Language
    Microinstructions

## Slide 5: Designing Efficient Processors
Microprogrammed processors are much slower that hardwired processors
Even hardwired processors
  Have a lot of waste !!!
  We have 5 stages.
  What is the IF stage doing, when the MA stage is active ?
    ANSWER : It is idling

## Slide 6: The Notion of Pipelining
Let us go back to the car assembly line
  Is the engine shop idle, when the paint shop is painting a car ?
  NO : It is building the engine of another car
  When this engine goes to the body shop, it builds the engine of another car, and so on ….
  Insight :
    Multiple cars are built at the same time.
    A car proceeds from one stage to the next

## Slide 7: Pipelined Processors
The IF, ID, EX, MA, and RW stages process 5 instructions simultaneously
Each instruction proceeds from one stage to the next
This is known as pipelining
Instruction
Fetch
(IF)
Operand
Fetch
(OF)
Execute
(EX)
Memory
Access
(MA)
Register
Write
(RW)
inst 4
inst 3
inst 2
inst 1

## Slide 8: Advantages of Pipelining
We keep all parts of the data path, busy all the time
Let us assume that all the 5 stages do the same amount of work
  Without pipelining, every T seconds, an instruction completes its execution
  With pipelining, every T/5 seconds, a new instruction completes its execution

## Slide 9: Design of a Pipeline
Splitting the Data Path
  We divide the data path into 5 parts : IF, OF, EX, MA, and RW
Timing
  We insert latches (registers) between consecutive stages
  4 Latches → IF-OF, OF-EX, EX-MA, and MA-RW
  At the negative edge of a clock, an instruction moves from one stage to the next

## Slide 10: Pipelined Data Path with Latches
Add a latch between subsequent stages.
  Triggered by a negative clock edge
Instruction
Fetch
(IF)
Operand
Fetch
(OF)
Execute
(EX)
Memory
Access
(MA)
Register
Write
(RW)
Latches

## Slide 11: The Instruction Packet
What travels between stages ?
  ANSWER : the instruction packet
Instruction Packet
  Instruction contents
  Program counter
  All intermediate results
  Control signals
Every instruction moves with its entire state, no interference between instructions

## Slide 12: Outline
Overview of Pipelining
A Pipelined Data Path
Pipeline Hazards
Pipeline with Interlocks
Forwarding
Performance Metrics
Interrupts/ Exceptions

## Slide 13: IF Stage
Instruction contents saved in the instruction field
IF/OF Register
instruction
instruction

## Slide 14: OF Stage
A, B → ALU Operands, op2 (store operand), control (set of all control signals)
Control
unit
control
branchTarget
Immediate and
branch target
instruction
instruction
op2

## Slide 15: EX Stage
aluResult → result of the ALU Operation
op2, control, pc, instruction (passed from OF-EX)
ALU
?ags
Branch
unit
isBeq
isBgt
isUBranch
aluSignals
instruction
pc
control
branchTarget
B
A
pc
control
aluResult
op2
instruction
op2
isBranchTaken
1
0
isRet
OF-EX
EX-MA
branchPC
To fetch unit
flags

## Slide 16: MA Stage
ldResult → result of the load operation
aluResult, control, pc, instruction (passed from EX-MA)
Data memory
Memory
unit
mar
mdr
isLd
isSt
pc
control
aluResult
instruction
op2
pc
control
ldResult
instruction
aluResult
EX-MA
MA-RW

## Slide 17: RW Stage
Register
file
pc
control
ldResult
instruction
01
isLd
data
rd
isWb
aluResult
00
10
4
isCall
ra(15)
0
1
A
D
E
A
D
address
data
E
enable

## Slide 18
DRAFT
C Smruti R. Sarangi <srsarangi@cse.iitd.ac.in>
pc
1
0
Instruction
memory
1
0
ALU
flags
Immediate and
branch target
Register
file
Branch
unit
Data
memory
Memory
unit
mar
mdr
isBeq
isBgt
isUBranch
pc + 4
rs2
rd
instruction
1
0
immx
op2
op1
reg
isSt
isImmediate
aluSignals
Control
unit
isLd
isSt
instruction
pc
instruction
pc
control
branchTarget
B
A
pc
control
aluResult
op2
instruction
op2
pc
control
ldResult
instruction
isBranchTaken
01
isLd
data
rd
isWb
data
isWb
rs1
1
0
ra(15)
isRet
1
0
isRet
aluResult
00
10
4
isCall
ra(15)
0
1

## Slide 19: Abridged Diagram
IF-OF
Fetch
unit
Instruction
memory
Immediate
and branch
unit
Register
file
Control
unit
OF-EX
op2
op1
ALU
Unit
Branch
unit
flags
EX-MA
Memory
unit
Data
memory
MA-RW
Register
write unit

## Slide 20: Outline
Overview of Pipelining
A Pipelined Data Path
Pipeline Hazards
Pipeline with Interlocks
Forwarding
Performance Metrics
Interrupts/ Exceptions

## Slide 21: Pipeline Hazards
Now, let us consider correctness
Let us introduce a new tool → Pipeline Diagram
[1]: add r1, r2, r3
[2]: sub r4, r5, r6
[3]: mul r8, r9, r10
1
1
1
1
1
2
2
2
2
2
3
3
3
3
3
IF
OF
EX
MA
RW
1
2
3
4
5
6
7
8
9
Clock cycles

## Slide 22: Rules for Constructing a Pipeline Diagram
It has 5 rows
  One per each stage
  The rows are named : IF, OF, EX, MA, and RW
Each column represents a clock cycle
Each cell represents the execution of an instruction in a stage
  It is annotated with the name(label) of the instruction
Instructions proceed from one stage to the next across clock cycles

## Slide 23: Example
[1]: add r1, r2, r3
[2]: sub r4, r2, r5
[3]: mul r5, r8, r9
1
1
1
1
1
2
2
2
2
2
3
3
3
3
3
IF
OF
EX
MA
RW
1
2
3
4
5
6
7
8
9
Clock cycles

## Slide 24: Data Hazards
Instruction 2 will read incorrect values !!!
[1]: add r1, r2, r3
[2]: sub r3, r1, r4
1
1
1
1
1
2
2
2
2
2
IF
OF
EX
MA
RW
1
2
3
4
5
6
7
8
9
clock cycles

## Slide 25: Data Hazard
Definition: A hazard is defined as the possibility of erroneous execution of an
instruction in a pipeline. A data hazard represents the possibility of erroneous
execution because of the unavailability of data, or the availability of incorrect
data.
This situation represents a data hazard
In specific,
  it is a RAW (read after write) hazard
The earliest we can dispatch instruction 2, is cycle 5

## Slide 26: Other Types of Data Hazards
Our pipeline is in-order
We will only have RAW hazards in our pipeline.
Out-of-order pipelines can have WAR and WAW hazards
Definition: In an in-order pipeline (such as ours), a preceding instruction is
always ahead of a succeeding instruction in the pipeline. Modern processors
however use out-of-order pipelines that break this rule. It is possible for later
instructions to execute before earlier instructions.

## Slide 27: WAW Hazards
Instruction [2] cannot write the value of r1, before instruction [1] writes to it, will lead to a WAW hazard
[1]: add r1, r2, r3
[2]: sub r1, r4, r3

## Slide 28: WAR Hazards
Instruction [2] cannot write the value of r2, before instruction [1] reads it → will lead to a WAR hazard
[1]: add r1, r2, r3
[2]: add r2, r5, r6

## Slide 29: Control Hazards
If the branch is taken, instructions [2] and [3], might get fetched, incorrectly
[1]: beq .foo
[2]: mov r1, 4
[3]: add r2, r4, r3
...
...
.foo:
[100]: add r4, r1, r2

## Slide 30: Control Hazard – Pipeline Diagram
The two instructions fetched immediately after a branch instruction might have been fetched incorrectly.
[1]: beq .foo
[2]: mov r1, 4
[3]: add r2, r4, r3
1
1
1
1
1
2
2
2
2
2
3
3
3
3
3
IF
OF
EX
MA
RW
1
2
3
4
5
6
7
8
9
Clock cycles

## Slide 31: Control Hazards
The two instructions fetched immediately after a branch instruction might have been fetched incorrectly.
These instructions are said to be on the wrong path
A control hazard represents the possibility of erroneous execution in a pipeline because instructions in the wrong path of a branch can possibly get executed and save their results in memory, or in the register file

## Slide 32: Structural Hazards
A structural hazard may occur when two instructions have a conflict on the same set of resources in a cycle
Example :
  Assume that we have an add instruction that can read one operand from memory
  add r1, r2, 10[r3]

## Slide 33: Structural Hazards - II
This code will have a structural hazard
  [3] tries to read 10[r3] (MA unit) in cycle 4
  [1] tries to write to 20[r5] (MA unit) in cycle 4
Does not happen in our pipeline
[1]: st r4, 20[r5]
[2]: sub r8, r9, r10
[3]: add r1, r2, 10[r3]

## Slide 34: Solutions in Software
Data hazards
  Insert nop instructions, reorder code
[1]: add r1, r2, r3
[2]: sub r3, r1, r4
[1]: add r1, r2, r3
[2]: nop
[3]: nop
[4]: nop
[5]: sub r3, r1, r4

## Slide 35: Code Reordering
add r1, r2, r3
add r4, r1, 3
add r8, r5, r6
add r9, r8, r5
add r10, r11, r12
add r13, r10, 2
add r1, r2, r3
add r8, r5, r6
add r10, r11, r12
nop
add r4, r1, 3
add r9, r8, r5
add r13, r10, 2

## Slide 36: Control Hazards
Trivial Solution : Add two nop instructions after every branch
Better solution :
  Assume that the two instructions fetched after a branch are valid instructions
  These instructions are said to be in the delay slots
  Such a branch is known as a delayed branch

## Slide 37: Example with 2 Delay Slots
The compiler transfers instructions before the branchto the delay slots.
If it cannot find 2 valid instructions, it inserts nops.
add r1, r2, r3
add r4, r5, r6
b .foo
add r8, r9, r10
b .foo
add r1, r2, r3
add r4, r5, r6
add r8, r9, r10

## Slide 38: Outline
Overview of Pipelining
A Pipelined Data Path
Pipeline Hazards
Pipeline with Interlocks
Forwarding
Performance Metrics
Interrupts/ Exceptions

## Slide 39: Why interlocks ?
We cannot always trust the compiler to do a good job, or even introduce nop instructions correctly.
Compilers now need to be tailored to specific hardware.
We should ideally not expose the details of the pipeline to the compiler (might be confidential also)
Hardware mechanism to enforce correctness → interlock

## Slide 40: Two kinds of Interlocks
Data-Lock
  Do not allow a consumer instruction to move beyond the OF stage till it has read the correct values. Implication : Stall the IF and OF stages.
Branch-Lock
  We never execute instructions in the wrong path.
The hardware needs to ensure both these conditions.

## Slide 41: Comparison between Software and Hardware
Attribute
Software
Hardware(withinterlocks)
Portability
Limited to a specific
processor
Programs can be run on any
processor irrespective of the nature
of the pipeline
Branches
Possible to have no
performance penalty, by
using delay slots
RAW
hazards
Possible to eliminate
them through code
scheduling
Need to stall the pipeline
Performance
Highly
dependent on the
nature of the program
The basic version of a pipeline with
interlocks is expected to be slower
than the version that relies on
software
Need to stall the pipeline for 2 cycles
in our design

## Slide 42: Conceptual Look at Pipeline with Interlocks
We have a RAW hazard
We need to stall, instruction [2] at the OF stage for 3 cycles.
We need to keep sending nop instructions to the EX stage during these 3 cycles
[1]: add r1, r2, r3
[2]: sub r4, r1, r2

## Slide 43: Example
[1]: add r1, r2, r3
[2]: sub r4, r1, r2
1
1
1
1
1
2
2
2
2
2
IF
OF
EX
MA
RW
1
2
3
4
5
6
7
8
9
Clock cycles
bubble
2
2
2

## Slide 44: A Pipeline Bubble
A pipeline bubble is inserted into a stage, when the previous stage needs to be stalled
It is a nop instruction
To insert a bubble
  Create a nop instruction packet
  OR, Mark a designated bubble bit to 1

## Slide 45: Bubbles in the Case of a Branch Instruction
[1]: beq. foo
[2]: add r1, r2, r3
[3]: sub r4, r5, r6
....
....
.foo:
[4]: add r8, r9, r10
1
1
1
1
1
2
2
4
4
4
IF
OF
EX
MA
RW
1
2
3
4
5
6
7
8
9
Clock cycles
bubble
4
3
4

## Slide 46: Control Hazards and Bubbles
We know that an instruction is a branch in the OF stage
When it reaches the EX stage and the branch is taken, let us convert the instructions in the IF, and OF stages to bubbles
Ensures the branch-lock condition

## Slide 47: Ensuring the Data-Lock Condition
When an instruction reaches the OF stage, check if it has a conflict with any of the instructions in the EX, MA, and RW stages
If there is no conflict, nothing needs to be done
Otherwise, stall the pipeline (IF and OF stages only)

## Slide 48
Algorithm 5: Algorithm to detect conflicts between instructions
Data: instructions, [A], and [B]
Result: conflict exists (true), no conflict (false)
if [A].opcode ∈ (nop,b,beq,bgt,call) then
/* Does not read from any register */
return false
end
if [B].opcode ∈ (nop, cmp, st, b, beq, bgt, ret) then
/* Does not write to any register */
return false
end
/* Set the sources */
src1 ← [A].rs1
src2 ← [A].rs2
if [A].opcode = st then
src2 ← [A].rd
end
if [A].opcode = ret then
src1 ← ra
end
hasSrc1 ← true
if ([A] ∈ (not, mov)) hasSrc1 ← false

## Slide 49
dest ← [B].rd
if [B].opcode = call then
dest ← ra
end
/* Check the second operand to see if it is a register */
hasSrc2 ← true
if [A].opcode ≠ ( st) then
if [A].I = 1 then
hasSrc2 ← false
end
end
/* Detect conflicts */ */
if (hasSrc1 = true) and (src1 = dest) then
return true
end
else if (hasSrc2 = true) and (src2 = dest) then
return true
end
return false

## Slide 50: How to Stall a Pipeline ?
Disable the write functionality of :
  The IF-OF register
  and the Program Counter (PC)
To insert a bubble
  Write a bubble (nop instruction) into the OF-EX register

## Slide 51: Data Path with Interlocks (Data-Lock)
I
F
-
O
F
Instruction
memory
Immediate
and branch
unit
Register
file
Control
unit
O
F
-
E
X
op2
op1
ALU
unit
Branch
unit
flags
E
X
-
M
A
Memory
unit
Data
memory
M
A
-
R
W
Register
write unit
Fetch
unit
Data-lock Unit
stall
bubble
stall

## Slide 52: Ensuring the Branch-Lock Condition
Option 1 :
  Use delay slots (interlocks not required)
Option 2 :
  Convert the instructions in the IF, and OF stages, to bubbles once a branch instruction reaches the EX stage.
  Start fetching from the next PC (not taken) or the branch target (taken)

## Slide 53: Ensuring the Branch-Lock Condition - II
Option 3
  If the branch instruction in the EX stage is taken, then invalidate the instructions in the IF and OF stages. Start fetching from the branch target.
  Otherwise, do not take any special action
  This method is also called predict not-taken (we shall use this method because it is more efficient that option 2)

## Slide 54: Data Path with Interlocks
IF-OF
Fetch
unit
Instruction
memory
Immediate
and branch
unit
Register
file
Control
unit
OF-EX
op2
op1
ALU
unit
Branch
unit
flags
EX-MA
Memory
unit
Data
memory
MA-RW
Register
write unit
Data-lock unit
stall
bubble
stall
Branch-lock unit
isBranchTaken
bubble

## Slide 55: Outline
Overview of Pipelining
A Pipelined Data Path
Pipeline Hazards
Pipeline with Interlocks
Forwarding
Performance Metrics
Interrupts/ Exceptions

## Slide 56: Relook at the Pipeline Diagram
(a) → with bubbles
(b) → no bubbles (may lead to wrong results)
[1]: add r1, r2, r3
[2]: sub r4, r1, r2
1
1
1
1
1
2
2
2
2
2
IF
OF
EX
MA
RW
1
2
3
4
5
6
7
8
9
Clock cycles
bubble
2
2
1
1
1
1
1
2
2
2
2
1
2
3
4
5
6
7
8
9
Clock cycles
2
(a)
(b)
2

## Slide 57: Crucial Insight (Figure (b))
When does instruction 2 need the value of r1 ?
  ANSWER : Cycle 3, OF Stage (wrong!!!)
  CORRECT ANSWER : Cycle 4, EX Stage
When does instruction 1 produce the value of r1 ?
  ANSWER : Cycle 5, RW Stage (wrong!!!)
  CORRECT ANSWER : End of Cycle 3, EX Stage

## Slide 58: Forwarding
If the correct value is already there in another stage, we can forward it.
[1]: add r1, r2, r3
[2]: sub r4, r1, r2
1
1
1
1
1
2
2
2
2
1
2
3
4
5
6
7
8
9
Clock cycles
2
IF
OF
EX
MA
RW

## Slide 59: Forwarding from MA to EX
Fowarding in cycle 4 from instruction [1] to [2]
[1]: add r1, r2, r3
[2]: sub r4, r1, r2
1
1
1
1
1
2
2
2
2
1
2
3
4
5
6
7
8
9
Clock cycles
2
IF
OF
EX
MA
RW

## Slide 60: Different Forwarding Paths
We need to add a multitude of forwarding paths
Rules for creating forwarding paths
  Add a path from a later stage to an earlier stage
  Try to add a forwarding path as late as possible. For, example, we avoid the EX → OF forwarding path, since we have the MA → EX forwarding path
  The IF stage is not a part of any forwarding path.

## Slide 61: Forwarding Path
3 Stage Paths
  RW → OF
2 Stage Paths
  RW → EX
  MA → OF (X Not Required)
1 Stage Paths
  RW → MA (load to store)
  MA → EX (ALU Instructions, load, store)
  EX → OF (X Not Required)

## Slide 62: Forwarding Paths : RW → MA
[1]: ld r1, 4[r2]
[2]: st r1, 10[r3]
1
1
1
1
1
2
2
2
2
1
2
3
4
5
6
7
8
9
Clock cycles
2
IF
OF
EX
MA
RW

## Slide 63: Forwarding Paths : RW → EX
[1]: ld r1, 4[r2]
[2]: st r8, 10[r3]
[3]: add r2, r1, r4
1
1
1
1
1
2
2
2
2
1
2
3
4
5
6
7
8
9
Clock cycles
2
IF
OF
EX
MA
RW
3
3
3
3
3

## Slide 64: Forwarding Path : MA → EX
[1]: add r1, r2, r3
[2]: sub r4, r1, r2
1
1
1
1
1
2
2
2
2
1
2
3
4
5
6
7
8
9
Clock cycles
2
IF
OF
EX
MA
RW

## Slide 65: Forwarding Path : RW → OF
[1]: ld r1, 4[r2]
[2]: st r4, 10[r3]
1
1
1
1
1
2
2
2
2
1
2
3
4
5
6
7
8
9
Clock cycles
2
IF
OF
EX
MA
RW
[3]: st r5, 10[r6]
3
3
3
3
3
4
4
4
4
4
[4]: sub r7, r1, r2

## Slide 66: Data Hazards with Forwarding
Forwarding has unfortunately not eliminated all data hazards
We are left with one special case.
Load-use hazard
  The instruction immediately after a load instruction has a RAW dependence with it.

## Slide 67: Load-Use Hazard
Cannot forward (arrow goes backwards in time)
Need to add a bubble (then use RW → EX forwarding)
[1]: ld r1, 10[r2]
1
1
1
1
1
2
2
2
2
1
2
3
4
5
6
7
8
9
Clock cycles
2
IF
OF
EX
MA
RW
[2]: sub r4, r1, r2

## Slide 68: Implementation of Forwarding
At every stage there is a choice of inputs for each functional unit
  Use the default inputs from the previous stage
  OR, use one of the forwarded inputs
  Use a multiplexer to choose between the inputs
  A dedicated forwarding unit generates the signals for the forwarding multiplexers

## Slide 69: OF Stage with Forwarding
IF-OF
Immediate
and branch
unit
Register
file
Control
unit
OF-EX
op2
op1
from RW
B
A
op2
M1
M2
M'

## Slide 70: EX Stage with Forwarding
OF-EX
ALU
unit
Branch
unit
flags
EX-MA
op2
from MA
from RW
to IF
M3
M4
M5
A
B

## Slide 71: MA Stage with Forwarding
EX-MA
Memory
unit
Data
memory
MA-RW
from RW
to EX
to EX and OF
op2
aluResult
M6

## Slide 72: RW Stage with Forwarding
MA-RW
Register
write unit
to OF, EX, and MA

## Slide 73: Data Path with Forwarding
IF-OF
Fetch
unit
Instruction
memory
Immediate
and branch
unit
Register
file
Control
unit
OF-EX
op2
op1
ALU
unit
Branch
unit
flags
EX-MA
Memory
unit
Data
memory
MA-RW
Register
write unit
op2

## Slide 74: Forwarding Conditions
Determine if there is a conflict between two instructions in different stages
  Find if there is a conflict for the first operand (rs1/ ra)
  Find if there is a conflict for the second operand (rs2/rd)
Always forward from the latest instruction (that is earlier than the current instruction)

## Slide 75
Algorithm 6: Conflict on the first operand (rs1/ra)
Data: instructions, [A], and [B] (possible forwarding: [B] → [A])
Result: conflict exists on rs1/ra (true), no conflict (false)
if [A].opcode ∈ (nop,b,beq,bgt,call,not,mov) then
/* Does not read from any register */
return false
end
if [B].opcode ∈ (nop, cmp, st, b, beq, bgt, ret) then
/* Does not write to any register */
return false
end
/* Set the sources */
src1 ← [A].rs1
if [A].opcode = ret then
src1 ← ra
end
/* Set the destination */
dest ← [B].rd
if [B].opcode = call then
dest ← ra
end
/* Detect conflicts */
if src1 = dest then
return true
end
return false

## Slide 76
Algorithm 7: Conflict on the second operand (rs2/rd)
Data: instructions, [A], and [B] (possible forwarding: [B] → [A])
Result: conflict exists on second operand (rs2/rd) (true), no conflict
(false)
if [A].opcode ∈ (nop,b,beq,bgt,call) then
/* Does not read from any register */
return false
end
if [B].opcode ∈ (nop, cmp, st, b, beq, bgt, ret) then
/* Does not write to any register */
return false
end
/* Check the second operand to see if it is a register */
if [A].opcode ≠( st) then
if [A].I = 1 then
return false
end
end
/* Set the sources */
src2 ← [A].rs2
if [A].opcode = st then
src2 ← [A].rd
end

## Slide 77
/* Set the destination */
dest ← [B].rd
if [B].opcode = call then
dest ← ra
end
/* Detect conflicts */
if src2 = dest then
return true
end
return false

## Slide 78: Interlocks with Forwarding
Data-Lock
  We need to only check for the load-use hazard
  If the instruction in the EX stage is a load, and the instruction in the OF stage uses its loaded value, then stall for 1 cycle
Branch-Lock
  Remains the same as before.

## Slide 79: The Curious Case of the call instruction
The call instruction generates the value of ra in the RW stage
Any instruction that uses the value of ra (such as ret) still works correctly !!!
Prove it ....

## Slide 80: Complete Data Path
IF-OF
Fetch
unit
Instruction
memory
Immediate
and branch
unit
Register
file
Control
unit
OF-EX
op2
op1
Execute
unit
Branch
unit
flags
EX-MA
Memory
unit
Data
memory
MA-RW
Register
write unit
op2
Data-lock Unit
stall
Branch-lock Unit
isBranchTaken
bubble
Forwarding unit
Notes: Arrow difference in right side

## Slide 81: Outline
Overview of Pipelining
A Pipelined Data Path
Pipeline Hazards
Pipeline with Interlocks
Forwarding
Performance Metrics
Interrupts/ Exceptions

## Slide 82: Measuring Performance
What do we mean by the performance of a processor ?
  ANSWER : Almost nothing
What should we ask instead ?
  What is the performance with respect to a given program or a set of programs ?
  Performance is inversely proportional to the time it takes to execute a program

## Slide 83: Computing the Time a Program Takes
CPI → Cycles per instruction
f → frequency (cycles per second)

## Slide 84: The Performance Equation
IPC → 1/CPI (Instructions per Cycle)
What are the units of performance ?
  ANSWER : arbitrary

## Slide 85: Number of Instructions (#insts)
Note that these are dynamic instructions
  NOT static instructions
A smart compiler can reduce the number of executed instructions
Static Instruction: The binary or executable of a program, contains a list of static instructions.
Dynamic Instruction: A dynamic instruction is a running instance of a static instruction, which is created by the processor when an instruction
enters the pipeline.

## Slide 86: Number of Instructions(#insts) – 2
Dead code removal
  Often programmers write code that does not determine the final output
  This code is redundant
  It can be identified and removed by the compiler
Function inlining
  Very small functions have a lot of overhead → call, ret instructions, register spilling, and restoring
  Paste the code of the callee in the code of the caller (known as inlining)

## Slide 87: Computing the CPI
CPI for a single cycle processor = 1
CPI for an ideal pipeline(no hazards)
  Assume we have n instructions, and k stages
  The first instruction enters the pipeline in cycle 1
  It leaves the pipeline in cycle k
  The rest of the (n-1) instructions leave in the next (n-1) consecutive cycles

## Slide 88: Computing the Maximum Frequency
Let the maximum amount of time that it takes to execute any instruction be :
  tmax (also known as algorithmic work)
Minimum clock cycle time of a single cycle pipeline → tmax
In the case of a pipeline, let us assume that all the pipeline stages are balanced
Time per stage → tmax / k

## Slide 89: Maximum Frequency - II
Let the latch delay be l
We thus have :
The minimum cycle time (1/f) is equal
to tstage . Let us thus, assume that
our cycle time is as low as possible.

## Slide 90: Performance of an Ideal Pipeline
Let us assume that the number of instructions are a constant

## Slide 91: Optimal Number of Pipeline Stages
k is inversely proportional to
k is proportional to

## Slide 92: Implications
As we increase the latch delay, we should have less pipeline stages
  We need to minimise the time wasted in accessing latches
As we increase the amount of algorithmic work, we require more pipeline stages for ideal performance
  More pipeline stages help distribute the work better, and increase the overlap across instructions

## Slide 93: Implications - II
As the number of instructions tends to ∞, the number of ideal pipeline stages also tends to ∞
  The higher startup time gets amortized in the long run

## Slide 94: A Non-Ideal Pipeline
Our ideal CPI (CPIideal = 1) is 1
However, in reality, we have stalls
Let us assume that the stall rate is a function of the program, and its nature of dependences

## Slide 95: Non-Ideal Pipeline - II
Let us assume that the stall penalty is proportional to the number of pipeline stages
Both these assumptions are strictly not correct. They are being used to make a coarse grained mathematical model.
CPI = (n+k-1)/n + rck
  r → stall rate, c → constant of proportionality

## Slide 96: Mathematical Model

## Slide 97: Mathematical Model - II

## Slide 98: Implications
For programs with a lot of dependences (high value of r) → Use less pipeline stages
For a pipeline with forwarding → c is smaller (than a pipeline that just has interlocks)
  It requires a larger number of pipeline stages for optimal performance

## Slide 99: Implications
The optimal number of pipeline stages is directly proportional to √(tmax / l)
  This ratio is not significantly changing across technologies.
  This explains why the number of pipline stages has remained more or less constant for the last 5-10 years

## Slide 100: Example
Example Consider two programs that have the following characteristics.
Program 1 |  | Program 2 | 
Instruction Type | Fraction | Instruction Type | Fraction
loads | 0.4 | loads | 0.3
Branches | 0.2 | Branches | 0.1
ratio(taken branches) | 0.5 | ratio(taken branches) | 0.4

## Slide 101: Example

## Slide 102: Performance, Architecture, Compiler
P
f
IPC
Architecture
Technology
Architecture
Compiler

## Slide 103: Outline
Overview of Pipelining
A Pipelined Data Path
Pipeline Hazards
Pipeline with Interlocks
Forwarding
Performance Metrics
Interrupts/ Exceptions

## Slide 104: What happens when you press a key ?
The keyboard logs the key press
  Converts the key to ASCII or Unicode
  Sends the code to the processor
  The processor thus receives an interrupt
  It suspends the current program
  Jumps to the interrupt handler.
  The interrupt handler draws the shape associated with the key
  The processor returns to execute the original program

## Slide 105: Exceptions
Exceptions are generated when
  A program accesses an illegal address
  We try to divide 5/0
  We issue an invalid instruction
  …
Exception are treated the same way as interrupts
  Jump to the exception handler
  Come back and start executing programs

## Slide 106: Precise Exceptions
Informal definition
  We need to return to the original program at exactly the same point, at which we had left it
  The execution of the interrupt handler should not disrupt the execution of the original program in any way. The outcome of the original program should be independent of the interrupt (unless the program caused an exception).

## Slide 107: Precise Exceptions - II
Formal Definition
  Let us number the dynamic instructions in a program : I1 … In
  Let us assume that an instruction completes after it either updates memory, writes to registers, or reaches the MA stage (cmp, b, beq, bgt, ret)
  Let the last program instruction that completes before the first instruction in the interrupt handler completes, be Ik
  Let all the program instructions that complete before the first instruction in the interrupt handler completes, be C

## Slide 108: Precise Exceptions - III
We need to ensure this condition.
Also no instruction of the form Ik' (k' > k) should complete before all the instructions in the interrupt handler complete
After returning, we can seamlessly execute Ik(same instruction)or Ik+1 (next instruction)

## Slide 109: Marking Instructions
When an interrupt arrives, let us mark the instruction in the MA stage
Otherwise, if there is an exception
  We mark the instruction, as soon as it encounters a fault/exception
Once, an insruction is marked, we have two kinds of instructions in the pipeline
  Instructions before/after the marked instruction

## Slide 110: Implementing Precise Exceptions
Wait till a marked instruction reaches the end of the pipeline
  Convert all the instructions after the marked instruction to bubbles
Ensures that both the conditions of a precise exception are met.
Once the marked instruction reaches the end of the pipeline, the exception unit loads the pc of the interrupt handler

## Slide 111: Saving/Restoring Program State
Program State
  PC
  Registers
  Flags
  Memory
Memory → Assume that there is no overlap of memory regions, unless explicitly intended

## Slide 112: oldPC Register
Let us add a npc field in the instruction packet
  For taken branches it is equal to the branch target
  For all other instructions it is equal to (pc + 4)
We populate the npc field in the EX stage
Depending on the type of the exception, we might want to return to pc or npc
  The exception unit sets the oldPC register to the right return address

## Slide 113: Spilling/ Restoring Registers
In the case of functions, we stored registers on the stack
  In this case, the interrupt handler has a separate stack.
  We cannot overwrite the stack pointer (we will lose its previous value)
Solution :
  Use an additional register, oldSP, to save the stack pointer of the program.
  Load the new stack pointer, and spill all the registers
  Save oldPC

## Slide 114: The Strange Case of the Flags
Naive solution :
  Do not allow any instruction after the marked instruction to update the flags register
  We detect an exception typically towards the middle or end of a cycle
  By that time, the instruction might have already updated the flags register (at least the master latch)

## Slide 115: Solution
Add a flags field to the instruction packet
Every instruction saves the updated value of the flags register to the flags field in its instruction packet.
The exception unit saves the flags field of the marked instruction to the oldFlags register
We store the oldFlags register to a location in the interrupt handler's stack

## Slide 116: Privileged Instructions
We add the following new registers to the ISA
  special registers → flags, oldFlags, oldPC, oldSP
  The flags register is now accessible to the ISA
Add the z series of priveleged instructions
movz instruction
  Transfers values between regular registers and special registers

## Slide 117: Priveleged Instructions - II
retz
  pc ← oldPC
The z series instructions can only be used by the interrupt handler, and the operating system
We use a CPL bit (current privelege level) bit for setting permissions
  User programs (CPL = 1)
  Interrupt handlers, kernel programs, (CPL = 0)

## Slide 118: Implementing movz and retz
Define two new opcodes
  These opcodes are usable only when CPL = 0
  Augment the OF and RW stages to use the special registers.
  movz, and retz see a different view of registers.
Register | Encoding
r0 | 0000
oldPC | 0001
oldSP | 0010
flags | 0011
oldFlags | 0100
sp | 1110

## Slide 119: Assembly Code for Spilling Registers
/* save the stack pointer */
movz oldSP, sp
mov sp, 0x FF FC
/* spill all the registers other than sp*/
st r0, -4[sp]
st r1, -8[sp]
st r2, -12[sp]
st r3, -16[sp]
st r4, -20[sp]
st r5, -24[sp]
st r6, -28[sp]
st r7, -32[sp]
st r8, -36[sp]
st r9, -40[sp]
st r10, -44[sp]
st r11, -48[sp]
st r12, -52[sp]

## Slide 120: Spilling Registers - II
st r13, -56[sp]
st r15, -60[sp]
/* save the stack pointer */
movz r0, oldSP
st r0, -64[sp]
/* save the flags register */
movz r0, oldFlags
st r0, -68[sp]
/* save the oldPC */
movz r0, oldPC
st r0, -72[sp]
/* update the stack pointer */
sub sp, sp, 72
/* code of the interrupt handler */
....
....
....

## Slide 121: Restoring Registers
/* update the stack pointer */
add sp, sp, 72
/* restore the oldPC register */
ld r0, -72[sp]
movz oldPC, r0
/* restore the flags register */
ld r0, -68[sp]
movz flags, r0
/* restore all the registers other than sp*/
ld r0, -4[sp]
ld r1, -8[sp]
ld r2, -12[sp]
ld r3, -16[sp]
ld r4, -20[sp]
ld r5, -24[sp]
ld r6, -28[sp]
ld r7, -32[sp]
ld r8, -36[sp]

## Slide 122: Restoring Registers – II
ld r9, -40[sp]
ld r10, -44[sp]
ld r11, -48[sp]
ld r12, -52[sp]
ld r13, -56[sp]
ld r15, -60[sp]
/* restore the stack pointer */
ld sp, -64[sp]
/* return to the program */
retz

## Slide 123
IF-OF
Fetch
unit
Instruction
memory
Immediate
and branch
unit
Register
file
Control
unit
OF-EX
op2
op1
ALU
unit
Branch
unit
flags
EX-MA
Memory
unit
Data
memory
MA-RW
Register
write unit
op2
Data-lock Unit
stall
Branch-lock Unit
isBranchTaken
bubble
Forwarding unit
Exception unit
PC of exception handler
(pc/npc), flags
oldPC
oldSP
flags
oldFlags
Register unit
CPL

## Slide 124
THE END