## Slide 1: SmrtComp: Intelligent and Online CAN Data Compression
Dipika Tanwar, Priyanka Singla, Soham Nag, Vireshwar Kumar, and Smruti R. Sarangi
Indian Institute of Technology Delhi (IIT-Delhi), India
1

## Slide 2
Introduction

## Slide 3: Modern Vehicles
3
100+ Electronic Control Units (ECUs)
Controller Area Network (CAN) is the de-facto for ECUs communication
On-board diagnostics
Performance monitoring
Cause of accidents
Driving pattern analysis
Cyber-attack detection
Courtroom evidence
CAN data

## Slide 4: Storing CAN Data
How to store large amount of data (~500kbps)?
Increase storage
Periodically store it externally
Compress and store
FRAM is expensive
Not scalable, cost ineffective
Lossless
Lossy
+ No information loss
Limited compression gain
+ High compression gain
High information loss
Can we have best of both worlds, ensuring data quality?

## Slide 5: Storing CAN Data
How to store large amount of data (~500kbps)?
Can we store data at line speed?
How long should the data be stored?
Compress and store
Can we have best of both worlds, ensuring data quality?
Often need ~250 hrs of data[1]
Can we have an intelligent compression algorithm?
Data generation rate: ~500kbps
Can we have a fast enough algorithm?
1. Y. Qiu, T. Misu, and C. Busso, “Driving Anomaly Detection with Conditional Generative Adversarial Network using Physiological and CAN-Bus Data,” in IEEE Trans. Inf. Forensics Secur., vol. 16. ICMI, 2021, pp. 4133 – 4146.

## Slide 6
Proposed Work
Introduction

## Slide 7: SmrtComp
Can we have best of both worlds, ensuring data quality?
Can we have an intelligent compression algorithm?
Can we have a fast enough algorithm?
SmrtComp:
Intelligent compression decisions
Pre-decided Qos
Efficiently use available storage
Fast online compression

## Slide 8: CAN Data
Entry
Accel Pedal
Brake Pedal
Steer Angle
Vehicle Speed
Gear
Engine RPM
…..
Timestamp | AccelPedal | BrakePedal | SteerAngle | .....
timestamp | value | value | Value | …
Entry
Frame
MacroFrame
Signals

## Slide 9: SmrtComp
2.Efficient use of available storage
1.Pre-decided Qos
3.Fast online compression
α -> threshold to discard very old data
β -> threshold to preserve recent data
Compression level
Data age
α
β
Discard
Lossy compression
Lossless compression
Lossless
α
β
Tunable lossy compression
Discard
Streaming databases use the same notion

## Slide 10: SmrtComp
1.Pre-decided Qos
2.Efficient use of available storage
A) Macro frame creation and logging
B) Continuous monitoring and recompression of the log
RAM
External Memory
Size == Frame size?
Size == MFsize?
3.Fast online compression
Log
Macro frame
Deflate: fast compression method with good compression gain
Lossless compression

## Slide 11: SmrtComp – Log Recompression
2. Continuous monitoring and recompression of the log
External Memory
Size > logmax?
RAM
 |  |  | X
 |  | X | 
 | X | X | 
PCA
DCT
Principal Component Analysis: Dimensionality reduction; capturing majority of data’s variance
Discrete Cosine Transformation: Removes lower-valued coefficients without affecting the data quality
For subsequent recompressions, only DCT threshold is increased, based on MF’s age (No PCA)

## Slide 12
Proposed Work
Introduction
Evaluation

## Slide 13: Experimental Setup
Silver
GUI
Unity car game
(Realistic driving)
Embedded board
Steering, break, and accelerator
Driving Pattern
Dataset
Source
Normal
Unity car
game
Rash
Autonomous
Carla
Real
Literature
-CAN bus bandwidth: 500 kbps
-Embedded board: 1GHz, ARM Cortex-A8 processor; 512 MB RAM, 4GB log size
-Frame: 20KB and Macro frame: 32MB
Metrics:
Compression gain: original_size/compressed_size
RMSE: Root mean square error
Used to simulate car’s internals
Integrated Carla and Unity game to Silver

## Slide 14: SmrtComp’s Efficacy
3.4X
~5X
No of MF stored (4GB log size, data rate- 500kbps)
Algorithm | #of MFs stored | Sufficient amount of data? | Good data quality?
Lossless | 128 (3 days) | No | Yes
Lossy | 800 (~20 days) | Yes | No
SmartComp | 400 (~10 days) | Yes | Yes

## Slide 15
SmrtComp’s Accuracy
Accurate reconstruction of data
Preserving vital features
Compared anomalies preserved at different compression levels
>10 levels: misclassifications increased to 40% -> not useful
1-10 levels: 80% space gain with only 15% increase in misclassifications

## Slide 16
Proposed Work
Introduction
Conclusion
Evaluation

## Slide 17: Conclusion
First work to store CAN bus data in a hybrid fashion (lossless + lossy)
Amount of information loss (based on compression levels) in data varied without uncompressing
SmrtComp compresses and stores CAN data at line speed
Considering 4GB of storage, can store data continuously for 10 days

## Slide 18
Questions
Contact:
priyanka@sit.iitd.ac.in
http://www.cse.iitd.ac.in/~priyankas/