## Slide 1: JASS: A Tunable Checkpointing System for NVM-based Systems
Akshin Singh
Smruti R. Sarangi
IIT Delhi

## Slide 2: Introduction

## Slide 3: Overview of Checkpointing
Regular operation
Checkpoint
Regular operation
Checkpoint
Checkpoint
Restore
There are failures in systems. We need periodic checkpointing.

## Slide 4: How long does it take to checkpoint?
CL
300-500 ms
3-5 ms
CL
Checkpoint latency
Software
CRIU, ULFM, ReInit++
Hardware
Tsoper, NvOverlay
Use NVMs

## Slide 5: Why do we need millisecond-level latencies?
Record-replay debugging
High-throughput Tx systems
Job migration in exascale systems
Banks, stock exchanges

## Slide 6: Why NVMs?
CPU
DRAM
NVM
Hard disk
Reads: 2-4X slower than DRAM
Writes: 8-50X slower
Horizontal integration
Flash
MRAM
PCM
Limited endurance

## Slide 7: Some Key Definitions
Regular operation
Checkpoint
Regular operation
Checkpoint
Term | Definition
CL | Checkpoint latency
CLdown | Downtime during checkpointing
ES | Epoch Size
MTBF | Mean time between failures
ES
CL
CLdown

## Slide 8: Key Definitions – II
CPU
DRAM
NVM
Hard disk
Transfer the checkpoint data
Transfer the checkpoint data
Checkpointing induces more writes
Periodically transfer the state to the NVM
Write amplification

## Slide 9: A Little Bit of Theory
Young, 1974
Optimal epoch size
Down time
Minimize the overall execution time
As,
Does not take WA into account.

## Slide 10: Our Objective Function
Objective function
Fix the ES
Given a CL, minimize WA
Given a WA, minimize CL

## Slide 11: Where do we stand vis-a-vis related work?
JASS
ES or CL
Year of Publication
ThyNVM
PiCL
NVoverlay
2015
2018
2021
ES and CL values continuously reduced increasing WA significantly.
Our Novelty
Tradeoff the ES and CL with WA in a controlled manner.
2023

## Slide 12: The Checkpointing Process
Flush all in-flight messages from the NoC and L1 caches
Flush pre-snapshot lines in the caches
Move pre-snapshot data to DRAM
Run a locality predictor
Move some DRAM data to the NVM

## Slide 13: Basic Concepts + Related Work

## Slide 14: Flushing the NoC is difficult ...
How do we guarantee that all the pre-snapshot messages are recorded in a checkpoint?
Answer:
Build a protocol using the classical Chandy-Lamport algorithm
Assume FIFO channels
1. Take local
snapshot
2a. Propagate token 2b. Send an ack
3. Record all
pre-snapshot messages

## Slide 15: Simplifications
Maintain only two versions – current and previous
Single page table in NVM (ckpt version)
Do not use a coherence-based epoch scheme

## Slide 16: How do you ensure a guaranteed CL and minimize WA?
How do I minimize my study time before the exam, yet still pass with a B?
Answer:
Study a little bit during the semester.
Keep persisting some DRAM data to the NVM regularly. Ensure that CL is bounded.

## Slide 17: Design

## Slide 18
Overview of the Scheme
Start the checkpoint
Flush the NoC
Scrub the caches and send data to the lower level
Scrub the LLC (send data to NVM and the DRAM)
Scrub the DRAM and send data to the NVM
Coalesce data on chip
Finish the scrubbing

## Slide 19
Cores/Caches: Tracking snapshot data requires a single bit!
SB =0
SB =1
SB =1
SB =0
Epoch 0
Post-Snapshot
Pre-Snapshot
Post-Snapshot
Pre-Snapshot
Epoch 1

## Slide 20
Step 2: FLUSH
Non-Trivial
Cache
Scrubber
Write
WAR
Persist long lived lines
Can a core read data from a newer version?

## Slide 21: Lemmae
Lemma 1: A post-snapshot message never reaches a router in state NTR.
Lemma 2: A pre-snapshot marked message is counted by only a single router.

## Slide 22
Not possible

## Slide 23
READ
GETS
  Evict pre-snapshotted lines
EVICT
GETX
WRITE
Step 3: Cache Operations on Modified Pre-snapshot Lines
Seamless read

## Slide 24
How to scrub the DRAM?
How to ensure an optimal CL?
How to coalesce DRAM and LLC accesses?
Step 4

## Slide 25
Incrementally walk the page table to find pages to persist to NVM
Level 3 Counter
Level 2 Counter
Level 1 Counter
Level 0 Counter
overflow and increment
overflow and increment
overflow and increment
Walk complete
Increment in every walk

## Slide 26
Keep n modified pages in DRAM and rest in NVM
Locality Predictor
Ensure an optimal CL

## Slide 27: Locality Predictor
DRAM page (256 Bytes)
DRAM page (256 B
)
DRAM page
(256 Bytes)
2 bits
3 bits
Increment when a pre-snapshot line is sent to the DRAM
Clear bits in these counters during period page walks
When the counters are zero, persist the page to the NVM

## Slide 28
Sub epoch 1
Sub epoch 2
…………………………………
Sub epoch 50
Dynamically tune the predictor to achieve
Epoch
DRAM scrubber’s frequency is inversely proportional to
modified lines
PD controller

## Slide 29: Evaluation

## Slide 30
8 OOO cores
Parsec benchmarks
L1: 32 KB
L2: 256 KB
L3: 2 MB
256 B (basic page size)
2 ranks, 8 banks (DRAM and NVM)
Configuration
Tejas simulator
http://www.cse.iitd.ac.in/tejas

## Slide 31: Performance Comparison
WA reduction by 35-96%
19.4%

## Slide 32: We meet the CL constraints

## Slide 33
WA
vs
CL

## Slide 34
Flushing the NoC is challenging.
Simple binary checkpointing that is epoch based.
Limit the CL (minimize WA). Use a PD controller
Conclusion

## Slide 35
Smruti R. Sarangi
srsarangi@cse.iitd.ac.in

## Slide 36
Lemma 3: Use timers to take care of messages in transit.
Rj
TOK
Ri
Proof
In-flight messages
NTR to TR
Transit timer elapsed
Lemma 1: A post-snapshot message never reaches a router in state NTR.
Lemma 2: A pre-snapshot marked message is counted by only a single router.

## Slide 37
Theorem: No pre-snapshot message remains in the NoC after termination detection.
New messages
Message
Directory
Request
Message
Message
Modify the directory’s router
Update xcount if outgoing > incoming
Update pcount if outgoing=0

## Slide 38
Message M arrived at a router R
Check state
M is a snapshot token?
M is a snapshot token?
Normal operation
M has reached its destination?
pcount++
State = TR; pcount = 0
Send xcount to checkpoint controller
Send token to neighbors (highest priority)
NTR
TR
no
yes
no
no
yes
Record the number of messages in flight (xcount)

## Slide 39
Workload | Completion Time | %Cache | %DRAM | %Coalescing | LLC MPKI | %DRAM WA
Blackscholes | 5.25 | 88 | 12 | 13 | 0.20 | 50.16
Bodytrack | 5.0 | 78 | 22 | 2 | 0.14 | 25.6
Canneal | 5.0 | 40 | 60 | 23 | 0.48 | 49.1
Dedup | 5.0 | 81 | 19 | 4 | 17.6 | 23.1
Facesim | 5.0 | 84 | 16 | 0.4 | 0.91 | 8.7
Ferret | 5.05 | 78 | 22 | 9.5 | 0.33 | 50.7
Fluidanimate | 5.0 | 47 | 53 | 1.6 | 0.51 | 10.7
Freqmine | 5.0 | 68 | 32 | 1.6 | 0.51 | 10.7
Raytrace | 5.0 | 84 | 16 | 1.5 | 0.78 | 15.2
Streamcluster | 5.1 | 84 | 16 | 0.9 | 0.55 | 18.7
Swaptions | 5.23 | 86 | 14 | 5.5 | 0.09 | 25.3
Vips | 5.01 | 84 | 16 | 2.6 | 0.17 | 49.9

## Slide 40
Workload | Completion Time | %Cache | %DRAM | %Coalescing | LLC MPKI | %DRAM WA
Blackscholes | 5.25 | 88 | 12 | 13 | 0.20 | 50.16
Bodytrack | 5.0 | 78 | 22 | 2 | 0.14 | 25.6
Canneal | 5.0 | 40 | 60 | 23 | 0.48 | 49.1
Dedup | 5.0 | 81 | 19 | 4 | 17.6 | 23.1
Facesim | 5.0 | 84 | 16 | 0.4 | 0.91 | 8.7
Ferret | 5.05 | 78 | 22 | 9.5 | 0.33 | 50.7
Fluidanimate | 5.0 | 47 | 53 | 1.6 | 0.51 | 10.7
Freqmine | 5.0 | 68 | 32 | 1.6 | 0.51 | 10.7
Raytrace | 5.0 | 84 | 16 | 1.5 | 0.78 | 15.2
Streamcluster | 5.1 | 84 | 16 | 0.9 | 0.55 | 18.7
Swaptions | 5.23 | 86 | 14 | 5.5 | 0.09 | 25.3
Vips | 5.01 | 84 | 16 | 2.6 | 0.17 | 49.9

## Slide 41
Workload | Completion Time | %Cache | %DRAM | %Coalescing | LLC MPKI | %DRAM WA
Blackscholes | 5.25 | 88 | 12 | 13 | 0.20 | 50.16
Bodytrack | 5.0 | 78 | 22 | 2 | 0.14 | 25.6
Canneal | 5.0 | 40 | 60 | 23 | 0.48 | 49.1
Dedup | 5.0 | 81 | 19 | 4 | 17.6 | 23.1
Facesim | 5.0 | 84 | 16 | 0.4 | 0.91 | 8.7
Ferret | 5.05 | 78 | 22 | 9.5 | 0.33 | 50.7
Fluidanimate | 5.0 | 47 | 53 | 1.6 | 0.51 | 10.7
Freqmine | 5.0 | 68 | 32 | 1.6 | 0.51 | 10.7
Raytrace | 5.0 | 84 | 16 | 1.5 | 0.78 | 15.2
Streamcluster | 5.1 | 84 | 16 | 0.9 | 0.55 | 18.7
Swaptions | 5.23 | 86 | 14 | 5.5 | 0.09 | 25.3
Vips | 5.01 | 84 | 16 | 2.6 | 0.17 | 49.9