## Slide 1: Chapter 2: Basics of Computer Architecture
Smruti R Sarangi
IIT Delhi

## Slide 2: Outline of this Chapter
Cores, registers and interrupts
x86 assembly
Virtual memory
I/O

## Slide 3: Design of a Modern Multicore Chip
Caches
Main memory
4-64 cores
Hierarchy of caches
  1st level: i-cache and d-cache
  2nd level: L2 cache (MBs)
  3rd level: L3 cache (MBs)
Off-chip main memory

## Slide 4: Cores and Registers
Every core has a set of registers – named storage locations
They number from 8-32. They can be accessed very quickly (fraction of a clock cycle).
Most of the CPU’s operations are performed usually on registers.
RISC machines first load memory values into registers and then perform operations on them
CISC machines can have one source operand from memory (lower register usage)
Core
Registers

## Slide 5: What does the register set of a typical machine look like?
General purpose registers: These registers can be used by all programs
The rest are all privileged registers. They can only be used in certain processor modes (e.g., by the OS, hypervisor, etc.)
  Hidden registers: Example  flags register. This stores the result of the last comparison.
  Control registers: Use them to enable/disable certain processor features
  Debug registers: Debug hardware and system software
  I/O registers: read/write I/O devices, access their status information

## Slide 6: Current Privilege Level
Current Privilege Level (CPL) bit (s)
In general CPL=0 indicates privileged OS mode and CPL=1 indicates user mode
Current Privilege Level
Extended to Rings
Ring 0
Ring 3
Lower the ring 
Higher the privilege

## Slide 7: Privileged and Non-Privileged Instructions
There are two kinds of instructions – privileged and non-privileged
Non-privileged instructions
  Regular instructions
  When they access privileged registers, several things can happen
    An exception may be generated
    There will be some effect
    There will be no effect at all (fully silent)
Privileged instructions
  Can access all registers
  Exceptions are not generated
Dangerous !!! (we will discuss when introducing VMs)

## Slide 8: Interrupts, Exceptions, and System Calls
Interrupts
An interrupt is an externally generated event whose main job is to draw the attention of the CPU. They are mainly generated by I/O devices and other chips in the chipset.
Exceptions
An exceptional condition in a program such as accessing an illegal memory address or dividing by zero. There is a need to suspend the program and take some action to rectify the situation.
System calls
There are specialized instructions in ISAs to generate a “dummy exception”. They lead to a suspension of the program’s execution and invocation of an OS routine. This mechanism can be used to pass data to the OS such that it can perform a service for the user program. Such a convoluted OS function call mechanism is known as a system call.

## Slide 9: System calls in x86-64 Linux
See arch/x86/entry/syscalls/syscall 64.tbl (548 systems calls)
mov $<sys call number>, %rax
syscall
Move the system call number to the rax register
Issue the “syscall” instruction
Another option: int $0x80 (software interrupt)

## Slide 10: All are handled in the same manner
The idea is to knock on the doors of the
operating system to draw its attention.
Either rely on a hardware interrupt that the CPU uses as a pretext to invoke an OS routine
OR, treat a fault/exception in the program as an interrupt
OR, generate a software interrupt yourself to ask the OS to do some work for you
Kind of a weird way of drawing the OS’s attention. The only way to talk to the fireman is by setting your house on fire.

## Slide 11: Now what does the CPU do?
Something has happened, the OS needs to take a look
Save the state of the executing process
Load the interrupt handler
Then figure out what needs to be done

## Slide 12: Saving the State: Context Switch
Registers
Flags and special registers
Program state
Memory
PC
Register state
Store the register state somewhere
The memory of the process should remain untouched
Store the PC of the last executed instruction, or next PC (point of resumption)
Then do other work
Later on, restart the process from the point of resumption
It never gets to know
No need to save and restore

## Slide 13: Lifecycle of a Process
Execution
Context
switch
OS + other processes execute
Execution
OS + other processes execute
Execution
Context
switch
The process has no way of knowing that it is being swapped out and being swapped in
It is agnostic to context switches

## Slide 14: How does the OS see a process?
The OS treats the process as a suitcase containing some state. It can be seamlessly moved from core to core on a multi-core CPU. It can be suspended at will and brought back to life at a future point of time without the process knowing.

## Slide 15: A Question to Ponder About?
What if there are no interrupts, exceptions, and system calls?
In principle, an application can continue to run forever.
It will never get swapped out and will continue to monopolize the processor.
Have an external time chip on the motherboard. Generates a dummy interrupt (timer interrupt) once every jiffy
A jiffy = 1 ms (as of today)
Guaranteed source of interrupts

## Slide 16: Why do you need a guaranteed source of interrupts?
This is to allow the OS to periodically execute and make process scheduling decisions.
Otherwise, the OS may never get a chance to execute. For it to execute, it needs to be invoked by any one of the three mechanisms: interrupts, exceptions or system calls.
The latter two are not relevant here. We need to thus generate timer interrupts.

## Slide 17: Relevant Kernel Code
include/linux/jiffies.h
extern unsigned long volatile jiffies;
The jiffy count is incremented once every time there is a timer interrupt. The interval is determined by the compile-time parameter HZ. If HZ = 1000, then it means that the timer interrupt interval = 1 ms

## Slide 18: Outline of this Chapter
Cores, registers and interrupts
x86 assembly
Virtual memory
I/O

## Slide 19: Introduction to Assembly Languages
We need low-level control of the hardware.
Speed and efficiency
Limited code size
Specify the exact code that will be executed
A large part of the kernel code is written in assembly language
x86 ISA
32 bit
64 bit

## Slide 20: View of Registers
Modern Intel machines are still ISA compatible with the arcane 16-bit 8086 processor
In fact, due to market requirements, a 64-bit processor needs to be ISA compatible with all 32-bit, and 16-bit ISAs (same family)
What do we do with registers?
Do we define a new set of registers for each type of x86 ISA? ANSWER : NO

## Slide 21: View of Registers – II
Consider the 16-bit x86 ISA – It has 8 registers: ax, bx, cx, dx, sp, bp, si, di
Should we keep the old registers, or create a new set of registers in a 32-bit processor?
NO – Widen the 16-bit registers to 32 bits.
If the processor is running a 16-bit program, then it uses the lower 16 bits of every 32-bit register.

## Slide 22: View of Registers – III
The 64-bit ISA has
8 extra registers
r8 - r15
8 registers
64, 32, 16
bit variants
eax
ebx
ecx
edx
esp
ebp
esi
edi
ax
bx
cx
dx
sp
bp
si
di
rax
rbx
rcx
rdx
rsp
rbp
rsi
rdi
r8
r9
r15
64 bits
32 bits
16 bits

## Slide 23: x86 can even Support 8-bit Registers
For the first four 16-bit registers
  The lower 8 bits are represented by al, bl, cl, dl
  The upper 8 bits are represented by ah, bh, ch, dh
ax
bx
cx
dx
ah
al
bh
bl
ch
dh
cl
dl

## Slide 24: x86 Flags Registers and PC
Similar to the classical flags registers in RISC ISAs
It has 16-bit, 32-bit, and 64-bit variants
The PC is known as the IP (instruction pointer)
Fields in the flags register
eflags
eip
flags
ip
rflags
rip
64 bits
32 bits
16 bits
Field
Condition
Semantics
OF
Overflow
Set on an overflow
CF
Carry flag
Set on a carry or borrow
ZF
Zero flag
Set when the result is 0, or the
comparison leads to an equality
SF
Sign flag
Sign bit of the result

## Slide 25: Intel and AT&T Formats
The same code can be written in two different formats: Intel and AT&T
The Linux kernel and the toolchain uses the AT&T format (which is older and often not preferred by modern developers)
add eax, ebx
Intel
AT&T
eax = eax + ebx
addl %ebx, %eax
destination comes at the end
mov [esp+4], eax
Set the memory
location with address
esp+4 to the contents of eax
movl %eax, 4(%esp)
Set the memory
location with address
esp+4 to the contents of eax

## Slide 26: Floating-point Registers
x86 has 8 (80-bit) floating-point registers
  st0 – st7
  They are also arranged as a stack
  st0 is the top of the stack
  We can perform both register operations, as well as stack operations
st0
st1
st5
st4
st0
st0
st2
st3
st6
st7
FP register
stack

## Slide 27: Memory Addressing Mode
x86 supports a base, a scaled index and an offset (known as the displacement)
Each of the fields is optional
address = base + index*scale + disp
Examples
-32(%eax, %ebx, 0x4)
(%eax, %ebx)
4(%esp)
Support for direct addressing

## Slide 28: Assembly code for computing a factorial
movl $1, %edx
movl $1, %eax
.L2:
imull %eax, %edx
addl $1, %eax
cmpl $11, %eax
jne .L2
edx = edx * eax
eax++
Exit condition

## Slide 29: Brief Detour: Compiling and Linking
Any large project comprises 100s of C/C++ files.
How do we create a single executable out of them?
x.c
y.c
z.c
The compiler can only look at one C file at a time
x.o
y.o
z.o
gcc –c x.c
a.out
The final executable that runs.
Machine-code versions of the code in the .c file. Cannot run.
Linking
Command: ld

## Slide 30: What does a .o file contain?
Sections (objdump -x <file.o>)
  .text (the machine instructions for the C code)
  .data (initialized data)
  .bss (uninitialized data)
  .rodata (read-only data)
  .comment
The symbol table (objdump --syms <file.o>)
  The list of all the symbols that are used (both defined and undefined)
The relocation table (objdump --reloc <file.o>)
  The symbols that need to be resolved at link time

## Slide 31: How are developers supposed to collaborate?
Defines the factorial function
factorial.c
Uses the factorial function defined in factorial.c
prog.c
How will this happen?
Compilers take a look at each C file individually
When the compiler is trying to convert prog.c to prog.o, it needs some information about the factorial function.
Answer:
What is the signature of the factorial function?
int factorial (int). Arguments and type of the return value

## Slide 32: A few follow-up questions
Where does prog.c get the signature of the factorial function from?
Bad way
Define it in prog.c before the function is used.
extern int factorial (int)
We cannot change the signature later. This will clutter the C code. If many C files are using this function, then there is a lot of code replication.
Good way
Define the signature in a header file: factorial.h
Just include factorial.h to get the signature: #include <factorial.h>
The pre-processor simply copy-pastes the contents of the header file to the relevant place in the C file.
Great idea for quickly exporting signatures to any C file that is interesting in using functions defined in another C file.

## Slide 33: New Structure
What is the address of the factorial function in prog.o?
  It is unresolved.
  There is an entry in the relocation table (in the .o file) that says that the symbol “factorial” is undefined.
At link time, the symbol is substituted with its real address
  The call instruction that calls factorial finally points to the correct address – address of the first byte of the factorial function in memory
Defines the factorial function
factorial.c
Uses the factorial function defined in factorial.c
prog.c
Declaration of the factorial function
factorial.h
#include
Symbol table

## Slide 34: Static Linking
Along with functions defined in other C files, a typical executable calls a lot of functions that are defined in the standard C libraries (essentially large .o files). Examples: printf, scanf, time, etc.
Do we bundle all of them together?
Let us try
gcc –static test.c
ldd a.out not a dynamic executable
du –h a.out 892K a.out
#include <stdio.h>
int main(){
int a = 4;
printf ("%d",a);
}
test.c
Check if all the functions are bundled or not
The size of the binary is quite large because the code of the entire library is included in a.out
Add the code to a.out

## Slide 35: Why is a.out so large?
This is because the code of all possible functions that can be invoked by a.out is added to it
Imagine a program can possibly invoke 100 functions. However, in a realistic run, only 3 functions are invoked.
There is no need to add the code of all the 100 functions to a.out.
Add the code of functions to the process’s address space on an on-demand basis
gcc test.c
ldd a.out linux-vdso.so.1 => (0x00007ffc51fd3000)
libc.so.6 => /lib/x86_64-linux-gnu/libc.so.6 (0x00007f984d6a7000)
/lib64/ld-linux-x86-64.so.2 (0x00007f984da71000)
du –h a.out 12K a.out
Dynamic Linking
a.out just has pointers to functions
Ultra-small

## Slide 36: All about Dynamic Linking
This means that we load functions “on demand” and the size of the binary remains small
When we study virtual memory, we shall realize that copying the full code of the function is not necessary. A simple mapping can achieve the same. This means that only a single copy of printf needs to be resident in memory.
printf
Stub function
Locate the function in a library
first time
Copy the function to the address space of the process
subsequently
Call the function using its address
Store the address of the function

## Slide 37: Example of Creating and Using a Static Library
Three files
#include "factorial.h"
int factorial (int val){
int i, prod = 1;
for (i=1; i<= val; i++) prod *= i;
return prod;
}
#ifndef FACTORIAL_H
#define FACTORIAL_H
extern int factorial(int);
#endif
#include <stdio.h>
#include "factorial.h"
int main(){
printf("%d\n",factorial(3));
}
factorial.c
factorial.h
prog.c

## Slide 38: Default
gcc factorial.c prog.c
./a.out 6
Plain, old, simple, and inefficient
gcc –c factorial.c –o factorial.o
gcc –c prog.c –o prog.o
gcc factorial.o prog.o
./a.out 6
Compile .o files separately
In a large project we maintain a list of compiled .o files and compile as few files as possible when there is a new change. A Makefile and the make command automate this process. All that the programmer needs to type is make. The rules are in the Makefile.

## Slide 39: Static and Dynamic Linking
gcc –c factorial.c –o factorial.o
ar –crs factorial.a factorial.o
gcc prog.o factorial.a
./a.out 6
factorial.a is a library that is statically linked in this case
The ar command creates a library out of several .o files
gcc –c –fpic –o factorial.o factorial.c
gcc –shared –o libfactorial.so factorial.o
gcc –L. prog.c -lfactorial
export LD_LIBRARY_PATH=`pwd`
./a.out 6
Generate position independent code
Create the shared library
Create the executable. Reference the shared library.
Tell the system that the factorial library is in the current directory

## Slide 40: Some Important Linux Commands
ldd  Display the location of the shared libraries on your file system
objdump  See all the contents of an object (.o) file Table, sections, machine instructions (also in the disassembled form)
readelf  More expressive than objdump
nm <file.o>  List the symbols in object files
strip <file.o>  Discard symbols from object files
ranlib <archive>  Generate an index for an archive

## Slide 41: Outline of this Chapter
Cores, registers and interrupts
x86 assembly
Virtual memory
I/O

## Slide 42: Compatibility, Overlap and Size Problems
How does a process view memory?
Answer:
One large array of bytes. Any location can be accessed.
In a 64-bit addressing system, the user assumes that all the locations from 0 to 264 – 1 can be accessed. The physical memory may be 1 GB (30 bits).
Compatibility problem

## Slide 43: Overlap and Size Problems
Can one process access the data written by another process?
Overlapping addresses
If a program requires 2 GB of memory but the system has only 1 GB of memory, do we always need to terminate the program?
Can’t we use the hard disk to temporarily expand the available memory?
Overlap Problem
Size Problem

## Slide 44: Memory Map of a Process
32-bit memory system
Different processes access similar addresses

## Slide 45: Solve the Compatibility and Overlap Problems
Virtual address
Seen by the compiler, process and CPU
Mapping Table
Physical address
Seen by the memory system

## Slide 46: Base and Limit Scheme
Each process is assigned a contiguous memory region between base and limit
A new process needs to be allotted memory in the holes (between regions)
There are a lot of problems with this scheme

## Slide 47: Problems with the Base and Limit Scheme
It is hard to guess the maximum amount of memory a process may use.
We need to use conservative estimates. Some memory will inevitably be wasted  internal fragmentation
A lot of memory will be wasted in holes. Even when adequate memory is available, it may be hard to allocate memory for a process because a large enough hole may not be found.
External fragmentation

## Slide 48: Solution: Virtualize the Memory
Process 1
Process 2
Divide memory into 4-KB chunks
Map process’s virtual pages to physical frames

## Slide 49: How is the Mapping Table Designed?
Page Table
64-bit virtual address
64-bit physical address
What do we know?
We know that a page or a frame has a size of 4 KB (212 bytes)
The virtual page or physical frame address is thus 52 bits
We cannot possibly create a structure that has 252 entries
12 bits
52 bits

## Slide 50: Leverage a Pattern (Use a Memory Map)
Metadata
0
0x400000
Text (instructions)
Global, static, and read-only objects
Run-time heap (created by new and malloc)
Use the pmap command
to find the memory map of a process
.data (initialized data)
.bss (uninitialized data)
Memory mapped region and libraries
Stack
248 - 1
Large empty
spaces !!!

## Slide 51: Design a Data Structure that Leverages the Structure of the Memory Map
LSB bits have more randomness,
MSB bits have less randomness
The MSB bits determine the memory region
Multi-level Page Table
Consider the first (36 + 12) bits in the 64-bit x86 memory address. Assume
that bits 49-64 are all zeros in the virtual address [standard assumption].
Bits 48-40
Bits 39-31
Bits 30-22
Bits 21-13
Level 1
CR3 register
Level 2
Level 3
48-bit Virtual address
Level 4
52-bit frame address
12 bits (intra-page)

## Slide 52: Use of the TLB
CPU generates the virtual address
The TLB (Translation Lookaside Buffer) tries to translate the address. It is a fast HW structure (32 to 128 entries)
If it does not have the mapping, it requests the SW-resident page table for a translation
The physical address is sent to the caches
A page table access is very slow.
Speed it up using a HW cache called the TLB that stores the most frequent mappings

## Slide 53: What about the “size” problem?
Assume that a process wishes to access 3 GB of memory, but we only have 2 GB of main memory.
Answer:
Store 2GB in main memory and store the remaining 1GB on the hard disk or any other storage device. Let us refer to the “non-main memory” region as the swap space.
Use the virtual memory mechanism to manage the memory map.
Page table entry
Frame in main memory
Frame stored in the swap space

## Slide 54: Swap Space
54
If there is a TLB miss and the page table indicates that the frame is in the swap space, then bring it into the main memory first.
The swap space could be on the local hard disk or could be on the hard disk of a remote machine. There could be several swap spaces as well.
Page fault
The swap space is a generic concept

## Slide 55: Memory Management
Before accessing data, it needs to be present in the main memory, regardless of wherever it is stored.
The main memory has finite size.
If it is full, then we need to evict a frame to make space.
Which one
There are different heuristics: least recently used, least frequently used in a given timeframe, most frequently used, FIFO, random, etc.
An optimal solution exists: Evict the frame that will be used farthest in the future

## Slide 56: Page Protection and Information Bits
Each entry of the page table or TLB has additional page protection bits.
Bit | Function
Present | Present in the main memory or not
RW | Set if the page can be written to
User | If the page can be accessed from user space
Dirty | Has a page been written to
These bits can be used to make a page read-only. This is a vital security measure for pages that contain code.

## Slide 57: Questions on Efficiency
Where does a page table save memory?
Answer:
Very few entries in the Level 1 page table are full. This means that there are a few Level 2 page tables. There are slightly more Level 3 page tables and much more Level 4 page tables. The sparse structure of the memory map minimizes the number of page tables.
Do we access the page tables on a memory access?
Answer:
Too slow
What do we do then?
Use a HW structure to cache frequent mappings. It is the TLB (Translation
Lookaside Buffer). We cache 32-128 entries. We can access in 1 cycle.
Answer:

## Slide 58
Segmentation

## Slide 59: Segmented View of Memory in x86
x86 follows a segmented memory model
  Each virtual address in x86 is generated by adding the computed address to the contents of a segment register.
  For example, an instruction address is computed by adding an offset to the contents of the code segment register
CS Register
Logical address
Virtual memory
Linear address

## Slide 60: Segmentation in x86
x86 has 6 different segment registers
  Each register is 16 bits wide
  Code segment (cs), data segment (ds), stack segment (ss), extra segment (es), extra segment 1 (fs), extra segment 2 (gs)
  Depending upon the type of access, the CPU uses the appropriate segment register
cs
ss
ds
es
gs
fs
16-bit segment registers
These registers are private to a CPU

## Slide 61: Segmented vs Linear Memory Model
In a linear memory model (e.g. RISC-V, ARM) the address specified in the instruction is sent to the memory system
  There are no segment registers
What are the advantages of a segmented memory model?
  The contents of the segment registers can be changed by the operating system at runtime. Randomizes the address (good for security).
  Can map the text section(code) to a dedicated part of memory, or in principle to other devices also (needed for security)
  Stores cannot modify the instructions in the text section. REASON : Stores use the data segment, and instructions use the code segment
  The segment registers can store pointers to special memory regions. No need to load their addresses over and over again.

## Slide 62: How does Segmentation Work?
The segment registers nowadays contain an offset into a segment descriptor table
  Because 16 bits are not sufficient to store a memory address
  The segment descriptor contains additional information: metadata, base address, limit, type, execute permission, privilege level
Modern x86 processors have two kinds of segment descriptor tables
  LDT (Local Descriptor Table), 1 per process, typically not used nowadays
  GDT (Global Descriptor Table), can contain up to 8191 entries
  Each entry in these tables contains a segment descriptor

## Slide 63: Segment Descriptor Cache (similar to a TLB)
Every memory access needs to access the GDT: VERY SLOW
Use a segment descriptor cache (SDC) at each processor that stores a copy of the relevant entries in the GDT
  Lookup the SDC first
  If an entry is not there, send a request to the GDT
  Quick, fast, and efficient
Virtual memory
Segment Register
Logical address
SDC
GDT
Linear address

## Slide 64: Segmentation in x86-64
Nowadays with x86 (64 bits) only two segment registers are used: fs and gs
The GDT is also not used. It has been replaced by MSRs (model specific registers)
The Linux kernel uses the gs segment to store per-CPU data.
The gcc compiler also uses them to store thread-local data
Example
movl $32, %fs:(%eax)

## Slide 65: Outline of this Chapter
Cores, registers and interrupts
x86 assembly
Virtual memory
I/O

## Slide 66: The Motherboard and Chipset
The CPU is assisted by a set of chips that help it manage the memory, storage, and I/O devices. They comprise the chipset.

## Slide 67: Diagram of the Motherboard
CPU
Northbridge
Memory
slots
GPU
Southbridge
PCI
slots
Keyboard, mouse, USB ports, I/O chips, ...

## Slide 68: x86 I/O Instructions
When the system boots, each I/O device is provided multiple 16-bit I/O addresses
The OS can query this information and figure out the I/O addresses associated with each device.
These are known as ports.
It is possible to write a value to a port or read a value from it.
x86 has dedicated in and out instructions to access I/O ports
Scalability is an issue. We cannot read and write a lot of data in one go.
Port-Mapped I/O (PMIO)

## Slide 69: Memory Mapped I/O
Use the virtual memory mechanism to map a portion of the virtual address space to I/O devices
Use regular reads and writes to access I/O devices
The system automatically routes memory traffic to the I/O devices (bulk transfers possible)
Virtual address space
Mapped to I/O addresses
I/O device ports

## Slide 70: DMA (Direct Memory Access)
Assume that a large amount of data (several MBs) needs to be transferred from the hard disk to the main memory.
Why should the program involve itself in this process, if this can be outsourced to a separate chip – the DMA controller?
Just give it a pointer to the region in the storage device (hard disk in the case), and the main memory. It does the transfer on its own and interrupts the chip once done.
CPU
DMA
1. Transfer details (device ↔memory)
2. Interrupt the CPU (transfer done)

## Slide 71
srsarangi@cse.iitd.ac.in