## Slide 1: A Java-Based Versatile Micro Architectural Simulator
Supported by
Ministry of Information Technology,
Government of India
Website : www.cse.iitd.ac.in/tejas/

## Slide 2
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 3
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Need for Architectural Simulators Need for Tejas High Level Architecture of Tejas | 
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 4: Need for Architectural Simulators
Study the impact of different
components of a chip on the
application performance
Image Source: http://www.123rf.com/processor-scan.html
Education
Research
Industry

## Slide 5
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Need for Architectural Simulators Need for Tejas High Level Architecture of Tejas | 
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 6: Existing Architectural Simulators
Simics
GEM5
Sniper
Multi2Sim
Graphite
SESC
MARS
FastMP
C/C++: Platform Specific !!
Problems exacerbated when moving the simulation to a cloud !!
Library
Build environment

## Slide 7: Existing Architectural Simulators
Simics
GEM5
Sniper
Multi2Sim
Graphite
SESC
MARS
FastMP
Emulator
Simulator
Correctly Execute Program
Simulation Engine
Implement both in the same package
ISA inflexibility
Bulky code

## Slide 8: Why Tejas ?
Platform Independence as a Design Goal
TEJAS: The Java-based Architectural Simulator
First architectural simulator written entirely in Java
WANTED
Simple
Flexible
Easy to use
Cloud compliant simulator

## Slide 9: Tejas: Family
Tejas
ParTejas
GPUTejas
TejasJava
Parallel Version of Tejas
Tejas for GPU’s
Tejas for Java
Used in 15 universities of India to teach computer architecture
Around 1000 users world wide

## Slide 10: License
Apache license, version 2
Free to use
Free to modify
Free to re-distribute
You are more than welcome to contribute to Tejas 

## Slide 11: Comparison with other simulators
Functionality
Out of Order pipeline, NOC, NUCA, GPU, DRAM, Full system simulation
Speed
Speedup of 25% over Multi2sim
Validation
Validated against actual hardware
Speedup of 220% over GEM5
Comparable with other simulators

## Slide 12: Small Code Base
Code base (Lines of code)
Tejas (32 K)
Sniper (76 K)
Multi2Sim (108 K)
GEM5 (170 K)
Image Source: www.picturespider.com
Others vs Tejas
Almost similar functionalities

## Slide 13: Why Java?
Defects per line is 15-50% more in C++!
Debugging time can be six times more!! [Phipps 1999]
Programming Constructs
Generics, interfaces
Type Safety
Strongly Typed
Ease of Debugging
Rich debug information
Library Support
Efficient data structures
XML parsing
Intuitive IDEs
Control over casting
No pointer manipulations
String manipulations

## Slide 14: Speed: Java Vs C++
Dynamic Compilation: Associated with slow performance
Data-structures
  Memory System: set associative cache
  Event Queue: priority event queue
  ROB: circular queue
C++ : g++(4.7.2), O3 optimization, STL
Java : JDK 7
Chart: Data-structure
| Cache | Priority Queue | Circular Queue
C++ | 24 | 48 | 21
Java | 18 | 44 | 22
Memory System
Event Queue
ROB

## Slide 15
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Need for Architectural Simulators Need for Tejas High Level Architecture of Tejas | 
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 16
1. Emulator
2. Transfer Engine
3. Translator
(VISA)
4. Simulation Engine
X86, ARM, Byte code
VISA

## Slide 17: Emulator (Black Box)
Emulator
Benchmark
Execution traces
Correctly execute the benchmark
Program counter
Memory (load, store)
Branch (taken, not-taken)
Synchronization
  Thread create, destroy
  Locks, barriers
X-86 application
Full system
GPU kernel
RISC-V application
Java bytecode

## Slide 18: Emulators (Feeders for Tejas)
Intel Pin
X86 App
Normal x86 applications
Qemu
OS
Full system simulation
App
Jikes RVM
Java App
Java applications
GPU Ocelot
Kernel
GPU workloads
Spike
RISC V App
RISC V applications (work in progress)

## Slide 19
Intel PIN Tool
Hardware (x86/x86-64)
Operating System
App
Intel PIN
Intel PIN is essentially an instrumentation engine for X86 programs. Uses DBT to add special hooks.
  Load/store operation
  Branch
  Thread create/destroy
  Understands executable formats and hence can be used to identify special functions in the executable
Software Stack

## Slide 20
Intel PIN Tool
Hardware (x86/x86-64)
Operating System
App
Intel PIN
Gives execution traces for x86 applications
Suitable for application-mostly suites such as SPEC, PARSEC, and Splash
Software Stack

## Slide 21
Intel PIN Tool
X86 application
Intel PIN
Software Stack
Tejas
Execution
Traces
(X86 program)
Pipeline (VISA)

## Slide 22: Translation Engine
X86
ARM
MIPS
RISC V
Translator
VISA
Tejas’s ISA

## Slide 23: Virtual Instruction Set Architecture
Classify all the operations of any assembly language into simple basic operations.
Instruction Class |  |  | 
Data Flow | Move | Load | Store
Integer Arithmetic | Integer ALU | Integer Multiplication | Integer Division
Float Arithmetic | Float ALU | Float Multiplication | Float Division
Control Flow | Unconditional Jump | Branch | 
Other | Exchange | NOP | 

## Slide 24
Input Application (X86)
Translator
Operating System
Emulator
Fuse
App
VISA static
add %rax, (%rbx)
load <(%reg1), ?>, %tmpreg1
int-alu %reg0, %tmpreg1, %tmpreg1
store %tmpreg1, <(%reg1), ?>
load <(%reg1), 0x1234>, %tmpreg1
int-alu %reg0, %tmpreg1, %tmpreg1
store %tmpreg1, <(%reg1), 0x1234>
Packet <IP,value,target>
(0x10, memread, 0x1234)
VISA dynamic
X86 instruction
VISA instruction (static)
Runtime information
VISA instruction (dynamic)
Intel PIN
(x86 to VISA translation)
Input Application: X86
Simulation Engine: VISA

## Slide 25: Coverage of the Translator
Static Coverage
Dynamic Coverage
Translator
Rating
Dynamic Coverage

## Slide 26: Coverage of the Translator
Chart: 
| GemsFDTD | sphinx3 | cactusADM | bwaves | wrf | bzip2 | gromacs | sjeng | calculix | astar | povray | omnetpp | mcf | gcc | h264ref | namd
Static Coverage | 93.6578 | 92.3458 | 92.3701 | 95.1538 | 97.5882 | 95.4066 | 93.5141 | 95.2969 | 95.1251 | 94.5743 | 90.8525 | 92.5806 | 95.1515 | 98.6158 | 95.4971 | 93.8711
Dynamic Coverage | 99.8308 | 93.3679 | 95.0462 | 98.8645 | 99.9857 | 99.7529 | 99.5057 | 99.9467 | 95.0864 | 98.0421 | 99.3973 | 98.7727 | 99.1564 | 99.5269 | 99.2396 | 99.697

## Slide 27
Qemu (Full System Mode)
Qemu
Guest H/W
Guest OS
App1
App2
Native H/W
Native OS
Qemu
VMM
Guest H/W
Guest
OS1
App1
Guest
OS2
App2
Native H/W
Native OS
Important for studying the execution of different workloads in native as well as virtualized environments

## Slide 28
Qemu Emulation
(Full System Mode)
Translation
ip, assembly, add rax, [rbx], rcx
ip, memread, addr X
load [r1 (addr X)], tmp
int-alu r0, tmp, r2
Translate
And cache
Mapping Available ?
Fuse
Yes
No
Qemu
Guest H/W
Guest OS
App1
App2

## Slide 29
Qemu (Framework)
Qemu
Guest H/W
Guest OS
App1
App2
Traces contain:
Regular (memory, and branch)
Assembly text of each instruction
OS Events
  System call ID
  Interrupt ID
  Privilege level switches in x86
  Research specific (OS instrumentation)

## Slide 30: Communication Channel
Emulator
Tejas Simulator
Benchmark
Communication channel
Execution trace
Written in C/C++/Java
Written in Java
Options: Shared memory, Network, and Files
Any communication channel only needs to follow rules in terms of the order in which the information is passed

## Slide 31: Execution trace
Program counter (64 bits) | Type of packet (64 bits) | Packet value (64 bits)
p3
p2
p1
…
Simulator
Communication channel (Sequence of packets)
Individual Packet
Assembly packet can have variable size
Single instruction can have multiple packets
Emulator

## Slide 32: Shared Memory
Synchronization: Peterson lock
Java interaction with shared memory: JNI
Benchmark
Emulator
Tejas (Simulator)
control
used to transfer data
Producer
Consumer
Shared memory segment (circular queue)

## Slide 33: Network
Benchmark
Emulator
Remote machine
Native machine
Tejas Simulator
Network
(TCP Sockets)
Can be useful if the Emulator can run only on a particular machine.

## Slide 34: File
Benchmark
Emulator
Machine X
Machine Y
Tejas Simulator
Machine X and Machine Y can have completely different platform (hardware, software): Driver for clouds
Deterministic simulations: boon for debugging parallel programs
Implementation: GZip compressed (10X reduction in trace size)
Trace file

## Slide 35: Speed
Chart: Speed (MBps)
| Network | Shared Memory | File
Speed (MBps) | 9 | 24 | 21

## Slide 36
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 37
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Semi-Event Driven Model Simulating the Pipeline Simulating the Memory System Simulating the On-chip Interconnect Simulating the Off-Chip DRAM Simulation Tricks Validation and Performance Hacker’s Guide | 
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 38: Simulation Engine
Finite State Machines
  Any chip can be viewed as a set of components
  Whose functioning are defined by FSMs
  Capable of communicating with each other
C1
cache
C4
core
C3
NOC
C2
directory
A
B
C
E
D
A
B
C
D
A
B
C
E
D
A
B
C

## Slide 39: Simulation Engine
Iterative Model of Simulation
C1
C4
C3
C2
A
B
C
E
D
A
B
C
D
A
B
C
E
D
A
B
C
cycle : n
cycle : n+1
Expensive if each component is not accessed in each cycle !!

## Slide 40: Simulation Engine
Event Driven Model of Simulation
C1
C4
C3
C2
A
B
C
E
D
cycle : 100
C1 : 100
C2 : 102
C1 : 105
Event Queue

## Slide 41: Simulation Engine
Event Driven Model of Simulation
C1
C4
C3
C2
A
B
C
E
D
A
B
C
D
cycle : 100
cycle : 101
C2 : 102
C1 : 104
cycle : 102
Event Queue
C1 : 105
Expensive to modify the event queue !!

## Slide 42: Simulation Engine
Iterative Model
  Expensive when component is not active every cycle
Event Driven Model
  Expensive when components are highly active
TEJAS : Semi – Event Driven Model
  Iterative when simulating highly active components
    Ex. Pipeline stages
  Event-driven when simulating less active components
    Ex. Caches, directories

## Slide 43
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Semi-Event Driven Model Simulating the Pipeline Simulating the Memory System Simulating the On-chip Interconnect Simulating the Off-Chip DRAM Simulation Tricks Validation and Performance Hacker’s Guide | 
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 44: On-chip Components
Pipeline
Instruction Cache
Data Cache
Interconnect
Shared Cache
Coherence
Core
Memory Controller

## Slide 45: Pipeline
Pipeline
Instruction Cache
Data Cache
Interconnect
Shared Cache
Coherence
Core
Memory Controller

## Slide 46: Branch Predictor
Execution model: (Emulator Simulator) ensures correct order of instructions
if (instruction-type=branch)
Pipeline flush is simulated by stalling the pipeline by a fixed number of cycles
Predictor
State
Program counter
Taken/not taken
Decision (taken/not-taken)
based on the state before
this insn

## Slide 47: Branch Predictor Options
Simple: Perfect Predictor, No Predictor, Always taken, Always not-taken
Tournament
Bimodal
GAg, GAp, PAg, PAp
Gshare
Modern: TAGE
Predictor
State
Program counter
Taken/not taken
Decision (taken/not-taken)
based on the state before
this insn
Takes 3-4 days to code a branch predictor in Tejas

## Slide 48: Multi-Issue Inorder Pipeline
Decode
Execute
Memory
Write-Back
Fetch
Issue in-order as long as
No branch
No producer
No write to same destination
in this cycle
Intel Pentium [Alpert ‘1993]

## Slide 49: Out-of-Order Pipeline (9 stages + wakeup select logic)
Decode
Rename
IW Push
Select
Execute
Fetch
Wake-Up
Write-Back
Commit
ROB
LSQ
IW
Register Files

## Slide 50: Wakeup-Select
Issue those instructions in IW with operands ready and FU available
Higher priority for older instructions
Decode
Rename
IW Push
Select
Execute
Fetch
Wake-Up
Write-Back
Commit
ROB
LSQ
IW
Register Files
Wake up those instructions in IW waiting for this result

## Slide 51: Load-Store Forwarding
LD ? | LD 0x30 | ST 0x20 | ST 0x10
Load address ready : 0x10
LSQ
Head
LSQ
Tail

## Slide 52: Load-Store Forwarding
LD 0x10 | LD 0x30 | ST 0x20 | ST 0x10
LSQ
Head
LSQ
Tail
Search for store
Use this value to complete load

## Slide 53: Load-Store Forwarding
LD 0x10 | LD 0x30 | ST 0x20 | ST ?
Store address ready : 0x10
LSQ
Head
LSQ
Tail

## Slide 54: Load-Store Forwarding
LD 0x10 | LD 0x30 | ST 0x20 | ST 0x10
LSQ
Head
LSQ
Tail
Search for loads
Use value to complete this load

## Slide 55
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Semi-Event Driven Model Simulating the Pipeline Simulating the Memory System Simulating the On-chip Interconnect Simulating the Off-Chip DRAM Simulation Tricks Validation and Performance Hacker’s Guide | 
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 56: Memory hierarchy
Pipeline
Instruction Cache
Data Cache
Interconnect
Shared Cache
Coherence
Core
Memory Controller

## Slide 57: Memory System
Highly configurable caches
Thorough Miss Status Holding Register (MSHR) design
Flexibility to create a graph of caches to form the memory system

## Slide 58: Specifying Memory Hierarchy
Inverted Tree
Root: Main memory
L1 (private caches)
L2
L3

## Slide 59
Core 0
I D
L2
L3 cache
Example Configurations
Core 1
I D
L2
Core 2
I D
L2
Core 3
I D
L2
Core 0 Core1
I D I D
L2
L3 cache
Core 2 Core3
I D I D
L2
Core 0
I D
L2
Core 1
I D
L2
Core 2
I D
L2
Core 3
I D
L2
L3 (0)
L3 (1)
L3 (2)
L3 (3)
Core 0
I D
L2
Core 1
I D
L2
Core 2
I D
L2
Core 3
I D
L2
L3 (4)
L3 (5)
L3 (6)
L3 (7)
ConfigurationA (Private L2)
ConfigurationB
(L2 shared between 2 cores)
ConfigurationC
(L3 is broken down (NUCA))

## Slide 60: Non Uniform Cache Access (NUCA)
L1
L2
Lower Level Memory
L2
L2
L2
L2
L2
L2
L2
L2
UCA
NUCA
Sets
Placement, Migration and Replacement
- SNUCA: Find memory element based on the bits in the address field
- DNUCA: Allow caches to migrate data based on usage patterns

## Slide 61: Coherence
Pipeline
Instruction Cache
Data Cache
Interconnect
Shared L2 Cache
Coherence
Core
Memory Controller

## Slide 62: Coherence Protocol (MESI: Directory)
Simple 4-state textbook protocol does not capture the complexity of a real world system with complexities such as NUCA and NOC
H/W approach: 100’s of states
Simulating so many states would make the code bulky and difficult to maintain. Idea is to use code simple textbook protocol and use a ‘corrective’ operation when an inconsistency is found
Corrective operations form 0.001% of the total coherence operations
Image Reference: http://sc.tamu.edu/systems/eos/hardware.php

## Slide 63
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Semi-Event Driven Model Simulating the Pipeline Simulating the Memory System Simulating the On-chip Interconnect Simulating the Off-Chip DRAM Simulation Tricks Validation and Performance Hacker’s Guide | 
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 64: Interconnect
Pipeline
Instruction Cache
Data Cache
Interconnect
Shared L2 Cache
Coherence
Core
Memory Controller

## Slide 65: Inter-connect: BUS and NOC
Core 1
BUS
Shared L2 Cache
Core 2
Core 3
Core 4
Core 5
Core 6
Core 7
Core 8
Core 1
Core 2
Core 3
Core 4
L2 1
L2 2
L2 3
L2 4
Core 1
Core 2
Core 3
Core 4
L2 1
L2 2
L2 3
L2 4
NOC

## Slide 66: Network On Chip
Sender ‘S’
Receiver ‘R’
Interconnect
R.port.put(msg)
Same Network
Interface
Different Network
Interface

## Slide 67: Network On Chip
Interconnect
Bus
Network
Medium
Electrical
Optical
Routing Algorithm
Simple West first
North last Negative first
Topology
Mesh Torus Ring Bus
Fat Tree Butterfly Omega
Route Selection
Static
Adaptive (based on congestion)

## Slide 68: Network On Chip
Bandwidth governed by
Flit width
Flow control provided by
Router buffer size
Number of router ports
Any SimulationElement can communicate with another through the NOC
Deadlock Avoidance
Prioritizing messages

## Slide 69
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Semi-Event Driven Model Simulating the Pipeline Simulating the Memory System Simulating the On-chip Interconnect Simulating the Off-Chip DRAM Simulation Tricks Validation and Performance Hacker’s Guide | 
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 70: Tejas DRAM Implementation
Salient features:
  Modelled all DRAM timing parameters
  Cycle accurate (verified against DRAMSim 2)
  Multiple physical channels supported
  Support for Open page, Close page policies
  DDR2/DDR3 can be modelled by supplying appropriate timing parameters
  Semi-event driven model

## Slide 71
L2 Cache
MainMemoryDRAMController
Request (read/write)
MemoryResponse
Address Mapping
pending queue
CommandQueue
RamBus (address)
MainMemoryBusPacket
At RAM Clock
Rank_Response
Ranks
Block diagram showing the flow of events

## Slide 72: Block diagram
Caches
Directory
NoC
Pipeline
Package: dram
Rank 0
Rank 1
Rank k
Bank States
Bank States
Address
Mapping
Main Memory Controller
Ranks
Command Queue
Command
Scheduling
CMD
DATA
Refresh
Generate
RAS
REF
CAS
PRE
Cache miss event
Response
event
Basic block diagram for Tejas-DRAM

## Slide 73
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Semi-Event Driven Model Simulating the Pipeline Simulating the Memory System Simulating the On-chip Interconnect Simulating the Off-Chip DRAM Simulation Tricks Validation and Performance Hacker’s Guide | 
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 74: Cache Locality: Block of Instructions
Emulation
Data transfer
Translation
Simulation
Instruction
Large piece of code: i-cache and d-cache miss
Approach: Operate at a granularity of 50 instructions
Emulation
Data transfer
Translation
Simulation
Block of Instruction

## Slide 75: GC Overhead
Automated way of allocating and de-allocating objects
Translation
Fetch
……..
Commit
Java
Heap Memory
VISA
Malloc’ed objects
No de-allocate routine !!

## Slide 76: GC Overhead
Automated way of allocating and de-allocating objects
Translation
Fetch
……..
Commit
Java
Heap Memory
Malloc’ed objects
Image source: www.sjbparish.com
Garbage Collector

## Slide 77: Approach1: Pooling of Objects
Pre-allocate a pool of objects
Translation
Fetch
……..
Commit
VISA
VISA
VISA
VISA
Borrow from pool
Return to pool
Data footprint remains bounded

## Slide 78: Approach2: Event Re-use
Modify and re-use the same object
Router 1
Router 2
Router 3
Router 4
Message (A, B) : <A, Router1>
NOC
A
B
Message (A, B) : <Router1, Router2>
Message (A, B) : <Router2, Router3>
Message (A, B) : <Router3, Router4>

## Slide 79
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Semi-Event Driven Model Simulating the Pipeline Simulating the Memory System Simulating the On-chip Interconnect Simulating the Off-Chip DRAM Simulation Tricks Validation and Performance Hacker’s Guide | 
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 80: Validation (Dell PowerEdge R620 server)
Machine
Intel XEON 2620 (2GHz)
µ-arch
Sandybridge
# cores
24
LLC
15 MB
RAM
Multi-threading / DVFS
31 GB
No
JRE
Java 7

## Slide 81: Validation : Serial Workloads (SPEC CPU2006)
11.45%
27%

## Slide 82: Validation : Parallel Workloads (SPLASH 2)
18.77%
33%

## Slide 83: Comparison with other simulators
Simulator | Benchmark Suite | Average Absolute Error % | Max. Absolute Error%
MARSS | SPEC 2006 | 23.46 % | 59.2 %
FastMP | SPEC 2006 | 9.56 % | 40 %
Tejas | SPEC 2006 | 11.45 % | 27 %
Sniper | SPLASH-2 | 25 % | 59.3 %
Tejas | SPLASH-2 | 18.77 % | 33 %

## Slide 84: Performance : Serial Workloads (SPEC CPU2006)
220 % faster than GEM5
25 % faster than Multi2Sim

## Slide 85: Performance : Parallel Workloads (SPLASH 2)
132 KIPS

## Slide 86: Full system simulations

## Slide 87: Overall Picture of the Infrastructure

## Slide 88: The Kernels
Linux FreeBSD OpenBSD
3.13.0 9.2.0 5.5

## Slide 89: Workloads
Network:
  ISCP: Secure copy file from remote machine to local machine (SCP)
  OSCP: Secure copy file from local machine to remote machine (SCP)
Database:
  OLTP: Online Transaction Processing (Sysbench benchmark suite)
File system
  Find: File system browsing (Utility application Find)
  File IO: Random reads and writes to file (Sysbench benchmark suite)
Memory intensive
  MemorySB: Multiple threads perform random read/write to memory (Sysbench benchmark suite)

## Slide 90: CPU Spec
Intel® Xeon® Processor X5650 (2 CPUs: 6 cores each)
  Nehalem Micro architecture
  Frequency: 2.66 GHz
  L1 – 32KB, ICache – 32KB
  L2 – 256KB
  L3 – 12MB (Shared)

## Slide 91: Linux Statistics Validation
Average Error = 15%
Average Error = 3%
Average Error = 3.5%
Average Error = 10.7%
Average Error = 9.3%

## Slide 92: FreeBSD Statistics Validation
Average Error = 14.1%
Average Error = 0.9%
Average Error = 6.6%
Average Error = 14.9%

## Slide 93: OpenBSD Statistics Validation
Average Error = 12.7%
Time command to measure CPU time

## Slide 94
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Semi-Event Driven Model Simulating the Pipeline Simulating the Memory System Simulating the On-chip Interconnect Simulating the Off-Chip DRAM Simulation Tricks Validation and Performance Hacker’s Guide | 
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 95: At the Highest Level
main.ArchitecturalComponent.createChip();
while (simulation is not complete) {
for each benchmark thread {
get trace from emulator
translate to VISA
}
while more VISA instructions to simulate{
for each benchmark thread {
simulate corresponding core
}
clock++
}
}
Notes: Talk about how each benchmark thread is simulated on a separate core

## Slide 96: At the Highest Level
main.ArchitecturalComponent.createChip();
while (simulation is not complete) {
for each benchmark thread {
get trace from emulator
translate to VISA
}
while more VISA instructions to simulate{
for each benchmark thread {
simulate corresponding core for 1 cycle
}
clock++
}
}
Create components and establish links between them

## Slide 97: At the Highest Level
main.ArchitecturalComponent.createChip();
while (simulation is not complete) {
for each benchmark thread {
get trace from emulator
translate to VISA
}
while more VISA instructions to simulate{
for each benchmark thread {
simulate corresponding core
}
clock++
}
}
Get data from the emulator and translate instructions to VISA format
Notes: Talk about how each benchmark thread is simulated on a separate core

## Slide 98: At the Highest Level
main.ArchitecturalComponent.createChip();
while (simulation is not complete) {
for each benchmark thread {
get trace from emulator
translate to VISA
}
while more VISA instructions to simulate{
for each benchmark thread {
simulate corresponding core
}
clock++
}
}
Feed VISA instructions to pipeline and increment simulation clock
Notes: Talk about how each benchmark thread is simulated on a separate core

## Slide 99: At the Highest Level
main.ArchitecturalComponent.createChip();
while (simulation is not complete) {
for each benchmark thread {
get trace from emulator
translate to VISA
}
while more VISA instructions to simulate{
for each benchmark thread {
simulate corresponding core for 1 cycle
}
clock++
}
}
Create components and establish links between them

## Slide 100: main.ArchitecturalComponent.createChip()
Cores
Private caches
Shared caches
Coherence elements
Memory controllers
Interconnect
DRAM
Connect the elements

## Slide 101: main.ArchitecturalComponent.createChip()
Cores
Private caches
Shared caches
Coherence elements
Memory controllers
Interconnect
DRAM
Create the Memory Hierarchy

## Slide 102: At the Highest Level
main.ArchitecturalComponent.createChip();
while (simulation is not complete) {
for each benchmark thread {
get trace from emulator
translate to VISA
}
while more VISA instructions to simulate{
for each benchmark thread {
simulate corresponding core for 1 cycle
}
clock++
}
}

## Slide 103: emulatorinterface.RunnableThread
for each thread {
ipcBase.fetchManyPackets()
for each packet {
ObjParser.fuseInstruction()
}
}

## Slide 104: emulatorinterface.RunnableThread
for each thread {
ipcBase.fetchManyPackets()
for each packet {
ObjParser.fuseInstruction()
}
}
IpcBase
FilePacket
SharedMem
Network
Pipe

## Slide 105: emulatorinterface.RunnableThread
for each thread {
ipcBase.fetchManyPackets()
for each packet {
ObjParser.fuseInstruction()
}
}
Fuse
VISA static
Packet <IP,value,target>
(0x10, memread, 0x1234)
VISA dynamic
VISA instruction (static)
Runtime information
VISA instruction (dynamic)
load <(%reg1), ?>, %tmpreg1
int-alu %reg0, %tmpreg1, %tmpreg1
store %tmpreg1, <(%reg1), ?>
load <(%reg1), 0x1234>, %tmpreg1
int-alu %reg0, %tmpreg1, %tmpreg1
store %tmpreg1, <(%reg1), 0x1234>

## Slide 106: At the Highest Level
main.ArchitecturalComponent.createChip();
while (simulation is not complete) {
for each benchmark thread {
get trace from emulator
translate to VISA
}
while more VISA instructions to simulate{
for each benchmark thread {
simulate corresponding core for 1 cycle
}
clock++
}
}

## Slide 107: emulatorinterface.RunnableThread
void runPipelines() {
while more VISA instructions to simulate{
for each benchmark thread t {
pipelineInterfaces[t].oneCycleOperation()
}
clock++
}
}

## Slide 108: pipeline.outoforder.OutOfOrderPipeline.java
void oneCycleOperation() {
performCommits();
performWriteBack();
performSelect();
processEvents();
performIWPush();
performRename();
performDecode();
performFetch();
}

## Slide 109: pipeline.outoforder.OutOfOrderPipeline.java
void oneCycleOperation() {
performCommits();
performWriteBack();
performSelect();
processEvents();
performIWPush();
performRename();
performDecode();
performFetch();
}
Iterative Model: done every cycle

## Slide 110: pipeline.outoforder.OutOfOrderPipeline.java
void oneCycleOperation() {
performCommits();
performWriteBack();
performSelect();
processEvents();
performIWPush();
performRename();
performDecode();
performFetch();
}
Discrete Event Simulator Model
Notes: Talk about per core event queue. It offers scalability.

## Slide 111: Discrete Event Simulator Model: Example (pipeline.outoforder.IWEntry.java)
eventQ.addEvent( //at time of issue
new ExecCompleteEvent(
curTime+FU_latency, //event time
IW, //requester
executer, //processor
RequestType.EXEC_COMPLETE,//event type
associatedROBEntry)); //payload
Event
Address Carrying
NOC
ExecComplete
Notes: Different instructions take different times to execute

## Slide 112: SimulationElement
class generic.SimulationElement {
public abstract void handleEvent(event);
generic.Port port;
generic.CommunicationInterface comInterface;
public void sendEvent(event);
}

## Slide 113: Global Event Queue
void addEvent (Event e) {
timedQueue.add(e.getTime())
}
void processCyclesForCycle(long c) {
while (true) {
events = getEventsForCycle(c)
if (events==NULL) {
break
} else {
for (event e: events) {
e.getProcessingElement.handleEvent(e)
}
}
}
}

## Slide 114: Discrete Event Simulator Model: Example
void handleEvent(event) {//called by processEvents
if event type is RequestType.EXEC_COMPLETE {
handleExecutionCompletion(event);
}
}
void handleExecutionCompletion(event) {
event.associatedROBEntry.setExecuted(true);
}
File: pipeline.outoforder.ExecutionLogic.java
Notes: handleEvent is invoked at curTime+FU_lat by processEvents()

## Slide 115: SimulationElement
class generic.SimulationElement {
public abstract void handleEvent(event);
generic.Port port;
generic.CommunicationInterface comInterface;
public void sendEvent(event);
}

## Slide 116: Ports of SimulationElements
class generic.Port {
PortType portType; //Unlimited or FCFS
int noOfPorts;
long latencyOfConnectedElement;
long occupancy;
long[] portBusyUntil;
public void put() {
find earliest time T that a port is free
set event time to T
add event to event queue
}

## Slide 117: SimulationElement: ComInterface
class generic.SimulationElement {
public abstract void handleEvent(event);
generic.Port port;
generic.CommunicationInterface comInterface;
public void sendEvent(event) {
dest = event.getProcessingElement
if dest.getComInterface == this.getComInterface {
dest.getPort.put(event);
} else {
this.getComInterface.sendMessage(event);
}
}

## Slide 118: SimulationElement: ComInterface
class generic.SimulationElement {
public abstract void handleEvent(event);
generic.Port port;
generic.CommunicationInterface comInterface;
public void sendEvent(event) {
dest = event.getProcessingElement
if dest.getComInterface == this.getComInterface {
dest.getPort.put(event);
} else {
this.getComInterface.sendMessage(event);
}
}
If they use the same interface to connect to the chip interconnect, we can access this component directly

## Slide 119: SimulationElement: ComInterface
class generic.SimulationElement {
public abstract void handleEvent(event);
generic.Port port;
generic.CommunicationInterface comInterface;
public void sendEvent(event) {
dest = event.getProcessingElement
if dest.getComInterface == this.getComInterface {
dest.getPort.put(event);
} else {
this.getComInterface.sendMessage(event);
}
}
Let the interconnect handle delivering the message to the destination element

## Slide 120: Example: Cache Access
void handleAccess(addr, request_type, event) {
CacheLine cl = accessAndMark(addr);
if (cl != null)
cacheHit(addr, requestType, cl, event);
else {
if (this.mycoherence != null) {
if (request_type == Cache_Write)
mycoherence.writeMiss(addr, this);
else if (request_type == Cache_Read)
mycoherence.readMiss(addr, this);
} else
sendRequestToNextLevel(addr, Cache_Read);
mshr.addToMSHR(event);
}
}

## Slide 121: Example: Cache Access
void handleAccess(addr, request_type, event) {
CacheLine cl = accessAndMark(addr);
if (cl != null)
cacheHit(addr, requestType, cl, event);
else {
if (this.mycoherence != null) {
if (request_type == Cache_Write)
mycoherence.writeMiss(addr, this);
else if (request_type == Cache_Read)
mycoherence.readMiss(addr, this);
} else
sendRequestToNextLevel(addr, Cache_Read);
mshr.addToMSHR(event);
}
}
Send response to requester through this.sendEvent()
If coherent cache, and if it is a write request, inform coherence of write hit. Again through this.sendEvent()

## Slide 122: Example: Cache Access
void handleAccess(addr, request_type, event) {
CacheLine cl = accessAndMark(addr);
if (cl != null)
cacheHit(addr, requestType, cl, event);
else {
if (this.mycoherence != null) {
if (request_type == Cache_Write)
mycoherence.writeMiss(addr, this);
else if (request_type == Cache_Read)
mycoherence.readMiss(addr, this);
} else
sendRequestToNextLevel(addr, Cache_Read);
mshr.addToMSHR(event);
}
}
Request coherence for line through this.sendEvent()

## Slide 123: Example: Cache Access
void handleAccess(addr, request_type, event) {
CacheLine cl = accessAndMark(addr);
if (cl != null)
cacheHit(addr, requestType, cl, event);
else {
if (this.mycoherence != null) {
if (request_type == Cache_Write)
mycoherence.writeMiss(addr, this);
else if (request_type == Cache_Read)
mycoherence.readMiss(addr, this);
} else
sendRequestToNextLevel(addr, Cache_Read);
mshr.addToMSHR(event);
}
}
Request next level cache or main memory through this.sendEvent()

## Slide 124: Example: Cache Access
void handleAccess(addr, request_type, event) {
CacheLine cl = accessAndMark(addr);
if (cl != null)
cacheHit(addr, requestType, cl, event);
else {
if (this.mycoherence != null) {
if (request_type == Cache_Write)
mycoherence.writeMiss(addr, this);
else if (request_type == Cache_Read)
mycoherence.readMiss(addr, this);
} else
sendRequestToNextLevel(addr, Cache_Read);
mshr.addToMSHR(event);
}
}

## Slide 125
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 126
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Practical Experiences of using Tejas for Research Practical Experiences of using Tejas for Teaching Hands-on Demo | 
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 127: Efficient Detection of Soft Errors in Manycore Processors
“FluidCheck: A Redundant Threading based Approach for Reliable Execution in Manycore Processors”, Kalayappan et al, TACO 2016.

## Slide 128: Instruction Prefetching Scheme for OS Intensive Applications (MICRO 2016)
Non-privileged: Application
Privileged: OS
Time
OS Events
1) System call
2) Interrupt (top-half)
3) Interrupt (bottom-half)
4) Schedule routine
Execution block of 125 functions
HyperTask

## Slide 129: Optical Overlay NUCA: A High Speed Substrate for Shared L2 Caches
Published in HiPC 2014
Excerises NUCA
32 cores and 32 L2 cache banks connected through optical interconnects
Optical NUCA protocols at L2 level
  NUCA messages are passed through optical interconnects
Dynamic creation of bank sets
  Based on benchmark characteristics to improve cache utilization and hit rate

## Slide 130: ColdBus - A Near-Optimal Power Efficient Optical Bus
Published in HiPC 2015
Uses optical NOC
On chip electrical interconnects are replaced by optical interconnects
  Fast but not energy efficient
This work proposes to use optical network reconfiguration
  At regular intervals
  Based on network usage prediction
    Predictor uses load/store memory address
  Reduce optical output power during low activity period

## Slide 131: BigBus : A scalable optical interconnect
Published in DATE 2016
Optical NOC
768 cores and 256 L2 cache banks
Energy efficient, scalable optical interconnect
  Multi level interconnect to save energy
  Network activity prediction
  Intelligent placements of cores and cache banks

## Slide 132
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Practical Experiences of using Tejas for Research Practical Experiences of using Tejas for Teaching Hands-on Demo | 
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 133
Course Aid for CSL718: Architecture of High Performance Computers at IIT Delhi

## Slide 134: Understanding the Working of a Cache
To design micro-benchmarks and simulate them on Tejas. The benchmarks must have the following properties:
100% misses, with most capacity misses
Increasing the L1 d-cache block size improves hit rate
Increasing the L1 d-cache block size degrades hit rate
Increasing the L1 d-cache associativity improves hit rate
Write through better than write back, in terms of L1-L2 traffic
Write back better than write through, in terms of L1-L2 traffic

## Slide 135: Load Store Predictors
LD ? | LD 0x30 | ST 0x20 | ST 0x10
Load address ready : 0x10
LSQ
Head
LSQ
Tail
Implement and evaluate
anyStore: “Memory Dependence Prediction Using Store Sets”, Chrysos et al., ISCA 98.
pairLS: “Dynamic Speculation and Synchronization of Data Dependences”, Moshovos et al., ISCA 97.

## Slide 136: Odd-Even Routing
“The odd-even turn model for adaptive routing”, Chiu, TPDS 2000.
Chart: IPC
| blackscholes | canneal | facesim | fluidanimate | streamcluster
Mesh | 18.63 | 2.19 | 3.42 | 2.31 | 4.01
Torus | 23.36 | 3.84 | 6.38 | 4.19 | 6.16

## Slide 137: Reactive NUCA
Chart: IPC
| blackscholes | canneal | facesim | fluidanimate | streamcluster
Uniform | 24.8317 | 5.8926 | 14.7764 | 8.5062 | 5.7781
SNUCA | 24.8779 | 7.282 | 15.6825 | 9.4085 | 11.2676
DNUCA | 24.6699 | 6.5128 | 14.2835 | 8.2414 | 10.8379
RNUCA | 24.9849 | 6.1241 | 16.5136 | 9.5032 | 6.1778
“Reactive NUCA: near-optimal block placement and replication in distributed caches”, Hardavellas et al., ISCA 2009.

## Slide 138
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Practical Experiences of using Tejas for Research Practical Experiences of using Tejas for Teaching Hands-on Demo | 
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 139
Installing Tejas

## Slide 140
Performing ROI Simulations

## Slide 141
Region-of-interest Simulations
Number of instructions
Special functions

## Slide 142: ROI Simulations
<Configuration>
…
<Simulation>
…
<subsetSim>false</subsetSim>
<numInsToIgnore>0</numInsToIgnore>
<subsetSimSize>0</subsetSimSize>
<markerFunctions>false<markerFunctions>
<startSimMarker></startSimMarker>
<endSimMarker></endSimMarker>
<Simulation>
…
</Configuration>

## Slide 143: ROI Simulations
<Configuration>
…
<Simulation>
…
<subsetSim>false</subsetSim>
<numInsToIgnore>0</numInsToIgnore>
<subsetSimSize>0</subsetSimSize>
<markerFunctions>false<markerFunctions>
<startSimMarker></startSimMarker>
<endSimMarker></endSimMarker>
<Simulation>
…
</Configuration>
Number of instructions
Set subsetSim to true to simulate execution block specified in terms of number of instructions
Benchmark start
Ignore
Simulate

## Slide 144: ROI Simulations
<Configuration>
…
<Simulation>
…
<subsetSim>false</subsetSim>
<numInsToIgnore>0</numInsToIgnore>
<subsetSimSize>0</subsetSimSize>
<markerFunctions>false<markerFunctions>
<startSimMarker>f_start</startSimMarker>
<endSimMarker>f_end</endSimMarker>
<Simulation>
…
</Configuration>
Set markerFunctions to true to simulate execution block whose start and end are special functions

## Slide 145
Deterministic Simulations Using Files
Execute benchmark and collect traces
Run simulations using trace files

## Slide 146: Storing Execution Traces in a File
$ java –jar tejas.jar config.xml statfile ./benchmark.o

## Slide 147: Storing Execution Traces in a File
<Configuration>
<Emulator>
…
<EmulatorType>pin</EmulatorType>
<CommunicationType>file</CommunicationType>
<StoreExecutionTracesInAFile>true</StoreExecutionTracesInAFile>
<BasenameForTraceFiles>/home/guest/bm<BasenameForTraceFiles>
…
</Emulator>
…
</Configuration>
$ java –jar tejas.jar config.xml statfile ./benchmark.o

## Slide 148: Storing Execution Traces in a File
<Configuration>
<Emulator>
…
<EmulatorType>pin</EmulatorType>
<CommunicationType>file</CommunicationType>
<StoreExecutionTracesInAFile>true</StoreExecutionTracesInAFile>
<BasenameForTraceFiles>/home/guest/bm<BasenameForTraceFiles>
…
</Emulator>
…
</Configuration>
$ java –jar tejas.jar config.xml statfile ./benchmark.o
Traces: /home/guest/bm_*.gz
Number of files: Number of threads
Trace file for thread #x: /home/guest/bm_x.gz

## Slide 149: Simulation Using Trace Files
<Configuration>
<Emulator>
…
<EmulatorType>pin</EmulatorType>
<CommunicationType>file</CommunicationType>
<StoreExecutionTracesInAFile>false</StoreExecutionTraceInAFile>
<BasenameForTraceFiles><BasenameForTraceFiles>
…
</Emulator>
…
</Configuration>
$ java –jar tejas.jar config.xml statfile /home/guest/bm

## Slide 150
Performing Full-system Simulations

## Slide 151
Qemu (Full System Mode)
QemuTrace
VMM
Guest H/W
Guest
OS1
App1
QemuTrace
Guest H/W
Guest OS
Guest
OS2
App2
App1
App2
Important for studying the execution of different workloads in native as well as virtualized environments

## Slide 152: Procedure for Performing Full System Simulations
Download and build Qemu Trace
Prepare a Full system disk image using any emulator/VMM
Collect traces of benchmarks inside your disk QemuTrace
Execution
Traces
Tejas

## Slide 153: Collecting Traces Using QemuTrace
Boot and login into your disk image
Execute the benchmark
De-initialize and poweroff your disk image
Initialization
Cleanup
T
I
M
E
Region of interest

## Slide 154
Region-of-interest Simulations
Adding Special Instructions
Manual Intervention Using Qemu Terminal

## Slide 155: Adding Special Instructions
int main(void) {
... //initialization
asm int(“int $100”) // start trace collection
ROI() //region of interest
asm int(“int $101”) // stop trace collection
... //cleanup
}
asm int (“int $100”) | asm int (“int $101”)
Ignore the instruction Start trace collection | Ignore the instruction Stop trace collection
Does not affect benchmark’s execution
Deterministic
Notes: Different instructions take different times to execute

## Slide 156: Manual Intervention
Cases when the special instruction approach will not work:
Proprietary benchmark which you cannot change
Special benchmark whose region of interest can only be verified through external help (GUI)
Give commands to QemuTrace to start and stop the trace collection at run time
$ <qemu-command>
$ qqq_start_trace
$ qqq_stop_trace

## Slide 157
Realizing Different Memory Hierarchies

## Slide 158
BUS
Pipeline
Core 0
i-cache
d-cache
L2 cache (LLC)
Directory
Pipeline
Core 1
i-cache
d-cache
Pipeline
Core 2
i-cache
d-cache
Pipeline
Core 3
i-cache
d-cache
Hierarchy 1

## Slide 159: Memory Hierarchy
<Core>
...
<Cache firstLevel=“true” name=“L1_I” nextLevel=“L2” type=“icache”/>
<Cache firstLevel=“true” name=“L1_D” nextLevel=“L2” type=“dcache”/>
</Core>
<SharedCaches>
<Cache name=“L2” type=“L2Cache”/>
<Cache name=“D1” type=“Directory1”/>
</SharedCaches>
Private Caches
Shared Caches

## Slide 160: Memory Hierarchy
<Core>
...
<Cache firstLevel=“true” name=“L1_I” nextLevel=“L2” type=“icache”/>
<Cache firstLevel=“true” name=“L1_D” nextLevel=“L2” type=“dcache”/>
</Core>
<SharedCaches>
<Cache name=“L2” type=“L2Cache”/>
<Cache name=“D1” type=“Directory1”/>
</SharedCaches>

## Slide 161: Memory Hierarchy
<Core>
...
<Cache firstLevel=“true” name=“L1_I” nextLevel=“L2” type=“icache”/>
<Cache firstLevel=“true” name=“L1_D” nextLevel=“L2” type=“dcache”/>
</Core>
<SharedCaches>
<Cache name=“L2” type=“L2Cache”/>
<Cache name=“D1” type=“Directory1”/>
</SharedCaches>
Used to specify a Cache element

## Slide 162: Memory Hierarchy
<Core>
...
<Cache firstLevel=“true” name=“L1_I” nextLevel=“L2” type=“icache”/>
<Cache firstLevel=“true” name=“L1_D” nextLevel=“L2” type=“dcache”/>
</Core>
<SharedCaches>
<Cache name=“L2” type=“L2Cache”/>
<Cache name=“D1” type=“Directory1”/>
</SharedCaches>
Identify which cache is level 1
Useful when a core has more than one level of private caches

## Slide 163: Memory Hierarchy
<Core>
...
<Cache firstLevel=“true” name=“L1_I” nextLevel=“L2” type=“icache”/>
<Cache firstLevel=“true” name=“L1_D” nextLevel=“L2” type=“dcache”/>
</Core>
<SharedCaches>
<Cache name=“L2” type=“L2Cache”/>
<Cache name=“D1” type=“Directory1”/>
</SharedCaches>
Used for creating links between caches using names

## Slide 164: Memory Hierarchy
<Core>
...
<Cache firstLevel=“true” name=“L1_I” nextLevel=“L2” type=“icache”/>
<Cache firstLevel=“true” name=“L1_D” nextLevel=“L2” type=“dcache”/>
</Core>
<SharedCaches>
<Cache name=“L2” type=“L2Cache”/>
<Cache name=“D1” type=“Directory1”/>
</SharedCaches>
Creates a link to a cache named “L2”
Search nextLevel cache if a line was not found in this cache
If next level is not specified, it implies that this cache is the last level cache

## Slide 165: Memory Hierarchy
<Core>
...
<Cache firstLevel=“true” name=“L1_I” nextLevel=“L2” type=“icache”/>
<Cache firstLevel=“true” name=“L1_D” nextLevel=“L2” type=“dcache”/>
</Core>
<SharedCaches>
<Cache name=“L2” type=“L2Cache”/>
<Cache name=“D1” type=“Directory1”/>
</SharedCaches>
Name of this element’s detailed configuration in the configuration library

## Slide 166: Cache: Detailed Configuration
<dcache>
  <WriteMode>WB</WriteMode>
  <BlockSize>64</BlockSize>
  <Associativity>8</Associativity>
  <Size>32768</Size>
  <Latency>3</Latency>
  <PortType>FCFS</PortType>
  <AccessPorts>4</AccessPorts>
  <PortOccupancy>1</PortOccupancy>
  <Coherence>D1</Coherence>
  <NumBuses>1</NumBuses>
  <MSHRSize>16</MSHRSize>
  <BusOccupancy>0</BusOccupancy>
  <Nuca>NONE</Nuca>
  <NucaMapping>S</NucaMapping>
  <LeakageEnergy>0.1092</LeakageEnergy>
  <ReadDynamicEnergy>0.33964264705</ReadDynamicEnergy>
  <WriteDynamicEnergy>0.33964264705</WriteDynamicEnergy>
  <CacheType>Data</CacheType>
</dcache>

## Slide 167: Cache: Detailed Configuration
<dcache>
  <WriteMode>WB</WriteMode>
  <BlockSize>64</BlockSize>
  <Associativity>8</Associativity>
  <Size>32768</Size>
  <Latency>3</Latency>
  <PortType>FCFS</PortType>
  <AccessPorts>4</AccessPorts>
  <PortOccupancy>1</PortOccupancy>
  <Coherence>D1</Coherence>
  <NumBuses>1</NumBuses>
  <MSHRSize>16</MSHRSize>
  <BusOccupancy>0</BusOccupancy>
  <Nuca>NONE</Nuca>
  <NucaMapping>S</NucaMapping>
  <LeakageEnergy>0.1092</LeakageEnergy>
  <ReadDynamicEnergy>0.33964264705</ReadDynamicEnergy>
  <WriteDynamicEnergy>0.33964264705</WriteDynamicEnergy>
  <CacheType>Data</CacheType>
</dcache>
Size parameters

## Slide 168: Cache: Detailed Configuration
<dcache>
  <WriteMode>WB</WriteMode>
  <BlockSize>64</BlockSize>
  <Associativity>8</Associativity>
  <Size>32768</Size>
  <Latency>3</Latency>
  <PortType>FCFS</PortType>
  <AccessPorts>4</AccessPorts>
  <PortOccupancy>1</PortOccupancy>
  <Coherence>D1</Coherence>
  <NumBuses>1</NumBuses>
  <MSHRSize>16</MSHRSize>
  <BusOccupancy>0</BusOccupancy>
  <Nuca>NONE</Nuca>
  <NucaMapping>S</NucaMapping>
  <LeakageEnergy>0.1092</LeakageEnergy>
  <ReadDynamicEnergy>0.33964264705</ReadDynamicEnergy>
  <WriteDynamicEnergy>0.33964264705</WriteDynamicEnergy>
  <CacheType>Data</CacheType>
</dcache>
Cache Ports

## Slide 169: Cache: Detailed Configuration
<dcache>
  <WriteMode>WB</WriteMode>
  <BlockSize>64</BlockSize>
  <Associativity>8</Associativity>
  <Size>32768</Size>
  <Latency>3</Latency>
  <PortType>FCFS</PortType>
  <AccessPorts>4</AccessPorts>
  <PortOccupancy>1</PortOccupancy>
  <Coherence>D1</Coherence>
  <NumBuses>1</NumBuses>
  <MSHRSize>16</MSHRSize>
  <BusOccupancy>0</BusOccupancy>
  <Nuca>NONE</Nuca>
  <NucaMapping>S</NucaMapping>
  <LeakageEnergy>0.1092</LeakageEnergy>
  <ReadDynamicEnergy>0.33964264705</ReadDynamicEnergy>
  <WriteDynamicEnergy>0.33964264705</WriteDynamicEnergy>
  <CacheType>Data</CacheType>
</dcache>
Name of the cache coherence scheme
Specify as None if the cache is not coherent

## Slide 170: Cache: Detailed Configuration
<dcache>
  <WriteMode>WB</WriteMode>
  <BlockSize>64</BlockSize>
  <Associativity>8</Associativity>
  <Size>32768</Size>
  <Latency>3</Latency>
  <PortType>FCFS</PortType>
  <AccessPorts>4</AccessPorts>
  <PortOccupancy>1</PortOccupancy>
  <Coherence>D1</Coherence>
  <NumBuses>1</NumBuses>
  <MSHRSize>16</MSHRSize>
  <BusOccupancy>0</BusOccupancy>
  <Nuca>NONE</Nuca>
  <NucaMapping>S</NucaMapping>
  <LeakageEnergy>0.1092</LeakageEnergy>
  <ReadDynamicEnergy>0.33964264705</ReadDynamicEnergy>
  <WriteDynamicEnergy>0.33964264705</WriteDynamicEnergy>
  <CacheType>Data</CacheType>
</dcache>
Energy Parameters
1) Dynamic Energy: Joules/access
2) LeakageEnergy: Joules/second

## Slide 171
BUS
L3 cache (LLC)
Directory
Hierarchy 2 (L2 Cache is now private)
Pipeline
Core 0
i-cache
d-cache
L2 cache
Pipeline
Core 1
i-cache
d-cache
L2 cache
Pipeline
Core 2
i-cache
d-cache
L2 cache
Pipeline
Core 3
i-cache
d-cache
L2 cache

## Slide 172: Memory Hierarchy
<Core>
...
<Cache firstLevel=“true” name=“L1_I” nextLevel=“L2” type=“icache”/>
<Cache firstLevel=“true” name=“L1_D” nextLevel=“L2” type=“dcache”/>
<Cache name=“L2” nextLevel=“L3” type=“L2Cache”/>
</Core>
<SharedCaches>
<Cache name=“L3” type=“L3Cache”/>
<Cache name=“D1” type=“Directory1”/>
</SharedCaches>

## Slide 173: Memory Hierarchy
<Core>
...
<Cache firstLevel=“true” name=“L1_I” nextLevel=“L2” type=“icache”/>
<Cache firstLevel=“true” name=“L1_D” nextLevel=“L2” type=“dcache”/>
<Cache name=“L2” nextLevel=“L3” type=“L2Cache”/>
</Core>
<SharedCaches>
<Cache name=“L3” type=“L3Cache”/>
<Cache name=“D1” type=“Directory1”/>
</SharedCaches>
High level modifications:
L2Cache is private, its nextLevel is L3
L3 replaces L2 as the LLC

## Slide 174: Memory Hierarchy
<Core>
...
<Cache firstLevel=“true” name=“L1_I” nextLevel=“L2” type=“icache”/>
<Cache firstLevel=“true” name=“L1_D” nextLevel=“L2” type=“dcache”/>
<Cache name=“L2” nextLevel=“L3” type=“L2Cache”/>
</Core>
<SharedCaches>
<Cache name=“L3” type=“L3Cache”/>
<Cache name=“D1” type=“Directory1”/>
</SharedCaches>
Changes to the detailed configuration of caches:
dcache:
  WriteThrough instead of WriteBack
  No coherence
L2 cache becomes coherent cache

## Slide 175
Hierarchy 3 (L2 Cache is now shared between two cores)

## Slide 176: Memory Hierarchy
<Core>
...
<Cache firstLevel=“true” name=“L1_I” nextLevel=“L2” nextLevelID=“$i/2” type=“icache”/>
<Cache firstLevel=“true” name=“L1_D” nextLevel=“L2” nextLevelID=“$i/2” type=“dcache”/>
</Core>
<SharedCaches>
<Cache name=“L2” numComponents=“2” nextLevel=“L3” type=“L2Cache”/>
<Cache name=“L3” type=“L3Cache”/>
<Cache name=“D1” type=“Directory1”/>
</SharedCaches>

## Slide 177: Memory Hierarchy
<Core>
...
<Cache firstLevel=“true” name=“L1_I” nextLevel=“L2” nextLevelID=“$i/2” type=“icache”/>
<Cache firstLevel=“true” name=“L1_D” nextLevel=“L2” nextLevelID=“$i/2” type=“dcache”/>
</Core>
<SharedCaches>
<Cache name=“L2” numComponents=“2” nextLevel=“L3” type=“L2Cache”/>
<Cache name=“L3” type=“L3Cache”/>
<Cache name=“D1” type=“Directory1”/>
</SharedCaches>

## Slide 178: Memory Hierarchy
<Core>
...
<Cache firstLevel=“true” name=“L1_I” nextLevel=“L2” nextLevelID=“$i/2” type=“icache”/>
<Cache firstLevel=“true” name=“L1_D” nextLevel=“L2” nextLevelID=“$i/2” type=“dcache”/>
</Core>
<SharedCaches>
<Cache name=“L2” numComponents=“2” nextLevel=“L3” type=“L2Cache”/>
<Cache name=“L3” type=“L3Cache”/>
<Cache name=“D1” type=“Directory1”/>
</SharedCaches>
Specify nextLevelID in terms of ID of this cache
ID of private caches = ID of the core
icache[0],icache[1],dcache[0], dcache[1]-> L2[0]
icache[2],icache[3],dcache[2], dcache[3]-> L2[1]

## Slide 179
Specifying the Chip Layout and Configuring the NoC

## Slide 180
Chip 1:
Core 0 | Core 1 | Core 2 | Core 3
Core 4 | Core 5 | Core 6 | Core 7
Core 8 | Core 9 | Core 10 | Core 11
Core 12 | Memory Controller | Directory | L2 (LLC)
4 4
C C C C
C C C C
C C C C
C M D L2
NocConfig.txt

## Slide 181
Chip 1:
Core 0 | Core 1 | Core 2 | Core 3
Core 4 | Core 5 | Core 6 | Core 7
Core 8 | Core 9 | Core 10 | Core 11
Core 12 | Memory Controller | Directory | L2 (LLC)
4 4
C C C C
C C C C
C C C C
C M D L2
NocConfig.txt
#rows #columns

## Slide 182
Chip 1:
Core 0 | Core 1 | Core 2 | Core 3
Core 4 | Core 5 | Core 6 | Core 7
Core 8 | Core 9 | Core 10 | Core 11
Core 12 | Memory Controller | Directory | L2 (LLC)
4 4
C C C C
C C C C
C C C C
C M D L2
NocConfig.txt
Cores in the first row
Core 0, Core 1, Core 2, Core 3

## Slide 183
Chip 1:
Core 0 | Core 1 | Core 2 | Core 3
Core 4 | Core 5 | Core 6 | Core 7
Core 8 | Core 9 | Core 10 | Core 11
Core 12 | Memory Controller | Directory | L2 (LLC)
4 4
C C C C
C C C C
C C C C
C M D L2
NocConfig.txt
M -> Memory Controller
D -> Directory
L2 -> L2 (LLC)

## Slide 184: NOC: Extra parameters in config.xml
<NOC> <NocConfigFile>NocConfig.txt</NocConfigFile> <NocSelScheme>STATIC</NocSelScheme> <NocNumberOfBuffers>4</NocNumberOfBuffers> <NocPortType>FCFS</NocPortType> <NocAccessPorts>4</NocAccessPorts> <NocPortOccupancy>1</NocPortOccupancy> <NocLatency>1</NocLatency> <NocOperatingFreq>2000</NocOperatingFreq> <NocTopology>TORUS</NocTopology> <NocRoutingAlgorithm>SIMPLE</NocRoutingAlgorithm> <NocLatencyBetweenNOCElements>4</NocLatencyBetweenNOCElements> <NocRouterArbiter>RR_ARBITER</NocRouterArbiter> <TechPoint>90</TechPoint> <NocConnection>ELECTRICAL</NocConnection> <LeakageEnergy>0.1877</LeakageEnergy> <DynamicEnergy>2.1164</DynamicEnergy> </NOC>

## Slide 185: NOC: Extra parameters in config.xml
<NOC> <NocConfigFile>NocConfig.txt</NocConfigFile> <NocSelScheme>STATIC</NocSelScheme> <NocNumberOfBuffers>4</NocNumberOfBuffers> <NocPortType>FCFS</NocPortType> <NocAccessPorts>4</NocAccessPorts> <NocPortOccupancy>1</NocPortOccupancy> <NocLatency>1</NocLatency> <NocOperatingFreq>2000</NocOperatingFreq> <NocTopology>TORUS</NocTopology> <NocRoutingAlgorithm>SIMPLE</NocRoutingAlgorithm> <NocLatencyBetweenNOCElements>4</NocLatencyBetweenNOCElements> <NocRouterArbiter>RR_ARBITER</NocRouterArbiter> <TechPoint>90</TechPoint> <NocConnection>ELECTRICAL</NocConnection> <LeakageEnergy>0.1877</LeakageEnergy> <DynamicEnergy>2.1164</DynamicEnergy> </NOC>
Mesh Torus Ring Bus
Fat Tree Butterfly Omega

## Slide 186
Chip 1:
Memory Controller 0 |  |  | Memory Controller1
Core 0 | Core 1 | Core 2 | Core 3
L2 0 | L2 1 | L2 2 | L2 3
Core 4 | Core 5 | Core 6 | Core 7
L2 4 | L2 5 | L2 6 | L2 7
Core 8 | Core 9 | Core 10 | Core 11
L2 8 | L2 9 | L2 10 | L2 11
Memory Controller 2 |  | Directory | Memory Controller3

## Slide 187
8 4
M - - M
C C C C
L2 L2 L2 L2
C C C C
L2 L2 L2 L2
C C C C
L2 L2 L2 L2
M – C M
NocConfig.txt

## Slide 188
8 4
M - - M
C C C C
L2 L2 L2 L2
C C C C
L2 L2 L2 L2
C C C C
L2 L2 L2 L2
M – C M
NocConfig.txt
Specify this cache as NUCA in its detailed cache configuration

## Slide 189
8 4
M - - M
C C C C
L2 L2 L2 L2
C C C C
L2 L2 L2 L2
C C C C
L2 L2 L2 L2
M – C M
NocConfig.txt
No element in these locations

## Slide 190
8 4
M - - M
C C C C
L2 L2 L2 L2
C C C C
L2 L2 L2 L2
C C C C
L2 L2 L2 L2
M – C M
NocConfig.txt
If there is cache miss at L2 level, the request will be sent to the nearest memory controller

## Slide 191: Energy Simulations
Branch Predictor
Private caches
Shared caches
Coherence elements
Memory controllers
Interconnect
DRAM
TLBs
Pipeline Units
Leakage Energy: Energy consumed in one second of execution
Dynamic Energy: Energy consumed in one access of the element
  Type of access: element specific
  Differentiated accesses: Need to be added. Example: Cache
    Read dynamic energy
    Write dynamic energy

## Slide 192
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00

## Slide 193
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00
ParTejas GPUTejas Tejas-Java | 

## Slide 194
Contributions
Separate clock domains
Special barriers (Phasers)
Lock free datastructures for shared caches
Core partitioning
AIM: To Parallelize a given sequential architectural simulator

## Slide 195: PARTEJAS
Parallelizing Simulation

## Slide 196: System Overview
Simulator thread
Simulator thread
Simulator thread
Simulator thread
EMULATOR
SHARED MEMORY
No. of Partitions = No. of Simulator Threads

## Slide 198: Challenges
Common Instruction Pools
Separate instruction pool for each simulator thread
Global clock
Different clock domains
Synchronization issues
Shared instances
Parallel port
Synchronization issues

## Slide 199: Evaluation
Four 8 core 2.20 Ghz Intel Xeon GHz processors
Architecture
Ubuntu Linux 12.10
OS
64 GB
RAM
64
Threads
Sun’s Java SE Runtime 1.6.0
Platform

## Slide 200: Performance
Multi-Issue Inorder : ~4.6 MIPS
Out-of-Order : ~2.34 MIPS

## Slide 201: Performance
Input Size:
simsmall
Synchronization:
Phaser
#Cores:
64
Transfer Engine:
Shared Memory
Pipeline:
Multi-Issue Inorder

## Slide 202: Performance
Input Size:
simsmall
Synchronization:
Phaser
#Cores:
64
Transfer Engine:
Shared Memory
Pipeline:
Out of Order

## Slide 203: GPU-TEJAS
Simulating GPU’s

## Slide 204: Why we need GPUTejas ?
Modern GPUs
have 1000+
processing
elements.
GPUs have gone general purpose.
A Simulator is needed to study and design new architectures.
Sequential simulators suffer from performance issues.
Very little prior work in parallel GPU simulation
GPUTejas

## Slide 205: Other GPU Simulators
Attila
Detailed cycle accurate GPU simulator.
GPGPU-Sim
Supports cycle accurate timing simulation for NVDIA GPUs.
Others
Gem5-GPU , Multi2Sim , FusionSim, Ocelot
Highly configurable.
Does not support CUDA and GPGPU framework.
Requires access to source code.
Barra-Sim
A parallel functional GPGPU emulator for the NVIDIA Tesla architecture.
Does not perform timing simulation
Ro et.al.
Parallelized GPGPU-Sim.
Demonstrate a speedup of 4.15x over the sequential GPGPU-Sim on a 8-core system.
GpuTejas is 429.89x faster than GPGPU-Sim

## Slide 206: System Architecture

## Slide 207: System Architecture

## Slide 208: System Architecture

## Slide 209: Evaluation
Four 8 core 2.20 Ghz Intel Xeon GHz processors, 64 threads
Architecture
Ubuntu Linux 12.10
OS
64 GB
RAM
Sun’s Java SE Runtime 1.6.0
Platform
NVIDIA TESLA
GPU

## Slide 210: Simulation Speed
16.42
22.21
11.52
1.48
21.04
23.38
25.44
17.33

## Slide 211: Validation

## Slide 212: Performance
Benchmarks | Execution Time |  | 
 | Native Execution (ms) | GPGPU-sim (s) | GpuTejas (s)
hotspot | 0.85 | 200 | 4.54
bfs | 29.48 | 4517 | 5.36
lud | 2.22 | 168 | 16.31
nn | 0.12 | 3 | 0.86
nw | 6.21 | 1673 | 27.76
pathfinder | 1.02 | 280 | 23.51
heartwall | 162.77 | 91861 | 151.24
mean | 28.95 ms | 14100.29 s | 32.80 s

## Slide 213
Session 1: Motivation and High Level Architecture | 08:30 to 09:00
Session 2: Simulating Different Architectural Components | 09:00 to 10:30
Session 3: Sample Use Cases and Hands-on Demo | 10:00 -- 11:30
Coffee break: 10:30 to 11:00 | 
Session 4: Sister Projects of Tejas | 11:30 to 12:00
ParTejas GPUTejas Tejas-Java | 

## Slide 214: Java Applications
Laptops
Supercomputers
Cell phones
Gaming Consoles
Softwares
Mobile applications
Java is Everywhere, there are billions of Java applications.

## Slide 215: Challenges
Traces enable architecture performance analysis
Challenges to get the execution traces
  Java code is dynamically compiled
  PIN, a binary instrumentation tool crashes
  Java program and virtual machine are represented by a single process to external process
  No publically available tool

## Slide 216: Scope of TejasJava
Performance analysis of Java applications on a particular hardware
Evaluation of different hardware garbage collectors
Other research work that requires execution traces of Java programs

## Slide 217: Running Traces on Tejas
TejasJava System Architecture

## Slide 218: Thank You